## Slide 1: CHAPTER 12 SHARED MEMORY

## Slide 2: Shared Memory
Shared memory is data that is accessed by two or more asynchronous instruction sequences.
Asynchronous means that there is no predictable time relationship among the various instruction sequences.
Thread: A sequence of instructions; threads are usually asynchronous relative to each other.
Threads include Interrupt Service Routines.

## Slide 3: Asynchronous Access Can Corrupt Shared Data!
Thread A
Thread B
shared = 3 ;
x = 2 * shared ;
shared++ ;
Asynchronous Task Switch or Interrupt

## Slide 4: Task Switch = Interrupt!
Note that interrupts (and thus a context switch) can occur between any two CPU instructions, not just between any two C language statements!

## Slide 5: Program Complexity
Threads are easier to design, understand, and debug when they are as independent of other threads as possible.
Shared memory reduces thread independence.
Shared memory increases program complexity.

## Slide 6: How Sharing Can Occur
Shared Global Data: A public (global) object is accessed by two or more threads, or
Shared Private Data: The address of a private object is given to another thread, or
Shared Functions: A static object is accessed by a function that is called by more than one thread.

## Slide 7: Shared Global Data
Easiest cause of sharing to recognize.
Minimize global objects, whether your program is multi-threaded or not, because global objects allow linkages between functions and thus contribute to program complexity.

## Slide 8: Shared Private Data
If one thread gives the address of one of its private objects to another thread, then that object can be accessed by both threads and is no longer private.
Neither changing the object's scope or memory allocation method will eliminate this form of shared memory.

## Slide 9: Shared Functions
A shared function is one that is called by more than one thread.
Any function called by a shared function is also a shared function.
Any static object (local or global) referenced within a shared function is shared data.

## Slide 10: Thread-Safe Functions
Thread-safe functions are shared functions that only modify thread-specific data.
Local automatic and dynamic objects are inherently thread-specific; local static objects are not.

## Slide 11
Enters strstr
Exits strstr
Enters, executes, and exits strstr
strstr suspended
Thread A
Thread B
Context Switch
Context Switch

## Slide 12: Re-Entrant Functions
Re-entrant functions are those which may be safely re-entered without data corruption.
Re-entrant functions never modify local static objects.
Re-entrant functions are inherently thread-safe.

## Slide 13: Read-Only Data
Data corruption only occurs when shared data is modified.
Shared data that is read but never written can never be corrupted.
Add the keyword “const” to have the compiler verify that all access to the object is read-only:
static const char digits[] = “0123456789” ;

## Slide 14: Coding Practices to Avoid
Functions that keep internal state in local static objects.
  E.g., strtok, rand
Functions that return the address of a local static object.
  E.g., ctime, asctime, localtime, gmtime, getenv, strerror and tmpnam.

## Slide 15: Function with Internal State
char *strtok(char *string, char *delimeters)
{
static char *cursor ;
char *beg, *end ;
if (string != NULL) cursor = string ;
if (cursor == NULL) return NULL ;
beg = cursor + strspn(cursor, delimeters) ;
if (*beg == '\0') return NULL ;
end = strpbrk(beg, delimeters) ;
if (end == NULL) cursor = NULL ;
else { *end++ = '\0'; cursor = end; }
return beg ;
}
Problem: Only one instance for all threads.

## Slide 16: Fixing Internal State
char *strtok_r(char *string, char *delimeters, char **cursor)
{
char *beg, *end ;
if (string != NULL) *cursor = string ;
...
return beg ;
}
char *my_cursor ; … p = strtok_r(…, …, &my_cursor) ; …
Thread-specific version supplied by caller.

## Slide 17: Function Returning Static Buffer
char *Make_Filename(char *name, int version)
{
static char fname_bfr[13] ;
...
return fname_bfr ;
}

## Slide 18: Fixing Static Buffer (Sol’n #1)
char *Make_Filename(char *name, int version, char *fname_bfr)
{
…
return fname_bfr ;
}
Let caller provide a thread-specific instance of a buffer.

## Slide 19: Fixing Static Buffer (Sol’n #2)
char *Make_Filename(char *name, int version)
{
char *fname_bfr = (char *) malloc(13) ;
if (fname_bfr == NULL) return NULL ;
…
return fname_bfr ;
}
Thread-specific instance of buffer allocated from heap when function is called; must be released by caller.

## Slide 20
Main Program
ISR
SUB R1,R1,#1
STR R1,[R0,#count_offset]
...
LDR R0,pointer2q
LDR R1,[R0,#count_offset]
ADD R1,R1,#1
STR R1,[R0,#count_offset]
...
pointer2q->count--
pointer2q->count++
LDR R0,pointer2q
LDR R1,[R0,#count_offset]

## Slide 21: Protected Access
extern long shared_counter ;
disable() ;
shared_counter++ ;
enable() ;
...
disable() ;
shared_counter = 0 ;
enable() ;
A simple increment may require more than one machine instruction - perhaps the processor has no single increment instruction, the compiler doesn't use it, or the integer exceeds the basic processor word size.
A simple store may also require more than one instruction if the object exceeds the processor word size.

## Slide 22: Multiple Read-Only Access
extern long shared_variable ;
long private_copy ;
/* make a copy with interrupts disabled */
disable() ;
private_copy = shared_variable ;
enable() ;
/* subsequent code can use "private_copy" */
/* without fear of data corruption. */

## Slide 23: When “x = 0” is a Critical Section
Architecture | Data Type | 8-bit CPU | 16-bit CPU | 32-bit CPU
Load/Store Architecture: The only instructions that can reference memory are Load and Store. E.g., RISC processors, such as ARM and MIPS | char |  |  | 
 | short | x1 |  | 
 | long | x | x1 | 
 | long long | x | x | x1
 | pointer | x | x1 | 
Other Architectures: Instructions like Add and Subtract may have memory operands. E.g., CISC processors, such as Intel x86. | char |  |  | 
 | short | x1 |  | 
 | long | x | x1 | 
 | long long | x | x | x1
 | pointer | x | x1 | 
1Assumes single instruction can store a memory operand no larger than the word size of the processor. However, some processors have instructions that can store a double-length operand (e.g., STRD).

## Slide 24: When “x++” is a Critical Section
Architecture | Data Type | 8-bit CPU | 16-bit CPU | 32-bit CPU
Load/Store Architecture: The only instructions that can reference memory are Load and Store. E.g., RISC processors, such as ARM and MIPS | char | x | x | x
 | short | x | x | x
 | long | x | x | x
 | long long | x | x | x
 | pointer | x | x | x
Other Architectures: Instructions like Add and Subtract may have memory operands. E.g., CISC processors, such as Intel x86. | char |  |  | 
 | short | x1 |  | 
 | long | x | x1 | 
 | long long | x | x | x1
 | pointer | x | x1 | 
1Assumes that a single instruction can increment an operand no larger than the word size of the processor.

## Slide 25: Type Qualifier “volatile”
Added to the declaration of any object in C to indicate that its value may be modified by mechanisms other than the code in which the declaration appears.
Serves as a reminder that shared data may be modified by another thread or ISR.
Prevents certain compiler optimizations that would otherwise be invalid.
But does not prevent data corruption due to shared memory.

## Slide 26: Volatile and Loop Invariants
long Get_Shared(void)
{
extern long shared ;
long validated ;
do
{
validated = shared ;
} while (validated != shared) ;
return validated ;
}
Since “shared” is not modified within the loop, an optimizing compiler might preload a CPU register with the value of "shared" before entering the loop, and access the register instead of the slower memory.
Insert the keyword “volatile” here to prevent the compiler optimizations.
This code attempts to read a shared variable without disabling interrupts or using spin locks or semaphores.