## Slide 1: CHAPTER 2 Data Representation

## Slide 2: Kinds Of Data
Numbers
  Integers
    Unsigned
    Signed
  Reals
    Fixed-Point
    Floating-Point
  Binary-Coded Decimal
Text
  ASCII Characters
  Strings
Other
  Graphics
  Images
  Video
  Audio

## Slide 3: Numbers Are Different!
Computers use binary (not decimal) numbers (0's and 1's).
  Requires more digits to represent the same magnitude.
Computers store and process numbers using a fixed number of digits (“fixed-precision”).
Computers represent signed numbers using 2's complement instead of the more natural (for humans) “sign-plus-magnitude” representation.

## Slide 4: Positional Number Systems
Numeric values are represented by a sequence of digit symbols.
Symbols represent numeric values.
  Symbols are not limited to ‘0’-’9’!
Each symbol’s contribution to the total value of the number is weighted according to its position in the sequence.

## Slide 5: Polynomial Evaluation
Whole Numbers (Radix = 10):
123410 = 1  103 + 2  102 + 3  101 + 4  100
With Fractional Part (Radix = 10):
36.7210 = 3  101 + 6  100 + 7  10-1 + 2  10-2
General Case (Radix = R):
(S1S0.S-1S-2)R =
S1  R1 + S0  R0 + S-1  R -1 + S-2  R-2

## Slide 6: Converting Radix R to Decimal
36.728 = 3  81 + 6  80 + 7  8-1 + 2  8-2
= 24 + 6 + 0.875 + 0.03125
= 30.9062510
Important: Polynomial evaluation doesn’t work if you try to convert in the other direction – I.e., from decimal to something else! Why?

## Slide 7: Binary to Decimal Conversion
Converting to decimal, so we can use polynomial evaluation:
101101012
= 127 + 026 + 125 + 124 + 023 + 122 + 021 + 120
= 128 + 32 + 16 + 4 + 1
= 18110

## Slide 8: Variation on Polynomial Evaluation for converting fractional values
Example: Convert 0.4378 to decimal:
= 48-1 + 38-2 + 78-3
= 40.125 + 30.015625 + 70.001953125
Multiple divisions
Adding long decimal fractions
Alternative approach:
= (482 + 381 + 780) / 83
= (464 + 38 + 71) / 512
= 287 / 512 = 0.56054687510

## Slide 9: Problems: NR  N10
1101012
.1101012
1378
.1378
103
.103
4325
.4325
3F.4A16
F0.0D16

## Slide 10: Decimal to Binary Conversion
Converting to binary – can’t use polynomial evaluation!
Whole part and fractional parts must be handled separately!
  Whole part: Use repeated division.
  Fractional part: Use repeated multiplication.
  Combine results when finished.

## Slide 11: Decimal to Binary Conversion (Whole Part: Repeated Division)
Divide by target radix (2 in this case)
Remainders become digits in the new representation (0 <= digit < R)
Digits produced in right to left order.
Quotient is used as next dividend.
Stop when the quotient becomes zero, but use the corresponding remainder.

## Slide 12: Decimal to Binary Conversion (Whole Part: Repeated Division)
97  2  quotient = 48, remainder = 1 (LSB)
48  2  quotient = 24, remainder = 0.
24  2  quotient = 12, remainder = 0.
12  2  quotient = 6, remainder = 0.
6  2  quotient = 3, remainder = 0.
3  2  quotient = 1, remainder = 1.
1  2  quotient = 0 (Stop) remainder = 1 (MSB)
Result = 1 1 0 0 0 0 12

## Slide 13: Decimal to Binary Conversion (Fractional Part: Repeated Multiplication)
Multiply by target radix (2 in this case)
Whole part of product becomes digit in the new representation (0 <= digit < R)
Digits produced in left to right order.
Fractional part of product is used as next multiplicand.
Stop when the fractional part becomes zero (sometimes it won’t).

## Slide 14: Decimal to Binary Conversion (Fractional Part: Repeated Multiplication)
.1  2  0.2 (fractional part = .2, whole part = 0)
.2  2  0.4 (fractional part = .4, whole part = 0)
.4  2  0.8 (fractional part = .8, whole part = 0)
.8  2  1.6 (fractional part = .6, whole part = 1)
.6  2  1.2 (fractional part = .2, whole part = 1)
Result = .000110011001100112…..
(How much should we keep?)

## Slide 15: .110 = .00011001100110011…..2 How much should we keep?
Mathematician’s Answer:
  Use the proper notation: .00011
Scientist’s Answer:
  Preserve significant digits and round:
  .1  1 part out of 10
  3 binary digits = 1 out of 8  need 4  .0001
  Round: 5th digit = 1, thus .0010
Engineer’s Answer:
  Depends on #bits in the variable (8, 16, 32, 64)

## Slide 16: Moral
Some fractional numbers have an exact representation in one number system, but not in another! E.g., 1/3rd has no exact representation in decimal, but does in base 3!
What about 1/10th when represented in binary?
Can these representation errors accumulate?
What does this imply about equality comparisons of real numbers?

## Slide 17: Problems: N10  NR
2710  N2
.2710  N2
2710  N5
.2710  N5
1/310  N3
2710  N8
.2710  N8
2710  N16
.2710  N16

## Slide 18: Counting
Principle is the same regardless of radix.
  Add 1 to the least significant digit.
  If the result is less than R, write it down and copy all the remaining digits on the left.
  Otherwise, write down zero and add 1 to the next digit position, etc.

## Slide 19: Counting in Binary
Dec | Binary
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
Note the pattern!
LSB (bit 0) toggles on every count.
Bit 1 toggles on every other count.
Bit 2 toggles on every fourth count.
Etc….

## Slide 20: Hexadecimal Numbers (Radix = 16)
The number of digit symbols is determined by the radix (e.g., 16)
The value of the digit symbols range from 0 to 15 (0 to R-1).
The symbols are 0-9 followed by A-F.
Conversion between binary and hex is trivial!
Use as a shorthand for binary (significantly fewer digits are required for same magnitude).

## Slide 21: Memorize This!
Hex | Binary
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
Hex | Binary
8 | 1000
9 | 1001
A | 1010
B | 1011
C | 1100
D | 1101
E | 1110
F | 1111

## Slide 22: Binary/Hex Conversions
Hex digits are in one-to-one correspondence with groups of four binary digits:
0011 1010 0101 0110 . 1110 0010 1111 1000
3 A 5 6 . E 2 F 8
Conversion is a simple table lookup!
Zero-fill on left and right ends to complete the groups!
Works because 16 = 24 (power relationship)

## Slide 23: Problems: NR1NR2, where R1=R2k
11010112  N16
11.010112  N16
11010112  N8
11010.112  N8
102203  N9
10.2203  N9
FACE16  N2
BEEF16  N4
FEED16  N8
18469  N3

## Slide 24: Question:
Do you trust the used car salesman that tells you that the 1966 Mustang he wants to sell you has only the 13,000 miles that it’s odometer shows?
If not, what has happened?
Why?

## Slide 25: Representation Rollover
Consequence of fixed precision.
Computers use fixed precision!
Digits are lost on the left-hand end.
Remaining digits are still correct.
Rollover while counting . . .
  Up: “999999”  “000000” (Rn-1  0)
  Down: “000000”  “999999” (0  Rn-1 )

## Slide 26: Rollover in Unsigned Binary
Consider an 8-bit byte used to represent an unsigned integer:
  Range: 00000000  11111111 (0  25510)
  Incrementing a value of 255 should yield 256, but this exceeds the range.
  Decrementing a value of 0 should yield –1, but this exceeds the range.
  Exceeding the range is known as overflow.

## Slide 27: Surprise! Rollover is not synonymous with overflow!
Rollover describes a pattern sequence behavior.
Overflow describes an arithmetic behavior.
Whether or not rollover causes overflow depends on how the patterns are interpreted as numeric values!
  E.g., In signed two’s complement representation, 11111111  00000000 corresponds to counting from minus one to zero.

## Slide 28: Two Interpretations
101001112
16710
-8910
Signed vs. unsigned is a matter of interpretation; thus a single bit pattern can represent two different values.
Allowing both interpretations is useful:
  Some data (e.g., count, age) can never be negative, and having a greater range is useful.
unsigned
signed

## Slide 29: Why Not Sign+Magnitude?
Complicates addition :
  To add, first check the signs. If they agree, then add the magnitudes and use the same sign; else subtract the smaller from the larger and use the sign of the larger.
  How do you determine which is smaller/larger?
Complicates comparators:
  Two zeroes!
+3 | 0011
+2 | 0010
+1 | 0001
+0 | 0000
-0 | 1000
-1 | 1001
-2 | 1010
-3 | 1011

## Slide 30: Why 2’s Complement?
+3 | 0011
+2 | 0010
+1 | 0001
0 | 0000
-1 | 1111
-2 | 1110
-3 | 1101
-4 | 1100
Just as easy to determine sign as in sign+magnitude.
Almost as easy to change the sign of a number.
Addition can proceed w/out worrying about which operand is larger.
A single zero!
One hardware adder works for both signed and unsigned operands.

## Slide 31: Changing the Sign
+5 = 0101
-5 = 1101
Sign+Magnitude:
2’s Complement:
+5 = 0101
1010 +1
-5 = 1011
Invert
Increment
Change 1 bit

## Slide 32: Easier Hand Method
+4 = 0100
-4 = 1100
Step 1: Copy the bits from right to left, through and including the first 1.
Step 2: Copy the inverse of the remaining bits.

## Slide 33: Representation Width
Be Careful! You must be sure to pad the original value out to the full representation width before applying the algorithm!
Wrong: +25 = 11001  00111  00000111 = +7
Right: +25 = 11001  00011001  11100111 = -25
If positive: Add leading 0’s If negative: Add leading 1’s
Apply algorithm
Apply algorithm
Expand to 8-bits

## Slide 34: Converting 2’s complement numbers to decimal – Approach #1
If MSB is 0, the number is positive.  convert as if it were unsigned.
If MSB is 1, the number is negative.
Find representation of –N, where N is the original number.
Convert N to decimal.
Put a minus sign in front.

## Slide 35: Converting 2’s complement numbers to decimal – Approach #1
Example: 101100102 = ?10
101100102  -010011102
010011102 = 64 + 8 + 4 + 2 = 7810
Answer: -7810

## Slide 36: Converting 2’s complement numbers to decimal – Approach #2
Use polynomial evaluation, but make the contribution of the MSB be negative:
Example: 101100102 = ?10
= -128 + 32 + 16 + 2 = -7810

## Slide 37: 2’s Complement Anomaly!
-128 = 1000 0000 (8 bits)
+128?
Step 1: Invert all bits  0111 1111
Step 2: Increment  1000 0000
Same result with either method! Why?

## Slide 38: Range of Unsigned Integers
Each of ‘n’ bits can have one of two values.
Total # of patterns of n bits = 2 2 2… 2
‘n’ 2’s
= 2n
If n-bits are used to represent an unsigned integer value:
Range: 0 to 2n-1 (2n different values)

## Slide 39: Problems: Unsigned Range
Base 2, 6 digits
Base 3, 6 digits
Base 8, 6 digits
Base 16, 6 digits

## Slide 40: Range of Signed Integers
Half of the 2n patterns will be used for positive values, and half for negative.
Half is 2n-1.
Positive Range: 0 to 2n-1-1 (2n-1 patterns)
Negative Range: -2n-1 to -1 (2n-1 patterns)
8-Bits (n = 8): -27 (-128) to +27-1 (+127)

## Slide 41: Problem: 2’s Comp Range
5 bits
10 bits
16 bits

## Slide 42: Addition & Carries
Cin | X | Y | n | Cout | S
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 1
0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 2 | 1 | 0
1 | 0 | 0 | 1 | 0 | 1
1 | 0 | 1 | 2 | 1 | 0
1 | 1 | 0 | 2 | 1 | 0
1 | 1 | 1 | 3 | 1 | 1
Column “n” is simply the sum of Cin, X and Y.
Columns Cout & S are simply the binary representation of n.

## Slide 43: Subtraction & Borrows
Bin | X | Y | n | Bout | D
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | -1 | -1 | 1 | 1
0 | +1 | 0 | +1 | 0 | 1
0 | +1 | -1 | 0 | 0 | 0
-1 | 0 | 0 | -1 | 1 | 1
-1 | 0 | -1 | -2 | 1 | 0
-1 | +1 | 0 | 0 | 0 | 0
-1 | +1 | -1 | -1 | 1 | 1
Column “n” is simply the sum of Bin, X and Y.
Columns Bout & S are simply the 2’s compl. representation of n.

## Slide 44: Unsigned Overflow
1100 (12)
+0111 ( 7)
10011
Lost
(Result limited by word size)
0011 ( 3) wrong
Value of lost bit is 2n (16).
16 + 3 = 19
(The right answer!)

## Slide 45: Signed Overflow
Overflow is impossible  when adding (subtracting) numbers that have different (same) signs.
Overflow occurs when the magnitude of the result extends into the sign bit position:
  01111111  (0)10000000
  This is not rollover!

## Slide 46: Signed Overflow
-12010  100010002
-1710 +111011112
sum: -13710 1011101112
011101112 (keep 8 bits)
(+11910) wrong
Note: 119 – 28 = 119 – 256 = -137

## Slide 47: Detecting Overflow
Unsigned:
  Carry-out of MSB when incrementing or adding.
  Borrow-out of MSB when decrementing or subtracting.
Signed (2’s complement):
  Impossible when adding numbers of different signs.
  Impossible when subtracting numbers of same sign.
  Human Method: Sign of result different from operands.
  Computer Method: Carries/Borrows in/out of MSB differ.

## Slide 48: Problems: Overflow
Unsigned (4 bits)
01010 11100
0101 1011
+0101 +0110
1010 0001
11100 01000
0100 1011
-0110 -0101
1110 0110
2’s comp. (4 bits)
01010 11100
0101 1011
+0101 +0110
1010 0001
11100 01000
0100 1011
-0110 -0101
1110 0110

## Slide 49: Comparing Integers Which is Greater: 1001 or 0011?
Unsigned:
Signed (2’s Complement):
Borrows | 0 | 1 | 1 | 0 | 0
X |  | 1 | 0 | 0 | 1
Y | - | 0 | 0 | 1 | 1
X-Y |  | 0 | 1 | 1 | 0
Borrow Out | Relationship
0 | X ≥ Y
1 | X < Y
1001 ≥ 0011
Overflow!
Positive
Sign of X-Y | Overflow | True Sign | Relationship
Positive | No | Positive | X ≥ Y
Negative | Yes | Positive | 
Positive | Yes | Negative | X < Y
Negative | No | Negative | 
Borrow Out = 1
1001 < 0011

## Slide 50: Floating-Point Reals
Three components:
   significand  2exponent
Sign
An unsigned fractional value
A biased integer value
Base is implied
31 | 30 | 23 | 22 | 0
 | Exponent |  | Fractional Bits of Significand | 

## Slide 51: Single-precision Floating-point Representation
S Exp+127 Significand
2.000 0 10000000 (1).00000000000000000000000
1.000 0 01111111 (1).00000000000000000000000
0.750 0 01111110 (1).10000000000000000000000
0.500 0 01111110 (1).00000000000000000000000
0.000 0 00000000 (0).00000000000000000000000
-0.500 1 01111110 (1).00000000000000000000000
-0.750 1 01111110 (1).10000000000000000000000
-1.000 1 01111111 (1).00000000000000000000000
-2.000 1 10000000 (1).00000000000000000000000

## Slide 52: Representation of Characters
00100100
Interpretation
Representation
$
ASCII Code

## Slide 53: Character Constants in C
To distinguish a character that is used as data from an identifier that consists of only one character long:
x is an identifier.
‘x’ is a character constant.
The value of ‘x’ is the ASCII code of the character x.

## Slide 54: Character Escapes
A way to represent characters that do not have a corresponding graphic symbol.
\b Backspace ‘\b’
\t Horizontal Tab ‘\t’
\n Linefeed ‘\n’
\r Carriage return ‘\r’
See Table 2-9 in the text for others.
Escape Character
Character Constant

## Slide 55: Representation of Strings
48
65
6C
6C
6F
00
05
H
e
l
l
o
H
e
l
l
o
C uses a terminating “NUL” byte of all zeros at the end of the string.
Pascal uses a prefix count at the beginning of the string.
48
65
6C
6C
6F

## Slide 56: String Constants in C
C string constant
Character string
COEN 20 is “fun”!
“COEN 20 is \“fun\”!”
43
4F
45
4E
20
32
30
20
69
73
C
O
E
N
2
0
i
\0
!
”
n
u
f
“
s
20
22
66
75
6E
22
21
00

## Slide 57: Binary Coded Decimal (BCD)
0111
0011
0000
0111
0000
0011
7
3
7
3
Packed (2 digits per byte):
Unpacked (1 digit per byte):