## Slide 1: CHAPTER 3 Implementing Arithmetic

## Slide 2: Two Interpretations
101001112
16710
-8910
Signed vs. unsigned is a matter of interpretation; thus a single bit pattern can represent two different values.
Allowing both interpretations is useful:
  Some data (e.g., count, age) can never be negative, and having a greater range is useful.
unsigned
signed

## Slide 3: Which is Greater: 1001 or 0011?
Answer: It depends!
So how does the computer decide:
“if (x > y)..” /* Is this true or false? */
It’s a matter of interpretation, and depends on how x and y were declared: signed? Or unsigned?

## Slide 4: Which is Greater: 1001 or 0011?
signed int x, y ; MOV EAX,[x] CMP EAX,[y] if (x > y) …  JLE Skip_Then_Clause
unsigned int x, y ; MOV EAX,[x] CMP EAX,[y] if (x > y) …  JBE Skip_Then_Clause

## Slide 5: One Hardware Adder Handles Both: Unsigned and 2’s Complement Signed
9
3
+
12
+
-7
+3
- 4
0011
Hardware Adder
1100
1001
Manipulates bit patterns, not numbers!

## Slide 6: Why Not Sign+Magnitude?
9
3
+
12
+
-1
+3
- 4
0011
Hardware Adder
1100
1001
Right!
Wrong!

## Slide 7: Subtraction Is Easy!
Adder
Controlled
Inverter
A
B
0 = add, 1 = sub (A-B)
Result
Just a bunch of exclusive-OR gates!

## Slide 8: Signed vs. Unsigned Multiplication
Unsigned
Decimal Binary
12 1100
4 0100
48 00110000
Signed (2’s complement)
Decimal Binary
-4 1100
4 0100
-16 11110000
Multiplying two n-bit numbers produces 2n bits of product.
Least-significant halves of products are always identical, but most-significant halves will sometimes differ.

## Slide 9: Arithmetic Shifting
Multiplying by a power of 2 = shift left:
  13 x 8 = 11012 x 23 = 11010002
Dividing by a power of 2 = right shift?
  +13 ÷ 4 = 011012 ÷ 22 = 000112 = +310 YES
  -13 ÷ 4 = 100112 ÷ 22 = 111002 = -410 NO!

## Slide 10: Multiplication by a Constant
1310 x N = 11012 x N = 8N + 4N + 1N
= (N << 3) + (N << 2) + N
2 shifts + 2 additions
On an old CPU, a multiply may take 100 times as long as an add or a shift, and the above will be 25 times faster!

## Slide 11: Division by a constant = Multiplication by a constant!
a7…….a0
0………0
a7…….a0
× 28/1 =
A
A × 28/1 =
a7…….a0
a0………0
0a7……a1
× 28/2 =
A × 28/2 =
A/2
a7…….a0
a1a0………0
00a7…a2
× 28/4 =
A × 28/4 =
A/4
a7…….a0
× 28/B =
A × 28/B =
A/B
Generalizing…

## Slide 12: Reciprocal Multiplication
A7..0 ÷ B7..0 = A × (1/B)
= [ A × (28/B) ]15..0 ÷ 28
= [A × (28/B)] 15..8

## Slide 13: Problems: Reciprocal Multiplication
8×8 Multiplication
A÷15  A×?
A÷100  A×?
16×16 Multiplication
A÷397  A×?
A÷1000  A×?

## Slide 14: Fixed-Point Reals
Three components:
0   00.00   0
Whole part
Fractional part
Implied binary point

## Slide 15: Fixed vs. Floating
Floating-Point:
  Pro: Large dynamic range determined by exponent; resolution determined by significand.
  Con: Implementation of arithmetic in hardware is complex (slow).
Fixed-Point:
  Pro: Arithmetic is implemented using regular integer operations of processor (fast).
  Con: Limited range and resolution.

## Slide 16: Fixed-Point & Scale Factors
The position of the binary point is determined by a scale factor.
Different variables can have different scale factors.
Determine scale factor by expected range and required resolution.
Programmer must keep track of scale factors! (Tedious)

## Slide 17: Fixed-Point Add/Subtract Using Operands w/Same Scale Factors
Operand/ Result | Bit Pattern | Integer | Scale Factor | =Value
A | 00011.110 | +30 | 2-3 = 1/8 | +3.750
B | 00110.011 | +51 | 2-3 = 1/8 | +6.375
A + B | 01010.001 | +81 | 2-3 = 1/8 | +10.125
A - B | 11101.011 | -21 | 2-3 = 1/8 | -2.625

## Slide 18: Fixed-Point Add/Subtract Using Operands w/Different Scale Factors
Must align binary points before adding or subtracting; this makes scale factors the same.
Two possibilities:
  If you shift the operand with fewer fractional bits left, be careful that it doesn't cause an overflow.
  If you shift the operand with more fractional bits right, be careful that it doesn't cause a loss of precision.
Either approach may be used, but the scale factor of the resulting sum or difference will be quite different.

## Slide 19: Fixed-Point Multiplication/Division
No need to pre-align binary points!
Number of fractional bits in result (determines the scale factor):
  Multiplication: The number of fractional bits in the multiplicand plus the number in the multiplier.
  Division: The number of fractional bits in the dividend less the number in the divisor.

## Slide 20: Multiplying Fixed-Point Real Numbers.
Operand/
Result
Bit Pattern
Int
Scale Factor
Value
A
0000000000011.110
30
2-3 = 1/8
+3.7500
B
00000000001100.11
51
2-2 = 1/4
+12.7500
A  B
00000101111.11010
=1530
2-3-2 = 1/32
+47.8125

## Slide 21: Dividing Fixed-Point Real Numbers.
Operand/
Result
Bit Pattern
Int
Scale Factor
=Value
A
00000101111.11010
1530
2-5 = 1/32
+47.8125
B
0000000001110.011
115
2-3 = 1/8
+14.3750
A  B
00000000000011.01
=13
2-5+3 = 1/4
+3.2500

## Slide 22: Shifting Before Dividing Fixed-Point Real Numbers.
Operand/
Result
Bit Pattern
Int
Scale Factor
=Value
23A
00101111.11010000
12240
2-8 = 1/256
+47.8125
B
0000000001110.011
115
2-3 = 1/8
+14.3750
23A  B
00000000011.01010
=106
2-8+3 = 1/32
+3.3125

## Slide 23: 16.16 Fixed-Point Format
0   00.00   0
16-bits
16-bits
Implied binary point

## Slide 24: Problems: 8.8 Fixed-Point Representation
-10.7210  ?2
45.3710  ?2
= -(10.7228)/28 = -2744/28
= -0000101010111000/28
= 11110101.01001000

## Slide 25: 16.16 Fixed-Point Multiplication
 |  | 31 | 0 | 
 |  | Whole Part | Fractional Part | Multiplicand
 |  | 31 | 0 | 
 |  | Whole Part | Fractional Part | Multiplier
63 | 32 | 31 | 0 | 
Discard | Whole Part | Fractional Part | Discard | Product
Note: On a 32-bit CPU, you can simply use the regular integer multiply instruction, which produces a 64-bit product stored in a pair of 32-bit registers.

## Slide 26: 16.16 Fixed-Point Division
63 |  |  | 0 | 
Sign Extension | Whole Part | Fractional Part | Fill with 0’s | Dividend
 |  | 31 | 0 | 
 |  | Whole Part | Fractional Part | Divisor
 |  | 31 | 0 | 
 |  | Whole Part | Fractional Part | Quotient

## Slide 27: “Brute-Force” 32.32 Format
0   00.00   0
32-bits
32-bits
Implied binary point
This format uses lots of bits, but memory is relatively cheap and it supports both very large and very small numbers. If all variables use this same format (i.e., a common scale factor), programming is simplified. This is the strategy used in the Sony PlayStation.

## Slide 28: 32.32 Fixed-Point Multiplication
 |  | 63 | 0 | 
 |  | Whole Part | Fractional Part | Multiplicand
 |  | 63 | 0 | 
 |  | Whole Part | Fractional Part | Multiplier
127 | 64 | 63 | 0 | 
Discard | Whole Part | Fractional Part | Discard | Product
Problem: How do you compute the product of two 64-bit numbers using a 32-bit CPU?

## Slide 29: 32.32 Fixed-Point Multiplication
Strategy:
Consider how to compute the 128-bit product of two 64-bit unsigned integers.
Modify that result to handle signed integers.
Note how discarding the 64 unused bits of the 128-bit product simplifies the computation.

## Slide 30: 32.32 Fixed-Point Multiplication
Ahi Bhi
AuBu = (232Ahi + Alo)( 232Bhi + Blo)
= 264Ahi Bhi + 232(Ahi Blo + Alo Bh) + Alo Blo
Ahi Blo + Alo Bh
Alo Blo
not used
Ahi Bhi
not used
Alo Blo

## Slide 31: 32.32 Fixed-Point Multiplication
First consider a 64-bit unsigned number:
Au = 263A63 + 262A62 + … + 20A0
= 263A63 + (262A62 + … + 20A0)
= 263A63 + A62..0
where A62..0 = 262A62 + … + 20A0

## Slide 32: 32.32 Fixed-Point Multiplication
Thus the 128-bit product of two 64-bit unsigned operands would be:
AuBu = (263A63 + A62..0 )(263B63 + B62..0 )
= 2126A63B63 + 263(A63 B62..0 + B63 A62..0 )
+ A62..0 B62..0

## Slide 33: 32.32 Fixed-Point Multiplication
Now consider a 64-bit signed number:
As = -263A63 + 262A62 + … + 20A0
= -263A63 + (262A62 + … + 20A0)
= -263A63 + A62..0

## Slide 34: 32.32 Fixed-Point Multiplication
Thus the 128-bit product of two 64-bit signed operands would be:
AsBs = (-263A63 + A62..0 )(-263B63 + B62..0 )
= 2126A63B63 - 263(A63 B62..0 + B63 A62..0 )
+ A62..0 B62..0

## Slide 35: Unsigned vs. Signed Multiplication
AuBu = 2126A63B63
+ 263(A63B62..0 + B63A62..0)
+ A62..0B62..0
AsBs = 2126A63B63
- 263(A63B62..0 + B63A62..0)
+ A62..0B62..0

## Slide 36: 32.32 Fixed-Point Multiplication
Thus the 128-bit product of two 64-bit signed operands would be:
AsBs = AuBu – 2 (263A63 B62..0 + 263B63 A62..0 )
= AuBu – 264A63 B62..0 – 264B63 A62..0

## Slide 37: 32.32 Fixed-Point Multiplication
What does this result mean?
AsBs = AuBu – 264A63 B62..0 – 264B63 A62..0
If A is negative, subtract B62..0 from the most-significant half of AuBu
If B is negative, subtract A62..0 from the most-significant half of AuBu

## Slide 38: 32.32 Fixed-Point Multiplication
AuBu (128 bits)
B62..0(63 bits)
-
(Subtract if A < 0)
A62..0 (63 bits)
-
(Subtract if B < 0)
don’t need
don’t need
AuBu (64 bits)
don’t need
B31..0
don’t need
A31..0
AsBs (128 bits)
not used
not used
AsBs (64 bits)