## Slide 1: CHAPTER 4 GETTING THE MOST OUT OF C

## Slide 2: Basic Names for Integer Types: char and int
unsigned, signed, short, and long are modifiers (adjectives).
If one or more modifiers is used, int is assumed and may be omitted.
If neither signed or unsigned is used, signed is assumed and may be omitted.
int with no modifier is a data type whose size varies among compilers.

## Slide 3: Integer Data Types

## Slide 4: Mixing Signed & Unsigned Integers
Always TRUE or always FALSE?
unsigned int u ;
...
if (u > -1) ...
The constant -1 is signed, but when combined with an unsigned, the bit pattern used to represent –1 is interpreted as unsigned with a full-scale value! Thus regardless of the value in ‘u’, the condition will always be FALSE.

## Slide 5: Minimum and Maximum Integer Values defined in LIMITS.H
Data Type | Minimum | Maximum
signed char | SCHAR_MIN | SCHAR_MAX
signed short int | SHRT_MIN | SHRT_MAX
signed long int | LONG_MIN | LONG_MAX
signed long long int | LLONG_MIN | LLONG_MAX
unsigned char | 0 | UCHAR_MAX
unsigned short int | 0 | USHRT_MAX
unsigned long int | 0 | ULONG_MAX
unsigned long long int | 0 | ULLONG_MAX

## Slide 6: Contents of ANSI File (limits.h) Notice anything odd?
#define SCHAR_MIN -127 #define SCHAR_MAX 127 #define SHRT_MIN -32767 #define SHRT_MAX 32767 #define INT_MIN -2147483647 #define INT_MAX 2147483647 #define LONG_MIN -2147483647 #define LONG_MAX 2147483647

## Slide 7: 1999 ISO (C99) New Data Types
Signed Unsigned
8-bits int8_t uint8_t
16-bits int16_t uint16_t
32-bits int32_t uint32_t
64-bits int64_t uint64_t
Note: If your compiler doesn’t already provide these data types, you can create your own using typedefs.

## Slide 8: If Your Compiler Doesn’t Support C99
#ifndef __STDC_VERSION__
typedef signed char int8_t ;
typedef signed short int int16_t ;
typedef signed long int int32_t ;
typedef signed long long int int64_t ;
typedef unsigned char uint8_t ;
typedef unsigned short int uint16_t ;
typedef unsigned long int uint32_t ;
typedef unsigned long long int uint64_t ;
#endif

## Slide 9: C99 Header File stdbool.h
#define bool _Bool // New C99 data type
#define false ((_Bool) 0)
#define true ((_Bool) 1)

## Slide 10: Other Alternative Booleans
#ifndef __STDC_VERSION__
#define bool unsigned char // using macros
#define false 0
#define true 1
#endif
#ifndef __STDC_VERSION__
typedef unsigned char bool ; // using unsigned char’s
const unsigned char false = 0 ;
const unsigned char true = 1 ;
#endif
#ifndef __STDC_VERSION__
typedef enum {false = 0, true = 1} bool ; // using an enumerated type
#endif

## Slide 11: #defines, continued
#define ENTRIES(a) (sizeof(a)/sizeof(a[0]))
unsigned counts[100] ;
for (i = 0; i < 100; i++) ...
for (i = 0; i < ENTRIES(counts); i++) ...

## Slide 12: Careful: #define is text substitution!
#define SUM(a, b) a + b
y = 5 * SUM(t1, t2) ;
Becomes…
y = 5 * t1 + t2 ;
#define TIMES(a, b) (a * b)
y = TIMES(t1-2, t2+3) ;
Becomes…
y = (t1 – 2 * t2 + 3) ;

## Slide 13: Packed Operands

## Slide 14: Boolean and Binary Operators
Boolean operators are primarily used to form conditional expressions (as in an if statement)
Bitwise operators are used to manipulate bits.

## Slide 15: Boolean Values
Most implementations of C don't provide a Boolean data type.
Boolean operators yield results of type int, with true and false represented by 1 and 0.
Any numeric data type may be used as a Boolean operand.
Zero is interpreted as false; any non-zero value is interpreted as true.

## Slide 16: Boolean Expressions
(5 || !3) && 6
= (true OR (NOT true)) AND true
= (true OR false) AND true
= (true) AND true
= true
= 1

## Slide 17: Bitwise Operators
Bitwise operators operate on individual bit positions within the operands
The result in any one bit position is entirely independent of all the other bit positions.

## Slide 18: Bitwise Expressions
(5 | ~3) & 6
= (00..0101 OR ~00..0011) AND 00..0110
= (00..0101 OR 11..1100) AND 00..0110
= (11..1101) AND 00..0110
= 00..0100
= 4

## Slide 19: Interpreting the Bitwise-AND

## Slide 20: Interpreting the Bitwise-OR

## Slide 21: Interpreting the Bitwise-XOR

## Slide 22: Testing Bits
A 1 in the bit position of interest is AND'ed with the operand. The result is non-zero if and only if the bit of interest was 1:
if ((bits & 64) != 0) /* check to see if bit 6 is set */
01000000
b7b6b5b4b3b2b1b0
0b6000000
&

## Slide 23: Testing Bits
Since any non-zero value is interpreted as true, the redundant comparison to zero may be omitted, as in:
    if (bits & 64) /* check to see if bit 6 is set */

## Slide 24: Testing Bits
The mask (64) is often written in hex (0x0040), but a constant-valued shift expression provides a clearer indication of the bit position being tested:
    if (bits & (1 << 6)) /* check to see if bit 6 is set */
Almost all compilers will replace such constant-valued expressions by a single constant, so using this form almost never generates any additional code.

## Slide 25: Setting Bits
Setting a bit to 1 is easily accomplished with the bitwise-OR operator:
    bits = bits | (1 << 7) ; /* sets bit 7 */
This would usually be written more succinctly as:
bits |= (1 << 7) ; /* sets bit 7 */
10000000
b7b6b5b4b3b2b1b0
1b6b5b4b3b2b1b0
|

## Slide 26: Clearing Bits
Clearing a bit to 0 is accomplished with the bitwise-AND operator:
    bits &= ~(1 << 7) ; /* clears bit 7 */
(1 << 7) 10000000
~(1 << 7) 01111111

## Slide 27: Inverting Bits
Inverting a bit (also known as toggling) is accomplished with the bitwise-XOR operator as in:
    bits ^= (1 << 6) ; /* flips bit 6 */

## Slide 28: Extracting Bits

## Slide 29: Inserting Bits

## Slide 30: Automatic Insertion and Extraction Using Structure Bit Fields
struct { unsigned seconds :5 , /* secs divided by 2 */ minutes :6 , hours :5 ;
} time ;
time.hours = 13 ;
time.minutes = 34 ;
time.seconds = 18 / 2 ;
Leave the insertion (or extraction) problems to the compiler!

## Slide 31: Packed Structures
#pragma pack(1) // turn off structure padding
typedef struct // This structure occupies 6 bytes
  {
  int8_t a ; // 1 byte (would otherwise pad to 4 bytes)
  int32_t b ; // 4 bytes
  int8_t c ; // 1 byte (would otherwise pad to 4 bytes)
  } ;
#pragma pack() // turn on structure padding

## Slide 32: Pros/Cons of Structure Bit-Fields
Pros:
  Cleaner syntax
  Fewer lines of C code
  Easier to read
  Compiles into bitwise operations
Cons:
  No standard regarding left-to-right vs. right-to-left Bit-Field assignment

## Slide 33: Variant Access with Pointers, Casts, & Subscripting
Given an address, we can cast it as a pointer to data of the desired type, then dereference the pointer by subscripting.
Without knowing the data type used in its declaration, we can read or write various parts of an object named operand using:
((BYTE8 *) &operand)[k]

## Slide 34: Variant Access with Unions

## Slide 35: Variant Access vs. Unions
Both:
  Bit-fields must lie on byte boundaries
Variant Access:
  Syntax is somewhat complex.
  No union declaration required.
Unions:
  Cleaner syntax
  Easier to read
  Compiles into variant access code

## Slide 36: Manipulating Bits in I/O Ports
I/O ports must be accessed using functions.
It is often common for I/O ports to be either read-only or write-only.
It is often common for several I/O ports to be assigned to a single I/O address.

## Slide 37: I/O Addresses Used by One of the IBM/PC Serial Ports.

## Slide 38: I/O Addresses Used by One of the PC Serial Ports.
THR
RBR
BRD
IER
IIR
LCR
MCR
LSR
MSR
2F8
2FA
2F9
2FB
2FD
2FC
2FE
Read-Only
Read-Only
Read-Only
Read-Only
Write-Only
DLAB=1
DLAB=1

## Slide 39: Modifying Bits in Write-Only I/O Ports
The read-modify-write techniques presented earlier for manipulating bits can’t be used.
Solution: Keep in memory a copy of the last bit-pattern written to the port. Apply the read-modify-write techniques to the memory copy, and then write that value to the port.

## Slide 40: Sequential Access to I/O Ports
Sometimes multiple read-only ports assigned to one address are distinguished by the order in which the data is read.
Multiple write-only ports assigned to one address can also be distinguished by order, or by the value of specific bits in part of the data that is written.

## Slide 41: I/O Ports of the 8259 Programmable Interrupt Controller.

## Slide 42: I/O Ports of the 8259 Interrupt Controller in the IBM/PC.
ISR
ICW1
OCW2
OCW3
OCW1
ICW2
ICW3
ICW4
0020
0021
XXX10XXX
XXX00XXX
XXX01XXX
1st
2nd
3rd
Only after writing ICW1

## Slide 43: Accessing a Display Buffer
 | Col 0 | Col 1 |  | Col 79
Row 0 |  |  | … | 
Row 1 |  |  | … | 
 | … | … | … | …
Row 24 |  |  | … | 
uint_8 *p = (char *) 0xB8000
+ 2 * (80 * row + col) ;
*(p + 0) = ascii_code ;
*(p + 1) = attribute_bits ;
-- or --
p[0] = ascii_code ;
p[1] = attribute_bits ;
-- or --
typedef uint_8 CELL[2] ;
typedef CELL ROW[80] ;
ROW *buffer = (ROW *) 0xB8000 ;
buffer[row][col][0] = ascii_code ;
buffer[row][col][1] = attribute_bits ;
Display buffer memory starts at address B800016. Each cell contains 2 bytes: ASCII code and an attribute byte
Each column increases address by 2
Each row increases address by 2×C