## Slide 1: CHAPTER 5 Programming in Assembly Part 1: Computer Organization

## Slide 2: Separate Memory & I/O Busses
CPU
(Arithmetic and Logic Unit, Control Logic, and Registers)
Memory
(Instructions and Data)
I/O
(Disk, keyboard, display, etc.)
Memory Data Transfers
DMA Controller
I/O Transfers

## Slide 3: Memory-Mapped Peripherals
CPU
(Arithmetic and Logic Unit, Control Logic, and Registers)
Memory
(Instructions and Data)
I/O
(Disk, keyboard, display, etc.)
Memory and I/O Data Transfers
DMA Controller

## Slide 4: Memory
2N bytes
Organized into
groups of 4 bytes
Address Bus: N wires
Data Bus: 4x8 wires
Content is 1’s and 0’s. Meaning determined by how data is used (context).
Control Bus:
Read vs Write,
Initiate Cycle,
Data Ready

## Slide 5: Memory (Little Endian Ordering)

## Slide 6: Single Accumulator Architecture

## Slide 7: The Fetch-Execute Cycle

## Slide 8: Instruction Fetch
Memory
IR
Address Bus
Data Bus
ALU
ACC
PC

## Slide 9: The Fetch Phase
1. Memory_Address_Bus  Program_Counter
2. Start Memory Read Operation
3. Increment Program_Counter
4. Wait for Memory Read to Complete
5. Instruction_Register  Memory_Data_Bus
6. Go to execute phase.

## Slide 10
Execution Phase: Load ACC
Memory
IR
Address Bus
Data Bus
ALU
ACC
PC

## Slide 11
Execution Phase: ADD
Memory
IR
Address Bus
Data Bus
ALU
ACC
PC

## Slide 12
Execution Phase: Store ACC
Memory
IR
Address Bus
Data Bus
ALU
ACC
PC

## Slide 13: Execution Phase: Branch
Memory
IR
Address Bus
Data Bus
ALU
ACC
PC

## Slide 14: result  op1 + op2
ACC  MEM[adrs_of_op1]
ACC  ACC + MEM[adrs_of_op2]
MEM[adrs_of_result]  ACC
REG[r]  MEM[adrs_of_op1]
REG[r]  REG[r] + MEM[adrs_of_op2]
MEM[adrs_of_result]  REG[r]
Single Accumulator Machine:
Register Machine:

## Slide 15: The ARM Processor Family

## Slide 16: Three Instruction Sets
ARM Instruction Set
  Instructions are 32 bits wide
  Original RISC (lots of parallelism)
  “Load/Store” Architecture
Thumb Instruction Set
  Subset of ARM instructions, some restrictions
  Instructions are 16 bits wide (more like CISC)
  Intended for compilers
  Less parallelism, longer instruction sequences
  but total code size is 30% smaller
Jazelle Instruction Set
  Java byte codes
Hardware Decoder
16-bit Thumb Instruction
32-bit ARM Instruction

## Slide 17: Three Instruction Sets
 | ARM | Thumb* | Jazelle
Instruction Size | 32 bits | 16 bits | 8 bits
Core instructions | 58 | 30 | > 60% of Java byte codes in hardware; rest in software
Conditional Execution | most | Only branch instructions or in an IT block | N/A
Data processing instructions | Access to barrel shifter and ALU | Separate barrel shifter and ALU instructions | N/A
Program status register | Read/write in privileged mode | No direct access | N/A
Register usage | 15 general purpose registers + pc | 8 general purpose registers + 7 high registers + pc | N/A
* LM3S811 (a Cortex M3 variation) uses the Thumb2 set

## Slide 18: Code Density vs. Performance

## Slide 19: The ARMv7-M “Cortex-M3” Architecture used in LM3S811

## Slide 20: ARM Cortex-M3 CPU
Registers
R0 – R15
Barrel Shifter
Sign Extender
Incrementer
MAC
Data Bus
Address Bus
R15 (pc)
Rn
Rd
Result Bus
ALU
Address Register
Rm

## Slide 21: ARM Registers
R0
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
R12
R13: Stack Pointer (SP)
R14: Link Register (LR)
R15: Program Counter (PC)
Thumb Mode:
8 general purpose registers
7 “high” registers
r8-R12 only accessible with MOV, ADD, or CMP
ARM Mode:
15 general purpose registers

## Slide 22: Status Registers (xPSR)
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 |  | 16 | 15 |  | 10 | 9 | 8 |  | 0
N | C | Z | V | Q |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 or exception # |  | 
 |  |  |  |  | ICI/IT |  | T |  |  |  | ICI/IT |  |  |  |  |  | 
Bits | Name | Description
31 | N | Negative (bit 31 of result is 1)
30 | C | Unsigned Carry
29 | Z | Zero or Equal
28 | V | Signed Overflow
Most important for application programming
APSR
IPSR
EPSR

## Slide 23: Pipelined Instruction Processing
Fetch
Decode
Execute
Read register(s) from Register Bank,
Shift and ALU operation,
Write register(s) back to Register Bank
Decompress thumb instruction, Decode ARM instruction Select registers
16-bit Instruction fetched from memory
PC
PC - 2
PC - 4

## Slide 24: Pipelined Instruction Processing
2nd Instruction (Adrs: PC+2)
Fetch
Decode
Execute
1st Instruction (Adrs: PC)
Fetch
Decode
Execute
3rd Instruction (Adrs: PC+4)
Fetch
Decode
Execute
Time

## Slide 25: ARM Cortex-M3 Bus Structure

## Slide 26: ARM Cortex-M3 Memory

## Slide 27: Bit-Banding
1 word (4 bytes) of address space in the bit-band area = 1 bit in the corresponding primary area.
bit-band alias = bit-band base + 128 × word offset + 4 × bit number
For example, if bit 3 at address 2000100016 is to be modified, the bit-band alias is calculated as: 2200000016 + 12810 × 100016 + 410 × 310 = 2208000C16
Address 2208000C allows direct access to only bit 3 of the byte at address 20001000:
Read from 2208000C: All other bits will be 0’s
Write to 2208000C: All other data bits are ignored; hardware performs a read-modify-write.

## Slide 28: ARM Cortex-M3 Bit-Banding

## Slide 29: Assembler Syntax
L1: ADD R0,R1,#5 ; Replace R0 by sum of R1 and 5
Label
Opcode
Operands
Comment

## Slide 30: Two-Pass Assembler