## Slide 1: CHAPTER 6 Programming in Assembly Part 2: Data Manipulation

## Slide 2: Loading Constants
MOV rd,constant
  Works for 0 - 255 and “some” others
MVN rd,constant ; rd <- ~constant
  Effectively doubles the # of constants
  Assembler converts MOV w/neg. const to MVN
LDR rd,=constant
  An assembler pseudo-op, not an instruction
  Converted to MOV or MVN if possible
  Else converts to LDR rd,[pc,#imm]

## Slide 3: Load (from memory) Instructions
Load/Store Memory | Operation | Notes
LDR Rd,<mem> | Rd  mem32[address] | 
LDRB Rd,<mem> | Rd  mem8[address] | Zero fills
LDRH Rd,<mem> | Rd  mem16[address] | Zero fills
LDRSB Rd,<mem> | Rd  mem8[address] | Sign extends
LDRSH Rd,<mem> | Rd  mem16[address] | Sign extends
LDRD Rt,Rt2,<mem> | Rt2.Rt  mem64[address] | Addr. Offset must be imm.
These instructions never affect flags in xPSR!

## Slide 4: LDRH (Load Halfword)
32-bit Register |  |  |  |  |  |  | 
31 |  |  | 16 | 15 |  |  | 0
15 | 0
16-bit Memory Half-Word (unmodified) | 
0 0 | 0 0
. . . . . . . . . .
. . . . . . . . . .

## Slide 5: LDRSH (Load Signed Halfword)
32-bit Register |  |  |  |  |  |  | 
31 |  |  | 16 | 15 |  |  | 0
15 | 0
16-bit Memory Half-Word (unmodified) | 
. . . . . . . . . .
. . . . . . . . . .

## Slide 6: Store (to memory) Instructions
Load/Store Memory | Operation | Notes
STR Rd,<mem> | Rd  mem32[address] | 
STRB Rd,<mem> | Rd  mem8[address] | 
STRH Rd,<mem> | Rd  mem16[address] | 
STRD Rt,Rt2,<mem> | Rt2.Rt  mem64[address] | Addr. Offset must be imm.
These instructions never affect flags in xPSR!

## Slide 7: STRH (Store Halfword)
31 |  |  | 16 | 15 |  |  | 0
32-bit Register (unmodified) |  |  |  |  |  |  | 
16-bit Memory Half-Word | 
15 | 0
. . . . . . . . . .
Most-significant 16 bits are not written into memory

## Slide 8
32-bit register(s)
int_32, uint_32
int_64, uint_64
uint_16
uint_8
int_8
int_16
LDRB/STRB
LDRSB/STRB
LDRH/STRH
LDRSH/STRH
LDR/STR
LDRD/STRD
unsigned char
signed char
unsigned short int
signed short int
signed long int
unsigned long int
signed long long int
unsigned long long int

## Slide 9: variable  constant
long x32 ;  LDR R0,=0 ; load constant zero
x32 = 0 ; STR R0,x32 ; store all 32 bits
short x16 ;  LDR R0,=0 ; load constant zero
x16 = 0 ; STRH R0,x16 ; store LS 16 bits
char x8 ;  LDR R0,=0 ; load constant zero
x8 = 0 ; STRB R0,x8 ; store LS 8 bits
long long x64 ;  LDR R0,=0 ; load constant zero
x64 = 0 ; STRD R0,R0,x64

## Slide 10: variable  variable (same size)
long a32, b32 ;  LDR R0,b32 ; load 32 bit word
a32 = b32 ; STR R0,a32 ; store all 32 bits
short a16, b16 ;  LDRH R0,b16 ; z-extend 16 to 32
a16 = b16 ; STRH R0,a16 ; store LS 16 bits
char a8, b8 ;  LDRB R0,b8 ; z-extend 8 to 32
a8 = b8 ; STRB R0,a8 ; store LS 8 bits
long long a64, b64 ;  LDRD R0,R1,b64
a64 = b64 ; STRD R0,R1,a64

## Slide 11: small variable  large variable (demotion)
long x32 ; short x16 ; char x8 ;
x8 = (char) x32 ;  LDR R0,x32 ; load all 32 bits
STRB R0,x8 ; store LS 8 bits
x16 = (short) x32 ;  LDR R0,x32 ; load all 32 bits
STRH R0,x16 ; store LS 16 bits
x8 = (char) x16 ;  LDRH R0,x16 ; z-extend 16 to 32
STRB R0,x8 ; store LS 8 bits

## Slide 12: large variable  small variable (unsigned promotion)
unsigned long long u64 ; unsigned long u32 ;
unsigned short u16 ; unsigned char u8 ;
u32 = (unsigned long) u8 ;  LDRB R0,u8
STR R0,u32
u32 = (unsigned long) u16 ;  LDRH R0,u16
STR R0,u32
u16 = (unsigned short) u8 ;  LDRB R0,u8
STRH R0,u16
u64 = (unsigned long long) u32 ;  LDR R0,u32
LDR R1,=0
STRD R0,R1,u64

## Slide 13: large variable  small variable (signed promotion)
signed long long s64 ; signed long s32 ;
signed short s16 ; signed char s8 ;
s32 = (signed long) s8 ;  LDRSB R0,s8
STR R0,s32
s32 = (signed long) s16 ;  LDRSH R0,s16
STR R0,s32
s16 = (signed short) s8 ;  LDRSB R0,s8
STRH R0,s16
s64 = (signed long long) s32 ;  LDR R0,s32
MOV R1,R0,ASR #31
STRD R0,R1,s64

## Slide 14: Memory Access Modes
Used only w/Load/Store Instructions.
Restrictions on LDRD & STRD
Offset Addressing Mode
Pre-Indexed Addressing Mode
Post-Indexed Addressing Mode
Refers to update of Rn
Each has 3 variations
MOST IMPORTANT!

## Slide 15: Offset Addressing (The Most Important Memory Access Mode!)
Syntax | Effective Address | Example
<label> | PC + imm | result
[<Rn>,#imm] | Rn + imm | [r5,#100]
[<Rn>,<Rm>] | Rn + Rm | [r4,r5]
[<Rn>,<Rm>,LSL #<imm>] | Rn + (Rm << imm) | [r4,r5,LSL #3]
Special case of Rn + imm, where Rn = pc
Not available with LDRD or STRD

## Slide 16: Address Calculation
Rm,LSL #constant
Rn
+
Memory Address (Offset and Pre-Indexed Modes)
s
w
i
t
c
h
Rm
left shifter
Instruction Register
#constant
Rm
constant
Pre- and Post-Indexed modes update Rn
Post-Indexed address

## Slide 17: Using Offset Addressing
long *p ;  LDR R0,=0
... LDR R1,p
*p = 0 ; STR R0,[R1]
long *p ;  LDR R0,=0
… LDR R1,p
*(p + 1) = 0 ; STR R0,[R1,#4]
long *p, k ;  LDR R0,=0
… LDR R1,p
*(p + k) = 0 ; LDR R2,k
STR R0,[R1,R2,LSL #2]

## Slide 18: Using Offset Addressing (Cont’d)
char a8[100] ;  LDR R0,=0
long k32 ; ADR R1,a8
… LDR R2,k32
a8[k32] = 0 ; STRB R0,[R1,R2]
short a16[100] ;  LDR R0,=0
… ADR R1,a16
a16[5] = 0 ; STRH R0,[R1,#10]
long a32[100] ;  LDR R0,=0
long k32 ; ADR R1,a32
… LDR R2,k32
a32[k32] = 0 ; STR R0,[R1,R2,LSL #2]

## Slide 19: Pre-Indexed Addressing (Used Infrequently)
Syntax | Effective Address | Example
[<Rn>,#imm] ! | Rn  Rn + imm EA = Rn | [r5,#100] !
[<Rn>,<Rm>] ! | Rn  Rn + Rm EA = Rn | [r4,r5] !
[<Rn>,<Rm>,LSL #<imm>] ! | Rn  Rn + (Rm << imm) EA = Rn | [r4,r5,LSL #3] !
Not available with LDRD or STRD

## Slide 20: Pre-Indexed Addressing (Used Infrequently)
Rm,LSL #imm
Rn
+
Effective Address
s
w
i
t
c
h
Rm
 | imm | 
left shifter
Instruction Register
#imm
Rm

## Slide 21: Post-Indexed Addressing (Used Infrequently)
Syntax | Effective Address | Example
[<Rn >],#imm | EA = Rn Rn  Rn + imm | [r5],#100
[<Rn >],<Rm> | EA = Rn Rn  Rn + Rm | [r4],r5
[<Rn>],<Rm>,LSL #<imm> | EA = Rn Rn  Rn + (Rm << imm) | [r4],r5,LSL #3
Not available with LDRD or STRD

## Slide 22: Post-Indexed Addressing (Used Infrequently)
Rm,LSL #imm
Rn
+
Effective Address
s
w
i
t
c
h
Rm
 | imm | 
left shifter
Instruction Register
#imm
Rm

## Slide 23: Stack Operations
Stack grows down (towards lower memory addresses) 

## Slide 24: Move/Add/Subtract Instructions
Move / Add / Subtract | Operation | {S} | <op> | Notes
ADR Rd,<label> | Rd  PC + imm | n/a | n/a | 
MOV Rd,<op> | Rd  <op> | NZC | imm. const. -or- reg{,<shift>} | 
ADD Rd,Rn,<op> | Rd  Rn + <op> | NZCV |  | 
ADD Rd,Rn,SP,<op> | Rd  Rn + SP + <op> | NZCV |  | 
ADC Rd,Rn,<op> | Rd  Rn + <op> + C | NZCV |  | 
SUB Rd,Rn,<op> | Rd  Rn – <op> | NZCV |  | 
SUB Rd,SP,<op> | Rd  SP – <op> | NZCV |  | 
SBC Rd,Rn,<op> | Rd  Rn – <op> + C – 1 | NZCV |  | 
RSB Rd,Rn,<op> | Rd  <op> –Rn | NZCV |  | 
NEG Rd,Rn | Rd  –Rn | n/a |  | updates NZCV

## Slide 25: Double-Precision Addition
C
R4: z31..0
R2: y31..0
R0: x31..0
+
R3: y63..32
R1: x63..32
+
R5: z63..32
LDRD R0,R1,x LDRD R2,R3,y ADDS R4,R0,R2 ADC R5,R1,R3 STRD R4,R5,z

## Slide 26: Multiply/Divide Instructions
Multiply / Divide | Operation | {S} | Notes
MUL Rd,Rn,Rdm | Rd  Rn x Rdm | NZC | 32-bit product; C  undefined
MLA Rd,Rn,Rm,Ra | Rd  Ra + (Rn x Rm) | n/a | 32-bit product
MLS Rd,Rn,Rm,Ra | Rd  Ra – (Rn x Rm) | n/a | 
UMULL Rdlo,Rdhi,Rn,Rm | RdhiRdlo  Rn x Rm | n/a | Unsigned 64-bit product
UMLAL Rdlo,Rdhi,Rn,Rm | RdhiRdlo  RdhiRdlo + Rn x Rm | n/a | 
SMULL Rdlo,Rdhi,Rn,Rm | RdhiRdlo  Rn x Rm | n/a | Signed 64-bit product
SMLAL Rdlo,Rdhi,Rn,Rm | RdhiRdlo  RdhiRdlo + Rn x Rm | n/a | 
UDIV Rd,Rn,Rm | Rd  Rn ÷ Rm | n/a | Unsigned 32-bit quotient; no remainder
SDIV Rd,Rn,Rm | Rd  Rn ÷ Rm | n/a | Signed 32-bit quotient; no remainder

## Slide 27: Remainder (C  A % B)
LDR R0,A ; R0  dividend (A)
LDR R1,B ; R1  divisor (B)
UDIV R2,R0,R1 ; R2  quotient (A/B)
MLS R0,R2,R1,R0 ; R0  A – B×(A/B)
STR R0,C ; C  remainder

## Slide 28: Bitwise Instructions
Bitwise Instructions | Operation | {S} | <op> | Notes
AND Rd,Rn,<op> | Rd  Rn & <op> | NZC | imm. const. -or- reg{,<shift>} | 
ORR Rd,Rn,<op> | Rd  Rn ¦ <op> | NZC |  | 
EOR Rd,Rn,<op> | Rd  Rn ^ <op> | NZC |  | 
BIC Rd,Rn,<op> | Rd  Rn & ~<op> | NZC |  | 
ORN Rd,Rn,<op> | Rd  Rn ¦ ~<op> | NZC |  | 
MVN Rd,Rn | Rd  ~Rn | NZC |  | 

## Slide 29: Bitwise Instructions
long a, b ; a = b & (1 << 4) ; | LDR R0,b AND R0,R0,#16 STR R0,a
long a ; a &= ~(1 << 4) ; | LDR R0,a BIC R0,R0,#16 STR R0,a

## Slide 30: Bitfield Instructions
Bitfield Instructions | Operation | {S} | Notes
BFC Rd,#lsb,#width | Rd<bits>  0 | n/a | 
BFI Rd,Rn,#lsb,#width | Rd<bits>  Rn<lsb’s> | n/a | 
SBFX Rd,Rn,#lsb,#width | Rd  Rn<bits> | n/a | Sign extends
UBFX Rd,Rn,#lsb,#width | Rd  Rn<bits> | n/a | Zero extends

## Slide 31
struct { uint16_t hours:5, mins:6, secs:5; } time ; uint32_t minutes ; | 
minutes = time.mins ; | LDRH R0,time UBFX R0,R0,#5,#6 STR R0,minutes
time.mins = 55 ; | LDRH R0,time LDR R1,=55 BFI R0,R1,#5,#6 STRH R0,time
6
15 | 11 | 10 | 5 | 4 | 0
hours |  | mins |  | secs (÷ 2) | 

## Slide 32
<shift> | Meaning | Notes
LSL #n | Logical shift left by n bits | Zero fills; 0 ≤ n ≤ 31
LSR #n | Logical shift right by n bits | Zero fills; 1 ≤ n ≤ 32
ASR #n | Arithmetic shift right by n bits | Sign extends; 1 ≤ n ≤ 32
ROR #n | Rotate right by n bits | 1 ≤ n ≤ 32
RRX | Rotate right w/C by 1 bit | 
Shift Codes:
Any of these may be applied to the register option of “<op>” in Move / Add / Subtract, Compare, and Bitwise Groups.

## Slide 33: Shift Instructions
C
RRX
ASR
C
LSR
C
0
ROR
C
LSL
C
0
RRX only shifts by 1 bit, 3rd operand omitted

## Slide 34: Double Precision Left Shift