## Slide 1: CHAPTER 7 Programming in Assembly Part 3: Control Structures

## Slide 2: Compare/Test Instructions
Compare Instructions | Operation | {S} | <op> | Notes
CMP Rn,<op> | Rn – <op> | n/a | imm. const. -or- reg{,<shift>} | Always updates: NZCV
CMN Rn,<op> | Rn + <op> | n/a |  | Always updates: NZCV
TST Rn,<op> | Rn & <op> | n/a |  | Always updates: NZC
TEQ Rn,<op> | Rn ^ <op> | n/a |  | Always updates: NZC
Note: Assembler converts CMP w/neg constant to CMN

## Slide 3: Branch Instructions
Branch Instructions | Operation | {S} | Notes
B{c} label | PC  PC + imm | n/a | “c” is an optional condition code (see next slide)
BL label | PC  PC + imm; LR  rtn adr | n/a | Subroutine call
BX reg | PC  reg | n/a | “BX LR” often used as function return
CBZ Rn,label | If Rn=0, PC  PC + imm | n/a | Cannot append condition code to CBZ
CBNZ Rn,label | If Rn≠0, PC  PC + imm | n/a | Cannot append condition code to CBNZ
ITc1c2c3 cond | Each ci is one of T, E, or empty | n/a | Controls 1-4 instructions in “IT block”

## Slide 4
Condition Code | Meaning | Requirements
EQ | Equal | Z = 1
NE | Not equal | Z = 0
CS | Carry set | C = 1
CC | Carry clear | C = 0
MI | Minus/negative | N = 1
PL | Plus/positive or zero (non-negative) | N = 0
VS | Overflow | V = 1
VC | No overflow | V = 0
HI | Unsigned > (“Higher”) | C = 1 && Z = 0
LS | Unsigned ≤ (“Lower or Same”) | C = 0 ¦¦ Z = 1
GE | Signed ≥ (“Greater than or Equal”) | N = V
LT | Signed < (“Less Than”) | N ≠ V
GT | Signed > (“Greater Than”) | Z = 0 && N = V
LE | Signed ≤ (“Less than or Equal”) | Z = 1 ¦¦ N ≠ V
AL | Always (unconditional) | only used with IT instruction
Any one of these may be appended to any instruction mnemonic when used inside an If-Then-Else (IT) block. (E.g., “IT NE followed by ADDNE” would add only if Z ≠ 0.)
Exceptions: CBZ, CBNZ, CMP, CMN, NEG, TST, or TEQ.

## Slide 5: if-then statement
LDR R0,A CMP R0,#0 BNE L1 LDR R0,=1 STR R0,B L1: …
- or –
LDR R0,A CMP R0,#0 ITT EQ LDREQ R0,=1 STREQ R0,B
A = 0?
B  1
Yes
No
L1:
if (a == 0) b = 1 ;

## Slide 6: Signed vs. Unsigned
Compare | Signed | Unsigned
== | BEQ | BEQ
!= | BNE | BNE
> | BGT | BHI
>= | BGE | Reverse Operands & Use BLS
< | BLT | Reverse Operands & Use BHI
<= | BLE | BLS

## Slide 7: if-then-else statement
LDR R0,A LDR R1,B CMP R0,R1 BLE L1 LDR R0,=1 B L2 L1: LDR R0,=0 L2: STR R0,C …
- or –
LDR R0,A LDR R1,B CMP R0,R1 ITE GT LDRGT R0,=1 LDRLE R0,=0 STR R0,C
A :: B?
C  1
C  0
>
≤

## Slide 8: Compound Conditionals
if (lower_limit <= x && x <= upper_limit) y = x ;
if (x < lower_limit) goto L1
if (x > upper_limit) goto L1
y = x ;
L1:
if (x < lower_limit || x > upper_limit) goto L1
y = x ;
L1:
if (!(lower_limit <= x && x <= upper_limit)) goto L1
y = x ;
L1:
LDR R0,x LDR R1,lower_limit CMP R0,R1 BLT L1 LDR R1,upper_limit CMP R0,R1 BGT L1 STR R0,y L1: ...

## Slide 9: Compound Conditionals
if (x < lower_limit || upper_limit < x) y = x ;
if (x < lower_limit) goto L1
if (x > upper_limit) goto L1
goto L2 ;
L1: y = x ;
L2:
if (x < lower_limit) goto L1
if (!(x > upper_limit)) goto L2
L1: y = x ;
L2:
LDR R0,x LDR R1,lower_limit
CMP R0,R1
BLT L1 LDR R1,upper_limit
CMP R0,R1
BLE L2
L1: STR R0,y
L2: ...

## Slide 10: Loops: Basic Structure
…
top: CMP …
B{cond} done
… …
B top
done:
initialization
done?
body of loop

## Slide 11: Loops: Predetermined #Iterations
for (n = 0; n < 100; n++) { n = 0,1,…,99 } | LDR R0,=0 top: CMP R0,#100 BGE done … ADD R0,R0,#1 B top done:

## Slide 12: Loops: Variable #Iterations Ex: GCD(a,b)
while (a != b) { if (a > b) a = a – b ; else b = b – a ; } | LDR R0,a LDR R1,b top: CMP R0,R1 BEQ done ITE GT SUBGT R0,R0,R1 SUBLE R1,R1,R0 B top done: ; R0 = R1 = GCD(a,b)

## Slide 13: Miscellaneous Instructions
Bits / Bytes / Words | Operation | {S} | Notes
CLZ Rd,Rn | Rd  CountZeroes(Rn) | n/a | # leading zeroes (0-32)
RBIT Rd,Rn | Rd  RevBits(Rn) | n/a | Reverses bit order
REV Rd,Rn | Rd  RevByteOrder(Rn) | n/a | Reverses byte order
REV16 Rd,Rn | Rd  RevHalfWords(Rn) | n/a | Reverses half words
REVSH Rd,Rn | Rd  RevLoHalf(Rn) | n/a | Reverses 2 LSbytes, sign extends
SXTB Rd,Rn | Rd  SignedByte(Rn) | n/a | Sign extends, may pre-rotate Rn
SXTH Rd,Rn | Rd  SignedHalf(Rn) | n/a | 
UXTB Rd,Rn | Rd  UnsignedByte(Rn) | n/a | Zero extends, may pre-rotate Rn
UXTH Rd,Rn | Rd  UnsignedHalf(Rn) | n/a | 

## Slide 14
Size: Byte, Half-word, Word, or Double-word?
Unsigned or 2’s complement signed?
Update the flags (NZCV)?
TIP: 3 THINGS TO CHECK WHEN WRITING ARM CODE

## Slide 15: ARM Procedure Call Standard
Use these to pass parameters to functions or to hold temporaries
Use these as temporaries, but preserve original contents!
In general, don’t modify these!

## Slide 16: Function Call and Return
Function Call: “BL function”
  Loads program counter (pc) with entry point address of function.
  Saves return address in the link register.
Function Return: “BX lr”
  copies link register back into program counter.

## Slide 17
void enable(void) ; ● ● ● enable() ; ● ● ● | 
● ● ● BL enable ● ● ● | export enable enable ● ● ● ● ● ● BX LR
Compiler

## Slide 18
● ● ● ● ● ● BL foo ● ● ● ● ● ●
foo PUSH {LR} ● ● ● ● ● ●
BL bar ● ● ● ● ● ● POP {LR} BX LR
bar ● ● ● ● ● ● BX LR
Preserve LR
Restore LR

## Slide 19
void display(uint8_t char [ ], int32_t) ; ● ● ● display(buffer, 5) ; ● ● ● | 
● ● ● ADR R0,buffer LDR R1,=5 BL display ● ● ● | export display display ● ● ● ● ● ● BX LR
Compiler
Registers R0-R3 used for first 4 parameters; any more have to be pushed on stack

## Slide 20
int32_t random(void) ; ● ● ● numb = random() ; ● ● ● | 
● ● ● BL random STR R0,numb ● ● ● | export random random ● ● ● ● ● ● MOV R0, ● ● ● BX LR
Compiler

## Slide 21
sint64_t multiply(sint32_t, sint32_t) ; ● ● ● product = multiply(a, b) ; ● ● ● | 
● ● ● LDR R0,a LDR R1,b BL multiply STRD R0,R1,product ● ● ● | export multiply multiply SMULL R0,R1,R0,R1 BX LR
Compiler

## Slide 22: Temporary Variables
Registers:
  r0 - r3 (those not used for parameters)
    Must preserve and restore around any call
  r4 – r8 (must always preserve and restore)

## Slide 23: Temporaries in Registers
func1 … … no function calls; OK to use r0 – r3 … BX lr | func2 PUSH {r4,..,r8} … … ; registers r4 – r8 may be in use ; by the function that called this ; function, so their values must ; be preserved if these registers ; are used here. … … POP {r4,..,r8} BX lr | func3 PUSH {lr,..} … ; Since functions are not required ; to preserve r0 – r3, then if used ; here, you must preserve/restore ; their values wherever this function ; calls other functions. … PUSH {r0,..,r3} BL func4 POP {r0,..,r3} … POP {lr,…} BX lr

## Slide 24
void strcpy(char *dst, char *src) ;
export strcpy
strcpy LDRB r2,[r1],#1 ; increments r1
STRB r2,[r0],#1 ; increments r0
CMP r2,#0 ; trailing NUL?
BNE strcpy
BX lr ; return

## Slide 25: Register Assignment
void DumbSort(int data[], int items)
{
int j, k ;
for (j = 0; j < items – 1; j++)
{
for (k = j + 1; k < items; k++)
{
if (Reversed(data, j, k))
{
Exchange(&data[j], &data[k]) ;
}
}
}
}
On entry:
R0: &data
R1: items
These routines may destroy R0-R3
This expression will need a register
R0 & R1 needed to pass parameters
j and k will need registers

## Slide 26: Register Assignment
If writing a routine in
assembly that does NOT
call another routine, then …
If you need to use R4-R8, preserve (PUSH) them on entry, restore (POP) them on return.
No need to PUSH & POP the link register (LR).
Try to use only R0-R3 for temporaries.
Function:
…  use only R0-R3
BX lr
-or-
Function:
PUSH {r4,r5,r6,r7,r8}
…  may use R0-R8
POP {r4,r5,r6,r7,r8}
BX lr

## Slide 27: Register Assignment
If writing a routine in
assembly that calls
another routine, then …
Preserve (PUSH) LR and R4-R8 on entry, restore (POP) on return.
Use R4-R8 for temps and to hold copies of input parameters.
PUSH {lr,r4,r5,r6,r7,r8}
MOV r4,r0
MOV r5,r1
…
…
…
POP {lr,r4,r5,r6,r7,r8}
BX lr
Use r0-r3 to pass params and to compute expressions

## Slide 28
int Reversed(int data[], int index1, int index2)
{
return data[index1] > data[index2] ;
}
EXPORT Reversed
; r0 = &data
; r1 = index1
; r2 = index2
Reversed LDR r1,[r0,r1,LSL #2] ; r1  data[index1]
LDR r2,[r0,r2,LSL #2] ; r2  data[index2]
CMP r1,r2
ITE GT
LDRGT r0,=1
LDRLE r0,=0
BX lr

## Slide 29
void Exchange(int *pItem1, int *pItem2)
{
int temp1 = *pItem1 ;
int temp2 = *pItem2 ;
*pItem1 = temp2 ;
*pItem2 = temp1 ;
}
EXPORT Exchange
; r0 = pItem1
; r1 = pItem2
Exchange LDR r2,[r0] ; r2 = temp1
LDR r3,[r1] ; r3 = temp2
STR r3,[r0]
STR r2,[r1]
BX lr

## Slide 30
EXPORT DumbSort
; Parameters: r0 = &data, r1 = items
; Temporaries: r4 = &data, r5 = items, r6 = j, r7 = k
DumbSort PUSH {r4,r5,r6,r7,lr}
MOV r4,r0 ; use r4 for &data
MOV r5,r1 ; use r5 for items
LDR r6,=0 ; j = 0 ;
OuterTop: SUB r0,r5,#1 ; r0 = items – 1
CMP r6,r0 ; j < items – 1 ?
BGE OuterDone
; inner loop goes here …
ADD r6,r6,#1 ; j++
B OuterTop
OuterDone:
POP {r4,r5,r6,r7,lr}
BX lr

## Slide 31
; Inner Loop …
ADD r7,r6,#1 ; k = j + 1
InnerTop: CMP r7,r5 ; k < items?
BGE InnerDone
MOV r0,r4 ; r0  &data
MOV r1,r6 ; r1  j
MOV r2,r7 ; r2  k
BL Reversed ; Reversed?
CMP r0,#1
BNE NoExchange
ADD r0,r4,r6,LSL #2 ; r0  &data[j]
ADD r1,r4,r7,LSL #2 ; r1  &data[k]
BL Exchange ; Exchange!
NoExchange:
ADD r7,r7,#1 ; k++
B InnerTop
InnerDone: