## Slide 1: CHAPTER 8 Programming in Assembly Part 4: I/O Programming

## Slide 2: Relative Speed
I/O devices are sometimes mechanical devices (e.g., solenoids, relays, etc.) that take a long time to perform an action.
The computer performs operations orders of magnitude faster than the I/O devices.
Synchronization: The CPU must wait for the I/O device to finish each command before issuing the next.

## Slide 3: Asynchronous Events
The events that determine when an input device has data available or when an output device needs data are independent of the CPU.
I/O programming, therefore, requires "hand-shaking" between the CPU and the I/O device to coordinate the transfer so that data is transferred reliably.

## Slide 4: Time Behavior
Data Rate
Pattern
Increasing Time 
Low
Random
      
Periodic
            
High
Random
  
Periodic
   

## Slide 5: Three Strategies
Polled Waiting Loops
Interrupt-driven I/O
Direct Memory Access (DMA)

## Slide 6: Relative Performance
 | Polled Waiting Loop | Interrupt-Driven | Direct Memory Access
Maximum Transfer Rate |  | Slowest | Fastest
 | ~3 MB/Sec | ~500 KB/Sec | ~70 MB/Sec
Worst-Case Latency | Unpredictable |  | Best
 |  | 1-2 µsec | ~60 nsec
Hardware Cost | Least | Low | Moderate
Software Complexity | Low | Moderate | Moderate

## Slide 7: Polled Waiting Loops
BYTE8 Input(void) { while ((inportb(STATUS_PORT) & READY) == 0) { /* wait for new data to arrive */ } return inportb(DATA_PORT) ; }
void Output(BYTE8 ch) { while ((inportb(STATUS_PORT) & READY) == 0) { /* wait for device to finish last command */ } outportb(DATA_PORT, ch) ; }

## Slide 8: Polled Waiting Loops
Test device status in a waiting loop before transferring each data byte.
Maximum data rate: Determined by the time required to execute one iteration of the waiting loop plus the transfer.
Latency: Unpredictable - no guarantee when the program will arrive at the waiting loop.

## Slide 9: Interrupt Processing
Hardware interrupt request occurs: CPU finishes , suspends or abandons the current instruction and then initiates an exception response sequence.
Interrupt Complete: Interrupted code continues where it left off as if nothing happened.
Exception Response Sequence: CPU stacks the processor state and return address, enables Handler Mode, identifies the requesting device, and transfers control to the corresponding Interrupt Service Routine.
Exception Handler / ISR:
1. Preserve R4-R11 as needed.
2. Transfer data between queue and I/O device.
3. Restore R4-R11 as needed.
4. Return to interrupted code.
Exception Return: Unstack and restore the processor state and mode.

## Slide 10: Exceptions
Definition:
Any condition that needs to halt the normal sequential flow of instruction execution.
Categories:
Reset
SVC Supervisor Call
  (Software Interrupt)
Fault
  E.g., undefined opcode
Interrupts

## Slide 11: Exceptions
Each exception has:
An exception number
A priority level
An exception handler routine
An entry in the vector table
  (Address of associated handler routine)

## Slide 12: Exception Response
Processor state (8 words) stored on stack:
  xPSR, Return Address, LR, R12, R3 - R0 Allows a regular C function to be an ISR!
Processor switched (from Thread Mode) to Handler Mode (recorded in xPSR).
PC  vector table[ exception # ]

## Slide 13: Interrupt Stacking
Old SP
SP
PSR
Return Address
LR
R12
R3
R2
R1
R0
Increasing Addresses
Eights words pushed onto stack by exception response.

## Slide 14: Exception Handlers
Definition: An exception handler is a software routine that is executed when a specific exception condition occurs.
Note: Most, but not all, exception handlers return to the previous code.

## Slide 15: Interrupt Latency
ISR
Unstacking
Stacking
12
Cycles
Latency:
17 Cycles
Input data read from device
Abandons any instruction longer than 1 cycle

## Slide 16: Exception Return
Exception return occurs when in Handler
Mode and one of the following instructions
is executed:
POP/LDM includes the PC, or
LDR with PC as the destination, or
BX with any register as the source

## Slide 17: Tail-Chaining
ISR #1
Unstacking
ISR #2
12 Cycles
24 Cycles
12 Cycles
12 Cycles
6 Cycles
12 Cycles
With Tail-Chaining
Stacking
Unstacking
Stacking
Stacking
ISR #1
ISR #2
Unstacking
Without Tail-Chaining

## Slide 18: Vector Table
Exception Type | Position | Priority | Comment
 | 0 | - | Initial SP value (loaded on reset)
Reset | 1 | -3 | Power up and warm reset
NMI | 2 | -2 | Non-Maskable Interrupt
Hard Fault | 3 | -1 | 
Memory Mgmt | 4 | S e t t a b l e | 
Bus Fault | 5 |  | Address/Memory-related faults
Usage Fault | 6 |  | Undefined instruction
 | 7-10 |  | Reserved
SVCall | 11 |  | Software Interrupt (SVC instruction)
Debug Monitor | 12 |  | 
 | 13 |  | Reserved
PendSV | 14 |  | 
SysTick | 15 |  | System Timer Tick
Interrupts | ≥16 |  | External; fed through NVIC

## Slide 19: Nested Vectored Interrupt Controller (Mapped to addresses E000E100-E000ECFF16)
The NVIC provides the ability to:
Individually Enable/Disable interrupts from specific devices.
Establishes relative priorities among the various interrupts.
Note: The CPSIE/CPSID instructions globally enable/disable the entire interrupt system.

## Slide 20: NVIC Interrupts
0-4 GPIO Ports A-E
5,6 UART 0 & 1
SSI
I2C
PWM Fault
10-12 PWM Generator 0-2
Reserved
14-17 ADC Sequence 0-3
Watchdog Timer
19-24 Timer0a-2b
Analog Comparator
26-27 Reserved
System Control
Flash Control
30-31 Reserved
Bit in Interrupt Registers

## Slide 21: NVIC Interrupt Registers
31 | 0
Interrupt Clear Enable Register | 
31 | 0
Interrupt Set Enable Register | 
Set a bit to 1 in this register to disable interrupts from the corresponding device
Set a bit to 1 in this register to enable interrupts from the corresponding device

## Slide 22: Interrupt Priority Registers
Each interrupt is assigned an 8-bit priority number:
  Highest Priority: 0
  Lowest Priority: 255

## Slide 23: Buffering
 |  |  |  | P | L | E | A | S | E |  | L | O | G | I | N | : |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
q.bfr
dequeue position (front)
enqueue position (rear)
20
q.size
13
q.count
17
q.nq
4
q.dq

## Slide 24: Direct Memory Access
Requires additional hardware to control data transfers independent of CPU.
Competes with CPU for control of memory.
Does not have to wait for current instruction to complete – only the current memory cycle.
  Latency is thus 1 memory cycle.
Data Rate determined by memory speed.

## Slide 25: Single Buffering
DMA Write |  | DMA Write | 
 | CPU Read |  | CPU Read
Double Buffering
DMA Write Buffer 1 | DMA Write Buffer 2 | DMA Write Buffer 1 | 
 | CPU Read Buffer 1 | CPU Read Buffer 2 | CPU Read Buffer 1