## Slide 1: CHAPTER 9 CONCURRENT SOFTWARE

## Slide 2: Program Organization of a Foreground/Background System
return
return
return
Interrupt
ISR for Event #2
Start
Initialize
Interrupt
ISR for Event #1
Interrupt
ISR for Event #3
Wait for Interrupts

## Slide 3: Foreground/Background System
Most of the actual work is performed in the "foreground" ISRs, with each ISR processing a particular hardware event.
Main program performs initialization and then enters a "background" loop that waits for interrupts to occur.
Allows the system to respond to external events with a predictable amount of latency.

## Slide 4
Return
Output Device Ready?
Yes
Input Ready
Input Data
Process Data
Output Data

## Slide 5: Removing the Waiting Loop from the ISR
Dequeue Data
Output Device Ready?
Yes
Input Data
Process Data
Enqueue Data
Input Ready
Enter Background
Output Data
Return
Data Enqueued?
Yes
Initialize
FIFO Queue

## Slide 6
Input
Ready
Output
Ready
Yes
Input Data
Process Data
Enqueue Data
Data Enqueued?
Dequeue Data
FIFO Queue
Output Data
return
return
Interrupt-Driven Output

## Slide 7
Data Enqueued?
CALL SendData
SendData Subroutine
Yes
Dequeue Data
FIFO Queue
Clear Busy Flag
Output Data
No!
Output
Device
Busy?
Input Data
Process Data
Enqueue Data
Input
Ready
CALL SendData
(Kick Start)
Output
Ready
Set Busy Flag
return
return
return
Kick Starting Output

## Slide 8: Moving Work into Background
Move non-time-critical work (such as updating a display) into background thread.
Foreground ISR writes data to queue, then background removes and processes it.
Better alternative than ignoring one or more interrupts as the result of input overrun.
Processor must still be fast enough to keep queue from overfilling.

## Slide 9: Limitations
Best possible performance requires moving as much as possible into the background.
Background becomes collection of queues and associated routines to process the data.
Optimizes latency of the individual ISRs, but background begs for a managed allocation of processor time.

## Slide 10: Multi-Threaded Architecture
Queue
Queue
Queue
Queue
ISR
ISR
ISR
ISR
Thread #1
Thread #2
Multi-threaded run-time function library (the real-time kernel)

## Slide 11: Thread Design
Threads usually perform some initialization and then enter an infinite processing loop.
At the top of the loop, the thread relinquishes the processor while it waits for data to become available, an external event to occur, or a condition to become true.

## Slide 12: Real-Time Kernel
Threads call a library of run-time routines (known as the real-time kernel) manages resources.
Kernel provides mechanisms to switch between threads, for coordination, synchronization, communications, and priority.

## Slide 13: Concurrency
Only one thread runs at a time while others are suspended.
Processor switches from one thread to another so quickly that it appears all threads are running simultaneously. Threads run concurrently.
Programmer assigns priority to each thread and the scheduler uses this to determine which thread to run next

## Slide 14: Independent Threads
Each thread runs as if it had its own CPU separate from those of the other threads.
Threads are designed, programmed, and behave as if they are the only thread running.
Partitioning the background into a set of independent threads simplifies each thread, and thus total program complexity.

## Slide 15: Each Thread Maintains Its Own Stack and Register Contents
R0
R1
R2
R3
flags
Stack
Registers
Context of Thread 1
R0
R1
R2
R3
flags
Stack
Registers
Context of Thread N

## Slide 16: Context Switching
Each thread has its own stack and a special region of memory referred to as its context.
A context switch from thread "A" to thread "B" first saves all CPU registers in context A, and then reloads all CPU registers from context B.

## Slide 17: Context Switching
Suspended
Suspended
Executing
Suspended
Executing
Executing
Restore context B
Save context A
Save context B
Restore context A
Thread A
Thread B

## Slide 18: Two Kinds of Multi-Threading
Non-Preemptive (aka “Cooperative”)
  Pro: Easier to manage shared memory.
  Con: Requires careful placement of explicit “yield” calls in source code of each thread to reduce latency.
Preemptive (event-driven context switch)
  Pro: No explicit “yield” calls required in source code.
  Con: More difficult to manage shared memory.

## Slide 19: Non-Preemptive Multi-Threading
Threads call a kernel routine to perform the context switch.
The context switch call is often referred to as a yield, and this form of multi-threading is often referred to as cooperative multi-threading.

## Slide 20: Non-Preemptive Multi-Threading
When external event occurs, processor may be executing a thread other than one designed to process the event.
The first opportunity to execute the needed thread will not occur until current thread reaches next yield.
In most cases, this makes it impossible or extremely difficult to predict the maximum response time of non-preemptive multi-threading systems.

## Slide 21: Non-Preemptive Multi-Threading
Programmer must call the yield routine frequently, or else system response time may suffer.
Yields must be inserted in any loop where a thread is waiting for some external condition.
Yield may also need to be distributed throughout a lengthy computation.

## Slide 22
Wait?
Yield to other threads
Data Processing
Thread Initialization
Start
Yes
Scheduler selects highest priority thread that is ready to run. If not the current thread, the current thread is suspended and the new thread resumed.
Yield Call in Cooperative Multi-Threaded System

## Slide 23: Preemptive Multi-Threading
When external event occurs, a hardware ISR is invoked, invoking a context switch.
The ISR calls a kernel routine to enqueue the data, which changes a thread from “pending” to “ready”.
A “scheduler” in the kernel then selects the highest priority thread that is “ready” and returns to it.
  This may or may not be the one that was interrupted.
Significantly improves system response time.

## Slide 24: Preemptive Context Switching
Interrupt
Thread A
Thread A
Executing
ISR
Context Switch
Thread B
Thread B
Suspended
Thread A
Suspended
Thread B
Executing
Scheduler selects highest priority thread that is ready to run. If not the current thread, the current thread is suspended and the new thread resumed.
Process Interrupt Request
return

## Slide 25: Preemptive Multi-Threading
Eliminates the programmer's obligation to include explicit calls to the kernel to perform context switches within the various background threads.
Programmer no longer needs to worry about how frequently the context switch routine is called; it's called only when needed - i.e., in response to external events.

## Slide 26: Critical Sections
Critical section: A code sequence whose proper execution is based on the assumption that it has exclusive access to the shared resources that are used during the execution of the sequence.
Critical sections must be made “atomic” – i.e., protected against preemption, or else integrity of the computation may be compromised.

## Slide 27: Atomic Operations
Atomic operations are those that execute to completion without preemption.
Critical sections must be made atomic:
  Acquire exclusive access to the shared resource through arbitration before entering the critical section and release it on exit.

## Slide 28: Forms of Preemption
Between 2 threads:
  Shared data may be corrupted unless execution of their critical sections is coordinated.
Between a thread and an ISR:
  Shared data may be corrupted if the thread's critical section is interrupted to execute the ISR.
Between 2 ISRs:
  Shared data may be corrupted if the critical section of one ISR can be interrupted to execute the other ISR.

## Slide 29: Shared Resources
A similar situation applies to other kinds of shared resources - not just shared data.
Consider two or more threads that want to simultaneously send data to the same (shared) disk, printer, network card, or serial port. If access is not arbitrated so that only one thread uses the resource at a time, the data streams might get mixed together, producing nonsense at the destination.

## Slide 30: Uncontrolled Access to a Shared Resource (the Printer)
Thread A
Thread B
Shared Printer
"HELLO\n"
"goodbye"
HgoELodLO
bye

## Slide 31: Protecting Critical Sections
Non-preemptive system: Programmer has explicit control over where and when context switch occurs.
  Except for ISRs!
Preemptive system: Programmer has no control over the time and place of a context switch.
Protection Options:
  Disabling interrupts
  Spin lock
  mutex
  semaphore

## Slide 32: Disabling Interrupts
The overhead required to disable (and later re-enable) interrupts is negligible.
  Good for short critical sections.
Disabling interrupts during the execution of a long critical section can significantly degrade system response time.

## Slide 33: Spin Locks
No
Set Flag
Critical Section
Clear Flag
do {
disable_interrupts() ;
ok = !flag ;
flag = TRUE ;
enable_interrupts() ;
} while (!ok) ;
flag = FALSE ;
Flag set?
If the flag is set, another thread is currently using the shared memory and will clear the flag when done.

## Slide 34: Spin Locks vs. Semaphores
Non-Preemptive System: Must add a “yield” call inside spin lock loop to let other threads run.
Constant context-switching during spin lock can be a significant overhead (saving and restoring threads’ registers and stack).
Semaphores eliminate the context-switch until flag is released.

## Slide 35: Semaphores
Semaphore “Pend”
Critical Section
Semaphore “Post”
Kernel suspends this thread if another thread has possession of the semaphore; this thread does not get to run again until the other thread releases the semaphore with a “post” operation.

## Slide 36: Kernel Services
Initialization
Threads
Scheduling
Priorities
Interrupt Routines
Semaphores
Mailboxes
Queues
Time