## Slide 1: Installing and Configuring PC Components

## Slide 2: Installing and Configuring PC Components
Use Appropriate Safety Procedures
PC Components
Common Connection Interfaces
Install Peripheral Devices
Troubleshooting Methodology

## Slide 3: Local Government Regulations
Types of regulations:
  Health and safety laws.
  Building codes.
  Environmental regulations.
OSHA is a prime example of safety regulations for US-based operations.
  Workplace free from recognized hazards.
  Personal protective equipment.
  Communication (labels, MSDSs, and hazmat training).
Employers and employees both have responsibilities.
  Employers provide a safe workplace.
  Employee actions promote safety of themselves and others.

## Slide 4: Health and Safety Procedures
Identify what to do in an emergency.
Identify responsible persons (first responders, etc.).
Identify hazardous areas and what precautions to take.
Describe best practices for use and care of workplace and equipment.
Establish incident reporting procedures.

## Slide 5: General Emergency Procedures
Raise the alarm and contact emergency services.
  Description of emergency.
  Location of emergency.
If possible, secure the scene.
  Escape routes for fire situations.
  Disconnect power for electrical shock situations.
If you have training, try to start handling the incident.
  Give first aid.
  Use firefighting equipment.
Keep calm, and don’t act rashly!

## Slide 6: Electrical Hazards
Most prevalent physical hazard for IT equipment and personnel.
For humans, electrical shock can cause:
  Muscle spasms
  Burns
  Paralysis
  Cardiac arrest
  Collateral injuries
  Death by electrocution
Keep equipment away from conductors.
  Metal
  Liquid

## Slide 7: Fuses
Fuse: A circuit breaker designed to protect the device and users of the device from faulty wiring or supply of power (overcurrent protection).
Electrical problems blow fuses to prevent further damage.
  Separates a device from the power source.
Ratings: 3A, 5A, 13A.
  Most computer equipment is 3A or 5A.
  Use fuses rated for the equipment.
Power strips connect multiple devices to a power source.
  Don’t daisy chain them!
  Total power draw should not exceed maximum load (12A).

## Slide 8: Equipment Grounding (Slide 1 of 2)
Ground: A safe path for electrical current to flow away in the event that a device or cable is faulty.
Creates a path of least resistance for electrical current to flow away and cause no damage.
Ground achieved for most PCs by connecting the power cord to an electrical outlet.
You might need to establish ground for equipment racks or other systems.

## Slide 9: Equipment Grounding (Slide 2 of 2)

## Slide 10: High Voltage Device Safety
Most PC circuits are low voltage/low current.
There are notable exceptions.
  Power supplies.
  CRT monitors.
  LCD display inverter card.
  Laser printers.
Do not open units that are marked with High Voltage warnings unless you’re specifically trained for servicing them.

## Slide 11: Electrical Fire Safety
When excessive current flows through a cable, the cable gets hot.
Adjacent flammable materials could ignite.
Use fire extinguishers designed for electrical fires.
  CO2 extinguishers with a black label are optimal.
  Dry powder extinguishers can damage electronic equipment.
Be sure to cut the power supply.
Know where the master switches are for the buildings you work in.

## Slide 12: Guidelines for Working Safely with Electrical Systems
Be aware of risks and safety practices.
Avoid repair work when you are not 100%.
Don’t assume—check things for yourself.
Cut power to circuits before handling them.
Press and hold the PC power button to dissipate residual power.
Use a multimeter to check live parts for voltage.
Use insulated tools and never grip tools by their metal parts.
Never touch a circuit with both hands. (Hand in pocket rule.)
Keep your hands and the surrounding area dry.
Clean up spills and make sure you aren’t walking on a wet floor.
Avoid wearing jewelry or other items that hang from the neck or wrists.

## Slide 13: Environmental Safety
Category | Description
Trip hazards | Caused by objects being placed in pathways where people walk. Cables, boxes, furniture, etc.
Lifting and carrying risks | Lifting heavy objects can cause back injuries. Dropped objects can cause leg or foot injuries. Bulky objects can also cause problems.

## Slide 14: Toxic Waste Handling
Contaminants can be:
  Gaseous
  Particulate
  Organic
  Poisonous
  Corrosive
Devices to be careful around:
  CRT monitors
  Batteries
  Electronic devices (PCs, cell phones, and tablets)
  Toner kits and cartridges

## Slide 15: Guidelines for Working Safely Among Environmental Hazards (Slide 1 of 2)
Secure cables with ties or other cable management products.
Keep devices and other objects out of walkways and away from desk edges.
Consider weight limitations as you lift or carry items.
If necessary, use protective clothing.
To lift heavy objects:
  Plant your feet around the object with one foot slightly toward your destination.
  Bend at the knees while keeping your back straight and chin up.
  Get a firm grip and lift smoothly by straightening your legs.
  As you carry the object, keep your back straight.

## Slide 16: Guidelines for Working Safely Among Environmental Hazards (Slide 2 of 2)
To lower heavy objects, reverse the lifting process. Don’t trap your fingers or lower the object onto your feet.
Ask a colleague for assistance or use a cart for bulky or excessively heavy items.
To work with toxic materials:
  Don’t disassemble or stack CRT monitors.
  Use gloves and goggles when working with corrosive materials.
  Use air filter masks when working with toner.

## Slide 17: ESD
Electrostatic discharge (ESD): A situation that occurs when electrons rush from one statically charged body to another with an unequal charge, following the path of least resistance.
Caused by excessive static electricity.
High voltage, but low current.
  Less dangerous to humans than to electronics.
  People feel ESD at 2,500V; equipment can be damaged by as little as 100V.
ESD generators:
  Synthetic clothing.
  Low humidity.
  Cooler temperatures.

## Slide 18: Component Handling (Slide 1 of 3)
Self-grounding: The act of touching a grounded object before touching electronic equipment.
Using ESD wrist or leg strap.
  More effective than self-grounding.
  Use the grounding plug or clip to attach to a ground point.
Using ESD service mats or smocks.
Using antistatic bags.

## Slide 19: Component Handling (Slide 2 of 3)

## Slide 20: Component Handling (Slide 3 of 3)

## Slide 21: Guidelines for Protecting Components from ESD Damage
Use proper component handling and storage procedures whenever you are performing PC maintenance work.
To protect components and equipment from ESD damage:
  Drain your body and clothing of static electricity before you start work.
  If possible, work in an uncarpeted area.
  The simplest (but least effective) means of self-grounding is to touch an unpainted metal part of the PC.
  Try to handle vulnerable components by their edges, and avoid touching the surfaces of the chips themselves.
Use ESD wrist or ankle straps and dissipative floor mats.

## Slide 22
Implementing an Anti-ESD Service Kit

## Slide 23: System Case Types (Slide 1 of 3)
Desktop computer: A computing device designed to be placed on or near a user's desk.
System case/chassis: A plastic and metal box that houses components such as the motherboard, CPU, memory, adapter cards, disk drives, and power supply unit.
Tower case: A desktop computer designed to sit vertically on a surface, so that it is taller than it is wide.
Tower case options:
  Full tower
  Mid tower
  Mini tower
  Slimline

## Slide 24: System Case Types (Slide 2 of 3)

## Slide 25: System Case Types (Slide 3 of 3)
SFF case: (small form factor) A case for motherboards and connectors that is designed to take up less space.
All-in-one unit: A desktop computer in which all the computer components, except the keyboard and mouse, are contained within the monitor case.

## Slide 26: Parts of the System Case (Slide 1 of 4)
Cover: The removable portion of the system case that allows access to the motherboard and internal components.
Front panel: The portion of the system case that provides access to removable media drives, power switch, and LEDs to indicate driver operation.

## Slide 27: Parts of the System Case (Slide 2 of 4)

## Slide 28: Parts of the System Case (Slide 3 of 4)
Rear panel: The portion of the system case with cut-out slots aligned with the position of adapter card slots.
Adapter card: Circuit board providing additional functionality to the computer system.
Blanking plate: Metal strips that cover unused adapter slots in the case so that proper air flow is maintained within the system case.

## Slide 29: Parts of the System Case (Slide 4 of 4)

## Slide 30: Repair or Replace?
Field replaceable unit (FRU): An adapter or other component that can be replaced by a technician on-site. Most PC and laptop components are FRUs, whereas the components of smartphones are not.
Not all components are considered FRUs.
More economical to swap out, or replace, with a new component.

## Slide 31: Guidelines for PC Disassembly
Back up all data stored on the internal drive(s).
Create a clean work environment where you can work comfortably.
Gather all necessary tools and equipment.
  Notepad and pen
  Digital camera
Make sure that all devices are powered off and unplugged from the building power before disconnecting them.
Take anti-static precautions.
  Place static-sensitive components (CPUs and RAM) in anti-static bags.

## Slide 32: Motherboards
Motherboard: Provides the basic foundation for all of the computer's hardware, including the processor, RAM, firmware, and expansion cards. Also referred to as mobo, system board, or main board.
Motherboard type dictates speed and upgrade capabilities.
Standoffs hold the motherboard in place within the system case.
  Brass or plastic.

## Slide 33: Motherboard Form Factors
Form Factor | Description
ATX | Developed in 1995 to replace legacy AT form factor. 12 by 9.6 inches, 305 by 244 mm. Up to seven expansion slots.
Micro-ATX | 9.6 inches (244 mm) square. Up to four expansion slots.
Mini-ITX | Used in SFF PCs. 6.7 inches (170 mm) square. One expansion slot.
Other ITX-based form factors | Smaller than mini-ITX. Used for embedded systems and portable computers.

## Slide 34: Motherboard Connector Types
Base set of connectors for CPU, memory, disk drives, peripherals, etc.
Type and number depend on the motherboard model.

## Slide 35: CPU Sockets
Socket type depends on CPU manufacturer.
Usually a square socket near the memory banks.
Often covered by a heatsink and fan.

## Slide 36: Memory Slots
Random access memory (RAM): The principal storage space for computer data and program instructions. Volatile memory that loses data when there is no power.
Volatile memory.
Normally packaged as DIMMs.

## Slide 37: Chipset and Memory Architecture
Chipset: Provides communications between different components by implementing various controllers.
Controller types:
  System memory.
  I/O.
  Integrated video, sound, and network interfaces.
Chipsets are not upgradeable.
CPU/memory link determines performance.
  Northbridge/Southbridge is legacy architecture.
  Different architectures now used, including on-die controllers.

## Slide 38: CMOS and RTC Batteries (Slide 1 of 2)
Complementary metal-oxide semiconductor (CMOS): A type of integrated circuit with a wide range of applications, including static RAM (for firmware and flash memory) and imaging sensors.
Holds basic configuration information.
Stores system firmware setup program settings.

## Slide 39: CMOS and RTC Batteries (Slide 2 of 2)
CMOS battery: Battery that powers the chipset that keeps track of date and time for the system. Also referred to as RTC battery or clock battery.
Normally last 5 to 10 years.
Powers the RTC, which keeps track of the system date and time.

## Slide 40: Bus Architecture
Bus: Connections between components on the motherboard and peripheral devices attached to the computer.
Traces: Wires etched on to the motherboard to provide electrical pathways.
Carries electronic signal along the motherboard.
  Information being processed (data) and information about where data is located (address).
  Power to components.
  Timing signals for synchronizing data transfer.
Usually refers to the expansion bus.

## Slide 41: Internal and External Buses
Local bus: The internal bus that links components directly to the processor, resulting in the highest possible data speed as required by components such as the video display.
Expansion bus: The external bus that allows additional components to be connected to the computer.
Internal bus connects core components.
External bus connects peripherals.
  Peripherals can be internal or external, too.
  The bus can extend beyond the system case, but not always.

## Slide 42: Expansion Slots (Slide 1 of 2)
Expansion slot: Connection slots on the motherboard in which adapter cards can be installed to extend the range of functions the computer can perform.
Multi-bus design allows different expansion slots on a motherboard.
  Support for older technologies.

## Slide 43: Expansion Slots (Slide 2 of 2)
Riser card: A space-saving feature of some motherboards that puts the PC's expansion slots on a separate board installed at right angles to the main board, allowing system components to fit within a slimline case.
Expansion slots parallel to the motherboard.
  Saves space.

## Slide 44: System Clock and Bus Speed
System clock: The computer's timing mechanism that synchronizes the operation of all parts of the computer and provides the basic timing signal for the CPU.
Clock speed measured in megahertz (MHz) or gigahertz (GHz).
Clock generator initiates timing signal.
Clock multipliers adjust timing signal for different buses.

## Slide 45: PCI Bus (Slide 1 of 3)
Peripheral Component Interconnect (PCI) bus: Introduced in 1995, it connects the CPU, memory, and peripherals. It supports bus mastering, IRQ steering, and PnP. 32-bit works at 33 MHz. 64-bit works at 66 MHz.
Slowly being replaced by PCI Express.
First commercial version was 2.0.
  Several revisions to the standard since then.
Standards information: pcisig.com/specifications.

## Slide 46: PCI Bus (Slide 2 of 3)
Feature | Description
Bus width and clock speed | Supports up to 5 devices via Plug-and-Play. Shared bandwidth. Supports bus mastering. Architecture: 32-bit bus operating at 33.3 or 66 MHz (133 or 266 MBps). 64-bit bus operating at 33.3 or 66 MHz (266 or 533 MBps).
Adapter card and slot form factors | 5V, 3.3V, and dual voltage supported by different form factors and keying. 5V cards are keyed at pins 50 and 51. 3.3V cards are keyed at pins 12 and 13. Dual-voltage cards are keyed at both. 64-bit cards and adapters have 60 more pins. All PCI slots deliver up to 25W of power.

## Slide 47: PCI Bus (Slide 3 of 3)

## Slide 48: PCI Express Bus (Slide 1 of 3)
Peripheral Component Interface Express (PCIe) bus: Serial communication with point-to-point links between I/O controller and devices.
Designed to replace PCI.
Point-to-point serial communications for dedicated links (lanes) to all components.
Switches make connections and provide QoS.
Lanes are 2 sets of wire pairs—one pair for transmit, one pair for receive.
  Each component supports a specific number of lanes.
  Switch negotiates how many lanes to use.
  250 MBps transfer rate.
Software compatible with PCI.

## Slide 49: PCI Express Bus (Slide 2 of 3)
Power features:
  Up to 75W supplied per device via motherboard slot.
  Another 75W available through a PCIe power connector.
  Power management functions available.
  Hot swap and hot plug adapters supported.
Versions:
  PCIe 2: 500 MBps transfer rates possible.
  PCIe 2.1: Power draw up to 150W, plus 150W via connector.
  PCIe 3: Transfer rates near 1 GBps per lane.
  PCIe 4: Transfer rates near 2 GBps per lane.
  PCIe 5: In development; projected transfer rates near 4 GBps per lane.

## Slide 50: PCI Express Bus (Slide 3 of 3)

## Slide 51: Storage Bus (SATA and IDE) (Slide 1 of 2)
Storage bus: A special type of expansion bus dedicated to communicating with storage devices.
Parallel ATA (PATA), IDE, and EIDE.
SCSI.
Serial ATA, or SATA:
  Serial bus that is faster than PATA or SCSI.
  Compact 7-pin connector.

## Slide 52: Storage Bus (SATA and IDE) (Slide 2 of 2)

## Slide 53: Other Motherboard Connectors (Slide 1 of 2)

## Slide 54: Other Motherboard Connectors (Slide 2 of 2)
Connector Type | Description
Front panel connectors | Power button. HDD activity lights. Audio ports.
Internal USB connectors | 1 or 2 USB ports on the front panel. Several USB ports on the back panel. 9-pin headers.
Power and fan connectors | Power connector is usually a 24-pin white or black block. Fan connectors are smaller (1 for CPU, 1 for case fan). 3-pin Molex KK. 4-pin Molex KK. 4-pin Molex.

## Slide 55
Discussing PC Components

## Slide 56: Interfaces, Ports, and Connections (Slide 1 of 2)
Interface: The point at which two devices connect and communicate with each other.
Port: An input-output port essentially describes a device connection through which data can be sent and received.
Connection: The physical access points that enable a computer to communicate with internal or external devices.

## Slide 57: Interfaces, Ports, and Connections (Slide 2 of 2)
Male and female ports.
Keyed ports.
Color codes for external ports.

## Slide 58: I/O Ports and Cables
I/O port: A hardware connection interface on a personal computer that enables devices to be connected to the computer.

## Slide 59: USB Connectors (Slide 1 of 4)
Universal Serial Bus (USB): A hardware interface standard designed to provide high performance connections for numerous peripherals with minimal device configuration.
Standard method for connecting peripherals.
Bus is a host controller and attached devices.
  Up to 127 devices.
Devices are hubs or functions.
  Hubs connect additional devices.
  Functions are human interface, storage, printer, audio, etc.

## Slide 60: USB Connectors (Slide 2 of 4)
Standards:
  USB 2.0: Data rate of 480 Mbps shared among all devices attached to a host.
  USB 3.0:
    SuperSpeed Mode provides bandwidth of 5 Gbps and a full duplex link.
    Introduces dual subcontrollers to split SuperSpeed and legacy devices.
  USB 3.1: SuperSpeed+ Mode provides bandwidth of 10 Gbps.
  USB 3.2: 20 Gbps possible when using USB-C ports and cables.
Power supplied by host:
  USB 2: 2.5 W per device.
  USB 3: 4.5 W per device.
USB OTG

## Slide 61: USB Connectors (Slide 3 of 4)
Connectors and ports:
  Type A (4-pin) connects to hosts.
  Type B (4-pin) connects to devices. Includes B Mini and B Micro.
  Type C connects to hosts and devices.
  Cable length:
    LowSpeed and SuperSpeed: 3 m.
    FullSpeed and HighSpeed: 5 m.

## Slide 62: USB Connectors (Slide 4 of 4)

## Slide 63: Other Peripheral Connector Types
Port & Connector Type | Description
Thunderbolt | Primarily used on Apple systems. Display or general peripheral interface. Lightning bolt icon. TB 2 supports links of up to 20 Gbps and allows up to 6 devices to a port. TB 3 uses same interface as USB-C.
Lightning | Used on iPhone and iPad. Reversible connector. Restricted to mobile devices, so adapter cables needed to connect to a PC.
RD-232 and DB-9 | Connect to serial ports. Data rates up to 115 Kbps. Used for modems and network equipment. Can be 25- pin or 9-pin interface.

## Slide 64: Storage Connector Types (Slide 1 of 2)

## Slide 65: Storage Connector Types (Slide 2 of 2)
SCSI and Molex

## Slide 66: Network Connector Types
RJ-45 Port and Connector
RJ-11 Port and Connector

## Slide 67: Expansion Cards
Expansion card: A printed circuit board that is installed in a slot on a system board to provide special functions for customizing or extending a computer’s capabilities. Also referred to as adapter card, I/O card, add-in, add-on, or board.
I/O adapters and storage cards
NICs and adapters.

## Slide 68
Identifying Connection Interfaces

## Slide 69
Demonstrating PC Disassembly and Reassembly

## Slide 70: Input Devices
Human Interface Devices: (HIDs) Peripherals that enable the user to enter data and select commands.
Peripherals that enable users to communicate with a PC.
Data entry or command issuance.
Keyboard and pointing devices most common input devices.

## Slide 71: Keyboards (Slide 1 of 2)
Keyboard: The oldest PC input device and still fundamental to operating a computer. There are many different designs and layouts for different countries. Some keyboards feature special keys.
Extended
Ergonomic

## Slide 72: Keyboards (Slide 2 of 2)

## Slide 73: Pointing Devices (Slide 1 of 2)
Pointing device: A peripheral used to move a cursor to select and manipulate objects on the screen.
Mouse

## Slide 74: Pointing Devices (Slide 2 of 2)
Game Controller

## Slide 75: KVM Switches
KVM switch: (keyboard, video, mouse) A switch supporting one set of input and output devices that control multiple PCs.
More typically used with servers.
  2-port versions allow one keyboard, mouse, and display to be used with 2 PCs.

## Slide 76: Security Input Devices (Slide 1 of 3)
Biometric authentication devices confirm identity via physical characteristics.
  Retinal patterns
  Fingerprints
  Voice print
Smart card readers feature a slot or sensor to interact with a smart card.
  Smart cards hold digital certificates.
  The combination of the certificate and a PIN or password provides security.

## Slide 77: Security Input Devices (Slide 2 of 3)
Magnetic strip/chip readers.
  Strip holds account information.
  Chip readers specifically for PoS systems.
NFC and tap pay devices.
  Contactless readers use NFC.

## Slide 78: Security Input Devices (Slide 3 of 3)
Signature pads.
  Used with database of approved signatures.
  Comparison with stored signature verifies identity.

## Slide 79: Installation and Configuration Considerations (Slide 1 of 2)
Plug-and-Play: A protocol framework allowing network devices to autoconfigure services.
System resources: Settings that enable a device to communicate with the CPU and memory without the device conflicting with other devices.
Resource | Description
Memory Ranges/ I/O Addresses | I/O address map defines each device’s memory addresses. Port addresses range from 0000 to FFFF.
IRQs | Request for CPU attention. IRQs range from 0 to 15. Interrupt controllers allow IRQ sharing by multiple devices.

## Slide 80: Installation and Configuration Considerations (Slide 2 of 2)
Hot swap enables devices to be added or removed without shutting down the PC.
Drivers might need to be installed or updated.
Connections made by plugging devices into the correct port.
Configuration after installation.
  Device Manager
  Control Panel
  Windows Settings
  Vendor software

## Slide 81: Guidelines for Installing Peripheral Devices
Always read the manufacturer's instructions and check that the device is compatible with the PC and operating system.
Hold the connector, not the cable, when removing a lead.
Inspect the connector and port for damage (notably broken or bent pins) before attaching a lead.
Take care to align the connector carefully and do not use excessive force, to avoid damaging the pins.
Check whether the device requires an external power source.

## Slide 82
Discussing Peripheral Device Installation

## Slide 83: Troubleshooting Basics
The process of problem-solving.
Causes, symptoms, and consequences.
  Hard disk drive fault (cause).
  Fault causes the PC to display a blue screen (symptom).
  Blue screen prevents user from accomplishing work (consequence).
Sometimes resolving the consequence is more important than addressing the cause.
Causes can also be symptoms of larger problems.
  Especially with recurring issues.

## Slide 84: Problem Management
Problem management: A method of identifying, prioritizing, and establishing ownership of incidents.
Incident: Something that is not normal and disrupts regular operations in the computing environment.
  User contacts Help Desk.
    Operator or technician is assigned, and trouble ticket is generated.
  User describes the problem.
    Operator asks clarifying questions, and categorizes the problem, assesses urgency, and estimates time to resolve.
  Operator might walk user through some initial troubleshooting steps.
    Ticket might be escalated to another support person.
  Troubleshooting continues until the problem is resolved.
    Operator confirms user satisfaction and records details on trouble ticket and closes it.

## Slide 85: The CompTIA A+ Troubleshooting Model (Slide 1 of 2)
Identify the problem.
  Question the user, and identify changes to the computer.
  Perform backups before implementing any changes.
  Ask about environmental or infrastructure changes.
  Review system and app logs.
Establish a theory of probable cause.
  Question the obvious.
  If necessary, conduct internal or external research based on symptoms.
Test the theory to determine causes.
  Once the theory is confirmed, determine the next steps to solve the problem.
  If the theory is not confirmed, re-establish a new theory or escalate the issue.

## Slide 86: The CompTIA A+ Troubleshooting Model (Slide 2 of 2)
Establish a plan of action to resolve the problem and implement the solution.
Verify full system functionality, and if applicable, implement preventive measures.
Document findings, actions, and outcomes.

## Slide 87: Customer Service and Communication Skills
Soft skills can be as important as technical skills.
Question types:
  Open questions: Encourage the user to explain in their own words.
  Closed questions: Yes/No, or reading an error message off the screen.
Develop a troubleshooting mindset.
  Be calm.
  Take breaks.
  Challenge assumptions.
  Assess costs and impact.
  Know when to escalate an issue.

## Slide 88: Problem Identification (Slide 1 of 2)
Work methodically to ensure you diagnose the correct problem and select the best resolution.
Troubleshooting combines problem-solving with decision-making.
Be prepared before starting the process.
  Gather tools, documentation, and other necessities.
  Use clear, concise, and accurate instructions when asking users to perform tasks.
  Schedule downtime as needed, but be sensitive to the user’s needs.
Back up locally stored data.
  Consider imaging the drive before changing any configuration parameters.

## Slide 89: Problem Identification (Slide 2 of 2)
Elicit factual information from the user or technician who reports the issue:
  What are the exact error messages on the screen or coming from the speaker?
  Has anyone else experienced the same issue?
  How long has the problem been occurring?
  What has changed? Did you change things, or did someone else?
  Has anything been tried to solve the problem?

## Slide 90: Sources of Information
Perform a physical inspection.
Reproduce the problem.
Check system and application logs or diagnostic software.
Check the system documentation, such as installation or maintenance logs.
Consult any other technicians who might have worked on the system recently or who might be working on a related issue.

## Slide 91: Determination of Probable Causes
Diagnose problems by identifying symptoms.
Symptoms can lead you to possible causes.
Question the obvious.
  Step through what should happen, either yourself or by observing the user, and identify the point at which there is a failure or error.
  Work up or down layers (for example, power, hardware components, drivers/firmware, software, network, and user actions).
Categorize and eliminate non-causes.
Be prepared to backtrack and try different paths.
Research the issue.
Re-establish a theory when necessary.

## Slide 92: Problem Escalation
Confer with colleagues and others when you are stuck.
Escalate when you can’t solve a problem.
  Senior staff, knowledge experts, SMEs, technical staff, developers, programmers, and administrators within your company.
  Suppliers and manufacturers—warranty and support contracts and helplines or web contact portals.
  Other support contractors and consultants, websites, and social media.
Balance timeliness with possible higher costs.
Follow organizational policies.

## Slide 93: Solution Implementation and Testing
Three possible solutions for most IT problems:
  Repair.
  Replace.
  Workaround.
Assess costs and time requirements.
Be aware of change management policies.
When implementing solutions:
  Consider the effect on others.
  Test after each change, and revert if the change does not solve the problem.

## Slide 94: Verification and Documentation
Tests:
  Try to use a component.
  Swap component out for a known good one.
  Inspect component for proper connection, damage, and indicator lights.
  Disable or uninstall a component.
  Check documentation and software diagnostic tools.
  Update software or device drivers.
Be sure you are satisfied the problem is solved.
Be sure the user is satisfied the problem is solved.
Implement preventive measures.
Document findings, actions, and outcomes.
  Helps immensely with future troubleshooting.

## Slide 95
Discussing Troubleshooting Methodology

## Slide 96
Will there be any specialty input devices that you will need to install or configure at your workplace? How might this affect your day-to-day activities as an IT professional?
Which part of the CompTIA A+ Troubleshooting Model do you expect to find most challenging, and why?