## Slide 1: Installing, Configuring, and Troubleshooting Display and Multimedia Devices

## Slide 2: Installing, Configuring, and Troubleshooting Display and Multimedia Devices
Install and Configure Display Devices
Troubleshoot Display Devices
Install and Configure Multimedia Devices

## Slide 3: Display Device Types
Monitors
Projectors
Virtual reality (VR) headsets

## Slide 4: Monitors
Legacy display devices: CRT
Flat panel LCDs:
  Digital signaling
  Thinner and lighter
  Use less power
LCD and TFT
  TN and IPS
LCD backlighting
  Edge lit
  Backlit
  Color temperature
OLED displays

## Slide 5: Digital Projectors
Video projector: A large format display in which the image is projected onto a screen or wall using a lens system.
CRT
LCD
DLP

## Slide 6: VR Headsets
VR headset: A headset worn like goggles to interact with images displayed in the headset.
Sensory input from computer applications.
Handheld controllers for moving your avatar and interacting with the VR environment.
Uses:
  Gaming
  Meetings
  Social networking
Tethered and mobile.

## Slide 7: Display Device Settings and Features
Resolution and analog/digital output
Screen size and aspect ratio
Refresh rate
Brightness, contrast ratio, and illuminance
Viewing angle and privacy filters
Coatings
XGA and HD standards:
  Resolution
  Color depth
  Aspect ratio

## Slide 8: VGA Standards
Standard | Resolution | Aspect Ratio
WXGA | 1280x800 | 16:10
SXGA | 1280x1024 | 5:4
HD | 1366x768 | 16:9
WSXGA | 1440x900 | 16:10
HD+ | 1600x900 | 16:9
Full HD | 1920x1080 | 16:9
QHD | 2560x1440 | 16:9
4K UHD | 3840x2160 | 16:9

## Slide 9: Display Device Connections and Cables
Many types of connectors and cables.
Video adapters and devices can support multiple cable types.
TFT displays use digital signals, but some support legacy analog signals, too.
  Analog to digital conversion.
  Digital to analog conversion.

## Slide 10: VGA Ports and Connectors
VGA port: 15-pin connector used to connect monitors to PCs.
Legacy standard analog video interface.
15-pin D-shell connector with screws.
Analog interface carries continuous variable signals for RGB component video.
Cabling is marketed according to supported resolutions.
  Lower quality 800x600.
  Higher quality 1600x1200.
Cable length typically 5 m.
  High quality cable might support up to 30 m.

## Slide 11: DVI Ports and Connectors (Slide 1 of 2)
Digital Visual Interface: (DVI) Video adapter designed to replace VGA port. It supports digital only or digital and analog signaling.
Designed for use with flat panel displays.
Being phased out for newer technology.
Types:
  DVI-A
  DVI-D (single link)
  DVI-I (single link)
  DVI-D (dual link)
  DVI-I (dual link)

## Slide 12: DVI Ports and Connectors (Slide 2 of 2)
Different types support analog and digital equipment.
  DVI-A: analog only
  DVI-D: digital only
  DVI-I: analog and digital
Bandwidth:
  Single link: 3.7 Gbps, full HD resolution, 1920x1200, at 60 fps
  Dual link: over 7.4 Gbps, HDTV, 2560x1600, at 85 fps

## Slide 13: HDMI Ports and Connectors (Slide 1 of 2)
High Definition Multimedia Interface (HDMI): High-specification digital connector for audio-video equipment.
Used in consumer electronics and computing.
Supports digital video and audio streams.
Versions support different bandwidths.
  Version 1.4 added 4K support (4096x2160 at 24 Hz).
  Version 2.1 supports up to 10K at 120 Hz.
Connectors:
  Type A 19-pin
  Type B 29-pin for dual link (less commonly used)
  Type C Mini HDMI
  Type D Micro HDMI

## Slide 14: HDMI Ports and Connectors (Slide 2 of 2)
Cable ratings:
  Standard (Category 1)
  High Speed (Category 2)
  Premium High Speed
  Ultra High Speed
Backwards compatible with DVI-D

## Slide 15: DisplayPort Ports and Connectors (Slide 1 of 2)
DisplayPort: Digital A/V interface developed by VESA. DisplayPort supports some cross-compatibility with DVI and HDMI devices.
Royalty-free HDMI alternative.
Packetized data transfer.
  Similar to PCIe.
  Lanes can have different data rates.
Each lane can be allocated a 1.62, 2.7, or 5.4 Gbps data rate.
Maximum data rate for a 4-lane link is 17.28 Gbps.
Support for 48-bit color, 3D, 4K/UHD, and HDCP.

## Slide 16: DisplayPort Ports and Connectors (Slide 2 of 2)
Supports copper and fiber-optic cables.
  Copper: 2560x1600
Connectors:
  20-pin
  DP++ enables connection to DVI-D and HDMI devices
  Mini DP

## Slide 17: Thunderbolt and USB-C Ports and Connectors
Emerging trend is to use USB-C.
Can carry HDMI and DisplayPort signaling, but most often seen in use with Thunderbolt 3.

## Slide 18: Video Adapters and Converters (Slide 1 of 2)
HDMI to DVI-I
VGA to DVI-I

## Slide 19: Video Adapters and Converters (Slide 2 of 2)
Thunderbolt to DVI

## Slide 20: Video Cards
Video card: Interface between graphics components of a PC and the display device.
Might use system CPU and memory; might have onboard processor and memory.
Integrated cards: onboard adapter.
  Usually on low-end PCs.
Add-on cards in PCIe slots.

## Slide 21: Adapter Components
Graphics Processing Unit (GPU): Type of microprocessor used on dedicated video adapter cards or within a CPU with integrated graphics capability.
Clock speed
Shader units
Frame rate
3D cards need more memory
  Onboard AM: from 2 to 12 GB
PCIe x16 interface
At least 1 digital video interface supported
Graphics APIs: DirectX and OpenGL

## Slide 22: Configuration Tools for Display Devices
Automatic detection and installation via Plug-and-Play.
System firmware setup program to disable onboard video adapter.
Settings such as resolution, etc.
  OS tools like Windows Settings or Control Panel.
  Vendor configuration utility.
  Monitor controls or onscreen menus.

## Slide 23: Multiple Displays (Slide 1 of 2)
Configuration options:
  Graphics adapter with multiple display ports.
  Multiple graphics adapters.
  Daisy-chaining DP or Thunderbolt monitors.
Windows display modes:
  Duplicated display.
  Extended display.
  Show only on 1/2.

## Slide 24: Multiple Displays (Slide 2 of 2)
Duplicated
Extended

## Slide 25
Discussing Display Device Installation and Configuration

## Slide 26
Installing a Graphics Adapter

## Slide 27: Common Display Issues
No image is displayed on the monitor.
Image is dim.
Image flickers or is distorted.
Images have low resolution or color depth.
Images and icons are oversized.
Incorrect color patterns.
Dead pixels.
Image is burned into the monitor.
Unexpected objects or patterns appear on the monitor.
Overheating.
Protected content.

## Slide 28: Guidelines for Troubleshooting Display Devices (Slide 1 of 3)
Display configuration issues:
  For no image:
    Verify power to the monitor, and make sure it’s not in standby mode.
    Verify connection between video card and monitor.
    Use OSD controls to verify display input.
    Try using the monitor with another PC.
  For a dim image, adjust brightness and contrast controls, and check for power-save mode.
  For image quality issues:
    Check the video cable and connector.
    Adjust hardware acceleration.
    Adjust resolution.
    Adjust refresh rate.
    Adjust image controls.
    Verify no physical damage

## Slide 29: Guidelines for Troubleshooting Display Devices (Slide 2 of 3)
Display configuration issues (continued):
  For low resolution or color depth, verify that the driver is current.
  For oversized images and icons:
    Increase resolution.
    Increase DPI scaling.
    Verify no zoom tool in use.
  For color quality issues:
    Calibrate to scanners and printers.
    Check connectors and cabling.

## Slide 30: Guidelines for Troubleshooting Display Devices (Slide 3 of 3)
Adapter and monitor faults:
  For dead pixels, try software utilities designed to reactivate them, or gently tapping the affected area of the screen.
  Use screen savers and power-saving modes to avoid burn-in.
  For unexpected objects or patterns being displayed:
    Static artifacts are often caused by a faulty adapter.
    For persistent images on TFT monitors, try shutting off the monitor for several hours.
    Verify the graphics card, driver, and API version support the application or game.
    Try disabling video effects or adjusting to a lower resolution.
    Check for and install updated device drivers.
  For unexpected shutdowns:
    Check the display adapter and driver if you experience BSoD.
    Verify that the graphics adapter is adequately cooled.
  For unauthorized content or HDCP errors:
    Verify that DRM and HDCP are not disabling the display subsystem.

## Slide 31
Discussing Display Device Troubleshooting

## Slide 32
Troubleshooting Monitor Issues

## Slide 33: Audio Subsystems (Slide 1 of 4)
Audio subsystem: Made up of sound card and one or more input and output devices.
DSP and DACs
Onboard audio chip for basic sound capabilities
Expansion cards have more and better features
  Onboard RAM
  Wave tables
  Multiple jacks
Support sound APIs
  DirectSound3D
  OpenAL
  EAX

## Slide 34: Audio Subsystems (Slide 2 of 4)

## Slide 35: Audio Subsystems (Slide 3 of 4)
Jack | Description
Audio in (light blue) | A low-level (1V) stereo signal as supplied by most tape decks, video players, tuners, CD players, and so on.
Mic in (pink) | A mono-only analog input.
Audio out (lime) | A low-level (1V) analog stereo signal suitable for feeding into amplified speakers or headphones.
Audio out (black) | Carries the signal for rear speakers in a surround sound system.
Audio out (orange) | Carries the signal for the subwoofer in a surround sound system.

## Slide 36: Audio Subsystems (Slide 4 of 4)

## Slide 37: Audio Output Devices (Slide 1 of 2)
Playback through speakers or headphones.
  Can be analog or digital sound.
Mono, stereo, and surround sound.
  5.1 Dolby Digital/DTS: 3 front speakers, 2 rear speakers, and a subwoofer.
  7.1 Dolby Digital Plus/DTS-HD: 3 front speakers, 2 side speakers, 2 rear speakers, and a subwoofer.
Connection to optical drive.
Playback quality depends on frequency response.

## Slide 38: Audio Output Devices (Slide 2 of 2)

## Slide 39: MIDI Equipment
Musical Instrument Digital Interface (MIDI): Allows a computer with a sound card to drive MIDI-compatible musical instruments, or for a synthesizer to drive a computer audio application
Synthesizers and electronic drum sets.
Information about a sound is shared, not the sound itself.
  Sample
  Volume
  Pitch
  Tempo
MIDI devices use 5-pin DIN connectors or USB connectors.

## Slide 40: Sound Recording Equipment
Sampling and resolution.
  Higher sampling rates and resolutions provide more accurate sound.
Distortion (noise).
  THD and SNR.
Multiple ports connect different types of recording gear.

## Slide 41: Headsets
Headsets contain headphones and a microphone.
Used for VoIP calls, and meeting and conferencing applications.
Connections are usually USB or wireless (Bluetooth).

## Slide 42: Audio Settings
OS tools:
  Windows Sound Control Panel
  Windows Sound Settings
Hardware volume controls:
  MM keyboards
  Laptop buttons and function keys

## Slide 43: Webcams (Slide 1 of 2)
Webcam: A digital camera connected to a computer that can be used to stream and record video.
Records video and audio.
Relatively low quality video.
Used for online video conferences, website feeds, and surveillance.
Integrated or external peripheral.

## Slide 44: Webcams (Slide 2 of 2)

## Slide 45: Digital Cameras (Slide 1 of 2)
Digital camera: A version of a 35 mm film camera where the film is replaced by light-sensitive diodes and electronic storage media.
Still pictures and video recording.
Images stored on flash memory cards.
Photo properties adjusted via software.
No viewfinder.
Available in many models.
Primary quality metric is resolution (megapixels).

## Slide 46: Digital Cameras (Slide 2 of 2)
Generally limited to one memory card type.
Images compressed to JPEG format,
Resolution | Uses
Less than 1 MP | Onscreen viewing.
1 to 2 MP | Onscreen viewing and prints up to around 7 inches.
3 MP | Larger prints up to around 12 inches.
4 to 8 MP and higher | Poster prints 30 inches and larger.

## Slide 47
Discussing Multimedia Device Installation and Configuration

## Slide 48
What types of monitors do you have experience with? What types of connections have you used to connect those monitors to computers?
In your current job role, have you had to troubleshoot display device problems? If so, what did you do and how did you resolve the issues?