## Slide 1: Installing, Configuring, and Troubleshooting Storage Devices

## Slide 2: Installing, Configuring, and Troubleshooting Storage Devices
Install System Memory
Install and Configure Mass Storage Devices
Install and Configure Removable Storage
Configure RAID
Troubleshoot Storage Devices

## Slide 3: System Memory (Slide 1 of 2)
System memory: The main storage area for programs and data when the computer is running.
RAM: (random access memory) The principal storage space for computer data and program instructions.
Volatile: A type of memory where data cannot be stored without power being supplied.
Virtual memory: An area on the hard disk allocated to contain pages of memory.

## Slide 4: System Memory (Slide 2 of 2)

## Slide 5: RAM Types
DRAM: A type of volatile memory that stores each bit of data as a charge within a single transistor.
SDRAM: A variant on the DRAM chip designed to run at the speed of the system clock, thus accelerating the periodic refresh cycle times.
DRAM:
  Stores each data bit as an electrical charge within a single bit cell.
  Bit cell composed of a capacitor and a transistor.
  Charge dissipates, causing memory to lose information.
  Dynamic memory has to be refreshed to keep the information.
SDRAM:
  Older technology.
  Synchronized to the system clock.

## Slide 6: DDR SDRAM
DDR SDRAM: Standard for SDRAM where data is transferred twice per clock cycle.
RAM Type | Memory Clock (MHz) | Bus Clock (MHz) | Data Rate (MT/s) | Transfer Rate (Gbps)
DDR-200/PC-1600 | 100 | 100 | 200 | 1.6
DDR-26/PC-2100 | 133 | 133 | 266 | 2.1
DDR-333/PC-2700 | 167 | 167 | 333 | 2.7
DDR-400/PC-3200 | 200 | 200 | 400 | 3.2

## Slide 7: DDR2/DDR3/DDR4 SDRAM (Slide 1 of 3)
RAM Type | Memory Clock (MHz) | Bus Clock (MHz) | Data Rate (MT/s) | Transfer Rate (Gbps)
DDR2 | 100 to 266 | 200 to 533 | 400 to 1066 | 3.2 to 8.533
DDR3 | 100 to 266 | 400 to 1066 | 800 to 2133 | 6.4 to 17.066
DDR4 | 200 to 400 | 800 to 1600 | 1600 to 3200 | 12.8 to 25.6

## Slide 8: DDR2/DDR3/DDR4 SDRAM (Slide 2 of 3)
Examples of DDR Standards:
DDR2 – 1066/PC28500:
  Memory works at 266 MHz, bus works at 533 MHz.
  Double data rate gives 1066 MT/s.
  Nominal transfer rate of 8.533 GBps.
DDR3 – 1600/PC321800:
  Memory works at 200 MHz, bus works at 800 MHz.
  Double data rate gives 1600 MT/s.
  Nominal transfer rate of 12.8 GBps.

## Slide 9: DDR2/DDR3/DDR4 SDRAM (Slide 3 of 3)
Examples of DDR Standards (continued):
DDR4 – 1600/PC4-12800:
  Memory works at 200 MHz, bus works at 800 MHz.
  Double data rate gives 1600 MT/s.
  Nominal transfer rate of 12.8 GBps.
  Lower voltage, so less power consumption than DDR3.
DDR4 – 2400/PC4-19200:
  Memory works at 300 MHz, bus works at 1200 MHz.
  Double data rate gives 2400 MT/s.
  Nominal transfer rate of 19.2 GBps.
  Faster than any DDR3.

## Slide 10: Memory Modules (Slide 1 of 3)
Memory module: A printed circuit board that holds a group of memory chips that act as a single unit.
DIMM: (dual inline memory module) Standard packaging for system memory. There are different pin configurations for different RAM types.
Located in slots on motherboard.
Removable and replaceable.
Defined by their design and by the number and type of chips contained.

## Slide 11: Memory Modules (Slide 2 of 3)
RAM Type | Pins | Voltage
DDR | 184 | 2.5 to 2.6 V
DDR2 | 240 | 1.8 to 1.9 V
DDR3 | 240 | 1.35 to 1.5 V
DDR4 | 288 | 1.2 V

## Slide 12: Memory Modules (Slide 3 of 3)
SODIMM: Memory that is half the size of DIMMs, is available in 32- or 64-bit data paths, and is commonly found in laptops and iMac systems.
Laptop RAM.
DDR and DDR2 have the same number of pins, but the key position is different.
Typically fits into slots that pop up at a 45º angle to allow the chips to be inserted or removed.
Pins:
  DDR 200 pin packages.
  DDR2 200 pin packages.
  DDR3 204 pin packages.
  DDR4 260 pin packages.

## Slide 13: Dual-Channel Memory (Slide 1 of 2)
Single-channel memory: Memory with one 64-bit bus between the CPU and RAM.
Dual-channel memory: Memory controller with two pathways to the CPU, enabling 128 bits of data transferred per transaction.
Effectively two pathways through the bus to the CPU.
128 bits of data can be transferred per transaction.
Installed memory modules should be identical in terms of:
  Speed
  Capacity
  Chip number
  Density
  Location
Refer to documentation for which slots to insert memory into.

## Slide 14: Dual-Channel Memory (Slide 2 of 2)

## Slide 15: Parity and ECC RAM
Parity checking: An error-checking method where each byte of data in memory is accompanied by a ninth bit used to check for corrupted data.
Nonparity: System memory that does not perform error checking.
ECC memory: RAM with built-in error correction security.
Parity checking:
  Uses 8 bits for memory and 1 bit to check parity.
  Old technology rarely if ever used now.
Most desktops now use non-parity memory.
Systems that require a high level of reliability use ECC memory.
  ECC memory has an extra chip and a 72-bit data bus.
  Motherboard must support the use of ECC memory modules.
  Cannot mix ECC and non-ECC modules.

## Slide 16: Memory Installation and Upgrade
If the motherboard supports an upgrade but the system is not configured to use it, enable a dual-channel configuration.
Increasing the bus speed requires purchasing a new motherboard and memory modules (and possibly CPU).

## Slide 17: Memory Compatibility Issues (Slide 1 of 2)
The DIMM format must match the motherboard.
Different capacity modules can be installed.
  Most vendors recommend installing the largest module in the lowest numbered slot.
Modules from different vendors can be mixed.
  This may cause problems with multi-channel configurations.
For best performance, the modules should be the same speed as the motherboard.
  Different speeds can be mixed.
  The system will only operate at the best speed supported by all installed.

## Slide 18: Memory Compatibility Issues (Slide 2 of 2)
For best performance and reliability, configure multi-channel systems with identical memory modules for each channel.
ECC memory cannot be mixed with non-parity memory and must be supported by the motherboard.
Registered memory cannot be mixed with unbuffered modules and must be supported by the motherboard.

## Slide 19
Discussing System Memory Installation

## Slide 20
Upgrading Memory

## Slide 21: Storage Devices
Mass storage devices: Non-volatile storage devices that are able to hold data when the system is powered off.
Hold data when system is powered off.
Can be internal or removable.
To store data, it uses one of these methods:
  Magnetic
  Optical
  Solid state

## Slide 22: Hard Disk Drives (Slide 1 of 2)
HDD: (hard disk drive) A device that provides persistent mass storage for a PC.
Primary persistent storage method.
On workstations, typically stores:
  OS files.
  Application program files.
  Drivers.
  User data.
On servers, typically stores:
  OS files.
  Individual user files.
  Shared information sources such as databases.

## Slide 23: Hard Disk Drives (Slide 2 of 2)
Tracks: Data written as concentric rings on a disk drive.
Cylinders: The aggregate of all tracks that reside in the same location on every disk surface.
HDD up to 8 TB.
Data is stored on metal or glass platters coated with magnetic substance.
Each platter has:
  Top and bottom read/write heads.
  Heads that float above platters.
Form factors include 3.5” and 2.5”.
  Height varies: 15 mm , 9.5 mm, 7 mm, and 5 mm.

## Slide 24: HDD Performance Factors (Slide 1 of 2)
Access time: Speed at which memory or a disk drive can be addressed and utilized.
Internal transfer rate: Measure of how fast read/write operations are performed on the disk platters.
External transfer rate: Measure of how fast data can be transferred to the CPU across the bus.
Early-life Failure Rate: A method of calculating how quickly a device will fail through accelerated testing.

## Slide 25: HDD Performance Factors (Slide 2 of 2)
MBTF: (mean time between failures) The rating on a device or component that predicts the expected time between failures.
Life expectancy: The length of time for which a device can be expected to remain reliable.
S.M.A.R.T.: Technology designed to alert the user to possible hard disk failures before the disk becomes unusable.

## Slide 26: Storage Adapters and Cables
HBA: (host bus adapter) A component that allows storage devices to exchange data with a computer system by using a particular interface.
Drive controller: The circuitry in the disk unit that allows it to put data on the bus, which the HBA shuttles to the CPU or RAM.
Connection point for internal mass storage devices.
Interface between drive, HBA, rest of the system is a type of bus.
  Old technology included PATA and SCSI.
  Most systems now use SATA.

## Slide 27: SATA (Slide 1 of 3)
SATA: A widely used hard disk interface using a 7-pin data connector and a 15-pin power connector.
Transfers data in serial format.
Cables can be up to 1 m and are thin and flexible.
Cables terminate with 7-pin connectors.
Each host adapter port supports a single device.
Drives are hot swappable.
SATA speeds:
  Original SATA: up to 1.5 Gbps.
  SATA 2: up to 3 Gbps.
  SATA 3: up to 6 Gbps.

## Slide 28: SATA (Slide 2 of 3)

## Slide 29: SATA (Slide 3 of 3)

## Slide 30: Solid State Drives
SSD: (solid state drive) A personal computer storage device that stores data in non-volatile special memory instead of on disks or tape.
Advantages:
  No moving parts.
  Quieter and more power efficient than HDD.
  Less prone to failure due to shock.
  Better read times:
    Seek time is faster.
    File fragmentation is eliminated.
  Less likely to lose data due to power failures.
Disadvantage:
  High cost.

## Slide 31: SSD Interfaces and Form Factors (Slide 1 of 2)
AHCI: (Advanced Host Controller Interface) A logical interface used by SATA drives to communicate with the bus.
NVMHCI: (Non-Volatile Memory Host Controller Interface Specification) A logical interface used by PCIe-based SSD drives to communicate with the bus.
NVMe: (NVM Express) An interface for connecting flash memory devices, such as SSDs, directly to a PCI Express bus.
Lanes: In PCIe, two wire pairs (four wires in total) using low voltage differential signaling, with one pair used to transmit and the other pair to receive (bi-directional).

## Slide 32: SSD Interfaces and Form Factors (Slide 2 of 2)
Often used for the OS and applications.
  HDD used for user data files.
Some SDDs are connected using SATA interface.
  6 Gbps capacity can be a bottleneck over AHCI logical interface.
SDDs often communicate directly to the PCIe bus using NVMe.
PCIe-based SSD:
  Can be implemented as regular PCIe adapter card or AiC.
  Uses the M.2 adapter interface.
M.2 adapters:
  Are not hot-swappable or hot-pluggable.
  Are smaller than a PCIe adapter.
  Supply the power over the bus.
  Can use up to 4 PCIe lanes.

## Slide 33: SDD Performance Factors (Slide 1 of 2)
SDD usually outperforms HDD.
  Serving large files, HDD usually performs better.
Compare different types of data transfer:
  Read performance.
  Write performance.
  Sequential access.
  Random access.
  Transferring lots of small files.
  Data throughput.
  Latency.
  IOPS.

## Slide 34: SDD Performance Factors (Slide 2 of 2)
Wear leveling: Routines used by flash drives to prevent any single storage location from being overused and to optimize the life of the device.
Flash chips are susceptible to degradation.
Use wear leveling:
  Prevents any single location from being overused.
Wear leveling helps optimize life of the drive.

## Slide 35: Hybrid Drives
Hybrid drive: A drive that contains an SSD portion, which functions as a large cache, containing frequently accessed data; and a magnetic disk portion, which is spun up only when non-cached data is accessed.
Host-hinted mode: A SATA standard (version 3.2) that defines a set of commands to allow the host computer to specify how the cache should be used.
SATA 3.2 standard allows host to specify how to use the cache.
Drive firmware can run self-optimizing routines.
User does not have direct control over which files are stored in cache.

## Slide 36: Dual-Drive Configurations
Install separate SSD and HDD devices.
System chipset and storage drivers make caching decisions.
  Often uses Intel SRT.
  User does not have control over use of the SSD cache.

## Slide 37: Legacy Storage Technologies (Slide 1 of 8)
PATA: Older drive technology that supported two devices per channel: master and slave. Also referred to as IDE or EIDE.
Channels: Paths between PATA drives and motherboard, called IDE1 and IDE2 or primary (PRI IDE) and secondary (SEC IDE).
Uses parallel data transfers, with 6 bits transferred per clock tick.
Motherboards supporting PATA include 1 or 2 host adapters (“channels”).
  IDE1 or PRI IDE and IDE2 or SEC IDE
Each PATA channel supports 2 devices.
  01 and 1.
  Master and slave.

## Slide 38: Legacy Storage Technologies (Slide 2 of 8)
PATA drives use 40-pin port and 80-wire shielded cables.
  Required for UDMA4 or better transfer modes.
PATA cable can be up to 18” long and has 3 connectors.
  One for motherboard.
  One for each device (master and slave).
Most cables are Cable Select.
  Drives are identified as master or slave based on position of the connector.
Pin 1 on cable must be oriented to pin 1 on the connector.
  Identified on cable with a red stripe.
  Keyed to prevent improper insertion.

## Slide 39: Legacy Storage Technologies (Slide 3 of 8)

## Slide 40: Legacy Storage Technologies (Slide 4 of 8)
Interface Standard | DMA Mode | Max Transfer Rate (MBps) | Special Features
ATA/ATAPI-4 | UDMA 2 (Ultra ATA/33) | 33 | Ultra DMA, 80-conductor cable, and cyclic redundancy checking
ATA/ATAPI-5 | UDMA 4 (Ultra ATA/66) | 66 | 
ATA/ATAPI-6 | UDMA 5 (Ultra ATA/100) | 100 | 48-bit LBA expansion, and disk noise reduction
ATA/ATAPI-7 | UDMA 6 (Ultra ATA/133) | 133 | Multimedia streaming

## Slide 41: Legacy Storage Technologies (Slide 5 of 8)
SCSI: (Small Computer Systems Interface) An older personal computer connection standard that provides high-performance data transfer between the SCSI device and the other components of the computer.
One SCSI HBA can control multiple devices.
  Attach with internal ribbon or external SCSI cables.
SCSI command language allows HBA to identify:
  Which devices are connected.
  How they are accessed.
Typically used to connect storage devices.
  Older devices such as scanners could also be connected through SCSI.
SCSI port is denoted with the symbol

## Slide 42: Legacy Storage Technologies (Slide 6 of 8)
Interface Protocol | Standard | Bandwidth (MBps) | Bus Width (bits) | Max. Cable Length (meters)
SCSI-1 | SCSI-1 | 5 | 8 | SE: 6 LVD: NA HVD: 25
Fast SCSI | SCSI-2 | 10 | 8 | SE: 3 LVD: NA HVD: 25
Fast-Wide SCSI | SCSI-2 | 20 | 16 | SE: 3 LVD: NA HVD: 25
Ultra SCSI | SCSI-3 | 20 | 8 | SE: 1.5 LVD: NA HVD: 25
Ultra Wide SCSI | SCSI-3 | 40 | 16 | SE: NA LVD: NA HVD: 25

## Slide 43: Legacy Storage Technologies (Slide 7 of 8)
Interface Protocol | Standard | Bandwidth (MBps) | Bus Width (bits) | Max. Cable Length (meters)
Ultra2 SCSI | SCSI-3 | 40 | 8 | SE: NA LVD: 12 HVD: 25
Ultra2 Wide SCSI | SCSI-3 | 80 | 16 | SE: NA LVD: 12 HVD: 25
Ultra3 SCSI (Ultra160 SCSI) | SCSI-3 | 160 | 16 | SE: 1.5 LVD: NA HVD: 25
Ultra 320 SCSI | SCSI-3 | 320 | 16 | SE: NA LVD: 12 HVD: NA

## Slide 44: Legacy Storage Technologies (Slide 8 of 8)
Term | Description
SCSI Host adapter | Must be installed and recognized for devices to be detected. May require third-party driver to be installed.
Bus width | Originally supported 8 devices. Wide SCSI supports up to 16 devices. HBA is counted as a device.
Signaling | Most buses and devices use LVD. SE devices can be added to an LVD bus. HVD is incompatible with LVD and SE devices.
Termination | Bus must be terminated at both ends. Termination can be enabled on the device by a switch or by connecting a terminator pack to the device or HBA.
ID | Each device is allocated a unique ID from 0 to 7 (to 15 for Wide SCSI). Can be automatically allocated or set using jumpers or click-wheel on the device. Priority goes 7 to 0, then 15 to 8.

## Slide 45: Guidelines for Installing Mass Storage Devices
Does the computer have existing internal storage devices?
Does the device need additional drivers installed?
Does the computer have an available power supply cable to supply power to the device?
Does the computer have an available drive bay for the storage device?
Do you have the necessary data cables to connect the storage device to the controller?
Does the placement of the device interrupt the air flow of the case?

## Slide 46
Discussing Mass Storage Device Installation and Configuration

## Slide 47
Installing Storage Devices

## Slide 48: Removable Storage
Removable storage: A storage device that can be removed from the computer, or the removable media that can be inserted in a drive, to store portable data.
Refers to either:
  Storage devices that can be removed.
  Storage media that can be removed.
Can be attached or inserted in different computers to move or copy files.
Can be used to create a backup.

## Slide 49: Optical Media (Slide 1 of 9)
CD: (compact disc) An optical storage technology that can hold 700 MB of data or 80 minutes of audio data.
DVD: (digital versatile disc) An optical storage technology that can hold 4.7 GB per layer.
CD has 700 MB capacity.
  Capable of delivering most software applications.
DVD has about 17 GB capacity.
  Often used for:
    Software installs.
    Games.
    Multimedia.

## Slide 50: Optical Media (Slide 2 of 9)
Pits: In optical storage media, recessed areas on the disk.
Lands: In optical storage media, raised areas on the disk.
CD-R: Compact disks containing a layer with photosensitive dye in which a laser transforms the dye to mimic the pits and lands of a premastered CD.
Burning: In optical disks, the process of using a special laser used to transform the dye to mimic the pits and lands of a premastered CD.
CD-RW: Compact disks containing a heat sensitive compound whose properties can be changed between crystalline and amorphous by a special laser.

## Slide 51: Optical Media (Slide 3 of 9)
CDs (continued):
  Composed of aluminum foil encased in protective plastic.
    Standard CD is 120 mm diameter.
    1.2 mm thick.
  Foil layer contains pits and lands arranged in a spiral.
    Changes between pits and lands used to encode data bits.
  CD-R contains photosensitive dye.
    Laser transforms the dye to mimic pits and lands of premastered CDs.
    A type of WORM media.
    After an area has been written to, it cannot be overwritten.
    If space is available, a new session can be started on the disc.
  CD-RW
    Uses a heat sensitive compound to change properties between crystalline and amorphous by a laser.
  CDs and DVDs have a tendency to degrade and become unusable.

## Slide 52: Optical Media (Slide 4 of 9)
DVDs:
  Higher density than CDs.
  Thinner than CDs.
  Can be dual-layer and/or double-sided.
    Double-sided discs have to be turned over to access the other side.
  Higher transfer rate than CDs.
    Multiples of 1.32 MBps.
    Fastest models are 24x read and write speeds.
  DVD-R/DVD-RW versus DVD+R/DVD+RW versus DVD±R discs.
    Most drives can read all formats.
    Most drives write in either + or – format.
    DVD±R supports dual layer and double-sided media.
    DVD±RW supports double-sided media only.
  DVD-RAM is not widely supported, but is optimized for multiple write operations.
    Well suited to data storage.

## Slide 53: Optical Media (Slide 5 of 9)
BD: (Blu-ray disc) Latest generation of optical drive technology, with disc capacity of 25 GB per layer. Transfer rates are measured in multiples of 36 MBps.
Used for High Definition (HD) video recording and playback.
HD requires more bandwidth and storage space.
  1920 x 1080 compared to 720x480 (NTSC) or 720x576 (PAL).
  Better quality digital surround sound audio.
Shorter wavelength laser than DVD uses, so has higher density.
  DVD uses 650 mm red laser.
  Blu-ray uses 405 mm blue laser.
Base speed is 4.5 MBps with maximum theoretical rate of 72 MBps (16x).
  2x is the minimum required for movie playback.

## Slide 54: Optical Media (Slide 6 of 9)
Blue-ray Discs (continued):
  Capacity:
    Standard BD: 25 GB per layer.
    Mini-discs (8cm): 7.8 GB per layer.
    Dual-layer discs: 50 GB.
  BD-XL specification requires compatible drives for reading and writing.
    Triple-layer discs: 100 GB.
    Quad-layer discs: 128 GB (not currently recordable).
CD Standard | CD Type
Red book | Audio CDs (16-bit sampled at 44.1 Hz).
Yellow book | Data CDs with error correction (Mode 1) or without (Mode 2). Mode 2 makes more space available but is only suitable for use where small errors can be tolerated.
Orange book | Defines the unused CD-MO and the more popular CD-R and CD-RW.

## Slide 55: Optical Media (Slide 7 of 9)
DVD Standard | Capacity (GB) | Description
DVD-5 | 4.7 | Single layer, single-sided.
DVD-9 | 8.5 | Dual layer, single-sided.
DVD-10 | 9.4 | Single layer, double-sided.
DVD-18 | 17.1 | Dual layer, double-sided.
DVD-Video | Up to 17.1 | Commercially produced DVDs using mpeg encoding and chapters for navigation. Can be single or dual layer and single or double-sided.
DVD-Audio | 8.5 | Format for high quality audio. Superior sampling rates and 5.1 surround sound, for instance.

## Slide 56: Optical Media (Slide 8 of 9)
Consumer DVDs feature DRM and region coding.
DVD region codes include:
  Region 0: No coding (playback is not restricted).
  Region 1: Canada and the US.
  Region 2: Europe, the Middle East, Japan, South Africa, and Egypt.
  Region 3: SE Asia.
  Region 4: South America, Australia, and New Zealand.
  Region 5: Russia, parts of Africa, and parts of Asia.
  Region 6: China.
Blu-ray Disc region codes include:
  Region A: America, Japan, and SE Asia.
  Region B: EMEA, Africa, Australia, and New Zealand.
  Region C: Russia and Central Asia (including China).

## Slide 57: Optical Media (Slide 9 of 9)

## Slide 58: Optical Drives (Slide 1 of 2)
CD drives, DVD drives, and Blu-ray drives.
Larger than HDDs.
  5.25 inch drive bay and SATA connectors for internal installation.
  USB, eSATA, or Thunderbolt connection and external power for external installations.
Rated by data transfer speed.
  150 KBps originally to over 7 MBps.
Most have read and write capabilities.
  Record/Rewrite/Read speed.
  BURN-proof technology.

## Slide 59: Optical Drives (Slide 2 of 2)
CD drive: An optical drive consisting of a spindle motor to spin the disc, a laser and lens to read the disc, and a tracking system to move the laser and lens assembly.
DVD drive: An optical drive similar to a CD drive, but with a different encoding method and a shorter wavelength laser. Typically can read and burn CD and DVD media.
Blu-ray drive: An optical drive for reading, and if so equipped, writing to Blu-ray disc media. Most drives can also read CD and DVD discs.

## Slide 60: Flash Memory Devices (Slide 1 of 3)
Solid state storage: Any type of persistent digital storage technology that does not use mechanical parts.
Flash memory: Similar to a ROM chip in that it retains information even when power is removed, but it adds flexibility in that it can be reprogrammed with new contents quickly.
Memory card: Flash drives typically used for digital cameras and smartphones; typically small and flat.

## Slide 61: Flash Memory Devices (Slide 2 of 3)
Non-volatile EEPROM or NAND flash.
Small and light compared to other types of storage.
Storage capacity typically ranges from 512 MB to 256 GB.
  Larger drives are available, but are very expensive.
Packaging of flash memory varies:
  USB thumb or pen drive.
  Memory cards.

## Slide 62: Flash Memory Devices (Slide 3 of 3)
Type of Memory Card | Description
Secure Digital (SD) | Maximum capacity Original SD cards up to 2 GB. SDHC is up to 32 GB. SDXC is up to 2 TB. Speed Original specification is up to 25 MBps. UHS allows up to 108 MBps. UHS-II is rated at up to 312 MBps.
Mini-SD | Smaller version of SD cards, with the same capacity and speed designations.
Micro-SD | Smallest version of SD cards, using the same capacity and speed designations.
Compact Flash (CF) | Supports up to 512 GB, but no cards were created larger than 256 GB. Speed is multiples of 150 Kbps (the same rating as CDs). Fastest devices work at 1066x read speeds (160 MBps).
xD | Format for Olympus cameras that has been discontinued.

## Slide 63: Memory Card Readers (Slide 1 of 2)
Memory card readers: A device containing one or more slots to accommodate reading (and writing) memory cards.
Can be an internal component with slots on the face, accessed externally.
  Supports most common memory card formats.
  Usually designed to fit in 3.5” or 5.25” drive bay.
Connects to a USB hub.
  Motherboards typically have at least one spare 9-pin USB header.
  Might connect to an expansion card.
  Might use a USB converter cable from the internal reader to an external USB port.
Also available as an external device that connects to an external USB port.

## Slide 64: Memory Card Readers (Slide 2 of 2)

## Slide 65: External Storage Drives
Drive enclosure: An external case that holds one or more disks and typically connects to the computer through USB or Thunderbolt ports.
Enclosure for external drives usually has USB or Thunderbolt ports.
eSATA can also be used to attach external drives to an eSATA external port.
  Power is not supplied over the cable.
Some enclosures support Ethernet connections.
  Referred to as Network Attached Storage (NAS).
  Enclosure might hold multiple disks configured as RAID.

## Slide 66
Discussing Removable Storage Device Installation and Configuration

## Slide 67: RAID
RAID: (redundant array of independent disks) A set of vendor-independent specifications for fault-tolerant configurations on multiple-disk systems.
Can act as backups for each other to increase reliability.
Can act together to create one very large drive.

## Slide 68: RAID Levels (Slide 1 of 9)
Disk striping: A disk array access pattern where data is written in stripes to two or more disks sequentially, improving performance. Also known as RAID 0.
RAID 0 (Striping without Parity):
  Logical volume size is combined total of smallest capacity physical disk.
  Ideally all disks are identical capacity, type, and performance.
  Adds no storage overhead.
  A means of creating a large logical volume from multiple low capacity disks.
  Provides no redundancy.
    If any physical disk fails, the entire array fails.

## Slide 69: RAID Levels (Slide 2 of 9)

## Slide 70: RAID Levels (Slide 3 of 9)
Disk mirroring: A type of RAID (RAID 1) that uses two hard disks, providing the simplest way of protecting a single disk against failure.
RAID 1 (Mirroring):
  Requires two hard disks, one being a duplicate of the other.
  Each write operation is duplicated on the second disk, creating a small performance overhead.
  Read operations can use either disk, which boosts performance slightly.
  If one disk fails, the other takes over.
  When a failed disk is replaced, performance suffers during the resync operation.
  More expensive per gigabyte than other RAID levels (only 50% of space is available for storage).
  Total volume size cannot exceed available disk capacity.

## Slide 71: RAID Levels (Slide 4 of 9)

## Slide 72: RAID Levels (Slide 5 of 9)
RAID 5 (Striping with Distributed Parity):
  Writes error checking data across all disks in the array.
  Data and parity are managed so they are always on different disks.
  If a single disk fails, information spread on the other disks allows data to be completely reconstructed.
  Performance considerations:
    Offers the best read operation performance.
    Read performance is degraded if a drive fails and data needs to be reconstructed.
    Write operations suffer reduced performance due to the parity calculation.
  Requires at least 3 drives.
    Allows flexibility for overall array capacity.
    Maximum number of drives determined by controller or OS.
    Adding more disks increases chance of failure.

## Slide 73: RAID Levels (Slide 6 of 9)
RAID 5 (continued):
  Level of fault tolerance and available disk space is inverse.
    Adding disks to the set, fault tolerance decreases.
    Usable disk space increases.
  Parity requirements vary with the number of disks.
    RAID 5 with 3 disks requires 1/3 of each disk for parity, so using three 80-GB disks provides 160 GB usable disk space.
    RAID 5 with 4 disks requires ¼ of each disk for parity.

## Slide 74: RAID Levels (Slide 7 of 9)

## Slide 75: RAID Levels (Slide 8 of 9)
RAID 1+0 (RAID 10):
  Combination of RAID 1 and RAID 0 provides high fault tolerance.
  Considered a nested array.
  Requires at least 4 disks.
    More disks can be used, but there must be an even number of disks.
  Suffers the same 50% disk overhead as mirroring.

## Slide 76: RAID Levels (Slide 9 of 9)

## Slide 77: RAID Configuration Options (Slide 1 of 4)
Hardware RAID solution: A method of creating volumes from an array of physical disks by using a plug-in controller card or the motherboard, independently of the installed operating system.
Entry-level controllers typically support only RAID 0 or RAID 1.
  Typically use SATA drives.
Mid-level controllers might add support for RAID 5 or RAID 10.
Hot swap features are typically only available with high-end hardware.
  Requires compatible controllers and disk units.
  New disks are transparently synchronized with other disks in the set.
  Typically uses SCSI (SAS).
More expensive than a software RAID solution.

## Slide 78: RAID Configuration Options (Slide 2 of 4)
Hardware RAID (continued):
  Usually configured through firmware configuration utility.
  Sometimes RAID controller configuration tools are available within the OS.

## Slide 79: RAID Configuration Options (Slide 3 of 4)
Software RAID:
  Windows provides options to set up software RAID.
    Uses standard disks and controllers.
  Windows Server and Windows Professional/Enterprise editions support RAID 1 and RAID 5.
  Can use internal disks on varying interfaces.
    Typically cannot use external disks connected through USB or Thunderbolt.
    Windows 10 Storage Spaces feature provides RAID-like functionality for external disks.
  Linux uses Logical Volume Manager to implement various RAID levels.
  Software RAID is typically less expensive than hardware RAID controller cards.

## Slide 80: RAID Configuration Options (Slide 4 of 4)
Hot swappable drive: A device that can be added or removed without having to restart the operating system.
Hot swappable drives:
  Usually a server-level or high-end workstation feature.
  Drives mate into combined data/power port.
  Drives can be added from the front of the case without opening the chassis.
  Drives are secured and released with a latch.
Hot swap drive enclosure

## Slide 81
Discussing RAID Configuration

## Slide 82: Disk Failures
A hard drive that is failing might display the following symptoms:
  Read/write failure
  Blue Screen of Death (BSoD)
  Bad sectors
  Constant LED activity
  Noise

## Slide 83: Disk Integrity Testing (Slide 1 of 2)
Disk Integrity Tools
  chkdsk
  S.M.A.R.T. wmic /node:localhost diskdrive get status
  Run advanced diagnostic tests
    Obtain from hard drive vendor or PC manufacturer

## Slide 84: Disk Integrity Testing (Slide 2 of 2)

## Slide 85: Boot Failures (Slide 1 of 2)
If the hard drive is not detected at boot (or if a second hard drive is not shown under Windows):
  Verify that the storage device is powering up.
  If inactive, check that the drive has a power connector attached.
  If drive is powered up:
    Check that the boot sequence is set correctly in the PC firmware system setup program.
    Check that there are no removable disks in floppy or optical drives.
    Check the data cables.
    Check that it has not been disabled by a jumper or via system setup.

## Slide 86: Boot Failures (Slide 2 of 2)
For correctly configured drives:
  If a boot hard drive is detected by the POST but not by Windows, there is probably a problem with the file system.
    Boot into the recovery environment using the Windows setup disc and enter C: at the command prompt. If this produces the error message Invalid media type, try running bootrec You can also try to reformat the disk (at the expense of any data, of course).
    If this produces the error message Invalid drive specification, check the drive's partition structure with diskpart.

## Slide 87: Boot Block Repair (Slide 1 of 2)
MBR: (master boot record) Sector on a hard disk storing information about partitions configured on the disk.
GPT: (globally unique ID partition table) Modern disk partitioning system allowing large numbers of partitions and very large partition sizes.
Drive not detected at bootup.
Second drive not recognized or shown in Windows File Explorer.
Malware:
  Damage to the boot information on the drive.
Two methods of formatting boot information:
  MBR
  GPT

## Slide 88: Boot Block Repair (Slide 2 of 2)
Damage to boot information results in boot errors, including:
  OS not found.
  Invalid drive specification boot using anti-virus software to detect virus that caused the problem.
Try booting using the repair options on the Windows product disk.
  Boot from the product disk and select Repair.
  Try using the Startup Repair option.
  If necessary, select the Command Prompt option.
    Enter bootrec /fixmbr to attempt repair of the MBR.
    Enter bootrec /fixboot to attempt repair of the boot sector.
    Enter bootrec /rebuildbcd to add missing Windows installations to the Boot Configuration Database (BCD).
  Reboot the PC.

## Slide 89: File Recovery Options (Slide 1 of 2)
Remove the hard disk from the computer and insert into an external enclosure.
Connect external enclosure to a PC via a USB port.
Mount the externally connected drive through Disk Management or analyze through file recovery software.
Try using chkdsk to restore file fragments from bad sectors.
  Files saved as file####.chk files on the root of the volume.
  file####.chk files are rarely directly usable.
  Third-party software might be more successful in accessing the data.

## Slide 90: File Recovery Options (Slide 2 of 2)

## Slide 91: Disk Performance Issues
Disk defragmentation: A software routine that compacts files back into contiguous areas of the disk.
Slow disk performance can be a bottleneck.
Often improved by adding more RAM.
Ensure file fragmentation is minimized.
Low disk capacity can cause slow performance.
  Windows warns users in notification area when space is under 200 MB.
  Use Disk Cleanup program to free up space.
  Manually move or delete files.
  Uninstall unnecessary applications.

## Slide 92: Guidelines for Troubleshooting Optical Drives (Slide 1 of 2)
Troubleshooting read problems in optical drives:
  Most problems related to dirt are caused by dirt on the disc itself. Special cleaning kits are available for cleaning optical drives.
  If the CD drive is not able to read any CDs, it is likely a hardware problem.
  DVD-Video requires MPEG decoding hardware or software (codecs) to be installed for playback (included in Windows 7, except Starter and Home Basic).
  A DVD-ROM cannot be read from a CD-ROM drive.
  There is currently no native support for Blu-ray in any version of Windows.

## Slide 93: Guidelines for Troubleshooting Optical Drives (Slide 2 of 2)
Troubleshooting write errors in optical drives:
  Where Windows does not support a particular recordable or rewritable format directly, third-party software is required.
  Check that you are using the write speed recommended for the brand of discs you have purchased.
  Most problems are connected to buffer underruns. To prevent these:
    Burn discs at a lower write speed.
    Copy source files to the local hard disk (rather than removable or network drives).
    Avoid using other applications when burning a disc.

## Slide 94: Common RAID Configuration Issues
RAID not found
RAID stops working

## Slide 95: Guidelines for Troubleshooting RAID Issues (Slide 1 of 2)
If Windows doesn’t detect RAID during setup or at boot:
  Verify RAID controller drivers are installed.
  Use the RAID configuration utility to verify the status.
  If the configuration utility cannot be accessed, the controller may have failed.

## Slide 96: Guidelines for Troubleshooting RAID Issues (Slide 2 of 2)
If RAID stops working:
  Volume is listed as degraded, but the data on the volume is still accessible.
  Examine event logs in the OS system log.
  Replace failed disks as soon as possible.
  If the volume is unavailable, too many disks may have failed or the controller may have failed.

## Slide 97
Discussing Storage Device Troubleshooting

## Slide 98
Troubleshooting Storage Devices

## Slide 99
Which types of storage devices have you worked with? Have you installed additional hard drives or replaced hard drives?
What sorts of issues have you experienced with storage devices? How will the troubleshooting tools and guidelines presented in this lesson help with future issues?