## Slide 1: Configuring and Troubleshooting Networks

## Slide 2: Configuring and Troubleshooting Networks
Configure Network Connection Settings
Install and Configure SOHO Networks
Configure SOHO Network Security
Configure Remote Access
Troubleshoot Network Connections
Install and Configure IoT Devices

## Slide 3: NIC Properties
Computer’s network adapter connects to a network appliance
Card settings should be configured to match network

## Slide 4: Wired Network Cards
Ethernet adapter and switch must have same media type:
  Signaling speed
  Half/full duplex
Most will auto-negotiate; can be configured
Most settings can be left at default

## Slide 5: QoS
Network protocol that prioritizes some types of traffic.
Can help ensure real-time applications such as VoIP or video conference have priority.
QoS usually configured on managed switches.
May need to enable QoS protocol on adapter.

## Slide 6: Onboard Network Cards
Most computers have built-in Gigabit Ethernet adapter.
Uses RJ-45 port/twisted-pair cabling.
Check system setup if issues or to disable if installing a plug-in card.

## Slide 7: Wireless Network Cards
Set up 802.11 standard supported by access point
Card should support any standard available
Configure Roaming Aggressiveness to adjust for weak signals
Transmit Power usually set to highest level by default

## Slide 8: Wake on LAN
Start computer remotely
Network card is active, on standby
“Magic packet” starts boot
To set up WoL:
  Enable WoL in system setup
  Enable WoL on adapter
  Configure network to send magic packets

## Slide 9: Network Connections in Windows 7 and Windows 8 (Slide 1 of 4)
Configure network card with client software and protocol
Use Network and Sharing Center

## Slide 10: Network Connections in Windows 7 and Windows 8 (Slide 2 of 4)
Access adapter properties
Wired/wireless adapter names vary

## Slide 11: Network Connections in Windows 7 and Windows 8 (Slide 3 of 4)
Change properties or view status
Configure client, protocol, service
Default bindings include Microsoft clients, IPv4 and IPv6, and link-layer discovery

## Slide 12: Network Connections in Windows 7 and Windows 8 (Slide 4 of 4)
To join WLAN, select network from list in notification area
Can connect automatically
Can configure manually if network not broadcasting

## Slide 13: Network Connections in Windows 10
Settings: Network & Internet
Use to access Network and Sharing Center and Network Connections applets

## Slide 14: IP Address Configuration (Slide 1 of 2)
Configure wired and wireless through connection’s Properties
Default is dynamic IP
Can configure a static IP address manually

## Slide 15: IP Address Configuration (Slide 2 of 2)
Select “Obtain an IP address automatically” for DHCP/APIPA
Can set up alternate configuration if desired

## Slide 16: Other Network Connections (Slide 1 of 3)
SOHO router is typical; usually combines several functions
Other connection options include dial-up
Analog modem connects to ISP
Use Set Up a Connection or Network to configure

## Slide 17: Other Network Connections (Slide 2 of 3)
WAN cellular connects to a cell provider’s network
Can be USB or internal
Install vendor software, plug in adapter, use software to view and configure

## Slide 18: Other Network Connections (Slide 3 of 3)
VPN tunnels privately through network
Windows supports several types; can configure in Network Connections
Click network status icon to access

## Slide 19
Discussing Network Connection Configuration Settings

## Slide 20: SOHO Networks
Business network; may use centralized server as well as clients.
Often uses single Internet device for connectivity.
May be home/residential network as well.

## Slide 21: Common SOHO Network Hardware (Slide 1 of 2)
DSL or cable modem installed on customer premises.
Bundles several device types: modem, router, switch, access point.
On DSL, RJ-11 port connects to phone jack; voice/data splitter usually part of modern socket.

## Slide 22: Common SOHO Network Hardware (Slide 2 of 2)
On DSL, RJ-11 port connects to phone jack.
Voice/data splitter usually part of modern socket.

## Slide 23: SOHO Network Configuration (Slide 1 of 2)
Connect device to SOHO appliance to configure.
Access management interface through browser.
Change default password!
Follow wizard interface to configure Internet access.

## Slide 24: SOHO Network Configuration (Slide 2 of 2)
View line status and system log in management console.
Helpful for troubleshooting.

## Slide 25: Wireless Settings
Configure wireless settings; most hosts connect wirelessly.
May be part of setup wizard; can use management software directly.
Adjust settings as appropriate:
  Frequency band (2.4 GHz or 5 GHz)
  SSID (name for WAN)
  Security and encryption
  Password (pre-shared key)
  802.11 mode
  Channel/channel width

## Slide 26: DHCP and IP Address Configuration
May need to adjust DHCP server settings
Enabled by default
If you disable, IP addresses must be assigned manually
Easy for attacker to determine scope

## Slide 27: WPS
Simplifies secure access point setup.
AP and all adapters must be WPS-capable.
Pushbutton on device typically causes device and AP to associate automatically over WPA2.
Generates random SSID and passphrase.

## Slide 28: Access Point Placement
Correct antenna and access point placement helps ensure robust network.
AP placement may be constrained by provider’s cabling location.
Can use extenders.
Site survey can help identify dead zones.

## Slide 29: Channel Selection
In US, 2.4 GHz band subdivided into 11 channels at 5 MHz intervals.
Best to allow 25 MHz spacing for channels in active use.
No more than 3 nearby APs can have non-overlapping channels.
Newer APs detect least-congested channel at boot; may need to adjust.
Use spectrum analyzer to find least busy channels.

## Slide 30: Radio Power Levels
Can turn down AP power to prevent war driving.
Need to ensure enough coverage for legitimate users.
May expose to “evil twin” attack if a rogue AP is detected first.
Increasing power may also cause signal bouncing.
Client must match AP.
Best to allow autonegotiation.

## Slide 31: Wi-Fi Security Protocols (Slide 1 of 2)
Wi-Fi requires careful security configuration
Media “unguided;” RF scanner can intercept signals
Encryption is crucial
Cipher scrambles message; key decodes message
Keep key secure

## Slide 32: Wi-Fi Security Protocols (Slide 2 of 2)
Security Protocol | Description
WEP | Legacy encryption system based on RC4 cipher 64-bit or 128-bit key Flaw in key production method; easy for attacker to generate key Deprecated and should not be used
WPA WPA2 | Based on RC4 Adds TKIP to fix security problem WPA2 developed to meet 802.11i security standards Use WPA2 whenever possible If not supported by devices, use WPA

## Slide 33: Wi-Fi Authentication
Authentication Mode | Description
Personal | Based on pre-shared key generated from passphrase. Cannot completely secure distribution of key; on home network may not be secure passphrase; all users share key (no accounting); hard to change key. Simple setup. Only choice for WEP; can use with WPA/WPA2 on SOHO networks or workgroups.
Enterprise | Enterprise mode authentication in WPA/WPA2. Authentication passed to RADIUS server. Suitable for server-/domain-based networks.

## Slide 34: Common SOHO Security Issues
Security Issue | Description
SSID | Simple name to identify the WAN Change default SSID Do not use personal information Disable SSID broadcast Enable encryption
Physical Security | Restrict physical access to enterprise routers and switches Attacker with physical access could reset to defaults, gain access
Updating Firmware | Keep Internet appliance firmware and driver up to date Make sure power stays on during update process
Static IP Addresses | Static IP assignments will not deter a determined attack Router/modem must have static IP to function as DHCP server/default gateway

## Slide 35: Latency and Jitter
Quality of Service (QoS): Using a network protocol to prioritize types of traffic
Modern networks provide two-way communications (VoIP, video conferencing, gaming).
Standard protocols sensitive to data loss, not delivery delay (latency/jitter).
Real-time data applications sensitive to latency and jitter, not packet loss.
  Latency: the time for a signal to reach recipient
  Jitter: variation in delay (congestion, configuration problems).
QoS:
  Hard to guarantee on Internet.
  Can be deployed on enterprise networks.
  On SOHO network, may be able to configure on router/modem.

## Slide 36
Discussing SOHO Network Installation and Configuration

## Slide 37
Installing and Configuring SOHO Networks

## Slide 38: Firewalls (Slide 1 of 2)
Many types and implementations
Primary distinction:
  Network firewall:
    Inline on the network
    Inspects all traffic
  Host firewall:
    Installed on host
    Inspects traffic to that host

## Slide 39: Firewalls (Slide 2 of 2)
Firewall Type | Description
Packet Filtering | Earliest type; all firewalls capable of this function Inspects IP packet headers, accepts or drops based on rules Filtering rules based on: IP filtering Protocol ID/type Port filtering/security Configure ACL
Host Firewall | Software on individual host; may be in addition to network firewall Can do packet filtering Can also grant/deny access based on software programs, services/processes, and users Two firewalls increase security; more complex to configure and troubleshoot

## Slide 40: Firewall Settings (Slide 1 of 2)
Firewall Setting | Description
Disabling Ports | Only enable required services; can remove service at the host. May want service available locally but not on Internet. Configure firewall ACL to block the port, or block by default rule.
MAC Filtering | Firewalls, switches, and APs can whitelist/blacklist MAC addresses. Can be time-consuming, but good security option for SOHO networks.
Content Filtering / Parental Controls | Blocks websites and services based on keywords, ratings, or classification. Can restrict times. ISP-enforced filters cannot distinguish account types. Filters can also be enforced by OS.
Whitelists / Blacklists | Blacklists document URLs known to harbor specific undesired content. Whitelists document sites that will be accessible even if filter is applied.

## Slide 41: Firewall Settings (Slide 2 of 2)

## Slide 42: NAT
All routers/modems use NAT/NAPT
Router has single public address; clients use local private addresses
Router translates between Internet and host
Usually auto-configured
Some protocols may need ALG to open ports dynamically

## Slide 43: Port Forwarding and Port Triggering
Internet hosts only see router’s public address.
Configure port forwarding/DNAT if running an Internet-facing service on your internal network.
Router transmits Internet requests to a given port to a designated internal host.
Port triggering is for applications using multiple ports.

## Slide 44: DMZ
If internal server is exposed to Internet, consider local network security; compromised server can expose LAN to attacks.
Enterprise networks use DMZ; hosts in DMZ are not trusted by local network.
Traffic from Internet cannot access local network through DMZ.
SOHO vendors’ “DMZ” = LAN computer that receives all Internet communications not forwarded to other hosts.

## Slide 45: Universal Plug-and-Play
Users may be tempted to turn off firewall if configuration is complex. Services requiring complex configuration can use UPnP to instruct firewall with correct configuration.
Does have security vulnerabilities:
  Use only if required.
  Don’t let UPnP accept Internet requests.
  Keep firmware, security advisories up to date.

## Slide 46: Windows Firewall (Slide 1 of 2)
Each version has become more advanced
Configure in Control Panel

## Slide 47: Windows Firewall (Slide 2 of 2)
Can configure exceptions
Use Windows Defender Security Center on Windows 10

## Slide 48: Windows Firewall with Advanced Security (Slide 1 of 2)
Add-in to basic firewall
Can configure outbound filtering, IPSec, monitoring
Configure in Group Policy on domain, in management console in workgroup

## Slide 49: Windows Firewall with Advanced Security (Slide 2 of 2)
Configure inbound and outbound rules as appropriate
Rules can use various triggers

## Slide 50: Location Awareness (Slide 1 of 2)
Firewall settings can be applied depending on connected network.
Displays dialog when new network is detected.

## Slide 51: Location Awareness (Slide 2 of 2)
Set location (Home, Work, Public, Domain).
Use Network and Sharing Center to change location.
In Windows 8/Windows 10, networks are either public or private.
Change using Settings app.

## Slide 52: Browser Configuration (Slide 1 of 7)
Browser is very important software, for browsing and as app interface.
Internet Explorer has been dominant, but other browsers have similar configurations.
General settings include home pages, browsing history, etc.
Clear browsing history on public computer.

## Slide 53: Browser Configuration (Slide 2 of 7)
Configure connections:
  Dial-up
  Router

## Slide 54: Browser Configuration (Slide 3 of 7)
Configure proxy:
  User machines send requests to proxy server, which sends to Internet.
  May also perform caching for improved performance.
Use LAN Settings to configure proxy address.

## Slide 55: Browser Configuration (Slide 4 of 7)
Security settings protect system from malicious content on web pages.
In Windows, configure by security zone.

## Slide 56: Browser Configuration (Slide 5 of 7)
Privacy settings control use of cookies
  Text files containing session data
Configure pop-up blocker

## Slide 57: Browser Configuration (Slide 6 of 7)
Check or set default browser
Manage add-ons

## Slide 58: Browser Configuration (Slide 7 of 7)
Various advanced settings and options
Resetting the browser

## Slide 59
Discussing SOHO Network Security

## Slide 60: Windows Remote Access Tools
Tool | Description
Remote Desktop | Allows user to connect to desktop remotely Desktop machine = terminal server; connecting machine = Windows terminal Good for home workers Can also be used for troubleshooting TCP port 3389
Remote Assistance | Allows user to request help from technician Helper can join user session, take control of desktop Port assigned dynamically from ephemeral range; intended for local support, not to pass through firewalls

## Slide 61: Remote Settings Configuration
Remote Assistance allowed by default; Remote Desktop is not
Configure in System Properties/Remote Settings
Choose RDP client options, including NLA
RDP authentication/session data always encrypted
Define which users can connect remotely (local or domain accounts)

## Slide 62: Remote Credential Guard
Remote Desktop credentials are vulnerable on machine compromised by malware.
RDPRA Mode and Remote Credential Guard mitigate this risk.

## Slide 63: The Remote Assistance Process
Remote Assistance request placed with Remote Assistance tool (file, email, or Easy Connect).
Helper opens invitation file and waits for user to accept offer.
Remote Desktop window and chat tool open.
Remote Assistance session encrypted, same as RDP.

## Slide 64: Remote Desktop
Open via the Communications menu in Accessories or by typing mstsc at a command prompt.
Enter the server's computer name or IP address to connect.
You will need to define logon credentials.
Use the format ComputerOrDomainName\UserName
No one else can use the target system while in remote mode.

## Slide 65: Remote Access Technologies
Remote Desktop and Remote Assistance are Microsoft technologies.
Can connect from Linux, macOS, iOS, or Android to Windows RDP server using mstsc client.
Use other protocols and software for incoming connections to non-Windows devices.

## Slide 66: Telnet (Slide 1 of 2)
Command-line terminal emulation protocol and program
Host runs Telnet Daemon on TCP port 23
Client uses Telnet program
Once connected, can use same commands as local user
Common commands: open HostPort; ?; status; close; quit
Troubleshooting for SMTP or HTTP
Remote router or switch configuration

## Slide 67: Telnet (Slide 2 of 2)

## Slide 68: SSH (Slide 1 of 2)
Replaces unsecure administration and file copy programs (Telnet, FTP)
Uses TCP port 22
Encrypts each session
Many commercial products
SSH servers identified by public/private key pairs
SSH clients can keep mappings or use commercial SSH key management products

## Slide 69: SSH (Slide 2 of 2)
Server’s host key used to set up secure channel for SSH client authentication
Various authentication methods possible; can be enabled/disabled as needed:
  Username/password
  Kerberos
  Host-based
  Public key

## Slide 70: Screen Sharing and VNC
In MacOS, use Screen Sharing for remote desktop
  Based on VNC
  Can use any VNC client
  Encrypted
VNC itself is freeware
  Similar to RDP
  TCP port 5900
  Freeware versions have no connection security
  Commercial products include encryption solutions

## Slide 71: File Share
Network file sharing can be complex (file sharing protocol; permissions; user accounts)
Vendors offer simple file sharing options:
  AirDrop (Apple iOS/macOS)
  NearShare (Microsoft)
  Third-party and open-source alternatives
Products include security, but always potential for misuse
Only accept requests from known contacts
Security vulnerabilities may allow unsolicited transfers

## Slide 72
Discussing Remote Access Configuration

## Slide 73: Common Wired Network Connectivity Issues (Slide 1 of 2)
Rule out hardware-layer connectivity (cable connection)
Troubleshoot wired connectivity:
  Test with ping
  Verify patch cord between host/panel and panel/switch
  Connect a different host
  Verify network adapter link properties
  Connect to a different port
  Check the switch (if multiple users)
  Use cable testing tools

## Slide 74: Common Wired Network Connectivity Issues (Slide 2 of 2)
Troubleshoot slow transfer speeds:
  Check network adapter driver configuration
  Check setting for switch port
  Check for:
    Switch or router congestion or network-wide problem
    Adapter driver issues
    Malware
    Interference on network cabling

## Slide 75: Common Wireless Network Connectivity Issues (Slide 1 of 2)
Consider problems with physical media, configuration:
  RF signal weakens with distance
  Check security and authentication configuration
Configuration issues:
  If in range, check SSID mismatch or SSID broadcast
  Standards mismatch
  Dual-band support
Low RF/RSSI
Signal issues:
  Channel interference
  Signal blocking

## Slide 76: Common Wireless Network Connectivity Issues (Slide 2 of 2)
Use Wi-Fi analyzer such as inSSIDer to perform site survey
Site survey can:
  Identify sources of interference problems
  Measure signal strength
  Identify congested channels

## Slide 77: IP Configuration Issues (Slide 1 of 2)
If host IP configuration is incorrect it will not be able to communicate
View adapter status in Windows
Use ipconfig at command line
Typical switches:
  /all
  /release
  /renew
  /displaydns
  /flushdns

## Slide 78: IP Configuration Issues (Slide 2 of 2)
Use ipconfig to test adapter configuration:
  Static or DHCP? If DHCP, correct parameters?
If configuration is correct, check for:
  Communication with DHCP server
  Configuration with DHCP server
  Multiple conflicting DHCP servers
On Linux, use ifconfig; some different functionality

## Slide 79: IP Connectivity Issues (Slide 1 of 3)
If link and IP are correct, problem may be in network topology.
Test connections by trying to use resources (but doesn’t eliminate application fault).
Use other connectivity tests:
  Ping
  DNS testing
  IP conflict

## Slide 80: IP Connectivity Issues (Slide 2 of 3)
Use ping to test communications.
Ping loopback, workstation, default gateway, remote host.
If successful, reply with time in milliseconds.
If unsuccessful:
  Destination unreachable
  No reply (request timed out)

## Slide 81: IP Connectivity Issues (Slide 3 of 3)
Test DNS:
  Ping DNS names.
  Try reverse lookup.
Troubleshoot IP conflicts:
  Possible configuration error due to static assignment.
  Windows disables IP.
  Identify affected machines and resolve duplicate.

## Slide 82: Routing Issues
Use tracert to investigate routing problems
Command will time out if host not located
Will list:
  Router hops
  Ingress interface
  Response time
  Asterisk if no response

## Slide 83: Unavailable Resources (Slide 1 of 5)
If not with cabling, switches/routers, or IP, problem is at higher layer
Failures possible in:
  Security
  Name resolution
  Application/OS
If Internet access or local resources are unavailable, establish scope by trying a different client:
  If works, problem with 1st client
  If fails, problem is with server, device, or infrastructure

## Slide 84: Unavailable Resources (Slide 2 of 5)
Troubleshooting Internet availability:
  If “No Internet access” message, no working Internet connection
  Check local PC settings
  Check ISP’s service status page/helpline
  Restart modem/router
  Suspect security issue (mis-configured proxy, firewall blocking host)

## Slide 85: Unavailable Resources (Slide 3 of 5)
Performing a reset:
  Restart server as stock response to persistent problems
  Restart application
  Run Windows network troubleshooter
  Reset the network stack
    Windows 10: Network & Internet > Status
    Windows 7/8: Network Adapter troubleshooter or command-line tools
  Remove network adapters and reboot; update all network settings

## Slide 86: Unavailable Resources (Slide 4 of 5)
Use netstat to investigate open ports and connections
Use –a, -b, -n switches
Linux has slightly different utility

## Slide 87: Unavailable Resources (Slide 5 of 5)
Use nslookup to investigate name resolution problems
nslookup -Option Host Server
Query a different name server and compare your results

## Slide 88
Discussing Network Connection Troubleshooting

## Slide 89: Internet of Things
Global network of devices equipped with sensors, software, network connectivity.
Devices can communicate and pass data M2M.
“Things” identified with unique numbers/codes.

## Slide 90: IoT Wireless Networking Technologies
Technology | Description
Bluetooth Bluetooth Low Energy | Radio communication speeds up to 3 Mbps; v3 or v4 up to 24 Mbps Maximum range of 10 m/30 ft (signal strength weak at max. distance) Used in many portable/wearable devices Pairing procedure BLE version for low-powered devices that transmit infrequently
Z-Wave | Wireless protocol for home automation Mesh topology over low-energy radio waves Can configure repeaters up to four “hops” High 800-low 900 MHz range; runs for years on battery power
ZigBee | Similar to/competitive with Z-Wave 2.4 GHz band Up to 65,000 devices in single network (232 for Z-Wave); no hop limit
RFID and NFC | Tagging and tracking devices with radio-frequency tags NFC: peer-to-peer version of RFID

## Slide 91: IoT Device Configuration
IoT functionality in home automation/smart home devices
To interoperate, devices must all share protocol (i.e., Z-Wave or Zigbee) and be compatible with same virtual assistant/hub
Endpoint devices (thermostats, light switches, etc.)
Smartphone control (using Wi-Fi, Bluetooth, NFC)
Smart hub control (Z-Wave, Zigbee, Wi-Fi, Bluetooth, NFC)
  Dedicated hub from vendor
  Generic smart speaker/digital assistant

## Slide 92: Digital Assistants
Voice interface responding to natural language
Smartphones, computers, smart-speaker hubs
Back-end server processing; raises privacy/security concerns
  Google Assistant
  Amazon Alexa
  Apple Siri
  Microsoft Cortana
Device may require “training” to recognize and respond to user’s voice

## Slide 93
Discussing IoT Devices

## Slide 94
Configuring IoT Devices

## Slide 95
What experiences do you have in working with the networking technologies discussed in this lesson?
Do you have any experience working with SOHO networks? What do you expect to support in future job functions?