## Slide 1: Supporting and Troubleshooting Laptops

## Slide 2: Supporting and Troubleshooting Laptops
Use Laptop Features
Install and Configure Laptop Hardware
Troubleshoot Common Laptop Issues

## Slide 3: Laptops
Laptop: A powerful portable computer offering similar functionality to a desktop computer.
Contains special hardware:
  Designed for portability.
  Runs on AC or battery.
Uses same OSs as desktop PCs.
Models:
  Entry level/Budget.
  Ultraportable.
  Desktop replacement.
  Media center.
  Gaming unit.

## Slide 4: Touchpads
Touchpad: Input device used on most laptops to replace the mouse, controlled by moving fingers over the pad surface.
Alternative to using a mouse.
Support for multi-touch and gestures.
Configured via the Mouse applet in Windows.

## Slide 5: Keyboards (Slide 1 of 2)
Function keys:
  Display.
  Screen orientation.
  Wireless/Bluetooth/Cellular/GPS.
  Volume.
  Screen brightness.
  Keyboard backlight.
  Touchpad.
  Media options.
Numeric keypad or key combinations.

## Slide 6: Keyboards (Slide 1 of 2)
Configured via the Keyboard applet in Windows.

## Slide 7: Displays and Touchscreens (Slide 1 of 2)
Touchscreen: A display screen combined with a digitizer that is responsive to touch input.
Finger touch or stylus.
Antenna for Wi-Fi adapter incorporated.
Rotating or removable screens/keyboards.
  Based on tablet form factors.
Configurable via Tablet PC Settings and Pen and Touch applets in Windows.
  Calibration utility.
  Gesture settings.

## Slide 8: Displays and Touchscreens (Slide 2 of 2)

## Slide 9: Expansion Options
Wired ports on left, right, and rear:
  At least one video port.
  Several USB Type A ports.
  At least one USB Type C/Thunderbolt port.
  Microphone and speaker jacks.
  Network (RJ-45) port.
  Possibly memory card reader.
USB adapters:
  USB to RJ-45.
  USB to Wi-Fi/Bluetooth.
  USB optical drive.

## Slide 10: Port Replicators
Port replicator: A simple device to extend the range of ports available for a laptop computer when it is used on a desk.
Connects keyboards, monitors, mice, and network cabling to a laptop.
Generally does not add new functionality.

## Slide 11: Docking Stations
Docking station: A sophisticated type of port replicator designed to provide additional ports and functionality to a portable computer when used at a desk.
Can provide additional functionality.
Media bay can support expansion cards or drives.

## Slide 12: Physical Locks
Help prevent theft.
Key-based or combination locks.
Kensington locks and connection points.

## Slide 13
Discussing Laptop Features

## Slide 14: Laptop Disassembly Processes
Hand tools and parts:
  Smaller screws than desktops—use jeweler's tools
  Document screw locations, ribbon cables, other connectors
  Organize removed parts
Form factors and plastics/frames
  Most use proprietary components
  Chassis incorporates:
    Motherboard
    Power supply
    Display screen
    Keypad
    Touchpad
  Review manufacturer’s service documentation before starting upgrades or repairs

## Slide 15: Laptop FRUs
Fewer FRUs than desktop PCs.
FRUs accessible from behind a screw plate on the bottom of the unit.
  HDD
  Optical drive
  RAM
  Wi-Fi and other adapters

## Slide 16: Mass Storage for Laptops
Same types as for PCs:
  HDD, SSD, and hybrid solutions.
  Normally one internal storage device.
Smaller form factors:
  2.5 and 1.8 inches.
  Slower than PC counterparts.
Data and power connectors:
  SATA for most magnetic and hybrid drives.
  Micro SATA for some 1.8” drive bays.
  SATA, mSATA, or M.2 for SSDs.
Laptop HDD

## Slide 17: Laptop RAM
SODIMM: Memory that is half the size of DIMMs, are available in 32- or 64-bit data paths, and are commonly found in laptops and iMac systems.
Packaging for different DDR types:
  DDR and DDR2: 200 pins
  DDR3: 204 pins
  DDR4: 260 pins
Angled slots allow for easy removal and installation.
Disassembly might be required to reach all installed RAM.

## Slide 18: Adapter Cards for Laptops
Uses:
  Modems
  Wireless networking
  SSD storage
Adapter formats:
  Mini-PCI
  mSATA
  M.2
For wireless adapter upgrades:
  Reconnect antenna wires or install new antenna kit.
  If cellular functionality, a SIM is required.

## Slide 19: Optical Drives for Laptops
Slimline models used.
Normally accessible through the bottom panel.
SATA data and power connectors.
For replacements, use same OEM part or same caddy design.

## Slide 20: Laptop CPU and Motherboard Upgrades
CPU is upgradeable if the new device is supported by the motherboard.
CPU is covered by a heatpipe.
  Long, flat metal strip.
Sometimes it’s more economical to replace the system board.
  Detach the stand-offs.
  Probably also need to update chipset driver or notebook system software.
  Allow Windows to discover the new device using Plug-and-Play.

## Slide 21: Laptop Video Card Upgrades
Often an integrated graphics adapter.
  Advantageous in terms of battery life and cooling.
Typically has limited video memory or shares system memory.
Not usually upgradeable, but may be replaceable.
  High-end video cards require specific power and cooling.
  Modular approach not possible due to limited space.

## Slide 22: Laptop Component Replacement
Find a source for “like-for-like” replacements
  Ensures proper fit and function

## Slide 23: Laptop Display and Digitizer Replacement
Built-in display will be:
  LCD (TFT) with fluorescent backlight
  LCD with LED backlight
  OLED

## Slide 24: Laptop Speaker Replacement
Replacing speakers requires disassembly down to the system board.
Model compatibility.
Connect the audio cables.

## Slide 25: Laptop Input Device Replacement
Keyboards
Touchpads
Webcams
Microphones
Smart card readers

## Slide 26: Laptop Power Supplies
Building power:
  Need AC to DC converter.
  Auto switching or manual.
  DC jacks prone to failure.
Battery operation:
  Li-ion battery packs.
  6, 9, and 12 cell versions.
  Normally accessed through bottom of the unit.
  Charging options.
  Tips for maximizing battery life.

## Slide 27
Discussing Laptop Hardware Installation and Configuration

## Slide 28
Installing and Configuring Laptop Hardware

## Slide 29: Common Laptop Issues
Display issues:
  Built-in displays
  Touchscreens
  External displays
Power and cooling issues
Input and output device issues
GPS and location services issues
OS and app issues:
  Performance
  Unresponsive apps

## Slide 30: Display Issues
Problems with built-in displays:
  Is it really the built-in display?
  Backlights and inverters prone to failure
Problems with touchscreen displays:
  Not responsive
  Does not act as expected
Problems with external displays:
  No image
  Wrong image
  Image is too large or too small

## Slide 31: Guidelines for Troubleshooting Display Issues (Slide 1 of 2)
Built-in displays:
  Where does the problem really lie?
  Check for physical damage.
  Check the resolution.
  Check the driver.
Touchscreen displays:
  Is it clean?
  Check for physical damage.
  Try using it in another location.
  If recently serviced, are wires reconnected?
  Check software configuration.

## Slide 32: Guidelines for Troubleshooting Display Issues (Slide 2 of 2)
External displays.
  Check the keyboard toggle switch.
  Check power and input mode.
  Check the resolution.
  Look for updated drivers.
  Swap out displays and cables.

## Slide 33: Power and Cooling Issues
Battery issues.
  Verify proper insertion and clean contacts.
Short battery life.
  Windows 10 Settings app for battery use by apps.
Swollen batteries.
AC power issues.
Overheating.
  Dust and heat.
  Lack of ventilation.

## Slide 34: Guidelines for Troubleshooting Power and Cooling Issues (Slide 1 of 2)
Battery issues:
  Follow manufacturer guidelines on charging.
  Use approved chargers.
  Avoid fire, water, drops, or other impacts.
  Use recommended battery.
  Use power management features.
AC power issues:
  Check and verify operational needs.
  Test the outlet with known good devices.
  Look for the LED on the AC adapter.
  Check the plug’s fuse.

## Slide 35: Guidelines for Troubleshooting Common Laptop Issues (Slide 2 of 2)
AC power issues (continued):
  Check the DC socket on the laptop.
  Verify the adapter supplies adequate power.
  Disconnect peripherals one at a time to see if power problems remain.
Cooling issues.
  Keep the air ducts clean.
  Use compressed air to blow dust out.
  Use computer vacuum to remove dust.

## Slide 36: Input and Output Device Issues
Input devices.
  Stuck keys.
  Improper or unintentional use of Fn keys.
  NumLock use.
  Oversensitive touchpad.
Sound and speaker issues.
  No sound.
  Sound is distorted.

## Slide 37: Guidelines for Troubleshooting Input and Output Device Issues
Clean the keyboard with compressed air.
If serviced recently, verify all cables were reconnected.
Check Fn key status.
Check NumLock key status.
Check drivers.
Check volume control, playback device configuration, sound card, and internal wiring.

## Slide 38: Communication and Connectivity Issues
Connectivity:
  Physical issues and software configuration problems.
  Wireless devices need power.
  Issues can arise after laptop wakes from Sleep or Hibernation mode.
  Possible electromagnetic interference.
GPS and Location Services:
  No functionality.
  Limited functionality.
  Signal strength decreases when indoors.

## Slide 39: Guidelines for Troubleshooting Communication and Connectivity Issues
Check adapters, Fn keys, and antenna connections.
Check batteries on wireless mice and other devices.
Check for driver updates to address sleep mode issues.
For intermittent connectivity, move the devices around or use an antenna.
For GPS issues, verify it’s enabled and not in airplane mode.
  Also be sure individual apps have been granted permission to use location services.

## Slide 40: OS and App Issues
Slow performance
Unresponsive devices and apps
Email issues

## Slide 41: Guidelines for Troubleshooting OS and App Issues
For slow performance, check apps that require lots of memory.
For unresponsive apps, perform a reset.
For email issues, check the support documentation for the email client/ encryption program to get certificate information.

## Slide 42
Troubleshooting Common Laptop Issues

## Slide 43
In your professional experience, have you supported laptop computers? If not, what kind of experience do you have with using them?
Of the common laptop issues discussed in this lesson, which do you expect to encounter most often? Briefly explain your response.