## Slide 1: Supporting and Troubleshooting Mobile Devices

## Slide 2: Supporting and Troubleshooting Mobile Devices
Mobile Device Types
Connect and Configure Mobile Device Accessories
Configure Mobile Device Network Connectivity
Support Mobile Apps

## Slide 3: Mobile Devices
Smartphones and tablets used in the workplace need support, too.
Mobile OSs (iOS, Android, or Windows Mobile).
Store-based software ecosystems.

## Slide 4: Smartphones
One-handed operation
Touchscreen displays
Screen sizes range from 4.5” to 5.7”
Multicore CPUs
2 to 6 GB system memory
16 GB+ flash memory storage
Features:
  Digital cameras
  Input sensors
  Networking via Wi-Fi or cellular data

## Slide 5: Tablets
Usually 7” or 10” screen
Might be able to connect to a removable physical keyboard
Some laptops can also function as a tablet by flipping the screen
Usually connect to a Wi-Fi network; some have cellular option
Phablets—cross between a phone and a tablet with 5.5” to 7” screen

## Slide 6: Mobile Devices vs. Laptops
Factor | Description
Processors | Mobile devices: CPUs and chipsets are based on ARM microarchitecture. Dual- and quad-core CPUs are common, with some 64-bit CPUs available. Provide more power and thermal efficiency. PCs and laptops: CPUs and chipsets are based on CISC and RISC microarchitecture. Dual- and quad-core CPUs are widespread, with many 64-bit CPUs available.
System memory | Tablet RAM is a low power DDR SDRAM variant. Works similarly to PC/laptop RAM.
Storage | SSDs used in mobile devices instead of HDDs.
Component replacements and upgrades | More FRUs for PCs and laptops. Tablet components are soldered and glued, making it necessary to replace the entire device.
OSs | More OS options for PCs and laptops. Mobile devices limited to the mobile OS they were designed to run.

## Slide 7: Mobile Display/Touch Interface
Touchscreen: A display screen combined with a digitizer that is responsive to touch input.
Capacitive touchscreens support multitouch (sweep, pinch, etc.).
Haptic feedback provides a more realistic feel to the user.
Protected by scratch- and shock-resistant tempered glass.
Screen orientation is changeable.

## Slide 8: Mobile Device Form Factors
Fewer field serviceable parts than PCs and laptops.
Return to manufacturer for replacing screens, storage devices, and possibly batteries.
Some batteries can be replaced by the user.
Some devices will have a SIM card port.

## Slide 9: E-Readers
e-reader: A tablet-sized device designed for reading, rather than for general-purpose computing.
E-ink technology creates EPD.
Low-power, high-contrast display.
Backlights often not needed, saving power.
USB chargers.
Wi-Fi connectivity for downloading e-books.

## Slide 10: Wearable Technology
Smart watches
Fitness monitors
VR/AR headsets and smart glasses

## Slide 11: GPS Navigation Devices
Global Positioning System (GPS): Means of determining a receiver's position on the Earth based on information received from GPS satellites. The receiver must have line-of-sight to the GPS satellites.
Built into smartphones and other devices.
Dedicated units for vehicles, cyclists, or walkers.
Geolocation system, map, and local traffic information.
Route planning and directions.
Some provide live traffic information.
Touch and voice controls available.

## Slide 12
Discussing Mobile Device Types

## Slide 13: Wired Connections for Accessories
Apple devices:
  Apple Dock for older devices.
  Apple Lightning connector.
Android devices:
  Micro-B USB connectors for most devices.
  Mini-B for older devices.
  USB-C on newer devices.

## Slide 14: Wireless Connections for Accessories (slide 1 of 2)
Bluetooth
NFC
IR

## Slide 15: Wireless Connections for Accessories (slide 2 of 2)
Tethering
Mobile hotspots

## Slide 16: Common Mobile Device Accessories
External keyboard
Headset
Speaker dock
Micro-SD slot
Docking stations
Protective covers and waterproofing
Credit card readers
Mobile power

## Slide 17
Discussing Mobile Device Accessory Connection and Configuration

## Slide 18: Cellular Data Networks (Slide 1 of 4)
Cellular data: Connecting to the Internet via the device's cell phone radio and the handset's cellar network provider.

## Slide 19: Cellular Data Networks (Slide 2 of 4)
Mobile hotspots and tethering
Cellular radios:
  Base station effective range up to 5 miles
  Transmitter connects phone to mobile and landline phone networks
  Works in the 850 and 1900 MHz frequency bands in Americas
  Works in the 900 and 1800 MHz frequency bands in the rest of the world
  GSM deployed worldwide
  CDMA used in the Americas

## Slide 20: Cellular Data Networks (Slide 3 of 4)
GSM networks and SIM cards:
  GSM works with SIM cards
  Handsets are identified by IMEI number
  Users are identified by IMSI number
SIM card number format:
  3-digit mobile country code
  2-digit mobile network code
  Up to 10-digit mobile station identification number

## Slide 21: Cellular Data Networks (Slide 4 of 4)
CDMA networks:
  Locks handset to original provider
  Does not require use of a SIM card
  Handsets are identified by MEID number
  Uses PRI and PRL databases for information needed to connect cellular radio to the network
  If the handset contains a SIM card, it is to connect to 4G networks, which are GSM-based networks

## Slide 22: Baseband Updates and Radio Firmware
Baseband update: Modification of the firmware of a cellular modem.
Radio firmware: An operating system that is separate from the end-user operating system in a mobile device.
Realtime Operating System (RTOS): An OS that is optimized for use in embedded or real-time apps.
Baseband updates modify the radio firmware.
  Firmware OS is separate from the user OS.
  Controls low-level timing-dependent functions (USB, network, and GPS).
  Runs all available radio functions (cellular, Wi-Fi, and Bluetooth).
Updates usually pushed by device vendor as part of an OS upgrade.

## Slide 23: Wi-Fi Networks and Hotspots (slide 1 of 2)
Hotspot: A mobile device setting or access point that enables using the cellular data plan of the mobile device to connect a PC or laptop to the Internet.
All smartphones and tablets support Wi-Fi communication.
  In iOS, select Settings→Wi-Fi to connect.
  In Android, use the notification shade or open the Settings→Wi-Fi menu.
Hotspot implementations:
  Public access point (free or paid).
  Smartphone or tablet.
  Wireless router designed for personal hotspots.

## Slide 24: Wi-Fi Networks and Hotspots (slide 2 of 2)

## Slide 25: Mobile VPN Configuration
Virtual Private Network (VPN): A secure tunnel created between two endpoints connected via an unsecure network (typically the Internet).
Mobile VPN: A VPN that can maintain the VPN link across multiple carrier networks, where the IP address assigned to the mobile device may change often.
Tunnel contents often encrypted to secure communications.
Mobile VPN assigns virtual IP address for connecting to VPN server.
Links maintained even in sleep mode.
Available as third-party apps for Android and iOS.

## Slide 26: Bluetooth (slide 1 of 3)
Bluetooth: Short-range radio-based technology, working at up to 10 m (30 feet) at up to 1 Mbps, used to connect peripherals for communication between two devices.
Latest versions support 24 Mbps data rate.
Used for PANs (Personal Area Networks).
  Share data with a PC.
  Connect to a printer, wireless headset, or other peripheral.
Pairing connects the devices.
  In iOS, select Settings→General→Bluetooth.
  In Android, access through the notification shade.
  In Windows, access through Control Panel, Windows Settings, or the Bluetooth icon in the notification area.

## Slide 27: Bluetooth (slide 2 of 3)

## Slide 28: Bluetooth (slide 3 of 3)

## Slide 29: Airplane Mode (slide 1 of 2)
Control Center: An iOS feature that is accessed by swiping up from the bottom of the display to access iOS feature settings.
Notification shade: An Android feature that is accessed by swiping down from the top of the display to access Android OS feature settings.
Airplane mode: A toggle found on mobile devices enabling the user to disable and enable wireless functionality quickly.

## Slide 30: Airplane Mode (slide 2 of 2)
Disables all wireless features.
  Cellular data
  Wi-Fi
  GPS
  Bluetooth
  NFC

## Slide 31: Email Configuration Options (Slide 1 of 4)
Commercial Provider Email Configuration

## Slide 32: Email Configuration Options (Slide 2 of 4)
Corporate and ISP Email Configuration:
  Autodiscover with Exchange and Exchange ActiveSync.
  For ISPs and corporate mail gateways that don’t support Autodiscover, manually enter the mail server address information:
    Incoming mail server type (IMAP or POP3)
    Outgoing mail server type (SMTP)
    SSL setting (enable or disable)
    Ports

## Slide 33: Email Configuration Options (Slide 3 of 4)

## Slide 34: Email Configuration Options (Slide 4 of 4)
S/MIME:
  Using secure ports does not provide end-to-end encryption for messages.
  Encryption with digital certificates and digital signatures does.
  PGP and S/MIME use digital certificates and public/private key pairs.
    When you sign a message, your private key validates who you are and the public key related to that private key goes to the recipients. The public key allows the recipient to verify who you are.
    When you want to receive secure messages, the sender uses your public key to encrypt the message. Once encrypted, only your private key can decrypt it (your public key cannot be used to reverse the encryption).
  Digital and root certificates are often added to the device by using MDM software.

## Slide 35
Discussing Mobile Device Network Connectivity Configuration

## Slide 36
Configuring Bluetooth

## Slide 37: Mobile Account Setup
User accounts:
  Normally 1 per device, created at initial use.
  For iOS: Apple ID.
  For Android: Google account, Samsung account, or similar.
  Unique ID and credentials required.
  Provides access to app store, email, cloud storage.
Sub-accounts for additional services and apps:
  Corporate email or messaging.
  Facebook.
  LinkedIn.

## Slide 38: Mobile Applications and App Stores (slide 1 of 2)
App: Installable programs the extend the functionality of a mobile device.
iOS apps:
  Get from App Store.
  Free or paid.
  Walled garden model—all apps reviewed and approved by Apple.

## Slide 39: Mobile Applications and App Stores (slide 2 of 2)
Android apps:
  Get from Google Play Store or third-party sites.
  Free or paid.
  More open model for app acquisition: store model, or APKs.

## Slide 40: Types of Data to Synchronize
Mobile device synchronization: The act of copying data back and forth between devices to keep the information up-to-date on all of the devices.
Contacts
Calendar
Email
Pictures, music, and video
Documents
E-books
Location data
Social media data
Apps
Bookmarks
Passwords

## Slide 41: Synchronization Methods (Slide 1 of 3)
iOS syncs to desktop via iTunes
iOS syncs to cloud via iCloud

## Slide 42: Synchronization Methods (Slide 2 of 3)
Android uses the gmail account to sync with cloud storage and Google Play Store.
You can connect to a PC via USB to transfer data directly.

## Slide 43: Synchronization Methods (Slide 3 of 3)
Microsoft synchronization products
  OneDrive
  Outlook.com
  Office 365
Third-party synchronization products
  Vendor-based cloud services
  Dropbox
Sync to automobiles.
  Newer vehicles use head unit to manage entertainment and navigation.
  Smartphone can be attached to head unit.
  Apple CarPlay
  Android Auto

## Slide 44: Mutual Authentication for Multiple Service
Single Sign On: (SSO) One service accepts the credentials from another service. Also known as federated identity management.
Sign in once to authenticate to many services
Enterprise networks:
  Email
  Database
  Document management system
Mobile device apps use device sign-in credentials:
  iPhone with an Apple ID
  Vendor cloud services

## Slide 45
Discussing Mobile App Support

## Slide 46
In your professional experience, have you supported mobile devices? If not, what kind of experience do you have with them?
What type of technical support do you think will be expected of an A+ technician as mobile devices become even more prominent within the workplace?