## Slide 1: CompTIA IT Fundamentals+ (Exam FC0‑U61)
Module 3 / Unit 1 / System Components

## Slide 2
Explain the way in which system components determine performance and how to specify an appropriate computer system
Describe the types and functions of motherboards, processors, memory, and the expansion bus
Explain the importance of a cooling system and the components used
Identify the role of PC firmware and access the firmware setup program

## Slide 3: Selecting a Computer
Key components for performance
Central Processing Unit
Memory (System RAM)
Fixed disk
  Hard Disk Drive (HDD)
  Solid State Drive (SSD)
Graphics Processing Unit (GPU)

## Slide 4: Network Interface
Wired network
  Ethernet port (RJ-45)
  Network Interface Card (NIC)
Wireless network
  Wi-Fi radio networking
  Wireless access points

## Slide 5: Motherboard Components

## Slide 6: Processors
Microprocessor/integrated circuit
Central Processing Unit (CPU) is main processor in computer
Intel versus AMD
  Intel = LGA (Land Grid Array)
  AMD = PGA (Pin Grid Array)

## Slide 7: Intel and AMD CPU Brands
INTEL:
  Core
  Pentium
  Celeron
  Atom (mobile)
  Xeon (servers)
Legacy—Athlon, Phenom, Sempron, Turion, AMD FX, Opteron
Zen microarchitecture
Ryzen/Threadripper and Ryzen Mobile
Epyc (servers)

## Slide 8: ARM CPUs
ARM (Advanced RISC Machine) microarchitecture
  Widely used on smartphones and tablets
  ARM don’t make CPUs but license the designs
  Apple A, Samsung Exynos, nVIDIA Tegra
RISC stands for Reduced Instruction Set Computing
RISC microarchitectures use simple instructions processed very quickly
Complex (CISC) microarchitectures use more powerful instructions but process each one more slowly
Intel's microarchitecture is CISC with RISC enhancements (micro-ops)

## Slide 9: Features of Processors
Control unit/pipeline
Execution units
Registers

## Slide 10: Instruction Set (32- versus 64-bit)
x86 instruction set
  x86 instruction set started in 1978 with 16-bit CPUs
  First 32-bit CPU with x86-32/IA-32 released in 1985
  x86-64/x64 developed by AMD in 2003 (Intel refer to it as EM64T)
32-bit versus 64-bit CPU
  32-bit CPU can address up to 4 GB memory
  64-bit CPU can address up to 16 Exabytes (currently CPUs use a 48-bit address space (256 Terabytes)
  64-bit CPUs can run 32-bit operating systems and software
  32-bit CPUs CANNOT run 64-bit operating systems or software
Most PC/laptop CPU models are now 64-bit

## Slide 11: Clock Speed and Bus Speed
Clock speed differentiates CPU models (premium models run faster)
  Clock speed number of instructions CPU can process in one second
  Measured in Hertz (Hz) 3 GHz
Front Side Bus between CPU and system memory is another important performance factor

## Slide 12: Multiprocessing and Dual-core
Symmetric Multiprocessing (SMP)
  Providing multiple CPU sockets on the motherboard
  Usually a feature of server systems
Chip Level Multiprocessing (CMP)
  Each CPU contains multiple “cores”
  Each core works as a (more-or-less) independent CPU
  2-core, 4-core, and 8-core models available

## Slide 13: System and Expansion Bus Technologies
Bus is circuitry that connects various microprocessors and other components on the motherboard
Motherboard is a printed circuit board with buses connecting processors. Buses carry 4 things:
  Data- the information
  Address- where the data is located
  Timing-
  Power
System bus (Front Side Bus) between CPU and system memory
Expansion bus (Input/Output Bus) between CPU and other processors

## Slide 14: Expansion Bus Types

## Slide 15: System Cooling
Heatsinks and thermal paste
  Passive cooling
  Transfer heat by convection
Fans
  Active cooling (powered)
  Dissipate warm air from component
  Case fans draw cool air through front vents and expel warm air through back

## Slide 16: Liquid-based Cooling Systems

## Slide 17: BIOS and UEFI System Firmware
Bootstrapping (booting)
  CPU starts and initializes other components
  Occurs before operating system loads
  Controlled by PC firmware
BIOS (Basic Input/Output System)
UEFI (Unified Extensible Firmware Interface)

## Slide 18: System Firmware Setup Program
Press a key during boot sequence—look at screen or refer to documentation
Navigate using keyboard and ESC (for BIOS)
UEFI can use a mouse

## Slide 19: UEFI Setup Programs

## Slide 20
Explain the way in which system components determine performance and how to specify an appropriate computer system
Describe the types and functions of motherboards, processors, memory, and the expansion bus
Explain the importance of a cooling system and the components used
Identify the role of PC firmware and access the firmware setup program
Notes: What type of component provides persistent storage? A mass storage device such as a Hard Disk Drive (HDD), Solid State Drive (SSD), or flash memory. You could also mention optical discs (CD, DVD, Blu-Ray).
What computer component is most restrictive in terms of determining upgrade potential for a desktop computer? The motherboard—it is difficult and expensive to replace.
True or false? A plug-in card is always required to support PC sound. False—sound functions are often provided by the motherboard chipset.
What is the main advantage of using a CPU in 64-bit mode? Makes more system memory accessible. A 64-bit CPU and OS is also required to run 64-bit applications, but there are not too many of these yet. 64-bit software is more reliable and a bit faster than 32-bit software.
What is a typical speed for a modern CPU to run at? Around 2 GHz; budget models might run as low as 1 GHz while the fastest run up to about 3 GHz.
You want to purchase a computer with a fast graphics interface. What type of expansion slot should you look for? PCIe x16—this is a type of PCI Express slot that uses 16 'lanes'. Each lane can transfer 250 MBps (or 500 MBps for PCIe 2 and 1 GBps for v3).
What type of component provides a passive cooling solution? A heatsink or heat spreader removes heat from the component by convection with no power required. However, it is usually necessary to cool the heatsink or heat spreader itself and this is likely to require active cooling (a fan).
How would you access the system setup program on a PC? Historically, by pressing the appropriate key during startup (ESC, DEL, F1, F2, or F10). Modern PCs often use fast boot modes that require some other means of booting to the firmware setup program.

## Slide 21
Lab 11 / Specifying PC Systems