## Slide 1: CompTIA IT Fundamentals+ (Exam FC0‑U61)
Module 3 / Unit 2 / Using Device Interfaces

## Slide 2
Distinguish peripheral, graphics, and networking interfaces and their uses
Install and configure input devices

## Slide 3: Computer Port and Connector Types

## Slide 4: Universal Serial Bus (USB)
Plug-and-Play interface; hot-swappable
Supplies enough power for small peripherals
Versions and data rates
  1.1 – 12 Mbps
  2.0 – 480 Mbps
  3.0 – 5 Gbps (5000 Mbps)
  3.1 – 10 Gbps
USB Type A
USB Type B
USB Mini Type B
USB Micro Type B
USB Type C

## Slide 5: Question of the Day
  GBps = Gigabytes per second
  Gbps = Gigabits per second
  8 bits = 1 Byte

## Slide 6: Firewire
Similar to USB but not widely adopted on PCs
Data rate of 400 Mbps
6-pin and unpowered 4-pin connectors

## Slide 7: Graphics Devices
Video card or graphics adapter generates the signal to send to a display device (monitor)
Most motherboards have integrated adapters
High performance adapters can be fitted through an expansion card
Video card often has its own CPU (GPU or Graphics Processing Unit) and memory
Resolution and color depth
  Resolution = Number of pixels horizontal X Number of pixels vertical
  Color depth = maximum number of colors that can be displayed
VGA (Video Graphics Array) standards
Standard 4:3 versus widescreen (16:10) resolutions
High Definition (HD) and 4K resolutions

## Slide 8: High Definition Multimedia Interface (HDMI)
Very widely used on computers and consumer electronics
Sufficient bandwidth for HD resolution (and 4K)
Mini and micro connectors also available

## Slide 9
Break! Be back 2:15

## Slide 10: DisplayPort and Thunderbolt
Competitor technologies to HDMI
Support for daisy-chaining monitors
Used on Apple Macs and some PCs—especially Thunderbolt 3
Thunderbolt 2
  20 Gbps over a MiniDP physical interface
Thunderbolt 3
  40 Gbps over a USB-C physical interface (with 0.5m cable)

## Slide 11: Digital Visual Interface (DVI)
Preceded HDMI as the principal display interface for PCs
DVI can support both digital and analog monitors
Single and dual-link versions
Most interfaces are DVI-I dual-link
Bulky connectors mean that this interface is rapidly falling out of favor
HDMI is backward-compatible with DVI-D using a suitable adapter cable

## Slide 12: Video Graphics Array (VGA)
Blue, 15-pin port (HD15F/DE-15)
Legacy analog interface—used principally with old Cathode Ray Tube (CRT) monitors
Some flat-panel displays and graphics adapters continue to provide VGA ports

## Slide 13: Input Devices (1)
Human Interface Devices (HID)
Keyboard
  USB/Bluetooth (or legacy PS/2)
  Layout and region
Mouse
  USB/Bluetooth (or legacy PS/2)
  Optical and laser designs (or legacy mechanical mice)
  Optional extra buttons and scroll wheel

## Slide 14: Input Devices (2)
Laptop keyboards and touchpads
  Fn switch for laptop keys
  Touchpad gesture support
Stylus pen

## Slide 15: Configuring a Mouse
Connect to an appropriate port
  PS/2
  USB
  Wireless
Install vendor driver for custom settings
Configure using Mouse applet

## Slide 16: Configuring a Keyboard
Connect to an appropriate port
Configure using Mouse applet
Set correct region/layout using Settings
Switch between multiple layouts using Notification icon (START+SPACEBAR)

## Slide 17: Configuring a Pen/Stylus

## Slide 18: Bluetooth
Personal Area Networks (PAN)
  Wireless communications enable short-range connections to peripheral and networks
Bluetooth
  Up to 10m
  3 Mbps (Bluetooth EDR)
  24 Mbps (using HS and Wi-Fi)

## Slide 19: Configuring Bluetooth
Put device into discoverable mode
Pair using passkey on both devices
Disabling Bluetooth

## Slide 20: RF and Near Field Communications (NFC)
Radio Frequency ID (RFID)
  Passive tags (typically) encoded with data
  Respond when scanned by an RFID reader
  Widely used for inventory management
Near Field Communications (NFC)
  Peer-to-peer version of RFID working at very close range (2”/6cm)
  Used on smartphones for contactless payment

## Slide 21: Networking Interfaces
Network Interface Card (NIC)
  Onboard (part of motherboard)
  Expansion cards
Ethernet connector (RJ-45)
  Patch cord with RJ-45 connectors between NIC and Ethernet switch (or wall port)

## Slide 22: Telephone Connector (RJ-11)
Smaller than RJ-45 and with fewer wires
Used for dial-up analog modems and fax modems
Also used between Digital Subscriber Line (DSL) Internet modems and telephone jack

## Slide 23
Distinguish peripheral, graphics, and networking interfaces and their uses
Install and configure input devices
Notes: True or false? Mice and keyboards must be connected to a computer via PS/2 ports. False—they are now much more likely to use USB or wireless (Bluetooth or other RF) interfaces.
True or false? USB cables have the same connectors at either end. Partly false—the connectors for the host (PC) and device use different form factors (there are also normal size and mini or micro device connectors). A new reversible Type C connector is starting to be used however.
A user has two USB drives connected to her PC. She complains that when she copies large files to both drives at the same time, it seems to take much longer. Why might this be? Bandwidth on the USB bus is shared between all devices.
You want to purchase a flat-panel monitor that can show widescreen movies. You are considering models with native resolutions of 1400x1050 and 1920x1200. Which should you choose? 1920x1200 as this is a widescreen format.
True or false? HDMI is the only type of display interface that supports High Definition picture resolutions. False—there is also DisplayPort and Thunderbolt and some DVI formats also support HD resolutions.
You are considering buying a new display device. The model you are considering accepts digital inputs only. Your computer's graphics adapter has a blue port with 15 holes. Would this flat-panel be a wise purchase? Probably not, as this connector is VGA, which supports analog output only. It is possible to buy converters however.
You need to configure settings for an input device. What should be your first step? Open the Settings app or Control Panel.
A friend is asking for your help in using her computer. When he presses the key marked @, a different symbol appears. What could be the cause? The keyboard is set to use a UK layout—you can correct this using the Language Bar.
What type of mouse would you recommend for someone who uses their computer principally to play computer games and why? Laser mouse—this registers cursor movements more quickly and accurately.

## Slide 24
Lab 12 / Configuring Input Devices