## Slide 1: Question of the Day
Which of these would be found in a laser printer? (Choose 2)
  Toner
  Print head
  Ink cartridge
  Fuser unit
  Digitizer
  Applet

## Slide 2: CompTIA IT Fundamentals+ (Exam FC0‑U61)
Module 3 / Unit 4 / Using Storage Devices

## Slide 3
Contrast volatile and non-volatile storage types
Describe the types of system memory modules used in PCs
Describe the types and features of Hard Disk Drives, Solid State Drives, optical drives, and flash memory

## Slide 4: System Memory
Random Access Memory (RAM)
Volatile storage
Vendors—Kingston, Crucial (Micron), Corsair, PNY, Integral
Dynamic RAM (DRAM)
Synchronous DRAM
  64-bit transfers per clock cycle
Module packaging
  DIMMs (Dual Inline Memory Module) 5.5 in
  Small Outline DIMM (SO-DIMM) 2.75 in

## Slide 5: Double Data Rate SDRAM (DDR SDRAM)
Two 64-bit transfers per clock cycle
Subsequent iterations increase bus speed
  DDR2
  DDR3
  DDR4
Motherboard sockets must match DDR version
DIMM and SO-DIMM modules with different pin positions

## Slide 6
Break! Be back 2:14

## Slide 7: Hard Disk Drives (HDD)
HDD is one type of fixed disk internal persistent storage device
Magnetic platters access by a drive head
2.5” (laptops) and 3.5” (desktops) formats
Capacity
  Measured in (gigabyte) GB or (terabyte) TB
Performance
  Spin speed (RPM or rotations per minute)
    Typical speeds 5400 and 7200 RPM
  Access time
  Transfer rate
Vendors—Seagate, Western Digital, Maxtor, Hitachi, Fujitsu, Toshiba, Samsung

## Slide 8: HDD Interfaces
Serial ATA (SATA) dominates internal devices (legacy drives used Parallel ATA/EIDE and SCSI)
External drives housed in an enclosure can use a number of interfaces

## Slide 9: Solid State Drives (SSD)
Non-volatile flash memory
Lighter, faster, and more reliable than mechanical HDDs
Costs falling rapidly but still very expensive above 512 GB
Large flash memory caches are also used to supplement HDDs (hybrid drives)
Can be packaged as 2.5” drive with SATA connector, PCIe adapter card, or M.2 adapter card

## Slide 10: Optical Discs and Drives
Specially formatted discs read by a laser
Multiple formats
  Compact Disc (CD)
  Digital Versatile / Video Disc (DVD)
  Blu-ray Disc (BD)
Recordable and rewritable formats
  CD-R: CD Recordable
  DVD-R: DVD Recordable
  CD-RW: CD Rewritable
  DVD-RW: DVD Rewritable

## Slide 11: Optical Drive Units
Fit to internal 5.25” drive bays and SATA interface
USB external units
Read/record/rewrite speeds

## Slide 12: Removable Flash Memory Devices
USB/thumb drive
  Up to 256 GB (at affordable prices)
Memory cards
  Multiple vendors and form factors/sizes
  Secure Digital (SD) and Compact Flash (CF)
  Typically up to 128 GB, though 2 TB cards have been made
  Multi-format memory card readers

## Slide 13
Contrast volatile and non-volatile storage types
Describe the types of system memory modules used in PCs
Describe the types and features of Hard Disk Drives, Solid State Drives, optical drives, and flash memory
Notes: You have a motherboard that is designed for DDR2 memory that works at a bus speed of 533 MHz. You have some DDR3 memory modules that also work at a bus speed of 533 MHz. Are the modules compatible with the motherboard? No—DDR3 modules cannot be used in DDR2 slots.
Why can't you use memory modules designed for a desktop computer in a laptop? Laptops use a smaller form factor called SO-DIMM while desktops use DIMMs.
A hard drive is rated at 10,000 RPM. What is the significance of this statistic? The number of revolutions per minute (RPM) is one of the basic factors determining the speed of the drive. 10,000 rpm represents good performance (15K rpm is the best available).
What type of connector would you use for an external hard drive to connect to a Windows PC? USB. Firewire, eSATA, or Thunderbird are also possible but not nearly so popular. Most drives are now USB3 or USB3.1. Note that you can plug a USB3 drive into a USB2 port, so long as you have a USB3 device cable.
Your computer has 4 SATA ports. How many hard drives can be installed? Four—each SATA port can be used to connect one drive.
True or false? A single layer Blu-ray Disc has greater capacity than a dual-layer, double-sided DVD. True—the capacity of a single layer Blu-ray disc is 25 GB compared to 17 GB for a dual-layer, double-sided DVD.
What sort of device would you need to transfer data from a "Memory Stick?" Memory card reader/multi-card reader. Do note that Memory Sticks are no longer in production so you could struggle to locate a suitable reader.
What sort of device could you use to expand the storage capacity of a smartphone? Flash memory card.

## Slide 14
Lab 15 / Adding a Removable Drive

## Slide 15
Describe the properties of file systems and select an appropriate file system for a given OS and usage
Use a file manager to create, open, move/copy, and delete files and folders/directories
Use search tools and view options to locate files quickly
Notes: In Windows, you can access data via letter-labeled "drives." Do these correspond exactly to physical disks? Not necessarily in the case of hard disks, which can be configured with multiple partitions, each of which can be assigned a drive letter. Optical drives and flash memory cards cannot be partitioned however.
What type of file system must the partition that Windows files are installed on use? NTFS.
What default installation folders contain system and application files that should not normally be deleted or modified manually? The 'Windows' and 'Program Files' folders.
What is the file path to the Documents folder for a user named "David," assuming Windows is installed to a hard disk with a single partition using the default settings? C:\Users\David\Documents
How is a Windows library different from a folder? A library acts as a virtual folder by displaying the contents of multiple folders, which could be located on different drives.
If you have made changes to a file and want to keep both the original file and the modified version, what command should you use? Save As.
Why should you be more careful about deleting files from a USB flash drive than from the main hard drive? The files will not be recycled so there is no possibility of retrieving them if you change your mind (at least, not without using specialist data recovery software).
What view options could you use to show files of a particular type sorted by date? Group the files by file type then sort by date.
What kind of data would you expect to find in a file with a TIFF extension? This is an image file format.
What is a zip file? A file archive containing other files in a compressed format.

## Slide 16
Lab 16 / Using File Explorer