## Slide 1: CompTIA IT Fundamentals+ (Exam FC0‑U61)
A 5-day Training Course

## Slide 2: What is CompTIA IT Fundamentals+?
“The CompTIA IT Fundamentals+ exam will certify the successful candidate has the knowledge and skills required to identify and explain the basics of computing, IT infrastructure, software development and database use. In addition, candidates will demonstrate their knowledge to install software, establish basic network connectivity and identify/prevent basic security risks. Further, this exam will assess the candidate’s knowledge in the areas of troubleshooting theory and preventative maintenance of devices. This exam is intended for candidates who are advanced end users, are considering a career in IT, and are interested in pursuing professional-level certifications, such as A+.”
International, vendor-neutral certification that is taught at colleges, universities and commercial training centers around the world
Recognized by the technology community as a valuable credential that proves foundation-level competency with PC support

## Slide 3
Set up a computer workstation and use basic software applications
Explain the functions and types of devices used within a computer system
Apply basic computer maintenance and support principles
Describe some principles of software and database development
Configure computers and mobile devices to connect to home networks and to the Internet
Identify security issues affecting the use of computers and networks

## Slide 4: Exam Format
Exam code: FC0-U61
Up to 75 questions in 60 minutes
Passing score: 650 on a scale 100-900
Domain | % of Exam
1.0 IT Concepts and Terminology | 17%
2.0 Infrastructure | 22%
3.0 Applications and Software | 18%
4.0 Software Development | 12%
5.0 Database Fundamentals | 11%
6.0 Security | 20%

## Slide 5: Introducing Yourself
Name / company
Job function
Type and amount of experience
Expectations and objectives

## Slide 6: CompTIA IT Fundamentals+ (Exam FC0‑U61)
Module 1 / Unit 1 / Common Computing Devices

## Slide 7
Describe the basics of how a computer processes data
Describe the functions and capabilities of types of computing devices, such as PCs, servers, mobiles, and home automation

## Slide 8: Information Technology
System to process, store, and transfer information
Words, numbers, pictures, sound, or video can all be represented as digital data—as strings of ones and zeroes
IT systems to process data includes computers, telecommunications networks, and any other programmable electronic device
The Information Age—data processing is critical to prospects in most industries

## Slide 9: Computer Hardware and Software
Hardware
  Components within the system case
  Peripheral devices
Software
  Operating System (OS)
  Applications/apps
User interfaces

## Slide 10: Basics of Computing and Processing
User selects a command or inputs data
  Command or data is converted into simple instructions by the applications software and OS
  Instructions are stored in system memory—Random Access Memory (RAM)
Central Processing Unit (CPU) retrieves each instruction or data file from memory and processes it
CPU then writes the result back to memory and directs other components to perform actions
Digital data is binary (1s and 0s)
Transistors in CPU and RAM can have on or off states that represent 1 or 0

## Slide 11: Input, Output, Processing, and Storage
Input
  Peripheral devices
  Mice, keyboards, scanners, cameras, and microphones
Processing
  Memory
  CPU
  Software instructions
Output
  Peripheral devices
  Monitor or loudspeaker system
Storage
  Hard disks or optical discs (media that does not need a power supply to store data persistently)
Networks

## Slide 12: Personal Computers
IT in business started with mainframe computers in the 1960s and 1970s
  Very large (based on racks of circuit boards)
  No 1:1 interface with users
Personal Computer revolution of the 1980s
  Microprocessors (“computer on a chip”) allowed smaller computers that could be operated directly by the user
  IBM PC
  Intel CPU
  Windows OS
Internet revolution of the 1990s and 21st century
  Laptops
  Tablets
  Smartphones
  Internet of Things (IoT)

## Slide 13: Desktop and Workstation Computers
Computer case with peripheral devices
Easy to modify and upgrade
  CPU speed
  Memory capacity
  Disk storage capacity
  Optional components
  Ergonomics
All-in-One PCs

## Slide 14: Servers
Server can mean any computer providing services
Server-class hardware supports many users and is very reliable
Redundancy and fault tolerance
Rack-mounted form factors

## Slide 15: Laptops
Self-contained units
Integrated input (keyboard and touchpad) and output (screen and speakers)
Size and weight
Display type
Input devices
Power source
Components
Networking

## Slide 16: PC and Laptop Vendors
Original Equipment Manufacturers (OEM)
PCs and laptops
  Dell, Hewlett-Packard (HP)/Compaq, Lenovo (previously IBM's PC division), Acer, and Huawei
Laptops and hybrids
  Samsung, Sony, Toshiba, and Asus
Apple
Chromebooks
Servers
  Dell, HP Enterprise (HPE), and Lenovo

## Slide 17: Smartphones and Tablets
Handheld computers
  Derived from early Personal Data Assistants (PDA) and “feature phone” cell phones
  Input via touchscreens
  Solid state storage
Different formats and sizes
  Smartphone (4.5-5.7”)
  Phablet (5-7”)
  Tablet (7-10”)
  Hybrid laptop/tablets
Vendors
  Smartphone market is dominated by Apple and Samsung
  LG, HTC, Huawei, Motorola/Lenovo, Microsoft, Nokia, Sony, and Amazon

## Slide 18: The Internet of Things (IoT)
Home automation
  Hub with voice control
  IoT wireless (Z-Wave, ZigBee, or Bluetooth LE)
  Thermostats
  Security systems
  IP cameras
  Home appliances
  Streaming media
Modern cars and drones
Medical devices

## Slide 19: Gaming Consoles
Same sort of components as a computer
Gaming pads
Vendors
  Sony (PlayStation)
  Microsoft (Xbox)
  Nintendo (Wii and Switch)
Handheld consoles
  Nintendo 3DS and Switch
  Sony Vita

## Slide 20
Describe the basics of how a computer processes data
Describe the functions and capabilities of types of computing devices, such as PCs, servers, mobiles, and home automation
Notes: True or false? All types of computers use CPU and system memory. True.
What type of computer is most likely to need peripheral devices? Desktop computer—you could also call this a Personal Computer (PC) or a workstation. An All-in-one PC also uses peripheral devices, with the obvious exception of a monitor.
What type of computer is best suited for using in a job where you have to make notes and be able to move around easily? A tablet or smartphone or possibly a hybrid laptop/tablet. Note-taking is supported by a touchscreen-based device.
Why don't laptops make good servers? There is no room for expansion and you are paying for components and design (maximum portability) you do not need.
Why isn't a smartphone a good tool for writing a report? Touchscreen or mini keyboards are not optimized for writing lots of text, though it is possible to attach them as peripheral devices.
What type(s) of IoT appliance are less likely to be controlled via a home automation hub? Modern cars and medical devices are unlikely to interface via a hub. Home automation hubs link to kitchen and domestic appliances, streaming media players, and potentially security systems.

## Slide 21: CompTIA IT Fundamentals+ (Exam FC0‑U61)
Module 1 / Unit 2 / Using a Workstation

## Slide 22
Set up a computer system with regard for safety and healthy working practices
Navigate an OS and use input devices effectively

## Slide 23: Setting up a Personal Computer
Check contents
Read instructions
Position devices and cables
  Trip hazards
  Air flow
  Usability
Connect peripherals
Connect power cables
Power on

## Slide 24: Ergonomic Concepts
Proper keyboard and mouse placement
Sitting position and monitor placement

## Slide 25: Navigating an OS
Signing in to the computer
Launching software applications
Managing data files
Configuring the system

## Slide 26: Signing In to Windows
Computer boot process/Power On Self Test (POST)
Sign in ID and authentication
  User name
  Password/other credential
Pass lock screen
Select user account
Enter password

## Slide 27: Using the Desktop and Taskbar
Desktop shortcuts
Taskbar
  Start/Windows button
  Pinned icons
  Notification area
Start Screen/Start Menu

## Slide 28: Using the Start Screen
Main interface for Windows 10
Press Start key
Works as desktop for mobile hardware
Tiles
Apps
Instant search

## Slide 29: Customizing the Start Screen and Taskbar
Pinning apps
Grouping tiles
Start Screen and Taskbar settings (Personalization)

## Slide 30: Using a Mouse or Touchpad
Selecting and opening icons
Selecting menu commands
Using a shortcut menu
Drag and Drop
Scrolling

## Slide 31: Using a Keyboard
Typing ordinary text
  Touch typing finger positions
  Keyboard layouts
Special/command keys
  ENTER/RETURN
  CTRL and ALT
  TAB and ARROW keys
  SHIFT
  NUM LOCK and keypad
  START (Windows key)
  SHORTCUT key
  FN keys
  BACKSPACE and DELETE

## Slide 32: Using a Touchscreen
Gesture support and on-screen keyboard
Typical gestures
  Tap—pressing once is the same as a left mouse click
  Tap and hold—right-mouse click
  Pinch and stretch—pinch together to zoom in or move apart (stretch) to zoom out
  Swipe
    Swiping from a particular screen edge performs different actions
    Swiping within an app window can also perform custom actions
    Swiping down from the top of the app window usually refreshes the content

## Slide 33: Recognizing Desktop Icons
File
Shortcut
Folder
Application
Device

## Slide 34: Working with Windows

## Slide 35
Set up a computer system with regard for safety and healthy working practices
Navigate an OS and use input devices effectively
Notes: What should you do before attempting to set up a new computer system? Verify that the environment is suitable and that the installation will be safe.
When setting up a desktop computer, what factor should you consider when deciding on the location of the system case? You do not want to leave trailing wires over walkways so you need to consider the position of power outlet(s) and where peripheral devices will be placed. You also want to ensure adequate air flow around the system unit.
What factors should you consider when positioning input and output devices? Ensure that they can be used without exerting strain, especially on the arms/wrists and back/neck. Ensure that cabling is not a trip hazard. Avoid locations that cause excessive screen glare.
You have to sign in to Windows—does it matter if the CAPS LOCK light on the keyboard is activated? Yes—passwords are case-sensitive.
You have to open a word processing application but you cannot see an icon on the desktop. What should you do? Look for the shortcut in Start Menu or Start Screen—not all programs add shortcuts on the Desktop.
Your colleague has to run many applications at the same time and finds it difficult to know which icon to choose when switching between them. What alternative method could you suggest? Press Alt+Tab—this shows previews of the window. Windows can also show previews of the window contents when pointing at the taskbar icon.
Your colleague is using a laptop and you notice that he laboriously clicks the mouse repeatedly to scroll through the document you are co-editing. What technique could he use to be more productive? Use the mouse scroll wheel (or if it doesn't have one drag the scroll button in the scroll bar).

## Slide 36
Lab 1 / Setting up the Computer
Lab 2 / Navigating the Windows User Interface

## Slide 37: CompTIA IT Fundamentals+ Study Guide (Exam FC0‑U61)
Module 1 / Unit 3 / Using an OS

## Slide 38
Distinguish between different types of operating systems designed for workstations, servers, mobiles, embedded systems, and virtualization
Identify commonly used commercial and open source operating systems, such as Windows, macOS, iOS, Linux, Chrome, and Android
Use a browser to view websites

## Slide 39: Functions of an Operating System
Interface between user and computer
  Shell
  Graphical User Interface (GUI)
  Command line
Interface between applications and hardware
  Kernel and devices drivers
  Utilities
  32-bit versus 64-bit
  Application compatibility
System health and functionality
Data management

## Slide 40: Workstation, Server, and Mobile Device OS
Workstation OS
  Microsoft Windows, Apple OS X/macOS, Linux, and Chrome OS
  Enterprise client
  Network OS (NOS)
  Home client
Mobile device OS
  Apple iOS and Android
  Tied to hardware
Server OS
  Windows Server, Linux, or UNIX
  Same code base as workstation equivalent
  Network server applications and client licensing
  Command line operation

## Slide 41: Open Source versus Commercial
Commercial OS
  User must purchase license
  Proprietary code kept secret by vendor
  Microsoft Windows, Apple macOS, Apple iOS
Open source OS
  Programming code freely published and can be reused (with some conditions)
  Might still be used as the basis of commercial products
  UNIX, Linux, Android

## Slide 42: Embedded OS
Embedded systems perform quite specific tasks (compared to general purpose PC/laptop/smartphones)
Static environment
Time-sensitive operation
Very high reliability requirement
Real Time Operating Systems (RTOS)

## Slide 43: Firmware
Type of software that is very closely tied to the function of hardware
Not designed to be changed often
PC/laptop firmware
  Basic Input/Output System (BIOS)
  Unified Extensible Firmware Interface (UEFI)
Many other components have embedded firmware
  Graphics adapters, disk drives, network adapters, printers,...

## Slide 44: Virtualization
Running multiple OS on a single computer
Host computer
Hypervisor
  Type I/”bare metal”
  Type II
Guest OS/Virtual Machines (VM)

## Slide 45: Microsoft Windows
Estimated to run on 90% of desktops and laptops
Client and server editions
Released in many different versions over the years

## Slide 46: Windows 10
First released in 2015
  Windows 10 Anniversary Update (1607)
  Fall Creators Update (1709)
  Spring Creators Update (1803)
Designed to run on both PC/laptops and smartphone/tablet/hybrids
Estimated market share of about 33% in 2017/2018

## Slide 47: Older Windows Versions
Windows 8 (2012)
  First version with Start Screen/touch-enabled interface
  Windows 8.0 (no Start button!)
  Windows 8.1 (Start button back)
  Not widely adopted (about 7% market share)
Windows 7 (2009)
  Last version with the Start Menu interface
  Still very widely used (43% market share)
Windows Vista (2007)
  Preceded Windows 7 but never widely adopted
Windows XP (2001)
  Once very widely adopted but security problems have seen it drop to 5%

## Slide 48: Windows Editions
Each Windows version made available in different editions
  Windows 10 Home—consumer and Small Office Home Office (SOHO) business use
  Windows 10 Pro—small and medium-sized businesses
  Windows 10 Enterprise/Windows 10 Enterprise (Long Term Servicing Channel)—similar to the Pro edition but designed for licensing by medium and large enterprises
  Windows 10 Education/Pro Education—variants of the Enterprise and Pro editions designed for licensing by schools and colleges
32-bit versus 64-bit
Windows 10 Mobile

## Slide 49: Apple macOS
Apple Macintosh computer hardware
Mac OS – can only be installed on Apple Mac hardware
Versions
  OS X
  macOS
  “dot” updates

## Slide 50: Apple iOS
Runs on iPhone and iPad hardware only
Currently version 11/12
Version updates can drop support for older hardware models

## Slide 51: UNIX, Linux, and Chrome OS
UNIX
  Developed in parallel by various institutions
  Contains proprietary/copyright/patented code
Linux
  Derived from UNIX but fully open source
  Multiple distributions (distros)
    SUSE, Red Hat, Fedora, Debian, Ubuntu, Mint
  More widely deployed as a server than desktop OS (about 2% market share)
Chrome OS
  Derived from Linux to run Chromebook and Chromebox hardware
  Designed to work with web applications rather than locally-installed software

## Slide 52: Android
Smartphone/tablet OS derived from Linux
Often customized by vendors
  Acer, Asus, HTC, Huawei, LG, Motorola, OnePlus, Oppo, Samsung, Sony, Xiamoi
Major and minor version updates

## Slide 53: File Explorer/Windows Explorer
File management interface
This PC / Computer
Network

## Slide 54: Windows Settings

## Slide 55: Control Panel
Configuration options (applets) for earlier Windows versions (and some aspects of Windows 10 and Windows 8)
Category and list views

## Slide 56: Ease of Access Options

## Slide 57: Advanced Management Utilities
“Power” menu
  START+X
  Right-click Start button
Consoles and tools for more advanced configuration

## Slide 58: Using a Web Browser
Choosing a browser
  Edge/Internet Explorer (IE)
  Mozilla Firefox
  Google Chrome
  Apple Safari
Web browser features
  Address bar
  Tabbed browsing

## Slide 59: URLs, Websites, and Hyperlinks
Uniform Resource Locator (URL)
  Web address
  Tells browser how to locate a page or resource
Websites and web pages
Site navigation and hyperlinks

## Slide 60: Using Browser Controls
Back
Forward
Stop
Refresh
Address bar
Setting the home page

## Slide 61
Distinguish between different types of operating systems designed for workstations, servers, mobiles, embedded systems, and virtualization
Identify commonly used commercial and open source operating systems, such as Windows, macOS, iOS, Linux, Chrome, and Android
Use a browser to view websites
Notes: What function of an operating system is performed by the "shell?" Interface between the user and the computer.
What type of file in an OS is the main means of providing coordination of hardware components? A driver (or device driver).
What is an example of an open source operating system? Linux, Chromium, or Android.
What type of computing device(s) is macOS designed for installation on? Desktop computers/workstations and laptops.
True or false? Windows 10 is the first 64-bit edition of Windows. False—Windows 10 is better described as a version than edition and there have been 64-bit editions of Windows versions since Windows XP.
You have to open a file located on a network server. What should be your first step? Open the Network object from Explorer and locate the server (computer) hosting the file.
What is the technical term for a web address? Uniform Resource Locator (URL). In fact, Uniform Resource Identifier (URI) is now preferred in web standards documentation but URL is more widely known and used.
What key combination can you use to force the browser to ignore any locally cached files when refreshing a page? Ctrl+F5.

## Slide 62
Lab 3 / Browsing a Website

## Slide 63: CompTIA IT Fundamentals+ (Exam FC0‑U61)
Module 1 / Unit 4 / Managing an OS

## Slide 64
Use GUI and command-line management interfaces to configure an operating system
Explain the importance of access control features and configure user accounts

## Slide 65: Management Interfaces
Control Panel/Windows Settings
Management consoles
  Computer Management default console
  Custom consoles with selected snap-ins
Registry Editor (regedit)
Command prompt and PowerShell
Linux configuration files

## Slide 66: Task Manager
Processes and threads
Use Task Manager to monitor and control processes (and other performance indicators)
End or “kill” a process that is not responding

## Slide 67: Service Management
Typical application processes run in a window that the user can interact with
Services are processes that run in the background
Support functionality of OS and many applications
Start, stop, and configure services via the Services snap-in

## Slide 68: Task Scheduler
Automate execution of processes
Use schedules or other triggers

## Slide 69: Memory and Disk Management
System memory
  Volatile, meaning that it is only preserved while the system is powered up
  System memory is provided by Random Access Memory (RAM) modules
Mass storage
  Preserves data when the system is turned off
  Primary fixed disk - hard disk or a Solid-State Drive (SSD)

## Slide 70: Memory Management
Mostly controlled by the OS
Monitor memory usage to see if upgrade is required
Monitor how processes use memory to detect leaks and other faults

## Slide 71: Virtual Memory/Pagefile
Use space on a fixed disk to supplement system RAM
Can be configured via System properties

## Slide 72: Disk Management
Create partitions and file systems on fixed disks to make them usable by the OS
Can also format removable and external disks

## Slide 73: Command Line Interfaces
Operate the OS using typed commands rather than GUI
Commands available depend on the environment
  Windows command prompt (cmd.exe)
  Windows PowerShell
  Linux Bash (Bourne Again SHell)

## Slide 74: Access Control and Protection
Access control systems ensure authorized use of computers, networks, and data resources
Users are identified via accounts
Users access an account by authenticating with credentials know or held only by them
Accounts are assigned privileges or rights to do things

## Slide 75: Account Types and UAC
Administrator versus standard user accounts
Least privilege
  Allocate as few rights and permissions to accounts as possible
User Account Control (UAC)
  Too many people use administrator accounts all the time
  UAC requires explicit authorization to perform a “protected” task

## Slide 76: Creating and Managing User Accounts
Microsoft versus local accounts
Account settings app (password, picture, etc)
Local Users and Groups snap-in

## Slide 77
Use GUI and command-line management interfaces to configure an operating system
Explain the importance of access control features and configure user accounts
Notes: What is the registry and how does it distinguish Windows and Linux? The registry is a database of configuration settings supporting the Windows OS. Linux uses individual text files to store settings.
What term is used to describe terminating a process that is not responding to user input? This is often called "killing" the process.
Why might you use the Services snap-in to manage background processes rather than Task Manager? Task Manager allows you to start and stop services but the Services snap-in also allows you to configure service properties.
The Task Scheduler allows you to run a process automatically in Windows. What is a widely-used Linux equivalent? cron is widely used to run tasks automatically in Linux.
What part of the system memory setup is most user-configurable? Use of virtual memory or a pagefile, where disk space is used to supplement system RAM.
What two things are configured on a disk to make storage space on the disk available to the Windows OS? The disk must contain at least one partition, typically allocated a drive letter, and the partition must be formatted with a suitable file system.
What is a CLI? A Command Line Interface allows the user to interact with the OS using typed commands or scripts rather than a GUI.
What protection feature in Windows is designed to prevent a script or software from making unauthorized changes to the OS configuration? User Access Control (UAC). UAC means that the user must input their credentials or click through an authorization prompt before the configuration change can be made.
True or false? A standard user cannot change their own password. False—ordinary users can change their own password but cannot change anyone else's.

## Slide 78
Lab 4 / Using Management Interfaces
Lab 5 / Managing User Accounts

## Slide 79: CompTIA IT Fundamentals+ (Exam FC0‑U61)
Module 1 / Unit 5 / Troubleshooting and Support

## Slide 80
Describe basic support and troubleshooting procedures
Use websites and tools to obtain support and search for advice and help

## Slide 81: Support and Troubleshooting
Troubleshooting skills and approach
Problem solving and diagnosis
Causes, symptoms, and consequences
Appreciate priorities and business needs

## Slide 82: CompTIA Troubleshooting Model
Identify the problem (Gather information, Duplicate the problem, if possible, Question users, Identify symptoms, Determine if anything has changed, Approach multiple problems individually)
Research knowledge base/Internet, if applicable
Establish a theory of probable cause (Question the obvious, Consider multiple approaches, Divide and conquer)
Test the theory to determine the cause (Once the theory is confirmed [confirmed root cause], determine the next steps to resolve the problem, If the theory is not confirmed, establish a new theory or escalate)
Establish a plan of action to resolve the problem and identify potential effects
Implement the solution or escalate as necessary
Verify full system functionality and, if applicable, implement preventive measures
Document findings/lessons learned, actions and outcomes

## Slide 83: Identifying the Problem
Question users and determine changes
Duplicate the problem and identify symptoms
Approach multiple problems individually
Gather information and research symptoms

## Slide 84: Understanding the Problem
Question the obvious
Divide and conquer
Consider multiple approaches
Test the theory
Escalate the problem?

## Slide 85: Resolving and Documenting the Problem
Establish a plan of action
  Repair
  Replace
  Ignore (workaround/document)
Implement the solution
Verify full system functionality and implement preventive measures
Document findings, actions, and outcomes

## Slide 86: Troubleshooting PC Issues
Startup process
  Basic Input Output System (BIOS)
  Power On System Test (POST)
Check power / LEDs / sounds of activity
Multiple beeps – check for cause
Dark screen - check monitor controls and power
Peripheral devices – check cables and connectors

## Slide 87: Getting Support
Manufacturer documentation
Online support and driver downloads

## Slide 88: Windows Help and Tips

## Slide 89: Technical Support
Contacting technical support
    Name and contact information
    Software or device you are having trouble with
      Version number (Help > About command)
      Model and serial number
    Purchase date
    Description of the problem
Using technical community groups

## Slide 90: Using a Search Engine

## Slide 91
Describe basic support and troubleshooting procedures
Use websites and tools to obtain support and search for advice and help
Notes: You are advising a colleague about best practices when troubleshooting. You have identified the following techniques to use to identify a problem: gather information, duplicate the problem, question users, identify symptoms, and approach multiple problems individually. If you are following CompTIA's troubleshooting model, what other piece of advice should you give? Determine if anything has changed—this is one of the most useful troubleshooting techniques.
You have asked a senior manager to authorize your plan of action for resolving a fault in a software application. What name is given to the process you are following? This is escalating the problem. You might escalate a problem to more experienced staff or seek help with a solution plan that is beyond your authority to put into action.
You are setting up a new computer, but it doesn't seem to be working. Should you check anything or contact the manufacturer? It would be best to double-check you have connected the cables correctly (especially power).
Your computer locks up periodically and feels hot to the touch. Could these things be related? Yes, many lockup problems are caused by overheating. The first step would be to clean the fan exhaust vents of dust.
What crucial piece of information would you need when trying to locate support information about a computer system on the manufacturer's website? The model number or a service code.
If you do not have a support contract, what is likely to be the best option for obtaining advice about a problem with an application? A product support or community forum.
You are looking for content on a topic but your search is returning millions of matches that are not particularly helpful. What two methods could you use to get better search results? Use more search keywords (ideally with 'uncommon' words) or search for an exact phrase by enclosing it in quotes.
You want to find something on a particular website, but the site does not have a search tool. Could you use a general search engine, and if so, how? Yes—you use an advanced search form or use the site: operator (for example 'certification site:comptia.org').

## Slide 92
Lab 6 / Using a Search Engine

## Slide 93: CompTIA IT Fundamentals+ (Exam FC0‑U61)
Module 2 / Unit 1 / Using Data Types and Units

## Slide 94
Recognize and use different notational systems, data types, and units of measure
Compare and contrast fundamental data types and their characteristics
Discuss the importance of data and ways that a company can use it to make business decisions

## Slide 95: Decimal Notation
Base 10 place value number system
Each single digit can be 0 to 9
Each column is worth ten times the previous
12 = 10*1 + 2*1

## Slide 96: Binary Notation
Base 2 place value number system
Each single digit can be 0 or 1
Each column is worth two times the previous
These values are easy to represent as the on/off states of electronic transistors

## Slide 97: Hexadecimal Notation
Base 16 place value number system
Each single digit can be 0 to 9, A, B, C, E, F
Each column is worth 16 times the previous
Used to represent large values more efficiently than binary

## Slide 98: Bits and Bytes
A bit stores the value of a single binary digit (1 or 0)
A byte stores the value of eight bits
Base 10 multiples of bytes are used to represent file and storage sizes
  KiloByte (KB)—1000 bytes (or 103 or 10*10*10 bytes)
  MegaByte (MB)—1000*1000 bytes (or 1,000,000 bytes)
  GigaByte (GB)—1000*1000*1000 bytes (1,000,000,000 bytes)
  TeraByte (TB)—1000 GB (1,000,000,000,000 bytes)
  PetaByte (PB)—1000 TB or 1015 bytes (1,000,000,000,000,000 bytes)
In some context base 2 multiples are used
  KibiByte (KiB)—1024 bytes (210 bytes)
  MebiByte (MiB)—1024*1024 bytes (or 1,048,576 bytes)
  GibiByte (GiB)—1024*1024*1024 bytes (1,073,741,824 bytes)
The units are not used consistently though

## Slide 99: Throughput Units
Transfer rates or “speed”
  Kbps (or Kb/s)—1000 bits per second
  Mbps (or Mb/s)—1,000,000 bits per second
  Gbps (or Gb/s)—1,000,000,000 bits per second
  Tbps (or Tb/s)—1,000,000,000,000 bits per second
Always base 10 values
Also Bytes per second (KBps, MBps, GBps, TBps)

## Slide 100: Processing Speed Units
Components work to a clock performing operations on a time cycle
1 Hertz (1 Hz) is one cycle per second
  Megahertz (MHz)—1 million (1,000,000) cycles per second
  Gigahertz (GHz)—1000 million (1,000,000,000) cycles per second
Speed and throughput are often different
Encoding allows more than 1 bit per cycle

## Slide 101: Data Types
Values processed by software must use a particular type
Number values versus strings
  Integers—whole numbers
  Floating-point numbers—decimal fractions
  Boolean values—a special numeric data type indicating that something is either TRUE or FALSE (with a 1 or 0)
  Characters—a character (or char) is a single textual character, and can be a letter of the alphabet, a symbol, or, indeed, a numerical character
  Strings—a collection of text characters

## Slide 102: Data Representation
Character sets—how to represent glyphs (characters) using binary values
ASCII (American Standard Code for Information Interchange)
  Limited storage means restricted to basic alphanumerics and a few symbols
Unicode
  Flexible system for representing international alphabets

## Slide 103: The Value of Data
Data as an asset
Investing in security
  Security controls are deployed to protect assets
  Return on Security Investment (ROSI) provides cost justification for security controls
  Risk assessment critical to process

## Slide 104: Security Controls
Controls come in different types and classifications
  Backup
  Access control
    Permissions
    Usage restrictions
    Data encryption
    Firewalls
  High availability

## Slide 105: Intellectual Property
Copyright ©
  Automatically granted to author
  Applies to whole works not to ideas
Trademark ™ ®
  A company’s name and logo are protected if distinctive
  Companies can apply to register their trademarks
Patent
  Legal protection for an invention or design
  Must be original, useful, and distinctive
  Must be applied for in different jurisdictions
Digital Rights Management (DRM)

## Slide 106: Data-driven Business Decisions
Driving business decisions and strategies
Production and fulfilment
  Analyze systems
  Improve productivity
Sales and marketing
  Market to individual consumers
  Develop products to anticipate trends

## Slide 107: Data Analytics
Relationship of data to information
Data is the raw values collected by the system
Information is some level of summarization of the individual data points
Insights are things that inform meaningful business decisions

## Slide 108: Facilitating Data-driven Business Decisions
Data capture and collection
Data correlation
Meaningful reporting

## Slide 109
Recognize and use different notational systems, data types, and units of measure
Compare and contrast fundamental data types and their characteristics
Discuss the importance of data and ways that a company can use it to make business decisions
Notes: Which notation system supports presenting the largest numbers using the fewest digits: Binary, Decimal, or Hexadecimal? Hexadecimal. Each hex digit can store 16 bits of information. A single decimal digit stores 4 bits while binary obviously stores 1 bit.
What is the decimal number 75 in binary and hexadecimal? 0100 1011 in binary and 4B in hex. Hex notation is often indicated using 0x to precede the hex digits, so you may see this written like 0x4b. To work out the answer without a calculator, write out the place values for each notation system. For binary you'd have columns for 64, 32, 16, 8, 4, 2, and 1 and put a 1 in each column you need to add up to 75 and a 0 in the others. For hex you only need 16 and 1 (75 divided by 16 is 4 remainder 11, which is represented as "B" in hex).
Which data type provides for whole numbers only? Integer.
What is the difference between the char and string data types? Char stores a single textual character in a fixed length field (typically 1 byte). A string is a variable length field for storing a sequence of characters.
Which data representation format can encode the widest range of characters? Unicode can represent millions of characters (glyphs). ASCII's 7-bit data structure can only support 128 characters, some of which are non-printable control characters.
What type of legal protection could be obtained for a novel software algorithm? Patent provides the best protection as it can enforce ownership even if someone tries to write the algorithm in a slightly different way. Software code is often protected both by patent and by copyright however.
What data protection technology could you implement in order to restrict the type of activity that users could employ on digital products that they have purchased or rented? Digital Rights Management (DRM).
What part of the process of data analytics is most closely supported by meaningful reporting? Insights are the "end product" of the analytic process. Humans need a suitable reporting format to make best use of insights.

## Slide 110: CompTIA IT Fundamentals+ (Exam FC0‑U61)
Module 2 / Unit 2 / Using Apps

## Slide 111
Install and uninstall software applications and configure compatibility settings
Explain the importance of software licensing and the types of license available
Describe the key features of different types of application and associated file formats

## Slide 112: Installing Applications
Applications/apps/software programs
Software installation best practices
  Compatibility with OS
  System requirements (hardware)
  Installation instructions/issues
  Licensing

## Slide 113: Installing a Desktop Application
Windows and Program Files folders
Setup programs
UAC and signed code
Advanced options

## Slide 114: Microsoft Store Apps
Run in a sandbox restricting access to rest of system
Cannot damage OS/other programs as desktop applications could
Consequently standard users can install Store apps

## Slide 115: Configuring Application Compatibility

## Slide 116: Repairing and Uninstalling Software

## Slide 117: Enabling and Disabling Windows Features

## Slide 118: Managing Software Licensing
Software licensing
  End User License Agreement (EULA)
  Single use license (product key and product ID)
  Group use/site license
  Concurrent license
  Client Access Licenses (CAL)
Registration
Subscription versus one-time purchase

## Slide 119: Shareware, Freeware, and Open Source
Shareware is software that you can install free of charge so that you can evaluate it for a limited period
Freeware is software that is available free of charge
Open source is software that also makes the program code used to design it available

## Slide 120: Productivity Software
Web browser software
Word processing
Spreadsheet
Presentation (slide show)
Visual diagramming

## Slide 121: Collaboration Software (1)
Email and Personal Information Managers
Online workspaces and document storage/sharing
Remote desktop and screen sharing software

## Slide 122: Collaboration Software (2)
Instant messaging software
Voice over IP
Video conferencing software and telepresence

## Slide 123: Business Software (1)
Desktop Publishing (DTP)
Graphic design
  Digital darkroom
  Digital paint
  Digital drawing
  3D and animation
Computer Aided Design (CAD)

## Slide 124: Business Software (2)
Project management
Accounting and commercial
Database software
Business specific/Line of Business (LoB)

## Slide 125
Install and uninstall software applications and configure compatibility settings
Explain the importance of software licensing and the types of license available
Describe the key features of different types of application and associated file formats
Notes: What compatibility information should you confirm before installing a software application? That it works with the version of Windows that you have and that your computer meets the system (hardware) requirements.
Following installation of a program written for an older version of Windows, you receive an alert that it might not have installed correctly. What feature could you use to make the program run correctly? Use the program's Compatibility tab to use settings for the older Windows version.
Why would Windows prompt you to enter a password if you try to install a software application? Installing an application requires administrator privileges and is an action protected by User Account Control. If you were logged on as an administrator already, you might have to enter the password on a domain; if you were logged on as an ordinary user, you would have to enter the administrator's user name and password.
Windows comes with web server software but it is not enabled by default. How would you install this software? Use the Turn Windows features on or off dialog from Programs and Features.
Following installation of an application, another program on your computer has stopped working. What could you do to try to fix it? Try using the Repair option in Programs and Features (if available) or re-installing the program.
Why might one of your first tasks on receiving a new computer be to remove software applications? The computer may be bundled with pre-installed software that you do not want.
In order to obtain support, the software vendor wants to know the application's product ID. How would you locate this information? Usually via the Help > About menu.
What is the difference between freeware and open source software? Open source means that the programming code used to design the software is also made available (and you must make it available in turn if you sell or distribute any part of it). Freeware means the software product costs nothing to use but this does not mean that the code is made available too or that you could modify the software and distribute it yourself.
What type of software would you use to configure a server by connecting to it over the network? Remote Desktop.
What type of software manages tasks, dependencies, and timelines? Project management software.

## Slide 126
Lab 7 / Managing Software Applications

## Slide 127: CompTIA IT Fundamentals+ (Exam FC0‑U61)
Module 2 / Unit 3 / Programming and App Development

## Slide 128
Describe programming organizational techniques and logic
Categorize types of programming languages and list the advantages and disadvantages of each type
Describe some of the main features of application code and Object-Oriented Programming
Describe the ways that an application can be deployed

## Slide 129: Programming Logic
Software development
  Programming languages
  Code
Program sequence
  Computers cannot tolerate ambiguity
  Input, processing, and output must be clearly defined

## Slide 130: Using a Flow Chart

## Slide 131: Writing Pseudocode
Move from a sequence of steps to developing blocks of code
Break steps into simple instructions
Use subroutines for repeated steps

## Slide 132: Features of Programming Code
Do not have to use the syntax of a particular programming language as some constructs are shared by all languages
Subroutines
Return (branches and loops)
Conditional statements
Variables
Functions
User interface
Comments

## Slide 133: Programming Languages
Choosing a language or development environment
  What type of program you are writing
  How experienced you are as a programmer
  What type(s) of device(s) your users will be using
Choice of programming language enforces a specific syntax
Java, Python, JavaScript, C++, C#, PHP, Perl, Ruby

## Slide 134: Compiled versus Interpreted Languages
Compiled languages
  Transformed to executable binary file
  Compiling converts programming code to machine code (binary)
  Runs quickly but platform-specific
  C++, C#, COBOL, PASCAL
Interpreted languages
  Run within an interpreter
    Interpreter within OS
    Virtual Machine (VM) running within OS
  Programming code compiled to bytecode
  Bytecode compiled to machine code by the interpreter
  Slower but allows for platform-independence (as long as interpreter is available)
  Java, JavaScript, Perl, Python

## Slide 135: Query, Assembly, and Markup Languages
Query languages
  Retrieve data from a database
  Structured Query Language (SQL)
Assembly language
  Shows machine code in human-readable text
Markup languages
  Tag documents to define structure and meaning
  HyperText Markup Language (HTML), eXtensible Markup Language (XML)

## Slide 136: Identifiers
Store values that the program can use
Variables
  Value that can change during program execution
  Usually declared as a particular data type
Constant
  Value does not change during execution

## Slide 137: Containers
Identifier referencing multiple elements
Arrays
  Store a fixed number of elements of the same data type
  Single and multidimensional arrays
Vectors
  Arrays that can grow or shrink in size

## Slide 138: Branches and Loops
Code that is linear cannot do very interesting things
Branches
  Execute parts of code based on a condition
  If…Then
Loops
  Repeat a block of code based on a condition
  For…Next
  Do While

## Slide 139: Operators
Comparison operators
  == is equal to (returns TRUE if both conditions are the same)
  != is not equal to
  < less than
  > greater than
  <= and >= less than or equal to and greater than or equal to
Logical operators
  AND—if both conditions are TRUE, then the whole statement is TRUE
  OR—if either condition is TRUE, then the whole statement is TRUE
  XOR—if either condition is TRUE but not both, then the whole statement is TRUE

## Slide 140: Procedures and Functions (and Comments)
Procedures and functions are used for blocks of code
Functions return a value
Comments
  Not executed by compiler/interpreter
  Document code
  // # ‘

## Slide 141: Object-Oriented Programming
Design code to represent “things”
The “things” interact through defined methods
Private workings versus public interfaces
Attributes
Methods
Properties

## Slide 142: Scripting Languages
Interpreted scripted general purpose languages (JavaScript, Perl)
Scripting languages used (mostly) for OS automation
Scripts are smaller than programs
Created to perform quite specific tasks
Batch files
Windows PowerShell
VBScript
Bash

## Slide 143: Application Platforms
Single-platform software
Cross-platform software
Web applications

## Slide 144: Application Delivery Methods
Local installation
  Executes on local hardware
  Stores data on local drives (or network location accessible from local computer)
  Doesn’t depend on network connection
Network installation
  Executes on server hardware
  Stores data on network server
  Requires network connection (but not Internet connection)
Cloud-hosted
  Executes on cloud
  Clients connect over Internet (typically)
  Stores data in the cloud
  Depends on cloud service availability

## Slide 145
Describe programming organizational techniques and logic
Categorize types of programming languages and list the advantages and disadvantages of each type
Describe some of the main features of application code and Object-Oriented Programming
Describe the ways that an application can be deployed
Notes: What shows the structure of code without using the specific syntax of any one language? Pseudocode.
What is an interpreted language? Interpreted languages do not need to be compiled. They run within the context of an interpreter which converts the code to machine code during runtime.
How is a markup language differ from a compiled language? Markup doesn't provide instructions for the CPU to run as such. Markup is a way of using nested tags within a document to describe its structure and contents.
What are constants and variables examples of? Programming identifiers.
What type of programming concept allows for a variable size container? A vector is a variable size container while an array is a fixed size one.
You want to check whether a condition has been met, and if it has, perform one action. Otherwise, you want your program to perform a second action. What sort of programming operation would help achieve this? A conditional branch, such as an If…Then statement.
In a program, what does a loop do? A loop performs one or more instructions until (or while) a condition is met.
What is the difference between a procedure and a function? A procedure does something while a function does something and then returns a value to the main program.
What three things define an object? Properties, attributes, and methods.
What three scripting options are commonly used in Windows 10 to perform administrative tasks? Batch files, Windows PowerShell scripts, and VBScripts.
True or false? You do not need to install a web application to your computer; it would be accessed via a browser. True.
What is the advantage of a local network hosted application, in terms of data storage? If data is stored on the server not on the local workstation, it is easier to apply access controls and to back it up.

## Slide 146
Lab 8 / Using Scripting Tools
Lab 9 / Using Programming Tools

## Slide 147: CompTIA IT Fundamentals+ (Exam FC0‑U61)
Module 2 / Unit 4 / Using Databases

## Slide 148
Describe databases and explain the purpose of a database
List the relational methods used by structured databases
List the ways that users and applications can interface with databases
Distinguish application architecture models

## Slide 149: Database Concepts
Highly structured data storage
Information is recorded in tables
  Columns (fields)
  Rows (records)

## Slide 150: Database Usage
Creation
Import/input
Storage (data persistence)
Queries
Reports

## Slide 151: Flat File Systems versus Databases
Spreadsheets and plain text—e.g. Comma Separated Value (CSV)—files
Databases define column data types and validate data entry
Databases can store and link multiple tables in a schema
Databases support many users and very high transaction (record update) rates
Databases are more scalable
Databases can use more sophisticated access controls

## Slide 152: Database Structure
Relational Database Management Systems (RDBMS)
Structured Query Language (SQL)
  Microsoft SQL Server
  Oracle Database
  MySQL
  Microsoft Office Access
Primary key and foreign key
  It is more efficient and reliable to store data in multiple tables
  The primary key is a designated table column with unique value for each record
  The foreign key is a column that references the primary key value of another table
  The definition of tables, columns, and relations is called the database schema

## Slide 153: Relational Database Example

## Slide 154: Constraints
Garbage In, Garbage Out (GIGO)
Columns (fields) are defined with a data type, which acts as a basic constraint on what can be entered
Constraints can be applied in other ways
  Uniqueness (e.g. primary key)
  Validation rules
  Cannot be left empty (blank)
  Specific format (e.g. input mask for a telephone number)
  Default value

## Slide 155: Semi-structured and Unstructured Databases
Structured relational database
  Defined tables and columns with data types
Unstructured data
  Documents, presentations, some types of spreadsheet, images,...
  User is not really constrained about what they enter
  Data can be extracted by searching and indexing the file content
Semi-structured
  Documents that contain metadata or markup that identifies the values contained

## Slide 156: Document and Key/Value Pair Databases
Document database
  Semi-structured database
  Database engine must be programmed with logic to parse (interpret) each document type
  Often use markup—XML (eXtensible Markup Language)
Key/value pair database
  Store object properties without predetermining fields and data types
  JavaScript Object Notation (JSON)
NoSQL (or Not Only SQL)

## Slide 157: Data Definition Methods
Data Definition Language (DDL) commands refer to SQL commands that add to or modify the structure of the database
CREATE
ALTER TABLE
DROP
CREATE INDEX

## Slide 158: Data Manipulation Methods
Data Manipulation Language (DML) commands allow you to insert or update records and extract information from records for viewing (a query)
INSERT INTO TableName
UPDATE TableName
DELETE FROM TableName
SELECT

## Slide 159: Permissions
Account-based access control system
Database owner
Grant rights for other accounts
GRANT permission TO user
DENY permission TO user

## Slide 160: Database Access Methods
Direct/manual access
Query/report builder
Programmatic access
User interface/utility access
Backups and data export

## Slide 161: Application Architecture Models
One-tier
  User interface (front-end) and database (back-end) hosted on same computer
Two-tier
  Client-server
  Client machine runs application and presentation (interface)
  Server machine runs database
Three-tier
  Client front-end (presentation)
  Application/business logic
  Database
N-tier
  Any multi-tier architecture
  More complex than 3-tier (access control/security layer)

## Slide 162
Describe databases and explain the purpose of a database
List the relational methods used by structured databases
List the ways that users and applications can interface with databases
Distinguish application architecture models
Notes: What are the structural elements of a database table? Each table stores information about records (rows in the table) in fields (columns in the tables).
What term is used to describe selecting and viewing information in a database? Query.
How does an RDBMS such as Microsoft SQL Server differ from Microsoft Excel when used to store a dataset? Excel is an example of a flat file system. These do not scale well, and usually support a single user only. RDBMS platforms enable many hundreds or thousands of users to connect concurrently, and can support very large datasets. Also, an RDBMS can enforce data types for each column and validate information entered as fields and records.
What language is usually used to request data from an RDBMS such as Oracle? Structured Query Language (SQL) is used to query RDBMS-based database platforms.
What is it that defines the relationship between tables in an RDBMS? Each table contains a primary key whose value is unique for each record in the table. A foreign table can use the value of a primary key as a relation, storing the value in a foreign key field.
Give an example of unstructured data. Images and text files and other document formats are unstructured data.
Give two examples of semi-structured data stores. Key/value pair databases and markup language document stores.
Is an INSERT statement an example of a definition or manipulation language statement? Manipulation language—it depends on the structure of a table (columns, data types, and constraints) being established already.
You need a development environment with a library of database functions. What type of interface are you using? Programmatic access.
How can a client-server application architecture be described if there is the potential for the structure of the application platform to be developed further? This could be described as a two-tier application. It could be re-developed as a three-tier application by specifying presentation, application, and data layers.

## Slide 163
Lab 10 / Creating and Using a Database

## Slide 164: CompTIA IT Fundamentals+ (Exam FC0‑U61)
Module 3 / Unit 1 / System Components

## Slide 165
Explain the way in which system components determine performance and how to specify an appropriate computer system
Describe the types and functions of motherboards, processors, memory, and the expansion bus
Explain the importance of a cooling system and the components used
Identify the role of PC firmware and access the firmware setup program

## Slide 166: Selecting a Computer
Key components for performance
Central Processing Unit
Memory (System RAM)
Fixed disk
  Hard Disk Drive (HDD)
  Solid State Drive (SSD)
Graphics Processing Unit (GPU)

## Slide 167: Network Interface
Wired network
  Ethernet port (RJ-45)
  Network Interface Card (NIC)
Wireless network
  Wi-Fi radio networking
  Wireless access points

## Slide 168: Motherboard Components

## Slide 169: Processors
Microprocessor/integrated circuit
Central Processing Unit (CPU) is main processor in computer
Intel versus AMD

## Slide 170: Intel and AMD CPU Brands
Core
Pentium
Celeron
Atom
Xeon
Legacy—Athlon, Phenom, Sempron, Turion, AMD FX, Opteron
Zen microarchitecture
Ryzen/Threadripper and Ryzen Mobile
Epyc

## Slide 171: ARM CPUs
ARM (Advanced RISC Machine) microarchitecture
  Widely used on smartphones and tablets
  ARM don’t make CPUs but license the designs
  Apple A, Samsung Exynos, nVIDIA Tegra
RISC stands for Reduced Instruction Set Computing
RISC microarchitectures use simple instructions processed very quickly
Complex (CISC) microarchitectures use more powerful instructions but process each one more slowly
Intel's microarchitecture is CISC with RISC enhancements (micro-ops)

## Slide 172: Features of Processors
Control unit/pipeline
Execution units
Registers

## Slide 173: Instruction Set (32- versus 64-bit)
x86 instruction set
  x86 instruction set started in 1978 with 16-bit CPUs
  First 32-bit CPU with x86-32/IA-32 released in 1985
  x86-64/x64 developed by AMD in 2003 (Intel refer to it as EM64T)
32-bit versus 64-bit CPU
  32-bit CPU can address up to 4 GB memory
  64-bit CPU can address up to 16 Exabytes (currently CPUs use a 48-bit address space (256 Terabytes)
  64-bit CPUs can run 32-bit operating systems and software
  32-bit CPUs CANNOT run 64-bit operating systems or software
Most PC/laptop CPU models are now 64-bit

## Slide 174: Clock Speed and Bus Speed
Clock speed differentiates CPU models (premium models run faster)
Front Side Bus between CPU and system memory is another important performance factor

## Slide 175: Multiprocessing and Dual-core
Symmetric Multiprocessing (SMP)
  Providing multiple CPU sockets on the motherboard
  Usually a feature of server systems
Chip Level Multiprocessing (CMP)
  Each CPU contains multiple “cores”
  Each core works as a (more-or-less) independent CPU
  2-core, 4-core, and 8-core models available

## Slide 176: System and Expansion Bus Technologies
Motherboard is a printed circuit board with buses connecting processors
  Data
  Address
  Timing
  Power
System bus (Front Side Bus) between CPU and system memory
Expansion bus (Input/Output Bus) between CPU and other processors

## Slide 177: Expansion Bus Types

## Slide 178: System Cooling
Heatsinks and thermal paste
  Passive cooling
  Transfer heat by convection
Fans
  Active cooling (powered)
  Dissipate warm air from component
  Case fans draw cool air through front vents and expel warm air through back

## Slide 179: Liquid-based Cooling Systems

## Slide 180: BIOS and UEFI System Firmware
Bootstrapping (booting)
  CPU starts and initializes other components
  Occurs before operating system loads
  Controlled by PC firmware
BIOS (Basic Input/Output System)
UEFI (Unified Extensible Firmware Interface)

## Slide 181: System Firmware Setup Program
Press a key during boot sequence—look at screen or refer to documentation
Navigate using keyboard and ESC

## Slide 182: UEFI Setup Programs

## Slide 183
Explain the way in which system components determine performance and how to specify an appropriate computer system
Describe the types and functions of motherboards, processors, memory, and the expansion bus
Explain the importance of a cooling system and the components used
Identify the role of PC firmware and access the firmware setup program
Notes: What type of component provides persistent storage? A mass storage device such as a Hard Disk Drive (HDD), Solid State Drive (SSD), or flash memory. You could also mention optical discs (CD, DVD, Blu-Ray).
What computer component is most restrictive in terms of determining upgrade potential for a desktop computer? The motherboard—it is difficult and expensive to replace.
True or false? A plug-in card is always required to support PC sound. False—sound functions are often provided by the motherboard chipset.
What is the main advantage of using a CPU in 64-bit mode? Makes more system memory accessible. A 64-bit CPU and OS is also required to run 64-bit applications, but there are not too many of these yet. 64-bit software is more reliable and a bit faster than 32-bit software.
What is a typical speed for a modern CPU to run at? Around 2 GHz; budget models might run as low as 1 GHz while the fastest run up to about 3 GHz.
You want to purchase a computer with a fast graphics interface. What type of expansion slot should you look for? PCIe x16—this is a type of PCI Express slot that uses 16 'lanes'. Each lane can transfer 250 MBps (or 500 MBps for PCIe 2 and 1 GBps for v3).
What type of component provides a passive cooling solution? A heatsink or heat spreader removes heat from the component by convection with no power required. However, it is usually necessary to cool the heatsink or heat spreader itself and this is likely to require active cooling (a fan).
How would you access the system setup program on a PC? Historically, by pressing the appropriate key during startup (ESC, DEL, F1, F2, or F10). Modern PCs often use fast boot modes that require some other means of booting to the firmware setup program.

## Slide 184
Lab 11 / Specifying PC Systems

## Slide 185: CompTIA IT Fundamentals+ (Exam FC0‑U61)
Module 3 / Unit 2 / Using Device Interfaces

## Slide 186
Distinguish peripheral, graphics, and networking interfaces and their uses
Install and configure input devices

## Slide 187: Computer Port and Connector Types

## Slide 188: Universal Serial Bus (USB)
Plug-and-Play interface
Supplies enough power for small peripherals
Versions and data rates
  1.1 – 12 Mbps
  2.0 – 480 Mbps
  3.0 – 5 Gbps
  3.1 – 10 Gbps

## Slide 189: Firewire
Similar to USB but not widely adopted on PCs
Data rate of 400 Mbps
6-pin and unpowered 4-pin connectors

## Slide 190: Graphics Devices
Video card or graphics adapter generates the signal to send to a display device (monitor)
Most motherboards have integrated adapters
High performance adapters can be fitted through an expansion card
Video card often has its own CPU (GPU or Graphics Processing Unit) and memory
Resolution and color depth
VGA (Video Graphics Array) standards
Standard 4:3 versus widescreen (16:10) resolutions
High Definition (HD) and 4K resolutions

## Slide 191: High Definition Multimedia Interface (HDMI)
Very widely used on computers and consumer electronics
Sufficient bandwidth for HD resolution (and 4K)
Mini and micro connectors also available

## Slide 192: DisplayPort and Thunderbolt
Competitor technologies to HDMI
Support for daisy-chaining monitors
Used on Apple Macs and some PCs—especially Thunderbolt 3
Thunderbolt 2
  20 Gbps over a MiniDP physical interface
Thunderbolt 3
  40 Gbps over a USB-C physical interface (with 0.5m cable)

## Slide 193: Digital Visual Interface (DVI)
Preceded HDMI as the principal display interface for PCs
DVI can support both digital and analog monitors
Single and dual-link versions
Most interfaces are DVI-I dual-link
Bulky connectors mean that this interface is rapidly falling out of favor
HDMI is backward-compatible with DVI-D using a suitable adapter cable

## Slide 194: Video Graphics Array (VGA)
Blue, 15-pin port (HD15F/DE-15)
Legacy analog interface—used principally with old Cathode Ray Tube (CRT) monitors
Some flat-panel displays and graphics adapters continue to provide VGA ports

## Slide 195: Input Devices (1)
Human Interface Devices (HID)
Keyboard
  USB/Bluetooth (or legacy PS/2)
  Layout and region
Mouse
  USB/Bluetooth (or legacy PS/2)
  Optical and laser designs (or legacy mechanical mice)
  Optional extra buttons and scroll wheel

## Slide 196: Input Devices (2)
Laptop keyboards and touchpads
  Fn switch for laptop keys
  Touchpad gesture support
Stylus pen

## Slide 197: Configuring a Mouse
Connect to an appropriate port
  PS/2
  USB
  Wireless
Install vendor driver for custom settings
Configure using Mouse applet

## Slide 198: Configuring a Keyboard
Connect to an appropriate port
Configure using Mouse applet
Set correct region/layout using Settings
Switch between multiple layouts using Notification icon (START+SPACEBAR)

## Slide 199: Configuring a Pen/Stylus

## Slide 200: Bluetooth
Personal Area Networks (PAN)
  Wireless communications enable short-range connections to peripheral and networks
Bluetooth
  Up to 10m
  3 Mbps (Bluetooth EDR)
  24 Mbps (using HS and Wi-Fi)

## Slide 201: Configuring Bluetooth
Put device into discoverable mode
Pair using passkey on both devices
Disabling Bluetooth

## Slide 202: RF and Near Field Communications (NFC)
Radio Frequency ID (RFID)
  Passive tags (typically) encoded with data
  Respond when scanned by an RFID reader
  Widely used for inventory management
Near Field Communications (NFC)
  Peer-to-peer version of RFID working at very close range (2”/6cm)
  Used on smartphones for contactless payment

## Slide 203: Networking Interfaces
Network Interface Card (NIC)
  Onboard (part of motherboard)
  Expansion cards
Ethernet connector (RJ-45)
  Patch cord with RJ-45 connectors between NIC and Ethernet switch (or wall port)

## Slide 204: Telephone Connector (RJ-11)
Smaller than RJ-45 and with fewer wires
Used for dial-up analog modems and fax modems
Also used between Digital Subscriber Line (DSL) Internet modems and telephone jack

## Slide 205
Distinguish peripheral, graphics, and networking interfaces and their uses
Install and configure input devices
Notes: True or false? Mice and keyboards must be connected to a computer via PS/2 ports. False—they are now much more likely to use USB or wireless (Bluetooth or other RF) interfaces.
True or false? USB cables have the same connectors at either end. Partly false—the connectors for the host (PC) and device use different form factors (there are also normal size and mini or micro device connectors). A new reversible Type C connector is starting to be used however.
A user has two USB drives connected to her PC. She complains that when she copies large files to both drives at the same time, it seems to take much longer. Why might this be? Bandwidth on the USB bus is shared between all devices.
You want to purchase a flat-panel monitor that can show widescreen movies. You are considering models with native resolutions of 1400x1050 and 1920x1200. Which should you choose? 1920x1200 as this is a widescreen format.
True or false? HDMI is the only type of display interface that supports High Definition picture resolutions. False—there is also DisplayPort and Thunderbolt and some DVI formats also support HD resolutions.
You are considering buying a new display device. The model you are considering accepts digital inputs only. Your computer's graphics adapter has a blue port with 15 holes. Would this flat-panel be a wise purchase? Probably not, as this connector is VGA, which supports analog output only. It is possible to buy converters however.
You need to configure settings for an input device. What should be your first step? Open the Settings app or Control Panel.
A friend is asking for your help in using her computer. When he presses the key marked @, a different symbol appears. What could be the cause? The keyboard is set to use a UK layout—you can correct this using the Language Bar.
What type of mouse would you recommend for someone who uses their computer principally to play computer games and why? Laser mouse—this registers cursor movements more quickly and accurately.

## Slide 206
Lab 12 / Configuring Input Devices

## Slide 207: CompTIA IT Fundamentals+ (Exam FC0‑U61)
Module 3 / Unit 3 / Using Peripheral Devices

## Slide 208
Use Plug-and-Play to install devices and understand the use of device drivers
Describe different display technologies and install and configure a PC display
Install and configure multimedia devices, such as sound cards, speakers, microphones, and webcams
Describe the features and capabilities of different types of printer and their associated interfaces
Install and configure a printers and scanners

## Slide 209: Installing and Uninstalling Peripherals
Plug-and-Play installation
  Windows locates and installs a device driver automatically on connection
  Hot-swappable devices do not require a system restart to connect or disconnect
Manual driver installation
  Locate driver setup program from vendor’s website and run it

## Slide 210: Devices and Printers
Post-installation configuration
Devices and Printers
Settings > Devices

## Slide 211: Removing and Uninstalling Devices
Device Manager
Completely uninstall driver
Check device properties
Scan for undetected devices

## Slide 212: IP-based Peripherals and Web Configuration

## Slide 213: Display Devices
Flat-screen displays
  Replaced analog Cathode Ray Tube (CRT) monitors
  Liquid Crystal Display (LCD)/TFT (Thin Film Transistor)
  Digital signal drives color value of each pixel
  Vendors—Viewsonic, Iiyama, Sony, Panasonic, Toshiba, LG, Acer, Sanyo, Mitsubishi
Touchscreens

## Slide 214: Digital Projectors
Presentation device to display image to an external screen or surface
Use same graphics interfaces as monitors

## Slide 215: Display Settings

## Slide 216: Screen Resolution

## Slide 217: Installing and Configuring Dual Monitors
Duplicate
Extend
  Arrange icons to ensure consistent cursor movement between screens
Project (show on one screen only)

## Slide 218: Configuring a Touchscreen
Tablet PC Settings
  Calibrate display
Pen and Touch
  Gesture settings

## Slide 219: Multimedia Ports and Devices
Audio card/sound card
Speaker and microphone jacks
  Audio in (light blue
  Microphone input (pink)
  Audio out (lime)—amplified stereo speakers/headphones
  Audio out (black)—rear speaker
  Audio out (orange)—subwoofer
  USB port (headsets)
Speaker configurations
  Stereo
  Surround sound (5.1 or 7.1)

## Slide 220: Audio Settings
Sound applet (Control Panel)
Volume control (Notification Area)

## Slide 221: Webcams
Compact video recording
Once very low quality, modern webcams are usually HD-quality at least
Can be built-in for laptops or attached using USB

## Slide 222: Printer Types
Laser printer—fuser unit and toner
Inkjet—ink cartridge and print head
Greyscale or Cyan, Magenta, Yellow, and Black (CMYK) color printing
Vendors—HP, Epson, Canon, Xerox, Brother, OKI, Konica/Minolta, Lexmark, Ricoh, Samsung

## Slide 223: Installing and Configuring a Printer
USB or Bluetooth wireless connection
Plug-and-Play installation
Manage via Devices and Printers or Settings > Devices

## Slide 224: Printer Properties and Preferences

## Slide 225: Types of Scanners
Imaging device similar to a photocopier
Flatbed form factor
Sheet fed form factor

## Slide 226: Scanning a Document
Scanners are connected using USB and Plug-and-Play
Software applications control scanner through an interface
  TWAIN (legacy)
  Windows Image Acquisition (WIA)
Output to file
  Image (JPG, TIFF)
  Portable Document Format (PDF)
  Optical Character Recognition (OCR)

## Slide 227: Digital Cameras
Portable cameras using digital imaging technology and flash memory cards for storage
Transferring images to PC
  Connect the camera to a USB port
  Use a memory card slot
  Use Wi-Fi

## Slide 228
Use Plug-and-Play to install devices and understand the use of device drivers
Describe different display technologies and install and configure a PC display
Install and configure multimedia devices, such as sound cards, speakers, microphones, and webcams
Describe the features and capabilities of different types of printer and their associated interfaces
Install and configure a printers and scanners
Notes: Which Windows interface is used for advanced management and troubleshooting of devices? Device Manager is used to update drivers and obtain more advanced troubleshooting information. The basic user interface is either Devices and Printers or the device pages in the Settings app, depending on the Windows version.
What do you need to know to connect to a device that is configured over the network? Typically the Internet Protocol (IP) address of its management page. Some devices may use a name to locate the page instead. You are also likely to be prompted for a user name and password.
True or false? If you want to configure the DPI of a display device, you would do so via the Personalization app. False—Dots Per Inch (DPI) or scaling is configured via Display properties. Personalization is for configuring themes and the appearance of the desktop.
You are configuring dual monitors positioned side-by-side. You want to increase the amount of screen space available. Which multiple display option should you set? Extend the displays.
You need to plug a microphone into a computer to make a recording. How would you identify which jack to use? The jack should be color-coded (pink). There may be an icon to represent usage though. If neither is present, check the system documentation.
What, if any, type of printer uses a fuser? Laser printer—the fuser bonds the toner to the surface of the paper using high heat and pressure.
What are the four inks used to produce color prints? Cyan, Magenta, Yellow, and Black (CMYK).
What type of wired interface is a printer MOST likely to use? Universal Serial Bus (USB).
You want to configure a printer to use both sides of the paper (duplex) by default. You have alt-clicked the printer object—which command should you select to proceed? Printing preferences.
What basic command demonstrates that a printer is connected properly to a computer and that its driver is installed correctly for Windows? Print Test Page.
What function of a scanner would you use if you want to convert a letter that someone has mailed to you into a computer-editable document? Optical Character Recognition (OCR).
True or false? If your PC does not have a flash memory card reader, you should be able to connect the camera itself to the PC over USB to copy images off the card. True—must cameras support USB connections.

## Slide 229
Lab 13 / Playing Audio
Lab 14 / Using a Printer

## Slide 230: CompTIA IT Fundamentals+ (Exam FC0‑U61)
Module 3 / Unit 4 / Using Storage Devices

## Slide 231
Contrast volatile and non-volatile storage types
Describe the types of system memory modules used in PCs
Describe the types and features of Hard Disk Drives, Solid State Drives, optical drives, and flash memory

## Slide 232: System Memory
Random Access Memory (RAM)
Volatile storage
Vendors—Kingston, Crucial (Micron), Corsair, PNY, Integral
Dynamic RAM (DRAM)
Synchronous DRAM
  64-bit transfers per clock cycle
Module packaging
  DIMMs (Dual Inline Memory Module)
  Small Outline DIMM (SO-DIMM)

## Slide 233: Double Data Rate SDRAM (DDR SDRAM)
Two 64-bit transfers per clock cycle
Subsequent iterations increase bus speed
  DDR2
  DDR3
  DDR4
Motherboard sockets must match DDR version
DIMM and SO-DIMM modules with different pin positions

## Slide 234: Hard Disk Drives (HDD)
HDD is one type of fixed disk internal persistent storage device
Magnetic platters access by a drive head
2.5” and 2.5” formats
Capacity
Performance
  Spin speed (RPM)
  Access time
  Transfer rate
Vendors—Seagate, Western Digital, Maxtor, Hitachi, Fujitsu, Toshiba, Samsung

## Slide 235: HDD Interfaces
Serial ATA (SATA) dominates internal devices (legacy drives used Parallel ATA/EIDE and SCSI)
External drives housed in an enclosure can use a number of interfaces

## Slide 236: Solid State Drives (SSD)
Non-volatile flash memory
Lighter, faster, and more reliable than mechanical HDDs
Costs falling rapidly but still very expensive above 512 GB
Large flash memory caches are also used to supplement HDDs (hybrid drives)
Can be packaged as 2.5” drive with SATA connector, PCIe adapter card, or M.2 adapter card

## Slide 237: Optical Discs and Drives
Specially formatted discs read by a laser
Multiple formats
  Compact Disc (CD)
  Digital Versatile / Video Disc (DVD)
  Blu-ray Disc (BD)
Recordable and rewritable formats

## Slide 238: Optical Drive Units
Fit to internal 5.25” drive bays and SATA interface
USB external units
Read/record/rewrite speeds

## Slide 239: Removable Flash Memory Devices
USB/thumb drive
  Up to 256 GB (at affordable prices)
Memory cards
  Multiple vendors and form factors/sizes
  Secure Digital (SD) and Compact Flash (CF)
  Typically up to 128 GB, though 2 TB cards have been made
  Multi-format memory card readers

## Slide 240
Contrast volatile and non-volatile storage types
Describe the types of system memory modules used in PCs
Describe the types and features of Hard Disk Drives, Solid State Drives, optical drives, and flash memory
Notes: You have a motherboard that is designed for DDR2 memory that works at a bus speed of 533 MHz. You have some DDR3 memory modules that also work at a bus speed of 533 MHz. Are the modules compatible with the motherboard? No—DDR3 modules cannot be used in DDR2 slots.
Why can't you use memory modules designed for a desktop computer in a laptop? Laptops use a smaller form factor called SO-DIMM while desktops use DIMMs.
A hard drive is rated at 10,000 RPM. What is the significance of this statistic? The number of revolutions per minute (RPM) is one of the basic factors determining the speed of the drive. 10,000 rpm represents good performance (15K rpm is the best available).
What type of connector would you use for an external hard drive to connect to a Windows PC? USB. Firewire, eSATA, or Thunderbird are also possible but not nearly so popular. Most drives are now USB3 or USB3.1. Note that you can plug a USB3 drive into a USB2 port, so long as you have a USB3 device cable.
Your computer has 4 SATA ports. How many hard drives can be installed? Four—each SATA port can be used to connect one drive.
True or false? A single layer Blu-ray Disc has greater capacity than a dual-layer, double-sided DVD. True—the capacity of a single layer Blu-ray disc is 25 GB compared to 17 GB for a dual-layer, double-sided DVD.
What sort of device would you need to transfer data from a "Memory Stick?" Memory card reader/multi-card reader. Do note that Memory Sticks are no longer in production so you could struggle to locate a suitable reader.
What sort of device could you use to expand the storage capacity of a smartphone? Flash memory card.

## Slide 241
Lab 15 / Adding a Removable Drive

## Slide 242: CompTIA IT Fundamentals+ (Exam FC0‑U61)
Module 3 / Unit 5 / Using File Systems

## Slide 243
Describe the properties of file systems and select an appropriate file system for a given OS and usage
Use a file manager to create, open, move/copy, and delete files and folders/directories
Use search tools and view options to locate files quickly

## Slide 244: Managing the File System
Physical disks and drives
Hard disk partitions
  Divide into logically separate storage areas
  Each partition can have different file system
  Must be at least one partition
  Active/system partition

## Slide 245: Windows Drives
Logical partitions, optical drives, and other removable drives can be assigned separate drive letters
Boot drive (usually “C:”) contains the Windows system files

## Slide 246: File Systems
Partition must be formatted with a file system before the OS can use it
File system determines compatibility with different operating systems
  FAT (File Allocation Table)
  NTFS (New Technology File System)
Windows must be installed to an NTFS partition
Optical drives
  Universal Disk Format (UDF)
  ISO 9660/CDFS
Linux and Mac file systems
  ext3 and ext4
  Hierarchical File System (HFS+) and Apple File System (APFS)

## Slide 247: File System Features
Compression
Encryption
Permissions
Journaling
Limitations
Naming rules

## Slide 248: Folders
While drives store files, folders can be used to organize those files
Create distinct logical areas with different security privileges
  Separate OS and application files from user data
  Separate user data belonging to different accounts
Partition root folder
Subfolders and file paths
  C:\
  C:\Windows
  C:\Windows\System32\

## Slide 249: Windows System Folders
Windows
  The "system root," containing drivers, logs, add-in applications, system and Registry files (notably the System32 subfolder), and so on
  System32 contains most of the applications and utilities used to manage and configure Windows
Program Files
  Subfolders for installed applications software
Users
  Storage for users' profile settings and data

## Slide 250: Linux Directories
“Folders” is Windows-specific terminology—Linux refers to “Directories”
Root folder and delimiter is forward slash /
No “drives”—different storage devices are mounted within the root file system

## Slide 251: File Explorer
Windows Explorer or just “Explorer”
Navigation pane
Quick Access and Desktop
  OneDrive
  User account
  This PC
  Libraries
  Network
  Control Panel
  Recycle Bin

## Slide 252: User Profiles and Libraries
Profile subfolders (Documents, Pictures...)
Public profile
Libraries

## Slide 253: Creating a Folder
Name must be unique at same level
Disallowed characters: \ / : * ? " < > |
Full path cannot usually exceed 260 characters
Case aware but not case sensitive (in Windows)

## Slide 254: Files
Containers for data written to disk
  Binary files
  Text files
File types and extensions
  Similar naming rules to folders
  Last part of file name (following final period) is an extension
  Extension shows file type
  Applications can be associated with different actions for file types (Open, Edit, Print, ...)

## Slide 255: Creating and Opening Files
Save/Save As command
Right-click > New
Open/Open With

## Slide 256: File Explorer Options
General
  Explorer behavior
View
  Show/hide extensions
  Show/hide system files
  ...

## Slide 257: Renaming, Copying, and Moving Files and Folders
Rename any file—do not change the extension (unless you mean to do so)
Copy and move methods
Resolving existing file conflicts

## Slide 258: Deleting Files and the Recycle Bin
Deleted files are normally kept in the Recycle Bin
Recovering files and emptying Recycle Bin
Recycle Bin properties
Erase a file using SHIFT+Delete
No recycling for flash drives or network shares (though server administrator might be able to recover)

## Slide 259: Selecting Multiple Files and Folders
Click-and-drag/SHIFT+click
CTRL+click
SHIFT+ARROW select
CTRL+ARROW+SPACEBAR select

## Slide 260: File Attributes

## Slide 261: File Properties Dialog

## Slide 262: Folder and File Permissions
Access Denied error message
Configure NTFS permissions on Security tab
Add/select account then configure permissions level
  Full control
  Modify
  Read/list/execute
  Write

## Slide 263: Searching for Folders and Files
Instant Search
Matches files, programs, apps, messages, and web pages
Press START
Use Cortana

## Slide 264: File Explorer Search
File name
File contents
By file size / date

## Slide 265: View, Group, and Filter Options
Details view – sort by column headers
Group
Filter
Arrange By

## Slide 266: File Types and Extensions
Word processing software
  txt—a text-only file with no "binary" file information linking the file to a particular software application
  rtf—Rich Text Format
  odf—the Open Document Format
  doc/docx—this format is the one used by Microsoft Word
Spreadsheet software
  xls/xlsx for Microsoft Excel
Presentation software
  ppt/pptx for Microsoft PowerPoint
PDF viewers and creators
  Portable Document Format (PDF)
  “Final” format for document distribution (printed or online)

## Slide 267: Image File Types
jpg/jpeg (Joint Pictures Expert Group)—this lossy compression format is the most widely used for photographic pictures
gif (Graphics Interchange Format)—this is an old lossless compression format
tiff (Tagged Image File Format)—this is a popular format for exchanging images between editing applications
png (Portable Network Graphics)—this is a full-color (24-bit) lossless format designed to replace GIF
bmp—this is a Windows-only lossless format

## Slide 268: Video File Types
mpg—this is an early MPEG (Motion Pictures Expert Group) standard for video files with lossy compression
mp4—the MPEG-4 standard audio/video file format
flv—another container file format designed to deliver Flash Video
wmv (Windows Media Video)—a video container file format developed by Microsoft
avi—a legacy Windows-only video format

## Slide 269: Audio File Types
mp3—developed from MPEG, this remains one of the most popular formats for distributing music
aac (Advanced Audio Coding)—developed from MPEG as a successor to mp3
m4a—this is an audio-only file format deriving from the MPEG-4 standards track
flac (Free Lossless Audio Codec)—as the name suggests, this format achieves file size compression without discarding audio data
wav—this is an early Windows audio file format

## Slide 270: Executable Files
exe—this is the basic type of program file in Windows
msi—this is a Windows Installer file used to install and uninstall software applications under Windows
app—this is the equivalent of an exe file for macOS
bat/cmd/vbs/js/ps1—contains a sequence of commands either from the operating system's command interpreter or from a scripting language supported by the OS

## Slide 271: Compression Formats
zip—this format was developed for the PKZIP utility but is now supported "natively" by Windows, Mac OS X, and Linux
tar—this was originally a UNIX format for writing to magnetic tape (tape archive) but is still used with gzip compression (tgz or .tar.gz) as a compressed file format for UNIX, Linux, and macOS
rar—this proprietary format is used by the WinRAR compression program
7z—this type of archive is created and opened using the open-source 7-Zip compression utility
gz—this type of archive is created and opened by the gzip utility, freely available for UNIX and Linux computers
iso—this is a file in one of the formats used by optical media. The main formats are ISO 9660 (used by CDs) and UDF (used by DVDs and Blu-Ray Discs).
vhd/vmdk—these are disk image file formats used with Microsoft Hyper-V and VMware virtual machines
dmg—this is a disk image file format used by Apple macOS

## Slide 272
Describe the properties of file systems and select an appropriate file system for a given OS and usage
Use a file manager to create, open, move/copy, and delete files and folders/directories
Use search tools and view options to locate files quickly
Notes: In Windows, you can access data via letter-labeled "drives." Do these correspond exactly to physical disks? Not necessarily in the case of hard disks, which can be configured with multiple partitions, each of which can be assigned a drive letter. Optical drives and flash memory cards cannot be partitioned however.
What type of file system must the partition that Windows files are installed on use? NTFS.
What default installation folders contain system and application files that should not normally be deleted or modified manually? The 'Windows' and 'Program Files' folders.
What is the file path to the Documents folder for a user named "David," assuming Windows is installed to a hard disk with a single partition using the default settings? C:\Users\David\Documents
How is a Windows library different from a folder? A library acts as a virtual folder by displaying the contents of multiple folders, which could be located on different drives.
If you have made changes to a file and want to keep both the original file and the modified version, what command should you use? Save As.
Why should you be more careful about deleting files from a USB flash drive than from the main hard drive? The files will not be recycled so there is no possibility of retrieving them if you change your mind (at least, not without using specialist data recovery software).
What view options could you use to show files of a particular type sorted by date? Group the files by file type then sort by date.
What kind of data would you expect to find in a file with a TIFF extension? This is an image file format.
What is a zip file? A file archive containing other files in a compressed format.

## Slide 273
Lab 16 / Using File Explorer

## Slide 274: CompTIA IT Fundamentals+ (Exam FC0‑U61)
Module 4 / Unit 1 / Networking Concepts

## Slide 275
Describe the components and functions of computer networks
List the protocols and technologies used for addressing on computer networks
Connect a computer to a wired or wireless network
Describe the uses of common application protocols

## Slide 276: Network Components
Clients and servers
Local Area Network (LAN)
Wide Area Network (WAN)

## Slide 277: Network Media
Nodes/hosts
Wired data connections
  Copper cabling
  Fiber optic cabling
  Ethernet
Wireless (Wi-Fi) data connections
WAN links
  Fiber optic cabling
  Point-to-point radio
  Cellular radio
  Satellite

## Slide 278: Addressing and Protocols
Standards and protocols provides
  Format for computers to exchange data over the network (frames and packets)
  Addresses to identify interfaces
Network frames and packets have headers and payload
Network media standards include Ethernet (cabled links) and Wi-Fi
Most local networks and the internet use TCP/IP and IP addressing

## Slide 279: TCP/IP and Packet Transmission
Transmission Control Protocol/Internet Protocol (TCP/IP)
Packet transmission versus circuit-based networks
  Communications broken into small packets
  Multiple paths between network nodes
  Routers choose best available path
  Lost or damaged packets can be resent

## Slide 280: TCP/IP Protocol Suite Layers (1)

## Slide 281: TCP/IP Protocol Suite Layers (2)
Link or Network Interface layer
  Ethernet/Wi-Fi
  Local network segment only
  Frames
Internet layer
  Internet Protocol (IP)—the main protocol in the TCP/IP suite is responsible for logical addressing and routing of packets between hosts and networks.
  Address Resolution Protocol (ARP)—used for hardware address resolution
  Internet Control Message Protocol (ICMP)—sends messages and reports on errors regarding packet delivery.
Transport layer
  Transport Control Protocol (TCP) provides connection-oriented delivery
  User Datagram Protocol (UDP) provides connectionless delivery
Application layer

## Slide 282: Internet Protocol (IP)

## Slide 283: IP Addresses
32-bit binary value expressed in dotted decimal
  172.30.15.12
IPv4 versus IPv6 (128-bit address)

## Slide 284: Network Prefixes and Subnet Masks
IP address contains network ID and host address
  Network ID—common to all hosts on the same IP network
  Host ID—identifies a host on a particular network or logical subnetwork
Network prefix/subnet mask is used to identify network portion within the IP address
Mask shows how many bits from the start of the address belong to the network ID

## Slide 285: Packet Delivery and Forwarding
Logical addressing (IP) versus local/hardware interface addressing
MAC Addresses
  48-bit expressed in hex
  00:60:8c:12:3a:bc
Address Resolution Protocol (ARP)
  Identifies the MAC address associated with an IP address
Routing
  If the network ID of the destination IP address is different to the source, the packet is sent to a router on the local segment (default gateway)
  Router forwards packet to its destination, possibly via intermediate routers

## Slide 286: Domain Name System (DNS)
IP and MAC addresses are very hard to remember
Simple names are much easier for people to use
Domain Name System (DNS) maps names to IP addresses
Hierarchical, distributed database
Root namespace
Top Level Domains (TLD)
  .com, .edu, .org, .gov, .ca, .uk, ...
Register domains within a TLD
Create hosts and subdomains within a domain name

## Slide 287: Hostnames and Fully Qualified Domain Names
Hostname allocated to hosts
  Up to 256 alphanumeric characters and hyphen
  Usually much shorter
Hostname + Domain Name + TLD Suffix = Fully Qualified Domain Name (FQDN)

## Slide 288: DNS Query Example

## Slide 289: Uniform Resource Locators (URL)
Protocol
  Access method/service type
  Followed by the characters ://
Host location
  IP address or (more typically) FQDN
File path
  Directory and file name location of the resource
  Delimited by forward slash

## Slide 290: Internet Application Services
Internet (IP) and transport layer (TCP/UDP) responsible for addressing and establishing connections
Application layer protocols provide “user-level” services

## Slide 291: HTTP and HTML
HyperText Transfer Protocol (HTTP)
Basis of the World Wide Web
Enables clients (typically web browsers) to request resources from an HTTP server
Web servers, intranets, and extranets
HyperText Markup Language (HTML) pages

## Slide 292: SSL/TLS
Secure Sockets Layer (SSL)/Transport Layer Security (TLS)
Establishes identity of website and protects communication between server and client using encryption
Site presents a digital certificate issued to it by a Certificate Authority (CA)
Client can choose to trust the certificate and CA

## Slide 293: Electronic Mail (Email)
Text messages and binary attachments—Multipurpose Internet Mail Extensions (MIME)
Sending mail
  Simple Mail Transfer Protocol (SMTP)
  MX (Mail Exchanger)
Retrieving messages from a mailbox
  Post Office Protocol v3 (POP3)
  Internet Message Access Protocol (IMAP)

## Slide 294: Configuring Email

## Slide 295
Describe the components and functions of computer networks
List the protocols and technologies used for addressing on computer networks
Connect a computer to a wired or wireless network
Describe the uses of common application protocols
Notes: What is a WAN? A Wide Area Network (WAN) connects sites in different geographic locations. WANs usually make use of telecommunications and service provider networks rather than being directly operated by the network administrators.
What is a packet made up of? A packet consists of a number of fields contained within a header section plus a payload. The payload could be a packet from the protocol layer above.
What are the key features of a packet switching network? Nodes within the network can perform a forwarding function, allowing a packet to utilize any available path through the network. This makes the network robust against link failures. If is beneficial for the network to use small packets that are easy to re-send.
What protocol is usually used to provide logical addressing on networks? Internet Protocol (IP).
What type of address identifies a network interface in the context of the local network segment only? A Media Access Control (MAC) address.
What type of device is used to transfer packets between different networks? A router.
Which protocol allows people to use names/labels to address network resources rather than numeric addresses? Domain Name System (DNS).
Which of the following parts of a web address is usually depends on a name resolution service: protocol type, host location, file path? The host location is usually represented by a Fully Qualified Domain Name (FQDN), such as www.comptia.org, resolved to a numeric IP address by DNS.
What does HTTP stand for? HyperText Transfer Protocol (HTTP).
Which email protocol(s) are used to download messages from a mail server? Either Post Office Protocol (POP) or Internet Message Access Protocol (IMAP).

## Slide 296: CompTIA IT Fundamentals+ (Exam FC0‑U61)
Module 4 / Unit 2 / Connecting to a Network

## Slide 297
Identify the roles of different network devices in providing local and Internet network connectivity
Distinguish the advantages and disadvantages of Internet connection types
Connect a computer to a wired or wireless network
Configure a wireless access point to use secure network settings

## Slide 298: Internet Service Types (1)
SOHO Internet router/modems
Multifunction appliances combining several networking devices
  Switch—connects four or eight computers together in an Ethernet LAN using RJ-45 network ports and twisted-pair cabling
  Access Point (AP)—creates a Wi-Fi wireless network (WLAN) between computers and mobile devices equipped with suitable adapters and also switches communications between the wired and wireless networks
  Internet router/modem—connects the wired and wireless network clients to the Internet via a WAN link

## Slide 299: Internet Service Types (2)
Digital Subscriber Line (DSL)
  Broadband over copper telephone cabling
  Router/modem interfaces with telephone network via RJ-11 port
  Asymmetric DSL (ADSL)—24 Mbps download and 1.4 Mbps upload
Fiber optic
  Fiber to the Home (FTTH)
  Fiber to the Curb (FTTC) and Very High Bit Rate DSL (VDSL)
    52 Mbps download (100 Mbps with VDSL2 at up to 100m) and 16 Mbps uplink
Cable
  Cable Access TV (CATV)/Hybrid Fiber Coax (HFC) networks
  Cable router/modem interface with network via coax F-connector
  Data Over Cable Service Interface Specification (DOCSIS)
    Up to 1.2 Gbps, though 100 Mbps is more typical of commercial packages

## Slide 300: Verifying a Connection
Network status icon
IP address configuration and Dynamic Host Configuration Protocol (DHCP)
Perform a simple test by browsing a website

## Slide 301: Microwave Satellite
Reception dish aligned with orbital satellite
Usually available, even in rural areas
High latency (packet delay)
DVB-S (Digital Video Broadcast Satellite) modem

## Slide 302: Cellular Radio
Transmitters or base stations service “cells” at up to about 5 miles (8 km)
  GSM (Global System for Mobile Communication)
  TIA/EIA IS-95 (cdmaOne)
Can provide data services as well as voice
  GPRS/EDGE (General Packet Radio Services/Enhanced Data Rates for GSM Evolution)
  Evolved High Speed Packet Access (HSPA+)
  CDMA2000/Evolution Data Optimized (EV-DO)
  Long Term Evolution (LTE)
  LTE Advanced (LTE-A)

## Slide 303: Radio Frequency
Wi-Fi networking
Open/public access points

## Slide 304: Wireless Standards and Compatibility
Wireless LAN (WLAN) Wi-Fi standard
IEEE 802.11a/b/g – legacy standards
802.11n and 802.11ac –current standards
Access points can support a mix of clients with adapters for different standards (e.g. 802.11ac AP might support 802.11g and 802.11n clients)
Compatibility modes can reduce performance though

## Slide 305: Configuring an Access Point
Connect to admin interface via IP address
Log in using admin credentials – change the password!
Configuration settings
  Service Set ID (SSID)
  Wireless mode / compatibility mode

## Slide 306: Configuring Wireless Security
Encryption
  Cipher scrambles message
  Key allows receiver to reverse cipher and unscramble message
Wireless security standards
  WEP (Wired Equivalent Privacy)
  Wi-Fi Protected Access (WPA)
  WPA2
Pre-shared key authentication (passphrase)

## Slide 307: Open Authentication and Captive Portals
Open authentication disables encryption
Used by public access points (hotspots)
May be secondary authentication via a captive portal

## Slide 308: Configuring a Wireless Client
Network status icon menu
Network location (private versus public)

## Slide 309: Speed Limitations (Attenuation and Interference)
Wi-Fi indoor range is nominally up to about 30m (100ft)
Signal attenuates at longer range
Dynamic Rate Switching/Selection (DRS) reduces data rate at range to preserve a reliable connection
Radio waves are weakened/blocked by dense material (concrete and metal)
Interference from other networks and radio sources

## Slide 310: Cabled Enterprise Network Access
Flood wired cabling and network wall ports
Enterprise-grade switches
Multiple switches and interconnections can provide thousands of ports

## Slide 311: Wireless Enterprise Network Access
Same Wi-Fi standards
Enterprise-grade access points

## Slide 312: Enterprise Network Routers
Switch ports are placed in logical groups using Virtual LANs (VLANs)
Each VLAN is assigned to an IP subnet
Communications between subnets go via a router
Routers also required for Internet access and WAN links

## Slide 313
Identify the roles of different network devices in providing local and Internet network connectivity
Distinguish the advantages and disadvantages of Internet connection types
Connect a computer to a wired or wireless network
Configure a wireless access point to use secure network settings
Notes: What device is used to connect computers together in an Ethernet network? A switch.
What is the difference between a modem and a router? A modem creates a serial link between two computers over some sort of long distance media. It operates at the data link layer. A router makes forwarding decisions between logical networks. It does not need to take account of the framing and transmission details—those are the responsibility of the modem (or of an Ethernet switch or wireless access point). It just needs to know that a particular logical network can be reached over one of its interfaces. Most SOHO devices pack all these functions into a single appliance but it is important to appreciate the differences between the functions.
Can you list at least four Internet access methods? Digital Subscriber Line (DSL), cable/Hybrid Fiber Coax, Fiber to the Curb (FTTC), satellite, and cellular radio.
What is the latest Wi-Fi standard and which frequency band(s) does it use? IEEE 802.11ac works in the 5 GHz band. Most 802.11ac access points do have 2.4 GHz radios but they use them to support legacy standards.
What information do you need to configure a wireless connection manually? Service Set ID (SSID)/network name, encryption type, and authentication information (a preshared key if not using enterprise authentication).
What is the risk of using a free Wi-Fi network to make an order from an online shop? Data on an open network may be intercepted by the person running the network or by other computers connected to the network. You need to ensure that the online store uses a secure (HTTPS) connection.
What does attenuation mean? Attenuation describes the loss of strength of a signal the farther it has to travel. Attenuation sets the distance limitations on different network media types.

## Slide 314
Lab 17 / Network Settings

## Slide 315: CompTIA IT Fundamentals+ (Exam FC0‑U61)
Module 4 / Unit 3 / Secure Web Browsing

## Slide 316
Explain risks of using open Internet access methods
Describe safe browsing practices and configure browser security/privacy features
Identify the use and basic configuration parameters of a firewall

## Slide 317: Using Free / Open Networks
Open access points allow consumers to access the internet
  Many run by telecoms companies
  Data sent over open Wi-Fi is not secure
  Email password details may be transmitted
  Email and web services must be protected by SSL connections
Public access workstations allow internet access
  Provided in libraries, internet cafes, and so on
  Be aware that workstations could be infected with malware
  Clear the browser cache when finished and do not allow saving of passwords

## Slide 318: Malware Threats
Types of malware
  Viruses and worms
  Trojan Horse
  Adware
  Spyware
Use up-to-date browser versions
Install security patches when they are released

## Slide 319: Spyware and Adware Symptoms
Malware spread with criminal intent is likely to try to remain hidden
Pop-up windows, new browser toolbars, change of search provider
Unexpected redirection
Banner ads and “fake anti-virus”

## Slide 320: Choosing a Compatible Browser
Browser versions can vary quite widely from agreed standards
Some websites and web applications are designed for specific browsers
May need to run more than one browser

## Slide 321: Active Content Types
Scripting
Add-ons
Flash/Silverlight
Java

## Slide 322: Disabling Client-side Scripting
Server-side versus client-side scripting
Most websites depend heavily on client-side scripting
Some browsers don’t support disabling scripting
Script blockers might be available

## Slide 323: Managing Add-ons
Types of add-ons
  Extensions
  Plug-ins
  Themes
Use browser-vendor repositories
Digitally-signed code is more likely to be trustworthy

## Slide 324: Cookies
Text file storing session information
Other browser metadata
Personally Identifiable Information (PII)
Cookie types
  First-party cookies
  Third-party cookies
Privacy and security issues
  What information is a site capturing?
  Cookies cannot install malware but may be read by malware that has infected the computer
  Cookies can be used to track browsing history
  Some cookies may not expire correctly
  The site designer should use encrypted cookies to mitigate these issues

## Slide 325: Pop-up Windows
Any window that a site creates
Might be generated from a script or by clicking a link
Similar effect from Cascading Style Sheets (CSS)
“Spawning” pop-ups indicate malware infection

## Slide 326: Controlling Cookies and Pop-ups
Browser settings on whether to accept cookie types
  First- versus third-party
  Block for certain domains
Built-in pop-up blockers
Ad-blocking add-ons

## Slide 327: Disabling AutoFill and Clearing Browser Cache
Browser records history of pages you visit
Can store passwords and information you type into forms
Information should be protected by your OS account credentials
Can delete any of it using browser settings
Private/incognito mode disables this storage—does not mean that sites cannot track you (via information your browser sends over HTTP anyway)

## Slide 328: Digital Certificates
Digital certificate proves identity of server and enables encryption
Asymmetric encryption over HTTPS
  Public key provided in digital certificate encrypts message—once encrypted the public key cannot decrypt the message
  Private key stored securely on HTTPS server is used to decrypt the message
Server identity is guaranteed by the issuing Certificate Authority (CA)
Public Key Infrastructure (PKI)
Browser must trust CA’s root certificate

## Slide 329: Valid and Invalid Certificates
Domain name highlighted—be wary of misspelled domains and misleading subdomains/hostnames
Padlock icon
Green certificate indicates Extended Validation
Site with untrusted or invalid certificate will be blocked by browser
Only proceed if you can guarantee the site is valid by other means

## Slide 330: Types of Firewall
Packet filtering—IP address and application TCP/UDP port number
Stateful inspection—analyze connections and possibly application-layer information
Firewall appliances versus software firewalls (installed under host OS)
Network firewalls versus host/personal firewalls

## Slide 331: Configuring the Windows Defender Firewall
Only run one host/personal firewall
Firewall settings and network locations
Allow apps and features to accept connections

## Slide 332: Configuring Proxy Settings
Enterprises use “border” network firewalls to monitor all incoming and outgoing traffic
Network firewalls might be implemented as proxy servers—client browsers must connect to the Internet via the proxy
Transparent proxies work without configuration
Other proxies have to be configured in browser settings—IP address and port of the proxy server service

## Slide 333
Explain risks of using open Internet access methods
Describe safe browsing practices and configure browser security/privacy features
Identify the use and basic configuration parameters of a firewall
Notes: If you use an open network, what email configuration setting should you ensure is enabled? Enable Secure Sockets Layer/Transport Layer Security (SSL/TLS) encryption to protect the account password.
You have installed a screensaver application. Later, after updating your anti-virus software, a malicious program is found. This appears to have infected your system at the same time as the screensaver was installed. What class of malware is this? Trojan Horse.
You want to use a website that hosts training modules in a custom media format. What type of add-on would you need to install to play this media? You would need to install a type of browser add-on called a plug-in. Plug-ins should be restricted to interacting with the media object on the web page.
What type of file might a website use to track whether you have visited it before? Cookie.
True or false? Browser pop-up windows are definite symptoms of virus infection. False—these could be a result of adware or part of the design of a particular site (admittedly, not a site you'd want to visit often).
You are using a computer in an Internet cafe. What should you do at the end of the session? Clear the browser cache or use the workstation's browser private/incognito browsing mode.
What identifies a website as using the secure HTTPS protocol with a valid certificate? The URL shows the "https://" protocol and the browser shows a padlock icon. For sites that have passed special validation regimes, the address bar will be shown in green. If a site uses https but the certificate is not trusted by the browser, an alert is displayed.
You want to restrict access to a computer on your network to a single Internet host running a particular application. What two things do you need to configure in your firewall's access control list? The IP address of the host and the port number of the application.

## Slide 334
Lab 18 / Web Security

## Slide 335: CompTIA IT Fundamentals+ (Exam FC0‑U61)
Module 4 / Unit 4 / Using Shared Storage

## Slide 336
List ways to share files and storage on a local network
Describe means of sharing files and services on the Internet
Explain the importance of backups and configure simple backup options

## Slide 337: File Server (Direct Attached Storage)
Any drive or folder attached to the computer can be shared on the network
Fixed disks and removable drives can be shared
The host computer must be turned on and the drive remain attached for the share to work

## Slide 338: Network Attached Storage (NAS)
Server appliance dedicated to file sharing
Can be configured with multiple disks
Supports multiple file sharing protocols
Connected to the network and allocated an IP address (and possibly a hostname)

## Slide 339: Network Printer Sharing
Share the printer via Windows
  Share any locally installed printer
  Printer can be connected to Windows host by USB, Bluetooth, Ethernet, or Wi-Fi
  Windows host must be switched on for share to be accessible
Use a hardware print server
  Network-enabled printers support direct connections to clients
  Could also connect printer to NAS server or Internet router/modem

## Slide 340: Joining a Workgroup or Domain
Windows provides all the client and server software required for file sharing
Workgroups versus domains

## Slide 341: File and Printer Sharing (1)
Share any folder via shortcut menu or folder properties
In a workgroup, each computer must be separately configured with the same user accounts

## Slide 342: File and Printer Sharing (2)
Configure advanced settings to allow anonymous access—no security

## Slide 343: Browsing Network Shares and Drives (1)
View computers, printers, routers (network infrastructure), and other devices via the Network object
UNC (Universal Naming Convention) paths

## Slide 344: Browsing Network Shares and Drives (2)
Map a shared folder as a local drive

## Slide 345: Hosted Sharing and Storage
HTTP/HTTPS and file downloads
  Upload files to a web server
  Clients can download using a link or URL over HTTP/HTTPS
  Website can require authentication if necessary
File Transfer Protocol (FTP)
  More efficient than HTTP/HTTPS
  Most browsers support basic FTP functionality but a dedicated FTP client is usually preferable
  More secure to use encrypted types of FTP

## Slide 346: Cloud Computing
Cloud computing versus hosted storage
  Pay-per-use (metered service)
  Rapid elasticity/scalability
Cloud depends on resource pooling and virtualization
  Less visibility and control about where your data is actually stored compared to hosted solutions

## Slide 347: Cloud-based Storage
Vendors—Apple, Google, Microsoft, DropBox, Amazon
Access via a browser or client app
OneDrive can be integrated with File Explorer

## Slide 348: Cloud-based Collaborative Applications
Provide apps and collaboration features as well as basic storage
Vendors—Microsoft Office 365, Google G Suite, Smartsheet

## Slide 349: Peer-to-Peer File Sharing
Files are uploaded to a network of peers
Each peer hosts fragments of files

## Slide 350: Backups
Data files backup
System configuration backup
Backup considerations
  On-site versus off-site
  Backup media security
  Point-in-time backups
  Backup schedule

## Slide 351: Backup Storage Types
Locally attached storage
Network Attached Storage
Offsite/cloud-based
Use multiple methods for comprehensive backup
  Local storage for regular point-in-time backups
  Cloud storage for periodic off-site backups

## Slide 352: File Backups and Critical Data
Selection of drives/folders/files to include in backup jobs
Where is critical data stored?
Do the locations selected cover all critical files?

## Slide 353: Database Backups
File copy methods are not sufficient to back up databases (in most cases)
Database must preserve integrity by tracking operations as transactions
Replication copies completed transactions between master and replica servers
Point-in-time backups must still be made to recover from errors (transaction rollback)
Snapshot backups can be used for “last ditch” recovery and for logging/auditing changes

## Slide 354: OS Backups
Restore a host without having to manually reinstall operating system and applications software
Recover from file corruption, faulty disk storage, malware infection,...
Bare metal/image-based backup
Keep OS and data backups as separate jobs—use well-defined areas for user data storage

## Slide 355: Windows Backup
Backup and Restore (Windows 7)
  Enables you to perform selective, scheduled, and ad-hoc backups
File History (Windows 8 and Windows 10)
  As files are modified, the versions are tracked and backed up automatically

## Slide 356: Scheduling and Frequency
Scheduling and frequency require careful consideration
  What are the recovery scenarios? When might we need to recover a file?
  How much backup storage capacity is there?
  How long do backups take to complete? Do they interfere with normal operations?
  How can offsite backups be facilitated?

## Slide 357: Restoring Data and Verifying Backups
Error detection
  Do backups complete successfully?
Configuration
  Is all critical data being backed up?
Test restore

## Slide 358
List ways to share files and storage on a local network
Describe means of sharing files and services on the Internet
Explain the importance of backups and configure simple backup options
Notes: True or false? A hard disk connected to a computer via a USB port could be described as "Direct Attached Storage." True.
What type of connection would a NAS device use? Network Attached Storage (NAS) means using either a cabled (Ethernet) or Wi-Fi link to the network.
Which admin tool or screen would you use to configure a Windows computer to join a domain? Via the System applet in Control Panel or via the Settings app (Access work or school).
True or false? Any version or edition of Windows can be used to share files with other users. True—non-server editions are restricted in the number of simultaneous clients though.
How could you access a network folder called DATA on a network server called TOWER1 using the Explorer address bar? By entering the UNC path: \\TOWER1\DATA
What is a mapped drive? A folder shared by a network server that the client connects to via a drive letter that redirects to the network share name (\\Server\Folder).
What protocol would be used to provide encrypted file downloads from a web server? HTTPS—HyperText Transfer Protocol with Secure Sockets Layer/Transport Layer Security (SSL/TLS).
You have made a backup of system data using a removable hard disk. What should you do next? Store the disk in a secure location—preferably in a different place to the PC.

## Slide 359
Lab 19 / File Sharing

## Slide 360: CompTIA IT Fundamentals+ (Exam FC0‑U61)
Module 4 / Unit 5 / Using Mobile Devices

## Slide 361
Identify the key features of different types of mobile devices and mobile operating systems
Configure network, email, and data transfer settings on mobile devices

## Slide 362: Using a Mobile Device
Gesture-based interaction
Kinetics and screen orientation
Speech recognition and hands free

## Slide 363: Passcode Locks
Protect information stored on the device with a screen lock
Authenticate with PIN or pattern code or biometric (fingerprint scanner)
Lockout policy
Remote wiping of data and settings

## Slide 364: Full Device Encryption
iOS
  Device is encrypted by one level of encryption by default but key is stored locally—facilitates fast remote wipe by deleting the key
  Attacker could “jailbreak” device if not wiped and obtain data
  Data protection option can securely encrypt user data via passcode-derived key
Android
  Full disk encryption is available but not enabled by default

## Slide 365: Mobile Applications and App Stores
Apps are platform-specific
Software Development Kit (SDK)
  For iOS apps, a macOS development workstation is required
  For Android apps, developer tools can be installed under Windows, Linux, or macOS
Stores
  iOS restricted to Apple’s store
  Android supports third-party stores and download sites (if enabled)
Sandbox
  Apps request certain permissions to access device features (dialer, contacts, camera, microphone, ...)

## Slide 366: Network Connectivity
Mobile data access
Wi-Fi
Airplane mode

## Slide 367: Email Configuration
Most email accounts can auto-configure themselves
Manual configuration
  Incoming mail server will either be an Internet Message Access Protocol (IMAP) or a Post Office Protocol (POP) server
  Outgoing mail server will be a Simple Mail Transfer Protocol (SMTP) server
  Enable SSL/TLS—very risky to use email if provider does not support a secure connection

## Slide 368: Synchronization and Data Transfer
iTunes for iOS devices
Gmail services for Android
USB connection with Windows
  Picture Transfer Protocol (PTP)
  Media Transfer Protocol (MTP)

## Slide 369: Remote Backup
Cloud-based backup and linked storage solutions
Apple iCloud
Google Cloud
Microsoft OneDrive
Dropbox

## Slide 370
Identify the key features of different types of mobile devices and mobile operating systems
Configure network, email, and data transfer settings on mobile devices
Notes: What type of gesture is typically used for zooming on a touchscreen? Pinch.
What is the purpose of an accelerometer, as fitted in a mobile device? It is one of the components that detects how the user is moving the device around. This is used to set the screen orientation and as an advanced control mechanism.
What feature allows data to be removed from a device if is lost or stolen? This is referred to as remote wipe or sometimes as a kill switch.
True or false? A smartphone cannot join a Wi-Fi network if the SSID is not being broadcast. False—the SSID (or network name) can be entered manually, as with a computer.
What is "airplane mode?" A quick toggle for disabling all wireless functionality (cellular, Wi-Fi, and Bluetooth).

## Slide 371: CompTIA IT Fundamentals+ (Exam FC0‑U61)
Module 5 / Unit 1 / Security Concerns

## Slide 372
Distinguish threats to the confidentiality, integrity, and availability of information processing systems
Identify social engineering techniques
Describe the importance of business continuity and how to make systems fault tolerant
Explain the importance of disaster recovery plans

## Slide 373: Computer Security Basics
Controlling access to resources
Balance security with accessibility
Properties of secure information—“CIA Triad”
  Confidentiality
  Integrity
  Availability
Security threats

## Slide 374: Confidentiality Concerns
Snooping
Eavesdropping/wiretapping/sniffing
Social engineering/dumpster diving

## Slide 375: Integrity Concerns
Man-in-the-Middle (MitM)
Replay
Impersonation

## Slide 376: Availability Concerns
Denial of Service (DoS)
Power outage
Hardware failure
Destruction
Service outage

## Slide 377: Authorization, Authentication, and Auditing
Access control system
Authentication
  Prove that a user is who they say they are
  Associate that person with a unique computer or network user account
Authorization
  Create barriers around the resource such that only authenticated users can gain access
  Resource permissions lists
Accounting
  Recording when and by whom a resource was accessed

## Slide 378: Social Engineering
Getting people to reveal confidential information
Attackers often build access with piecemeal steps
Any information about a company can be helpful in making social engineering attacks more likely to succeed

## Slide 379: Impersonation, Trust, and Dumpster Diving
Gain access by pretending to be someone else
  Intimidate through false rank or spurious technical jargon
  Exploit trust - coax and persuade
Building trust is easier if you have information that will convince your target (or put them off-guard)
  Department employee lists, job titles, phone numbers, diary, invoices, or purchase orders
“Dumpster diving” for discarded company information

## Slide 380: Identity Fraud and Shoulder Surfing
Identity fraud
  Masquerade as someone else
  Control accounts that are supposed to be operated by someone else
  Exploit stolen Personally Identifiable Information (PII)
“Shoulder surfing” to observe credentials

## Slide 381: Defeating Social Engineering Attacks
Training and education
Security policies
  Proper support procedures
  Account and device protection—e.g. using screen locks to prevent “lunchtime attacks”
  Identity badges, escorted visitors, and secure doors

## Slide 382: Business Continuity and Fault Tolerance
Outages cost—financially and reputational damage
Business continuity plans minimize outages or the effect of outages
Fault tolerance
  Design systems without single points of failure
  Develop contingency plans to cope with failures
  Provision redundant components and systems to allow failover

## Slide 383: Data Redundancy
Redundant Array of Independent Disks (RAID)
Configurations to allow the storage system to tolerate individual disk unit failures
  RAID 1—disk mirroring
  RAID 5—striping with parity
RAID cannot replace the need for backups

## Slide 384: Network Redundancy
Multiple adapter cards/ports for individual host
  Also allows load balancing
Multiple network paths between nodes
Routers can detect failed links and choose alternative paths

## Slide 385: Power Redundancy
Dual power supplies
Redundant circuits
Uninterruptible Power Supply (UPS)
Backup power generator

## Slide 386: Site Redundancy and Replication
Providing redundancy at the site level
Replication can be used to synchronize data between multiple sites

## Slide 387: Disaster Recovery
Plans for specific scenarios rather than overall business continuity
  Workflows and resources
  Wide range of possible major and minor scenarios
Prioritization
Data restoration
Restoring access

## Slide 388
Distinguish threats to the confidentiality, integrity, and availability of information processing systems
Identify social engineering techniques
Describe the importance of business continuity and how to make systems fault tolerant
Explain the importance of disaster recovery plans
Notes: Which property of secure information is compromised by snooping? Confidentiality—keeping information disclosure restricted to authorized persons only.
An attacker has used a rogue access point to intercept traffic passing between wireless clients and the wired network segment. What type of attack is this? This is typical of a Man-in-the-Middle (MitM) attack.
What type of access mechanism is MOST vulnerable to a replay attack? Use of a token generated by software. If the token is not authenticated properly by the server, it could be vulnerable to replay, where someone else obtaining the token can masquerade as the original user.
Which specific attack uses a botnet to threaten availability? Distributed Denial of Service (DDoS).
In considering availability concerns, what use might a lockable faceplate on a server-class computer be? It may prevent the user switching the machine on or off (useful for servers) or accessing removable drives and ports.
What does AAA stand for? Authentication, Authorization, Accounting.
Why should a security policy instruct users not to reveal their password to technical support staff? It exposes users to social engineering attacks to gather login credentials for malicious use. Any request for a password should be treated by users as suspicious.
How might someone masquerade as someone else when using email or Instant Messaging? By accessing their user account—this could be done by stealing their login information, using an unattended computer that was still logged in, or using malware such as a Trojan.
What are the three main areas where redundancy should be provisioned? Data/storage (RAID), network links, and power. You might additionally mention site-level redundancy, though this is very expensive to provision.
Why is prioritization a critical task for disaster recovery? Services may have dependencies that make restoring them in the wrong order futile. Also, disasters lead to scarce resources so the most critical services must be given priority. These should be identified before the disaster occurs so that staff working to recover systems are properly guided.

## Slide 389: CompTIA IT Fundamentals+ (Exam FC0‑U61)
Module 5 / Unit 2 / Using Best Practices

## Slide 390
Describe basic principles for hardening computer systems against attack
Distinguish types of malware and use anti-malware software
Identify spam and phishing threats
Install software patches and updates from secure sources

## Slide 391: Securing Devices
Device “hardening”
Anti-virus/anti-malware
Patching/updates
Enabling passwords
Default/weak passwords
Disabling unused features
Removing unwanted/unnecessary software

## Slide 392: Computer Viruses
Infection vector
  Program viruses
  Macro viruses
  Worms
Payload
Delivery
  Email attachments
  AutoRun media
  Application exploits (drive-by download)

## Slide 393: Other Types of Malware
Trojans
Spyware
Ransomware

## Slide 394: Operating System Vulnerabilities
Most malware infects computers by tricking users into running it
Malware can also exploit software vulnerabilities to execute without user intervention
Vulnerabilities could also be exploited to crash a host or process
Patch management ensures that software is protected against exploits for known vulnerabilities

## Slide 395: Preventing Malware Infections
Risks
  Unsafe websites
  Unsolicited email
  Other infected hosts
  Uncontrolled file execution
  Zero-day exploits
Reducing exposure
  Back up data
  Apply patches and updates
  Install and update security software
  Scan files on-access
  Limit administrative privileges
  Control file execution

## Slide 396: Anti-virus Software
Software that detects and blocks malware
  Identify known malware using signatures (definitions)
  Identify malware-like behaviour in a process using heuristics (behaviour analysis)
Personal software and enterprise suites
Vendors—Symantec (including the Norton brand), McAfee, Avast/AVG, Trend Micro, Sophos, Kaspersky, ESET, BitDefender

## Slide 397: On-access and Scheduled Scanning
On-access reduces dependence on user to remember to scan file before opening
Products should scan file system and memory
Configure exceptions for files that might cause performance problems if scanned
Scheduled scans can be run in the background or during user downtime to ensure protection

## Slide 398: Quarantining and Remediating
Anti-virus software will usually block access to suspect files
Might support option to remove/clean/disinfect file
Persistent malware requires manual removal

## Slide 399: Windows Defender

## Slide 400: Spam
Unsolicited email
Identify potentially hazardous content
  Hyperlinks
  Attachments

## Slide 401: Phishing
Email messages that try to trick the recipient into visiting a fake website to steal their credentials
Attacker may have knowledge of which sites the victim uses (targeted attack) or just send mass mails
Could also use pop-ups on web pages
Pharming refers to attacks that redirect traffic, possibly by corrupting DNS resolution

## Slide 402: Anti-spam
Junk email filtering
  Move messages automatically to a “Junk” folder
  Disable links and formatting to reveal the true message contents
  Block file attachments
Instant Messaging/VoIP authentication and identity proofing

## Slide 403: Software Sources
Obtain software and driver installation files from legitimate sources
  Vendor app stores
  Merchant app stores
  Authorized resellers, Original Equipment Manufacturer (OEM) vendors, and managed service providers
Abandonware
Signed code

## Slide 404: Patch Management
Patches contain updates for system or application files
Fix bugs or security problems (vulnerabilities / exploits)
Service Packs

## Slide 405: Windows Update
Identifies and installs updates automatically over the web
Configure scheduling

## Slide 406: Windows Update Scheduling and Frequency
Quality updates installed regularly (daily)
Feature updates introduce new functionality
Servicing channels allow more control for update testing
  Windows Insider Program
  Semi-annual channel (targeted)
  Semi-annual channel
  Long term servicing channel

## Slide 407: Other Updates
Application updates
Anti-virus updates
Driver updates

## Slide 408
Describe basic principles for hardening computer systems against attack
Distinguish types of malware and use anti-malware software
Identify spam and phishing threats
Install software patches and updates from secure sources
Notes: Part of host hardening is to reduce the attack surface. What configuration changes does reducing the attack surface involve? Removing unwanted and unnecessary software, disabling unused OS features and services, and closing unnecessary network ports. This reduces the ways other hosts or processes can interact with the hardened host.
What is the main difference between virus and worm malware? A virus has to infect a file whereas a worm propagates in memory and over computer networks.
How might malware hosted on a website be able to infect your computer simply by your browsing the site? By exploiting a vulnerability in software installed on your computer (a fault or "exploit" in the browser, a browser plug-in, or the OS for instance).
How might spyware be able to steal a password? Typically by monitoring key strokes (a key logger). It might also be able to steal password databases and decrypt them.
What type of malware is being described? The malware encrypts the user's documents folder and any attached removable disks then extorts the user for money to release the encryption key. Ransomware.
True or false? Most anti-virus software can remediate a system by blocking access to an infected file but not actually deleting it. True—this is called quarantining the file.
What is the main means by which anti-virus software identifies infected files? Using definitions or signatures of known virus code. These definitions must be kept up-to-date.
What are the two main ways that spam might expose recipients to hazardous content? Through malware-infected attachments and through links to malicious websites.
Your friend sent you an email link, which you have opened, and now the browser is asking whether you should install a plug-in to view all the content on the page. Should you proceed? No—this is a classic phishing attack and your friend's computer could be infected with a virus or Trojan. Check whether they sent the link in good faith first.
True or false? An OEM site is a reputable source of management software and drivers for a particular system. True—an Original Equipment Manufacturer (OEM) in the IT industry, such as Dell or HP, assembles systems made from the parts and software of various other suppliers. The components used in their systems may be specific to their brand and so they host their own support files for any system they sell.

## Slide 409
Lab 20 / Using Windows Defender and Windows Update

## Slide 410: CompTIA IT Fundamentals+ (Exam FC0‑U61)
Module 5 / Unit 3 / Using Access Controls

## Slide 411
Distinguish between identification, authentication, authorization, and accounting in access control systems
Identify different authentication factors and understand their use in providing strong authentication
List best practices when choosing passwords
Explain how encryption technologies are used for authentication and access control

## Slide 412: Access Controls
Access control system
  Subjects and objects
  Access Control List (ACL)
Identification—creating an account or ID that identifies the user or process on the computer system
Authentication—proving that a subject is who or what it claims to be when it attempts to access the resource
Authorization—determining what rights or permissions subjects should have on each resource and enforcing those rights
Accounting—tracking authorized and unauthorized usage of a resource or use of rights by a subject

## Slide 413: Least Privilege and Implicit Deny
Least privilege
  Assign as few rights and permission as possible
Implicit deny
  Access controls should deny access by default

## Slide 414: Authorization Access Models
Discretionary Access Control (DAC)
  Based on ownership
  Owner is granted full control over the resource, meaning that he or she can modify its ACL to grant rights to others
Role-based Access Control (RBAC)
  A set of organizational roles are defined and users allocated to those roles
Mandatory Access Control (MAC)
  Based on the idea of security clearance levels and labels
  Subjects are only permitted to access objects at their own clearance level or below
Rule-based access control
  Any sort of access control model where access control policies are determined by system-enforced rules rather than system users

## Slide 415: Accounting and Non-repudiation
Accounting
  Audit trail of how rights have been exercised
  Backed by system of logging
Non-repudiation
  Principle that a user cannot deny having done something
  Video
  Biometrics
  Signature
  Receipt

## Slide 416: User Account Types
Ensures that the identity of someone using a computer is validated by the operating system at log on
Mandatory logon
Windows default accounts
  Administrator—in modern Windows versions, disabled in favor of the user created during setup
  Guest—disabled by default in modern Windows versions
  A user account created during setup (becomes an administrator)
Additional user accounts should be configured as standard users, unless there are very good reasons for creating more administrators

## Slide 417: Group Accounts
Most user accounts get their privileges from membership of group accounts
A user account can be a member of multiple group accounts
Windows default group accounts
  Administrators—user accounts belonging to this group have complete control over the computer
  Standard users—this group allows use of Microsoft Store apps and basic configuration of display and input settings, but tasks such as installing software, configuring hardware, or changing system properties are restricted

## Slide 418: Something You Know Authentication
Authentication factors—methods of submitting user credentials
Something You Know
  Password/passphrase
  Personal Identification Number (PIN)
  Pattern lock
  Personally Identifiable Information (PII) and security questions

## Slide 419: Something You Have Authentication
Hardware tokens
  Smart card or key fob with digital certificate issued to user
  One-time password token generators
Software tokens
  Stored on a computer or smartphone rather than a dedicated security device
  Cookie

## Slide 420: Something You Are Authentication
Biometric recognition systems
Template scan
  Fingerprint
  Iris
  Retina
  Facial features
Confirmation scan
Privacy considerations
False positives and false negatives

## Slide 421: Somewhere You Are Authentication
Geographic location determined by location services
  Global Positioning System (GPS)
  Indoor Positioning System (IPS)
  GeoIP
Logical location
  Subnet or IP address range (or not on an excluded IP address list)
Continuous authentication and access controls

## Slide 422: Multifactor and Two-factor Authentication
Requiring credentials from a combination of factors is stronger than single-factor
Must be different factors

## Slide 423: Single Sign-On
Authenticate once to access multiple services
Kerberos authentication to Windows domains
Microsoft account PC sign-in gives access to cloud services too

## Slide 424: Uses of Encryption
Protect information even if it is stolen - thief must possess the information and the encryption key
Send data across a public network or channel while protecting confidentiality
Authenticate sender and receiver to one another
  Plain text (or clear text)—this is an unencrypted message.
  Cipher text—an encrypted message.
  Cipher—this is the process (or algorithm) used to encrypt and decrypt a message.
Cryptographic hashing, symmetric encryption, asymmetric encryption

## Slide 425: Symmetric Encryption
Uses the same secret key for encrypting and decrypting
Fast but difficult to distribute the key securely
Used to encode data for storage and network transmission
Ciphers—3DES, AES, RC (Rivest Cipher), IDEA, Blowfish/Twofish, CAST
Key size

## Slide 426: Asymmetric Encryption
Uses a key pair (public and private)
  Sender can tell recipients the public key—no need to keep this secret
  Recipients can use public key to encrypt a message but NOT to decrypt it again
  Only the sender can decrypt the message (using the linked private key)
Only works well on small amounts of data but solves the problem of key distribution
Use asymmetric encryption to encrypt a symmetric secret key and use the symmetric key to encode the larger message
Only the recipient can decrypt the secret key and therefore the message

## Slide 427: Public Key Infrastructure (PKI)
System for authenticating subjects—users and computers—on public networks
Subjects are issued digital certificates by Certificate Authorities (CA), which are responsible for verifying the identity of the subject
Digital certificate contains the subject’s public key
If client trusts the CA—by installing its root certificate—it can trust the subject’s digital certificate
Can also be used for smart card authentication
Most asymmetric encryption is based on the RSA cipher

## Slide 428: Digital Signatures
Digital certificates are used for authentication and confidentiality
Digital signatures are used for authentication and integrity
The private key is used to encrypt a signature while the public key is used to decrypt it

## Slide 429: Cryptographic Hashes
Hashing creates a fixed length string from a variable amount of data
Cryptographic hash functions are designed with the following properties
  It is not possible to recover any information about the original data from the hash
  No two data inputs create the same hash value (a collision)
Sender creates a cryptographic hash of a message and encrypts the hash with an asymmetric encryption private key—this is attached to the message as a digital signature
Recipient can use the public key to decrypt the signature and validate the hash by performing their own hash—should prove that the recipient created the message and that it has not been changed in transit
Also used for secure password storage
SHA-1 and SHA-2 (Secure Hash Algorithm) and MD5 (Message Digest) ciphers

## Slide 430: Data States and VPNs
Data at rest
  Data in some sort of persistent storage media
  Encrypt using techniques such as whole disk encryption, mobile device encryption, database encryption, and file- or folder-level encryption
Data in transit (or data in motion)
  Data is transmitted over a network
  Data can be protected by a transport encryption protocol, such as Secure Sockets Layer (SSL)/Transport Layer Security (TLS)
Virtual Private Networks (VPN)

## Slide 431: Password Cracking
Intercept network traffic to “sniff” passwords
Obtain password databases or files
Use cracking software to decrypt password hashes
  Dictionary approach
  Brute force approach

## Slide 432: Password Best Practices
Use long passwords
Use complexity (entropy)
  No dictionary words
  Mix alphanumeric and symbol characters
Use a phrase that is easy to remember but difficult to guess
Do not share passwords
Change the password periodically
Use a unique password for each account

## Slide 433: Password Managers/Fillers and Resets
Policies prevent users from writing down passwords or sharing the same password between sites
Password fillers store multiple credentials for secure submission to websites
Password reset mechanisms allow users to self-select a new password

## Slide 434
Distinguish between identification, authentication, authorization, and accounting in access control systems
Identify different authentication factors and understand their use in providing strong authentication
List best practices when choosing passwords
Explain how encryption technologies are used for authentication and access control
Notes: What are the four processes of an access control system? Identification, Authentication, Authorization, and Accounting.
Users should only be granted the minimum sufficient permissions. What system policy ensures that users do not receive rights unless granted explicitly? Implicit deny.
What is the main type of non-discretionary access control? Mandatory Access Control—though any rules-based system might restrict discretionary aspects of granting rights.
What type of control prevents a user from denying they performed an action? Non-repudiation. Examples of controls providing non-repudiation include logging, video surveillance, biometrics, signatures, and receipts/tokens.
What sort of account allows someone to access a computer without providing a user name or password? Guest account.
How does a one-time password work? The password is generated by an asymmetric encryption algorithm. This means that the authenticating server can determine that the number was generated by a particular device (fob) at a particular time. When used with a PIN, it also proves that the password was input by a particular user.
What type of system allows a user to authenticate once to access multiple services? Single Sign-On (SSO).
What type of cryptographic operation(s) are non-reversible? Cryptographic hashing. You might also mention asymmetric encryption and public/private key pairs, where an operation performed with one key can only be reversed by the linked key and NOT by the key that performed the original operation.
What class of data is a transport encryption protocol designed to protect? Data in transit (or data in motion).
Why is it important not to use simple words or names as a password? Password-cracking software is configured with dictionaries of such names and phrases. Even if the password is encrypted, if it matches a term in the password-cracking dictionary it will be discovered in seconds.

## Slide 435: CompTIA IT Fundamentals+ (Exam FC0‑U61)
Module 5 / Unit 4 / Behavioral Security Concepts

## Slide 436
Explain the importance of written policies and procedures in ensuring behavioral security
Describe basic principles for handling confidential information
List some privacy and usage issues for corporate systems and Internet/social media sites

## Slide 437: Policies and Procedures
Policies guide employees in secure behavior
Standards
Procedures
Guidance

## Slide 438: Personnel Management Policies
Policies governing phases of employment
  Recruitment (hiring)
  Operation (working)
  Termination or separation (firing or retiring)
Typical policies
  Privilege management, data/information handling, incident response, use of company devices and services, such as Internet access
Disciplinary procedures

## Slide 439: Handling Confidential Information
Classification of documents
Training on recognizing and handling confidential and sensitive information
Passwords
Personally Identifiable Information (PII)
Company confidential information
Customer confidential information

## Slide 440: Acceptable Use Policies
Used by businesses to govern employee use of systems and by service providers to enforce “fair use”
Rules of behavior
Use of personally owned devices in the workplace

## Slide 441: Privacy Policy
Privacy laws and employee contracts
Workplace surveillance
  Security assurance
  Monitoring data
  Physical monitoring

## Slide 442: Expectations of Privacy
Privacy issues when using social networking
Public and private settings when posting messages or uploading files
Use of your data (and metadata)
  Social networking sites
  Internet Service Providers
  Web search engines
Laws governing data collection and storage

## Slide 443
Explain the importance of written policies and procedures in ensuring behavioral security
Describe basic principles for handling confidential information
List some privacy and usage issues for corporate systems and Internet/social media sites
Notes: What is a SOP? Standard Operating Procedure.
Apart from passwords and PII, what other type(s) of confidential information should be governed by classification and handling procedures? Company confidential information and customer information.
Why might a company ban use of the corporate network and desktop software for personal communications? The company might be held responsible for inappropriate content posted by its employees. The issue of privacy is also complex and it is often better for both the company and the employee to use corporate systems for business communications only.
What two main privacy issues arise from using a social networking site? Firstly, you need to control how far information you post to the site is distributed. You could make it private, accessible to close friends only, accessible to all your contacts, or accessible to anyone. Secondly, you need to know how the company processes, stores, and transfers or sells any data it collects about you, including information you post and your activity on the site.