## Slide 1: CompTIA IT Fundamentals+ (Exam FC0‑U61)
Module 3 / Unit 1 / System Components

## Slide 2
Explain the way in which system components determine performance and how to specify an appropriate computer system
Describe the types and functions of motherboards, processors, memory, and the expansion bus
Explain the importance of a cooling system and the components used
Identify the role of PC firmware and access the firmware setup program

## Slide 3: Selecting a Computer
Key components for performance
Central Processing Unit
Memory (System RAM)
Fixed disk
  Hard Disk Drive (HDD)
  Solid State Drive (SSD)
Graphics Processing Unit (GPU)

## Slide 4: Network Interface
Wired network
  Ethernet port (RJ-45)
  Network Interface Card (NIC)
Wireless network
  Wi-Fi radio networking
  Wireless access points

## Slide 5: Motherboard Components

## Slide 6: Processors
Microprocessor/integrated circuit
Central Processing Unit (CPU) is main processor in computer
Intel versus AMD

## Slide 7: Intel and AMD CPU Brands
Core
Pentium
Celeron
Atom
Xeon
Legacy—Athlon, Phenom, Sempron, Turion, AMD FX, Opteron
Zen microarchitecture
Ryzen/Threadripper and Ryzen Mobile
Epyc

## Slide 8: ARM CPUs
ARM (Advanced RISC Machine) microarchitecture
  Widely used on smartphones and tablets
  ARM don’t make CPUs but license the designs
  Apple A, Samsung Exynos, nVIDIA Tegra
RISC stands for Reduced Instruction Set Computing
RISC microarchitectures use simple instructions processed very quickly
Complex (CISC) microarchitectures use more powerful instructions but process each one more slowly
Intel's microarchitecture is CISC with RISC enhancements (micro-ops)

## Slide 9: Features of Processors
Control unit/pipeline
Execution units
Registers

## Slide 10: Instruction Set (32- versus 64-bit)
x86 instruction set
  x86 instruction set started in 1978 with 16-bit CPUs
  First 32-bit CPU with x86-32/IA-32 released in 1985
  x86-64/x64 developed by AMD in 2003 (Intel refer to it as EM64T)
32-bit versus 64-bit CPU
  32-bit CPU can address up to 4 GB memory
  64-bit CPU can address up to 16 Exabytes (currently CPUs use a 48-bit address space (256 Terabytes)
  64-bit CPUs can run 32-bit operating systems and software
  32-bit CPUs CANNOT run 64-bit operating systems or software
Most PC/laptop CPU models are now 64-bit

## Slide 11: Clock Speed and Bus Speed
Clock speed differentiates CPU models (premium models run faster)
Front Side Bus between CPU and system memory is another important performance factor

## Slide 12: Multiprocessing and Dual-core
Symmetric Multiprocessing (SMP)
  Providing multiple CPU sockets on the motherboard
  Usually a feature of server systems
Chip Level Multiprocessing (CMP)
  Each CPU contains multiple “cores”
  Each core works as a (more-or-less) independent CPU
  2-core, 4-core, and 8-core models available

## Slide 13: System and Expansion Bus Technologies
Motherboard is a printed circuit board with buses connecting processors
  Data
  Address
  Timing
  Power
System bus (Front Side Bus) between CPU and system memory
Expansion bus (Input/Output Bus) between CPU and other processors

## Slide 14: Expansion Bus Types

## Slide 15: System Cooling
Heatsinks and thermal paste
  Passive cooling
  Transfer heat by convection
Fans
  Active cooling (powered)
  Dissipate warm air from component
  Case fans draw cool air through front vents and expel warm air through back

## Slide 16: Liquid-based Cooling Systems

## Slide 17: BIOS and UEFI System Firmware
Bootstrapping (booting)
  CPU starts and initializes other components
  Occurs before operating system loads
  Controlled by PC firmware
BIOS (Basic Input/Output System)
UEFI (Unified Extensible Firmware Interface)

## Slide 18: System Firmware Setup Program
Press a key during boot sequence—look at screen or refer to documentation
Navigate using keyboard and ESC

## Slide 19: UEFI Setup Programs

## Slide 20
Explain the way in which system components determine performance and how to specify an appropriate computer system
Describe the types and functions of motherboards, processors, memory, and the expansion bus
Explain the importance of a cooling system and the components used
Identify the role of PC firmware and access the firmware setup program
Notes: What type of component provides persistent storage? A mass storage device such as a Hard Disk Drive (HDD), Solid State Drive (SSD), or flash memory. You could also mention optical discs (CD, DVD, Blu-Ray).
What computer component is most restrictive in terms of determining upgrade potential for a desktop computer? The motherboard—it is difficult and expensive to replace.
True or false? A plug-in card is always required to support PC sound. False—sound functions are often provided by the motherboard chipset.
What is the main advantage of using a CPU in 64-bit mode? Makes more system memory accessible. A 64-bit CPU and OS is also required to run 64-bit applications, but there are not too many of these yet. 64-bit software is more reliable and a bit faster than 32-bit software.
What is a typical speed for a modern CPU to run at? Around 2 GHz; budget models might run as low as 1 GHz while the fastest run up to about 3 GHz.
You want to purchase a computer with a fast graphics interface. What type of expansion slot should you look for? PCIe x16—this is a type of PCI Express slot that uses 16 'lanes'. Each lane can transfer 250 MBps (or 500 MBps for PCIe 2 and 1 GBps for v3).
What type of component provides a passive cooling solution? A heatsink or heat spreader removes heat from the component by convection with no power required. However, it is usually necessary to cool the heatsink or heat spreader itself and this is likely to require active cooling (a fan).
How would you access the system setup program on a PC? Historically, by pressing the appropriate key during startup (ESC, DEL, F1, F2, or F10). Modern PCs often use fast boot modes that require some other means of booting to the firmware setup program.

## Slide 21
Lab 11 / Specifying PC Systems

## Slide 22: CompTIA IT Fundamentals+ (Exam FC0‑U61)
Module 3 / Unit 2 / Using Device Interfaces

## Slide 23
Distinguish peripheral, graphics, and networking interfaces and their uses
Install and configure input devices

## Slide 24: Computer Port and Connector Types

## Slide 25: Universal Serial Bus (USB)
Plug-and-Play interface
Supplies enough power for small peripherals
Versions and data rates
  1.1 – 12 Mbps
  2.0 – 480 Mbps
  3.0 – 5 Gbps
  3.1 – 10 Gbps

## Slide 26: Firewire
Similar to USB but not widely adopted on PCs
Data rate of 400 Mbps
6-pin and unpowered 4-pin connectors

## Slide 27: Graphics Devices
Video card or graphics adapter generates the signal to send to a display device (monitor)
Most motherboards have integrated adapters
High performance adapters can be fitted through an expansion card
Video card often has its own CPU (GPU or Graphics Processing Unit) and memory
Resolution and color depth
VGA (Video Graphics Array) standards
Standard 4:3 versus widescreen (16:10) resolutions
High Definition (HD) and 4K resolutions

## Slide 28: High Definition Multimedia Interface (HDMI)
Very widely used on computers and consumer electronics
Sufficient bandwidth for HD resolution (and 4K)
Mini and micro connectors also available

## Slide 29: DisplayPort and Thunderbolt
Competitor technologies to HDMI
Support for daisy-chaining monitors
Used on Apple Macs and some PCs—especially Thunderbolt 3
Thunderbolt 2
  20 Gbps over a MiniDP physical interface
Thunderbolt 3
  40 Gbps over a USB-C physical interface (with 0.5m cable)

## Slide 30: Digital Visual Interface (DVI)
Preceded HDMI as the principal display interface for PCs
DVI can support both digital and analog monitors
Single and dual-link versions
Most interfaces are DVI-I dual-link
Bulky connectors mean that this interface is rapidly falling out of favor
HDMI is backward-compatible with DVI-D using a suitable adapter cable

## Slide 31: Video Graphics Array (VGA)
Blue, 15-pin port (HD15F/DE-15)
Legacy analog interface—used principally with old Cathode Ray Tube (CRT) monitors
Some flat-panel displays and graphics adapters continue to provide VGA ports

## Slide 32: Input Devices (1)
Human Interface Devices (HID)
Keyboard
  USB/Bluetooth (or legacy PS/2)
  Layout and region
Mouse
  USB/Bluetooth (or legacy PS/2)
  Optical and laser designs (or legacy mechanical mice)
  Optional extra buttons and scroll wheel

## Slide 33: Input Devices (2)
Laptop keyboards and touchpads
  Fn switch for laptop keys
  Touchpad gesture support
Stylus pen

## Slide 34: Configuring a Mouse
Connect to an appropriate port
  PS/2
  USB
  Wireless
Install vendor driver for custom settings
Configure using Mouse applet

## Slide 35: Configuring a Keyboard
Connect to an appropriate port
Configure using Mouse applet
Set correct region/layout using Settings
Switch between multiple layouts using Notification icon (START+SPACEBAR)

## Slide 36: Configuring a Pen/Stylus

## Slide 37: Bluetooth
Personal Area Networks (PAN)
  Wireless communications enable short-range connections to peripheral and networks
Bluetooth
  Up to 10m
  3 Mbps (Bluetooth EDR)
  24 Mbps (using HS and Wi-Fi)

## Slide 38: Configuring Bluetooth
Put device into discoverable mode
Pair using passkey on both devices
Disabling Bluetooth

## Slide 39: RF and Near Field Communications (NFC)
Radio Frequency ID (RFID)
  Passive tags (typically) encoded with data
  Respond when scanned by an RFID reader
  Widely used for inventory management
Near Field Communications (NFC)
  Peer-to-peer version of RFID working at very close range (2”/6cm)
  Used on smartphones for contactless payment

## Slide 40: Networking Interfaces
Network Interface Card (NIC)
  Onboard (part of motherboard)
  Expansion cards
Ethernet connector (RJ-45)
  Patch cord with RJ-45 connectors between NIC and Ethernet switch (or wall port)

## Slide 41: Telephone Connector (RJ-11)
Smaller than RJ-45 and with fewer wires
Used for dial-up analog modems and fax modems
Also used between Digital Subscriber Line (DSL) Internet modems and telephone jack

## Slide 42
Distinguish peripheral, graphics, and networking interfaces and their uses
Install and configure input devices
Notes: True or false? Mice and keyboards must be connected to a computer via PS/2 ports. False—they are now much more likely to use USB or wireless (Bluetooth or other RF) interfaces.
True or false? USB cables have the same connectors at either end. Partly false—the connectors for the host (PC) and device use different form factors (there are also normal size and mini or micro device connectors). A new reversible Type C connector is starting to be used however.
A user has two USB drives connected to her PC. She complains that when she copies large files to both drives at the same time, it seems to take much longer. Why might this be? Bandwidth on the USB bus is shared between all devices.
You want to purchase a flat-panel monitor that can show widescreen movies. You are considering models with native resolutions of 1400x1050 and 1920x1200. Which should you choose? 1920x1200 as this is a widescreen format.
True or false? HDMI is the only type of display interface that supports High Definition picture resolutions. False—there is also DisplayPort and Thunderbolt and some DVI formats also support HD resolutions.
You are considering buying a new display device. The model you are considering accepts digital inputs only. Your computer's graphics adapter has a blue port with 15 holes. Would this flat-panel be a wise purchase? Probably not, as this connector is VGA, which supports analog output only. It is possible to buy converters however.
You need to configure settings for an input device. What should be your first step? Open the Settings app or Control Panel.
A friend is asking for your help in using her computer. When he presses the key marked @, a different symbol appears. What could be the cause? The keyboard is set to use a UK layout—you can correct this using the Language Bar.
What type of mouse would you recommend for someone who uses their computer principally to play computer games and why? Laser mouse—this registers cursor movements more quickly and accurately.

## Slide 43
Lab 12 / Configuring Input Devices

## Slide 44: CompTIA IT Fundamentals+ (Exam FC0‑U61)
Module 3 / Unit 3 / Using Peripheral Devices

## Slide 45
Use Plug-and-Play to install devices and understand the use of device drivers
Describe different display technologies and install and configure a PC display
Install and configure multimedia devices, such as sound cards, speakers, microphones, and webcams
Describe the features and capabilities of different types of printer and their associated interfaces
Install and configure a printers and scanners

## Slide 46: Installing and Uninstalling Peripherals
Plug-and-Play installation
  Windows locates and installs a device driver automatically on connection
  Hot-swappable devices do not require a system restart to connect or disconnect
Manual driver installation
  Locate driver setup program from vendor’s website and run it

## Slide 47: Devices and Printers
Post-installation configuration
Devices and Printers
Settings > Devices

## Slide 48: Removing and Uninstalling Devices
Device Manager
Completely uninstall driver
Check device properties
Scan for undetected devices

## Slide 49: IP-based Peripherals and Web Configuration

## Slide 50: Display Devices
Flat-screen displays
  Replaced analog Cathode Ray Tube (CRT) monitors
  Liquid Crystal Display (LCD)/TFT (Thin Film Transistor)
  Digital signal drives color value of each pixel
  Vendors—Viewsonic, Iiyama, Sony, Panasonic, Toshiba, LG, Acer, Sanyo, Mitsubishi
Touchscreens

## Slide 51: Digital Projectors
Presentation device to display image to an external screen or surface
Use same graphics interfaces as monitors

## Slide 52: Display Settings

## Slide 53: Screen Resolution

## Slide 54: Installing and Configuring Dual Monitors
Duplicate
Extend
  Arrange icons to ensure consistent cursor movement between screens
Project (show on one screen only)

## Slide 55: Configuring a Touchscreen
Tablet PC Settings
  Calibrate display
Pen and Touch
  Gesture settings

## Slide 56: Multimedia Ports and Devices
Audio card/sound card
Speaker and microphone jacks
  Audio in (light blue
  Microphone input (pink)
  Audio out (lime)—amplified stereo speakers/headphones
  Audio out (black)—rear speaker
  Audio out (orange)—subwoofer
  USB port (headsets)
Speaker configurations
  Stereo
  Surround sound (5.1 or 7.1)

## Slide 57: Audio Settings
Sound applet (Control Panel)
Volume control (Notification Area)

## Slide 58: Webcams
Compact video recording
Once very low quality, modern webcams are usually HD-quality at least
Can be built-in for laptops or attached using USB

## Slide 59: Printer Types
Laser printer—fuser unit and toner
Inkjet—ink cartridge and print head
Greyscale or Cyan, Magenta, Yellow, and Black (CMYK) color printing
Vendors—HP, Epson, Canon, Xerox, Brother, OKI, Konica/Minolta, Lexmark, Ricoh, Samsung

## Slide 60: Installing and Configuring a Printer
USB or Bluetooth wireless connection
Plug-and-Play installation
Manage via Devices and Printers or Settings > Devices

## Slide 61: Printer Properties and Preferences

## Slide 62: Types of Scanners
Imaging device similar to a photocopier
Flatbed form factor
Sheet fed form factor

## Slide 63: Scanning a Document
Scanners are connected using USB and Plug-and-Play
Software applications control scanner through an interface
  TWAIN (legacy)
  Windows Image Acquisition (WIA)
Output to file
  Image (JPG, TIFF)
  Portable Document Format (PDF)
  Optical Character Recognition (OCR)

## Slide 64: Digital Cameras
Portable cameras using digital imaging technology and flash memory cards for storage
Transferring images to PC
  Connect the camera to a USB port
  Use a memory card slot
  Use Wi-Fi

## Slide 65
Use Plug-and-Play to install devices and understand the use of device drivers
Describe different display technologies and install and configure a PC display
Install and configure multimedia devices, such as sound cards, speakers, microphones, and webcams
Describe the features and capabilities of different types of printer and their associated interfaces
Install and configure a printers and scanners
Notes: Which Windows interface is used for advanced management and troubleshooting of devices? Device Manager is used to update drivers and obtain more advanced troubleshooting information. The basic user interface is either Devices and Printers or the device pages in the Settings app, depending on the Windows version.
What do you need to know to connect to a device that is configured over the network? Typically the Internet Protocol (IP) address of its management page. Some devices may use a name to locate the page instead. You are also likely to be prompted for a user name and password.
True or false? If you want to configure the DPI of a display device, you would do so via the Personalization app. False—Dots Per Inch (DPI) or scaling is configured via Display properties. Personalization is for configuring themes and the appearance of the desktop.
You are configuring dual monitors positioned side-by-side. You want to increase the amount of screen space available. Which multiple display option should you set? Extend the displays.
You need to plug a microphone into a computer to make a recording. How would you identify which jack to use? The jack should be color-coded (pink). There may be an icon to represent usage though. If neither is present, check the system documentation.
What, if any, type of printer uses a fuser? Laser printer—the fuser bonds the toner to the surface of the paper using high heat and pressure.
What are the four inks used to produce color prints? Cyan, Magenta, Yellow, and Black (CMYK).
What type of wired interface is a printer MOST likely to use? Universal Serial Bus (USB).
You want to configure a printer to use both sides of the paper (duplex) by default. You have alt-clicked the printer object—which command should you select to proceed? Printing preferences.
What basic command demonstrates that a printer is connected properly to a computer and that its driver is installed correctly for Windows? Print Test Page.
What function of a scanner would you use if you want to convert a letter that someone has mailed to you into a computer-editable document? Optical Character Recognition (OCR).
True or false? If your PC does not have a flash memory card reader, you should be able to connect the camera itself to the PC over USB to copy images off the card. True—must cameras support USB connections.

## Slide 66
Lab 13 / Playing Audio
Lab 14 / Using a Printer

## Slide 67: CompTIA IT Fundamentals+ (Exam FC0‑U61)
Module 3 / Unit 4 / Using Storage Devices

## Slide 68
Contrast volatile and non-volatile storage types
Describe the types of system memory modules used in PCs
Describe the types and features of Hard Disk Drives, Solid State Drives, optical drives, and flash memory

## Slide 69: System Memory
Random Access Memory (RAM)
Volatile storage
Vendors—Kingston, Crucial (Micron), Corsair, PNY, Integral
Dynamic RAM (DRAM)
Synchronous DRAM
  64-bit transfers per clock cycle
Module packaging
  DIMMs (Dual Inline Memory Module)
  Small Outline DIMM (SO-DIMM)

## Slide 70: Double Data Rate SDRAM (DDR SDRAM)
Two 64-bit transfers per clock cycle
Subsequent iterations increase bus speed
  DDR2
  DDR3
  DDR4
Motherboard sockets must match DDR version
DIMM and SO-DIMM modules with different pin positions

## Slide 71: Hard Disk Drives (HDD)
HDD is one type of fixed disk internal persistent storage device
Magnetic platters access by a drive head
2.5” and 2.5” formats
Capacity
Performance
  Spin speed (RPM)
  Access time
  Transfer rate
Vendors—Seagate, Western Digital, Maxtor, Hitachi, Fujitsu, Toshiba, Samsung

## Slide 72: HDD Interfaces
Serial ATA (SATA) dominates internal devices (legacy drives used Parallel ATA/EIDE and SCSI)
External drives housed in an enclosure can use a number of interfaces

## Slide 73: Solid State Drives (SSD)
Non-volatile flash memory
Lighter, faster, and more reliable than mechanical HDDs
Costs falling rapidly but still very expensive above 512 GB
Large flash memory caches are also used to supplement HDDs (hybrid drives)
Can be packaged as 2.5” drive with SATA connector, PCIe adapter card, or M.2 adapter card

## Slide 74: Optical Discs and Drives
Specially formatted discs read by a laser
Multiple formats
  Compact Disc (CD)
  Digital Versatile / Video Disc (DVD)
  Blu-ray Disc (BD)
Recordable and rewritable formats

## Slide 75: Optical Drive Units
Fit to internal 5.25” drive bays and SATA interface
USB external units
Read/record/rewrite speeds

## Slide 76: Removable Flash Memory Devices
USB/thumb drive
  Up to 256 GB (at affordable prices)
Memory cards
  Multiple vendors and form factors/sizes
  Secure Digital (SD) and Compact Flash (CF)
  Typically up to 128 GB, though 2 TB cards have been made
  Multi-format memory card readers

## Slide 77
Contrast volatile and non-volatile storage types
Describe the types of system memory modules used in PCs
Describe the types and features of Hard Disk Drives, Solid State Drives, optical drives, and flash memory
Notes: You have a motherboard that is designed for DDR2 memory that works at a bus speed of 533 MHz. You have some DDR3 memory modules that also work at a bus speed of 533 MHz. Are the modules compatible with the motherboard? No—DDR3 modules cannot be used in DDR2 slots.
Why can't you use memory modules designed for a desktop computer in a laptop? Laptops use a smaller form factor called SO-DIMM while desktops use DIMMs.
A hard drive is rated at 10,000 RPM. What is the significance of this statistic? The number of revolutions per minute (RPM) is one of the basic factors determining the speed of the drive. 10,000 rpm represents good performance (15K rpm is the best available).
What type of connector would you use for an external hard drive to connect to a Windows PC? USB. Firewire, eSATA, or Thunderbird are also possible but not nearly so popular. Most drives are now USB3 or USB3.1. Note that you can plug a USB3 drive into a USB2 port, so long as you have a USB3 device cable.
Your computer has 4 SATA ports. How many hard drives can be installed? Four—each SATA port can be used to connect one drive.
True or false? A single layer Blu-ray Disc has greater capacity than a dual-layer, double-sided DVD. True—the capacity of a single layer Blu-ray disc is 25 GB compared to 17 GB for a dual-layer, double-sided DVD.
What sort of device would you need to transfer data from a "Memory Stick?" Memory card reader/multi-card reader. Do note that Memory Sticks are no longer in production so you could struggle to locate a suitable reader.
What sort of device could you use to expand the storage capacity of a smartphone? Flash memory card.

## Slide 78
Lab 15 / Adding a Removable Drive

## Slide 79: CompTIA IT Fundamentals+ (Exam FC0‑U61)
Module 3 / Unit 5 / Using File Systems

## Slide 80
Describe the properties of file systems and select an appropriate file system for a given OS and usage
Use a file manager to create, open, move/copy, and delete files and folders/directories
Use search tools and view options to locate files quickly

## Slide 81: Managing the File System
Physical disks and drives
Hard disk partitions
  Divide into logically separate storage areas
  Each partition can have different file system
  Must be at least one partition
  Active/system partition

## Slide 82: Windows Drives
Logical partitions, optical drives, and other removable drives can be assigned separate drive letters
Boot drive (usually “C:”) contains the Windows system files

## Slide 83: File Systems
Partition must be formatted with a file system before the OS can use it
File system determines compatibility with different operating systems
  FAT (File Allocation Table)
  NTFS (New Technology File System)
Windows must be installed to an NTFS partition
Optical drives
  Universal Disk Format (UDF)
  ISO 9660/CDFS
Linux and Mac file systems
  ext3 and ext4
  Hierarchical File System (HFS+) and Apple File System (APFS)

## Slide 84: File System Features
Compression
Encryption
Permissions
Journaling
Limitations
Naming rules

## Slide 85: Folders
While drives store files, folders can be used to organize those files
Create distinct logical areas with different security privileges
  Separate OS and application files from user data
  Separate user data belonging to different accounts
Partition root folder
Subfolders and file paths
  C:\
  C:\Windows
  C:\Windows\System32\

## Slide 86: Windows System Folders
Windows
  The "system root," containing drivers, logs, add-in applications, system and Registry files (notably the System32 subfolder), and so on
  System32 contains most of the applications and utilities used to manage and configure Windows
Program Files
  Subfolders for installed applications software
Users
  Storage for users' profile settings and data

## Slide 87: Linux Directories
“Folders” is Windows-specific terminology—Linux refers to “Directories”
Root folder and delimiter is forward slash /
No “drives”—different storage devices are mounted within the root file system

## Slide 88: File Explorer
Windows Explorer or just “Explorer”
Navigation pane
Quick Access and Desktop
  OneDrive
  User account
  This PC
  Libraries
  Network
  Control Panel
  Recycle Bin

## Slide 89: User Profiles and Libraries
Profile subfolders (Documents, Pictures...)
Public profile
Libraries

## Slide 90: Creating a Folder
Name must be unique at same level
Disallowed characters: \ / : * ? " < > |
Full path cannot usually exceed 260 characters
Case aware but not case sensitive (in Windows)

## Slide 91: Files
Containers for data written to disk
  Binary files
  Text files
File types and extensions
  Similar naming rules to folders
  Last part of file name (following final period) is an extension
  Extension shows file type
  Applications can be associated with different actions for file types (Open, Edit, Print, ...)

## Slide 92: Creating and Opening Files
Save/Save As command
Right-click > New
Open/Open With

## Slide 93: File Explorer Options
General
  Explorer behavior
View
  Show/hide extensions
  Show/hide system files
  ...

## Slide 94: Renaming, Copying, and Moving Files and Folders
Rename any file—do not change the extension (unless you mean to do so)
Copy and move methods
Resolving existing file conflicts

## Slide 95: Deleting Files and the Recycle Bin
Deleted files are normally kept in the Recycle Bin
Recovering files and emptying Recycle Bin
Recycle Bin properties
Erase a file using SHIFT+Delete
No recycling for flash drives or network shares (though server administrator might be able to recover)

## Slide 96: Selecting Multiple Files and Folders
Click-and-drag/SHIFT+click
CTRL+click
SHIFT+ARROW select
CTRL+ARROW+SPACEBAR select

## Slide 97: File Attributes

## Slide 98: File Properties Dialog

## Slide 99: Folder and File Permissions
Access Denied error message
Configure NTFS permissions on Security tab
Add/select account then configure permissions level
  Full control
  Modify
  Read/list/execute
  Write

## Slide 100: Searching for Folders and Files
Instant Search
Matches files, programs, apps, messages, and web pages
Press START
Use Cortana

## Slide 101: File Explorer Search
File name
File contents
By file size / date

## Slide 102: View, Group, and Filter Options
Details view – sort by column headers
Group
Filter
Arrange By

## Slide 103: File Types and Extensions
Word processing software
  txt—a text-only file with no "binary" file information linking the file to a particular software application
  rtf—Rich Text Format
  odf—the Open Document Format
  doc/docx—this format is the one used by Microsoft Word
Spreadsheet software
  xls/xlsx for Microsoft Excel
Presentation software
  ppt/pptx for Microsoft PowerPoint
PDF viewers and creators
  Portable Document Format (PDF)
  “Final” format for document distribution (printed or online)

## Slide 104: Image File Types
jpg/jpeg (Joint Pictures Expert Group)—this lossy compression format is the most widely used for photographic pictures
gif (Graphics Interchange Format)—this is an old lossless compression format
tiff (Tagged Image File Format)—this is a popular format for exchanging images between editing applications
png (Portable Network Graphics)—this is a full-color (24-bit) lossless format designed to replace GIF
bmp—this is a Windows-only lossless format

## Slide 105: Video File Types
mpg—this is an early MPEG (Motion Pictures Expert Group) standard for video files with lossy compression
mp4—the MPEG-4 standard audio/video file format
flv—another container file format designed to deliver Flash Video
wmv (Windows Media Video)—a video container file format developed by Microsoft
avi—a legacy Windows-only video format

## Slide 106: Audio File Types
mp3—developed from MPEG, this remains one of the most popular formats for distributing music
aac (Advanced Audio Coding)—developed from MPEG as a successor to mp3
m4a—this is an audio-only file format deriving from the MPEG-4 standards track
flac (Free Lossless Audio Codec)—as the name suggests, this format achieves file size compression without discarding audio data
wav—this is an early Windows audio file format

## Slide 107: Executable Files
exe—this is the basic type of program file in Windows
msi—this is a Windows Installer file used to install and uninstall software applications under Windows
app—this is the equivalent of an exe file for macOS
bat/cmd/vbs/js/ps1—contains a sequence of commands either from the operating system's command interpreter or from a scripting language supported by the OS

## Slide 108: Compression Formats
zip—this format was developed for the PKZIP utility but is now supported "natively" by Windows, Mac OS X, and Linux
tar—this was originally a UNIX format for writing to magnetic tape (tape archive) but is still used with gzip compression (tgz or .tar.gz) as a compressed file format for UNIX, Linux, and macOS
rar—this proprietary format is used by the WinRAR compression program
7z—this type of archive is created and opened using the open-source 7-Zip compression utility
gz—this type of archive is created and opened by the gzip utility, freely available for UNIX and Linux computers
iso—this is a file in one of the formats used by optical media. The main formats are ISO 9660 (used by CDs) and UDF (used by DVDs and Blu-Ray Discs).
vhd/vmdk—these are disk image file formats used with Microsoft Hyper-V and VMware virtual machines
dmg—this is a disk image file format used by Apple macOS

## Slide 109
Describe the properties of file systems and select an appropriate file system for a given OS and usage
Use a file manager to create, open, move/copy, and delete files and folders/directories
Use search tools and view options to locate files quickly
Notes: In Windows, you can access data via letter-labeled "drives." Do these correspond exactly to physical disks? Not necessarily in the case of hard disks, which can be configured with multiple partitions, each of which can be assigned a drive letter. Optical drives and flash memory cards cannot be partitioned however.
What type of file system must the partition that Windows files are installed on use? NTFS.
What default installation folders contain system and application files that should not normally be deleted or modified manually? The 'Windows' and 'Program Files' folders.
What is the file path to the Documents folder for a user named "David," assuming Windows is installed to a hard disk with a single partition using the default settings? C:\Users\David\Documents
How is a Windows library different from a folder? A library acts as a virtual folder by displaying the contents of multiple folders, which could be located on different drives.
If you have made changes to a file and want to keep both the original file and the modified version, what command should you use? Save As.
Why should you be more careful about deleting files from a USB flash drive than from the main hard drive? The files will not be recycled so there is no possibility of retrieving them if you change your mind (at least, not without using specialist data recovery software).
What view options could you use to show files of a particular type sorted by date? Group the files by file type then sort by date.
What kind of data would you expect to find in a file with a TIFF extension? This is an image file format.
What is a zip file? A file archive containing other files in a compressed format.

## Slide 110
Lab 16 / Using File Explorer