## Slide 1: CompTIA IT Fundamentals+ (Exam FC0‑U61)
Module 4 / Unit 1 / Networking Concepts

## Slide 2
Describe the components and functions of computer networks
List the protocols and technologies used for addressing on computer networks
Connect a computer to a wired or wireless network
Describe the uses of common application protocols

## Slide 3: Network Components
Clients and servers
Local Area Network (LAN)
Wide Area Network (WAN)

## Slide 4: Network Media
Nodes/hosts
Wired data connections
  Copper cabling
  Fiber optic cabling
  Ethernet
Wireless (Wi-Fi) data connections
WAN links
  Fiber optic cabling
  Point-to-point radio
  Cellular radio
  Satellite

## Slide 5: Addressing and Protocols
Standards and protocols provides
  Format for computers to exchange data over the network (frames and packets)
  Addresses to identify interfaces
Network frames and packets have headers and payload
Network media standards include Ethernet (cabled links) and Wi-Fi
Most local networks and the internet use TCP/IP and IP addressing

## Slide 6: TCP/IP and Packet Transmission
Transmission Control Protocol/Internet Protocol (TCP/IP)
Packet transmission versus circuit-based networks
  Communications broken into small packets
  Multiple paths between network nodes
  Routers choose best available path
  Lost or damaged packets can be resent

## Slide 7: TCP/IP Protocol Suite Layers (1)

## Slide 8: TCP/IP Protocol Suite Layers (2)
Link or Network Interface layer
  Ethernet/Wi-Fi
  Local network segment only
  Frames
Internet layer
  Internet Protocol (IP)—the main protocol in the TCP/IP suite is responsible for logical addressing and routing of packets between hosts and networks.
  Address Resolution Protocol (ARP)—used for hardware address resolution
  Internet Control Message Protocol (ICMP)—sends messages and reports on errors regarding packet delivery.
Transport layer
  Transport Control Protocol (TCP) provides connection-oriented delivery
  User Datagram Protocol (UDP) provides connectionless delivery
Application layer

## Slide 9: Internet Protocol (IP)

## Slide 10: IP Addresses
32-bit binary value expressed in dotted decimal
  172.30.15.12
IPv4 versus IPv6 (128-bit address)

## Slide 11: Network Prefixes and Subnet Masks
IP address contains network ID and host address
  Network ID—common to all hosts on the same IP network
  Host ID—identifies a host on a particular network or logical subnetwork
Network prefix/subnet mask is used to identify network portion within the IP address
Mask shows how many bits from the start of the address belong to the network ID

## Slide 12: Packet Delivery and Forwarding
Logical addressing (IP) versus local/hardware interface addressing
MAC Addresses
  48-bit expressed in hex
  00:60:8c:12:3a:bc
Address Resolution Protocol (ARP)
  Identifies the MAC address associated with an IP address
Routing
  If the network ID of the destination IP address is different to the source, the packet is sent to a router on the local segment (default gateway)
  Router forwards packet to its destination, possibly via intermediate routers

## Slide 13: Domain Name System (DNS)
IP and MAC addresses are very hard to remember
Simple names are much easier for people to use
Domain Name System (DNS) maps names to IP addresses
Hierarchical, distributed database
Root namespace
Top Level Domains (TLD)
  .com, .edu, .org, .gov, .ca, .uk, ...
Register domains within a TLD
Create hosts and subdomains within a domain name

## Slide 14: Hostnames and Fully Qualified Domain Names
Hostname allocated to hosts
  Up to 256 alphanumeric characters and hyphen
  Usually much shorter
Hostname + Domain Name + TLD Suffix = Fully Qualified Domain Name (FQDN)

## Slide 15: DNS Query Example

## Slide 16: Uniform Resource Locators (URL)
Protocol
  Access method/service type
  Followed by the characters ://
Host location
  IP address or (more typically) FQDN
File path
  Directory and file name location of the resource
  Delimited by forward slash

## Slide 17: Internet Application Services
Internet (IP) and transport layer (TCP/UDP) responsible for addressing and establishing connections
Application layer protocols provide “user-level” services

## Slide 18: HTTP and HTML
HyperText Transfer Protocol (HTTP)
Basis of the World Wide Web
Enables clients (typically web browsers) to request resources from an HTTP server
Web servers, intranets, and extranets
HyperText Markup Language (HTML) pages

## Slide 19: SSL/TLS
Secure Sockets Layer (SSL)/Transport Layer Security (TLS)
Establishes identity of website and protects communication between server and client using encryption
Site presents a digital certificate issued to it by a Certificate Authority (CA)
Client can choose to trust the certificate and CA

## Slide 20: Electronic Mail (Email)
Text messages and binary attachments—Multipurpose Internet Mail Extensions (MIME)
Sending mail
  Simple Mail Transfer Protocol (SMTP)
  MX (Mail Exchanger)
Retrieving messages from a mailbox
  Post Office Protocol v3 (POP3)
  Internet Message Access Protocol (IMAP)

## Slide 21: Configuring Email

## Slide 22
Describe the components and functions of computer networks
List the protocols and technologies used for addressing on computer networks
Connect a computer to a wired or wireless network
Describe the uses of common application protocols
Notes: What is a WAN? A Wide Area Network (WAN) connects sites in different geographic locations. WANs usually make use of telecommunications and service provider networks rather than being directly operated by the network administrators.
What is a packet made up of? A packet consists of a number of fields contained within a header section plus a payload. The payload could be a packet from the protocol layer above.
What are the key features of a packet switching network? Nodes within the network can perform a forwarding function, allowing a packet to utilize any available path through the network. This makes the network robust against link failures. If is beneficial for the network to use small packets that are easy to re-send.
What protocol is usually used to provide logical addressing on networks? Internet Protocol (IP).
What type of address identifies a network interface in the context of the local network segment only? A Media Access Control (MAC) address.
What type of device is used to transfer packets between different networks? A router.
Which protocol allows people to use names/labels to address network resources rather than numeric addresses? Domain Name System (DNS).
Which of the following parts of a web address is usually depends on a name resolution service: protocol type, host location, file path? The host location is usually represented by a Fully Qualified Domain Name (FQDN), such as www.comptia.org, resolved to a numeric IP address by DNS.
What does HTTP stand for? HyperText Transfer Protocol (HTTP).
Which email protocol(s) are used to download messages from a mail server? Either Post Office Protocol (POP) or Internet Message Access Protocol (IMAP).