## Slide 1: CompTIA IT Fundamentals+ (Exam FC0‑U61)
Module 4 / Unit 2 / Connecting to a Network

## Slide 2
Identify the roles of different network devices in providing local and Internet network connectivity
Distinguish the advantages and disadvantages of Internet connection types
Connect a computer to a wired or wireless network
Configure a wireless access point to use secure network settings

## Slide 3: Internet Service Types (1)
SOHO Internet router/modems
Multifunction appliances combining several networking devices
  Switch—connects four or eight computers together in an Ethernet LAN using RJ-45 network ports and twisted-pair cabling
  Access Point (AP)—creates a Wi-Fi wireless network (WLAN) between computers and mobile devices equipped with suitable adapters and also switches communications between the wired and wireless networks
  Internet router/modem—connects the wired and wireless network clients to the Internet via a WAN link

## Slide 4: Internet Service Types (2)
Digital Subscriber Line (DSL)
  Broadband over copper telephone cabling
  Router/modem interfaces with telephone network via RJ-11 port
  Asymmetric DSL (ADSL)—24 Mbps download and 1.4 Mbps upload
Fiber optic
  Fiber to the Home (FTTH)
  Fiber to the Curb (FTTC) and Very High Bit Rate DSL (VDSL)
    52 Mbps download (100 Mbps with VDSL2 at up to 100m) and 16 Mbps uplink
Cable
  Cable Access TV (CATV)/Hybrid Fiber Coax (HFC) networks
  Cable router/modem interface with network via coax F-connector
  Data Over Cable Service Interface Specification (DOCSIS)
    Up to 1.2 Gbps, though 100 Mbps is more typical of commercial packages

## Slide 5: Verifying a Connection
Network status icon
IP address configuration and Dynamic Host Configuration Protocol (DHCP)
Perform a simple test by browsing a website

## Slide 6: Microwave Satellite
Reception dish aligned with orbital satellite
Usually available, even in rural areas
High latency (packet delay)
DVB-S (Digital Video Broadcast Satellite) modem

## Slide 7: Cellular Radio
Transmitters or base stations service “cells” at up to about 5 miles (8 km)
  GSM (Global System for Mobile Communication)
  TIA/EIA IS-95 (cdmaOne)
Can provide data services as well as voice
  GPRS/EDGE (General Packet Radio Services/Enhanced Data Rates for GSM Evolution)
  Evolved High Speed Packet Access (HSPA+)
  CDMA2000/Evolution Data Optimized (EV-DO)
  Long Term Evolution (LTE)
  LTE Advanced (LTE-A)

## Slide 8: Radio Frequency
Wi-Fi networking
Open/public access points

## Slide 9: Wireless Standards and Compatibility
Wireless LAN (WLAN) Wi-Fi standard
IEEE 802.11a/b/g – legacy standards
802.11n and 802.11ac –current standards
Access points can support a mix of clients with adapters for different standards (e.g. 802.11ac AP might support 802.11g and 802.11n clients)
Compatibility modes can reduce performance though

## Slide 10: Configuring an Access Point
Connect to admin interface via IP address
Log in using admin credentials – change the password!
Configuration settings
  Service Set ID (SSID)
  Wireless mode / compatibility mode

## Slide 11: Configuring Wireless Security
Encryption
  Cipher scrambles message
  Key allows receiver to reverse cipher and unscramble message
Wireless security standards
  WEP (Wired Equivalent Privacy)
  Wi-Fi Protected Access (WPA)
  WPA2
Pre-shared key authentication (passphrase)

## Slide 12: Open Authentication and Captive Portals
Open authentication disables encryption
Used by public access points (hotspots)
May be secondary authentication via a captive portal

## Slide 13: Configuring a Wireless Client
Network status icon menu
Network location (private versus public)

## Slide 14: Speed Limitations (Attenuation and Interference)
Wi-Fi indoor range is nominally up to about 30m (100ft)
Signal attenuates at longer range
Dynamic Rate Switching/Selection (DRS) reduces data rate at range to preserve a reliable connection
Radio waves are weakened/blocked by dense material (concrete and metal)
Interference from other networks and radio sources

## Slide 15: Cabled Enterprise Network Access
Flood wired cabling and network wall ports
Enterprise-grade switches
Multiple switches and interconnections can provide thousands of ports

## Slide 16: Wireless Enterprise Network Access
Same Wi-Fi standards
Enterprise-grade access points

## Slide 17: Enterprise Network Routers
Switch ports are placed in logical groups using Virtual LANs (VLANs)
Each VLAN is assigned to an IP subnet
Communications between subnets go via a router
Routers also required for Internet access and WAN links

## Slide 18
Identify the roles of different network devices in providing local and Internet network connectivity
Distinguish the advantages and disadvantages of Internet connection types
Connect a computer to a wired or wireless network
Configure a wireless access point to use secure network settings
Notes: What device is used to connect computers together in an Ethernet network? A switch.
What is the difference between a modem and a router? A modem creates a serial link between two computers over some sort of long distance media. It operates at the data link layer. A router makes forwarding decisions between logical networks. It does not need to take account of the framing and transmission details—those are the responsibility of the modem (or of an Ethernet switch or wireless access point). It just needs to know that a particular logical network can be reached over one of its interfaces. Most SOHO devices pack all these functions into a single appliance but it is important to appreciate the differences between the functions.
Can you list at least four Internet access methods? Digital Subscriber Line (DSL), cable/Hybrid Fiber Coax, Fiber to the Curb (FTTC), satellite, and cellular radio.
What is the latest Wi-Fi standard and which frequency band(s) does it use? IEEE 802.11ac works in the 5 GHz band. Most 802.11ac access points do have 2.4 GHz radios but they use them to support legacy standards.
What information do you need to configure a wireless connection manually? Service Set ID (SSID)/network name, encryption type, and authentication information (a preshared key if not using enterprise authentication).
What is the risk of using a free Wi-Fi network to make an order from an online shop? Data on an open network may be intercepted by the person running the network or by other computers connected to the network. You need to ensure that the online store uses a secure (HTTPS) connection.
What does attenuation mean? Attenuation describes the loss of strength of a signal the farther it has to travel. Attenuation sets the distance limitations on different network media types.

## Slide 19
Lab 17 / Network Settings