## Slide 1: CompTIA IT Fundamentals+ (Exam FC0‑U61)
Module 3 / Unit 3 / Using Peripheral Devices

## Slide 2
Use Plug-and-Play to install devices and understand the use of device drivers
Describe different display technologies and install and configure a PC display
Install and configure multimedia devices, such as sound cards, speakers, microphones, and webcams
Describe the features and capabilities of different types of printer and their associated interfaces
Install and configure a printers and scanners

## Slide 3: Installing and Uninstalling Peripherals
Plug-and-Play installation
  Windows locates and installs a device driver automatically on connection
  Hot-swappable devices do not require a system restart to connect or disconnect
Manual driver installation
  Locate driver setup program from vendor’s website and run it

## Slide 4: Devices and Printers
Post-installation configuration
Devices and Printers
Settings > Devices

## Slide 5: Removing and Uninstalling Devices
Device Manager
Completely uninstall driver
Check device properties
Scan for undetected devices

## Slide 6: IP-based Peripherals and Web Configuration

## Slide 7: Display Devices
Flat-screen displays
  Replaced analog Cathode Ray Tube (CRT) monitors
  Liquid Crystal Display (LCD)/TFT (Thin Film Transistor)
  Digital signal drives color value of each pixel
  Vendors—Viewsonic, Iiyama, Sony, Panasonic, Toshiba, LG, Acer, Sanyo, Mitsubishi
Touchscreens

## Slide 8: Digital Projectors
Presentation device to display image to an external screen or surface
Use same graphics interfaces as monitors

## Slide 9: Display Settings

## Slide 10: Screen Resolution

## Slide 11: Installing and Configuring Dual Monitors
Duplicate
Extend
  Arrange icons to ensure consistent cursor movement between screens
Project (show on one screen only)

## Slide 12: Configuring a Touchscreen
Tablet PC Settings
  Calibrate display
Pen and Touch
  Gesture settings

## Slide 13: Multimedia Ports and Devices
Audio card/sound card
Speaker and microphone jacks
  Audio in (light blue
  Microphone input (pink)
  Audio out (lime)—amplified stereo speakers/headphones
  Audio out (black)—rear speaker
  Audio out (orange)—subwoofer
  USB port (headsets)
Speaker configurations
  Stereo
  Surround sound (5.1 or 7.1)

## Slide 14: Audio Settings
Sound applet (Control Panel)
Volume control (Notification Area)

## Slide 15: Webcams
Compact video recording
Once very low quality, modern webcams are usually HD-quality at least
Can be built-in for laptops or attached using USB

## Slide 16: Printer Types
Laser printer—fuser unit and toner
Inkjet—ink cartridge and print head
Greyscale or Cyan, Magenta, Yellow, and Black (CMYK) color printing
Vendors—HP, Epson, Canon, Xerox, Brother, OKI, Konica/Minolta, Lexmark, Ricoh, Samsung

## Slide 17: Installing and Configuring a Printer
USB or Bluetooth wireless connection
Plug-and-Play installation
Manage via Devices and Printers or Settings > Devices

## Slide 18: Printer Properties and Preferences

## Slide 19: Types of Scanners
Imaging device similar to a photocopier
Flatbed form factor
Sheet fed form factor

## Slide 20: Scanning a Document
Scanners are connected using USB and Plug-and-Play
Software applications control scanner through an interface
  TWAIN (legacy)
  Windows Image Acquisition (WIA)
Output to file
  Image (JPG, TIFF)
  Portable Document Format (PDF)
  Optical Character Recognition (OCR)

## Slide 21: Digital Cameras
Portable cameras using digital imaging technology and flash memory cards for storage
Transferring images to PC
  Connect the camera to a USB port
  Use a memory card slot
  Use Wi-Fi

## Slide 22
Use Plug-and-Play to install devices and understand the use of device drivers
Describe different display technologies and install and configure a PC display
Install and configure multimedia devices, such as sound cards, speakers, microphones, and webcams
Describe the features and capabilities of different types of printer and their associated interfaces
Install and configure a printers and scanners
Notes: Which Windows interface is used for advanced management and troubleshooting of devices? Device Manager is used to update drivers and obtain more advanced troubleshooting information. The basic user interface is either Devices and Printers or the device pages in the Settings app, depending on the Windows version.
What do you need to know to connect to a device that is configured over the network? Typically the Internet Protocol (IP) address of its management page. Some devices may use a name to locate the page instead. You are also likely to be prompted for a user name and password.
True or false? If you want to configure the DPI of a display device, you would do so via the Personalization app. False—Dots Per Inch (DPI) or scaling is configured via Display properties. Personalization is for configuring themes and the appearance of the desktop.
You are configuring dual monitors positioned side-by-side. You want to increase the amount of screen space available. Which multiple display option should you set? Extend the displays.
You need to plug a microphone into a computer to make a recording. How would you identify which jack to use? The jack should be color-coded (pink). There may be an icon to represent usage though. If neither is present, check the system documentation.
What, if any, type of printer uses a fuser? Laser printer—the fuser bonds the toner to the surface of the paper using high heat and pressure.
What are the four inks used to produce color prints? Cyan, Magenta, Yellow, and Black (CMYK).
What type of wired interface is a printer MOST likely to use? Universal Serial Bus (USB).
You want to configure a printer to use both sides of the paper (duplex) by default. You have alt-clicked the printer object—which command should you select to proceed? Printing preferences.
What basic command demonstrates that a printer is connected properly to a computer and that its driver is installed correctly for Windows? Print Test Page.
What function of a scanner would you use if you want to convert a letter that someone has mailed to you into a computer-editable document? Optical Character Recognition (OCR).
True or false? If your PC does not have a flash memory card reader, you should be able to connect the camera itself to the PC over USB to copy images off the card. True—must cameras support USB connections.

## Slide 23
Lab 13 / Playing Audio
Lab 14 / Using a Printer