## Slide 1: Surgical Instrumentation
Chapter 11 7th Ed.
Rosemary Thurston RN

## Slide 2
Stainless Steel
  Not really “stainless”
    Stainresistant
  Martensitic – 400 Series Stainless Steel
    Hardened – holds a sharp edge
      Used on cutting instruments
        Scissors, osteotomes, chisels, rongeurs
        Forceps, hemostats, needleholders

## Slide 3
  Austenitic – 300 Series Stainless Steel
    Softer – high corrosion resistance
      Used on retractors, and tubular structures
Manufacture
  Stamping outline –
  Forging - compressing with heat and cooling
  Grinding and milling
    Parts need to fit together
    Need finger rings, serrations and ratchets

## Slide 4
Tempering – hardening
  With controlled heat and cooling
Polishing – smooth finish
  Mirror finish –
    shiny – stains less
  Satin finish –
    dull – doesn’t reflect light

## Slide 5
Passivation – corrosion resistance
  Nitric Acid – removes iron content on surface
    Builds protective layer of chromium oxide
    Continues as instrument is used
    http://www.youtube.com/watch?v=fb7ugFNj8jc
http://youtu.be/Xw7s4iNsAfM
http://youtu.be/RU6Ri_1vdss - optional

## Slide 6
  Inspected and tested
  Etched with manufacturer’s name / number
Manufacturers
  Good instruments come from Germany
  Poorer usually come from Pakistan

## Slide 7: Instrument Parts
Tip – working part
Jaw - serations
Hinge / Box lock
Shank
Ratchet
Finger Rings
Length

## Slide 8
Jaw face
  Serations
  Needle holders

## Slide 9: Classifications
Hemostat

## Slide 10
Tungston Carbide
  Harder material
  Grip better
  Last longer
Inserted into
  Needleholder tips
  Scissors blades
Have Gold Handles

## Slide 11
Needle holders

## Slide 12
Forceps

## Slide 13
Tissue Forceps
  Have teeth in tip
Dressing forceps
  Have serrations

## Slide 14
Retractors

## Slide 15
Retractors
  Hand held
  Self-retaining
  Table-mounted

## Slide 16
Scissors

## Slide 17
Scissors
  Regular scissors have a crushing action
  Gold handled = tungston carbide blades
    Stay sharp longer
  Black Handle
    Supercut / Microgrind blades
    Simulate cutting action to slice tissue
      One knife is sharpened like a knife
      Other is standard action like guillotine

## Slide 18
Suction device
  May have a Stylet

## Slide 19
Rongeurs
  Singe action
  Double action
    Reduces force needed
    to close instrument

## Slide 20
Speculums

## Slide 21: Manufacturing instruments
http://youtu.be/oDY2qCG3GS8
http://youtu.be/RU6Ri_1vdss

## Slide 22: Post op care of instruments
Should be:
  Opened
  Moist – to prevent drying out
    with moist towel
    Sprayed with enzymatic solution

## Slide 23
Solutions that damage
  Saline (salt water) – also blood
  Betadine Household lubricants
  Peroxide Household powder cleaners
  Bleach Dish soap
  Iodine Laundry soap
  Soaking in water or saline
  Long term soaking in rust or stain remover

## Slide 24: Checking for Damage
Complete the worksheet
  Use the book to see what areas need to be checked
Circle areas that need checking and write down what you are checking for

## Slide 25
Testing for sharpness
  Scissors 4.5” long or more
    Red test material
    Cut material length of blade 3 – 4 X
    Tip must cut well
  Scissors 4” or less
    Yellow test material
    As above

## Slide 26
Index card test material
  Bone Cutter
    Cut off a piece
  Kerrison Rongeur
    Punch a hole
  Laminectomy Rongeur
    Use half of jaw for clean bite
  Double action Rongeur
    Clean bite out of edge

## Slide 27
Plastic dowel rod
  Bone Curette
    Shave off pieces with bowl down
  Chisels and Osteotomes
    Shave off pieces

## Slide 28: Identification
Marking instruments
  Tape
    For specific procedures or specialties
      Clean your hands with alcohol
      Clean instrument in area where tape will be placed (shank)
      Cut tape at an angle
      Wrap around 1 to 1.5X around shank only
        Use firm pulling tension
      Autoclave after so tape will bond

## Slide 29
Heat Fused Nylon
  “dipping” of colored nylon coating
  Powder coating process
  Can last years
    Once it starts to chip – must be all removed

## Slide 30
  Acid Base Etching –
    Semi permanent
    Can be buffed off
    Procedure:
      Use a stencil
      Solutions
      Electricity
      http://www.youtube.com/watch?v=ILPQDXV_Rf0&feature=share&list=PL626DB81D87B2582B

## Slide 31
Laser Etching
  Permanent
  Costly
Electric etching (engraving)
  Damages the surface of the instrument

## Slide 32
Lubrication
  Neutral pH
  Easier to use
  Extends life of the instrument
Available in
  Spray bottle
  Dipping
Application
  Especially all moving areas

## Slide 33: Tray Assembly
Organization factors:
  Presenting to sterile field
  Protecting instruments
Recommendations:
  Heavy on bottom
  Tray must allow
  adequate space for
  weight distribution
  Curved tips go in
  same direction
  Forceps should be
  gently nested together

## Slide 34
  Stringers hold finger ring of instruments
    Helps with faster setup of sterile field
    Keeps instruments safer
  Laser coated instrument
    Keep separated to prevent damaging coating
    Use silicon nipple mat, foam or lint-free towel

## Slide 35
  Delicate in protective case in tray