## Slide 1: Sterile Processing for Ambulatory Surgery and Other Practices
Chapter 23 7th Ed.
Rosemary Thurston RN

## Slide 2: Sterile Processing is Universal
Skills are used in various facilities
  Hospitals
  Ambulatory surgery centers
  Dental facilities
  VA institutions
  Clinics
  Veterinary hospitals
  3rd party processors
  Some manufacturers

## Slide 3
Skills are Universal
  Process is the same everywhere
  Facilities may be regulated differently
    May have different regulations and standards
    May cause modification in practice
  Ambulatory Surgery Center
    Have 1+ operating rooms
    With the equipment necessary for safe surgery

## Slide 4: Ambulatory Surgery Centers
Historical
  Surgical procedures occurred in physician offices
  Development of surgery centers separate from hospitals
  Hospital Outpatient departments - HOPDs
    Offer overnight services for patient needing extended recovery times
    Single specialty or multi specialty stand-alone centers

## Slide 5
  Types
    GI – Gastrointestinal Procedure units
      Do endoscopy
        Colonoscopy – viewing the colon
        EGD’s - esophagogastroduodenoscopy
      Diagnostic – Biopsies
      Therapeutic – Dilations
    Ophthalmic Procedures
      Surgical – cataracts and treating glaucoma
      Therapeutic – laser treatment of retina

## Slide 6
    MIS – Minimally Invasive Surgery
      Endoscopic through a small incision
        Cholecystectomy – gall bladder removal
        Tubal ligation – tying off fallopian tubes
      Sports Medicine
        Arthroscopies – torn meniscus trimming
        ACL Repairs
  Multi-Specialty ASC
    One facility provides many specialties in one place

## Slide 7: Ownership and Regulation
Ownership
  Physicians own about 90% of ASCs
  Jointly owned – MD and Hospitals
  Hospital owned – small amount
    Called “Satellite Surgery Centers”
Regulatory Standards
  Federal and State agencies regulate
  States may require licensure
    Includes Reporting and On-site Inspections

## Slide 8
Medicare reimbursement
  Since 1982
  Must comply with federal government standards
  Must be accredited by TJC (The Joint Commission)
    Limit procedures to
      Elective ones – not emergency
      Short procedures with anesthesia
      Don’t require overnight stay

## Slide 9
Growth continues
  More MIS procedures
  Faster acting anesthetic agents
  Aging population

## Slide 10: Accreditation
Accreditation –
  Voluntary process
    Measures quality of service and performance
    As compared to a national standard
      Reviews compliance with standards
    On-site inspection
  Applied to
    Hospitals
    Stand-alone healthcare facilities - ASCs

## Slide 11
Accrediting Organizations
  The Joint Commission – TJC
  Accreditation Assoc. of Ambulatory Health Care – AAAHC
  American Assoc. of Accreditation of ambulatory Surgery Facilities – AAAASF
  American Osteopathic Association - AOA

## Slide 12
Sterility Assurance
  2006 – AAMI and ANSI Guide
    Guidelines for ASC in Recommended Practices
  AORN
    Recommended Practices for ASCs
    References “ST 79” Recommended Practice for Steam Sterilization – from AAMI

## Slide 13: ASC Processing
Infection control in ASC
  Sterile processing control person
    Usually a person trained to oversee process
      May be an RN or Surgical Technologist
    References guidelines / best practices
      From Assoc. for Prof. in Infection Control and Epidemiology – APIC
  Fast paced environment
    Turnovers done quickly
      Terminal cleaning and sterilization processing
    End of day
      Pick cases for next day, stock inventory, maintain sterile storage

## Slide 14
  CS techs may be employed
    If there are multiple OR’s
    May require certification
  As instrumentation evolves
    Demand for CS Techs will grow

## Slide 15: Processing Environment
ASCs are fast paced
  May have to move between processing areas during day
  Instrument processing
    Done close to OR’s
    Need to work closely with OR personnel
    Configuration of processing area may vary
      Still need to separate “Dirty and Clean Areas”
      Work always flows from Dirty to Clean

## Slide 16
  Equipment – any combination of:
    Sink
    Ultrasonic
    Washer-decontaminator
    Automated Endoscope Preprocessors – AER
    High-level disinfection or low temp sterilizers
  Follow OEM’s recommendations for equipment
    Reusable instruments
    Special care with single / limited use instruments

## Slide 17
  Use of PPE and Standard Precautions
    Same as hospital safety protocols
  Monitoring of liquid sterilization / disinfection
    Processing may be done by non-dedicated staff
    More people = more chance for errors
    Accurate record keeping provides tracking for possible errors in best practice procedures

## Slide 18
  Instrument assembly and sterilization
    Area can vary
    Includes:
      Instrument inventory
      Wrapping, packaging and labeling
      Sterilizers
        Steam – may be table top in small unit
        Plasma vapor
        Gas or Ozone units
        ETO – NOT USED because of long turnover times
    Limited number of instrument sets for cases
      May mean FLASH sterilization – “Immediate Use Sterilization”
      May need to be started by CS personnel

## Slide 19
Role of CS professionals in ASC
  Contribute best practices in reprocessing areas
  Another area of growth for CS Techs
  Area for continuing education

## Slide 20: Dental Facilities
Basic Standards and Practices
  Require
    Decontamination
    Sterilization
    Inventory management
  Instrument range
    Small basic instrumentation
    Power hand drills

## Slide 21: CDC Guidelines
  Sterilization/disinfection
    Environmental Issues
      Processing Area divided into 4 areas:
        Receiving, cleaning, decontamination
        Preparation and packaging
        Sterilization
        Storage
      Ideally – separated by walls / partitions
        Or space
      Goal
        Minimize risk of cross-contamination – soiled to clean

## Slide 22
  Environmental Surfaces
    Surfaces that don’t contact patients directly
    Clinical Contact Surfaces
      Directly contaminated during patient care
        Switches
        Power unit switches
        Drawer knobs
      Contamination
        Sprays, spatter, contact with providers hand

## Slide 23
      Includes:
        Light handles
        Switches
        Chair side computer
        Drawers
        Faucet
        Counter tops
      Protected by BARRIERS
        Barrier products
        Routine cleaning / disinfection between patients

## Slide 24
    Housekeeping Surfaces
      Includes:
        Walls
        Floors
        Sinks
      Cleaned
        On schedule
        When soiled

## Slide 25: Instrument Processing
Contaminated instruments
  Transported in enclosed container from POU
  Process as quickly as possible
    Otherwise must be kept moist
  Cleaning option – manual or automatic
    Must fit instrument need
    Must be adequate to meet sterilization needs
      You can clean an item without sterilizing it . . . But you can’t sterilize it without cleaning it!
  Must wear PPE

## Slide 26
Preparation and Packaging
  Inspect for
    Soil
    Functionality
    Unlocked
    Other per OEM
  Assembly
    Unwrapped loads – CI in each tray
    Wrapped – CI inside + External CI outside

## Slide 27
Sterilization Types used
  Steam – usually
    Dependable, economical
    Usually table top gravity displacement – possible pre-vac
  Dry heat
    Economical and non-corrosive
    High temps and long exposure times
      Oven type – coils on bottom and sides – heat through convection (air) – Instruments – conduction
      Rapid heat - circulate heat at high speed – decreased time
    Burrs and Orthodontic instrument damaged by moist heat

## Slide 28
  Unsaturated chemical vapor
    Usually Alcohol and Formaldehyde under pressure
    Less corrosive than steam for burrs – carbon steel
    Cycle times less than dry heat
  Liquid chemical sterilization used at times
    Gluteraldehyde
    PA – paracetic acid
    Hydrogen peroxide plasma vapor
  ETO at times
Quality Assurance through
  Cycle monitoring
  CI’s and BI’s

## Slide 29
Storage
  Enclosed cabinets
  Must protect integrity of each package
  Inspect before use for contamination
Polices and Procedures
  Written procedures should be at all facilities for:
    Decontamination
    Inspection
    Packaging
    Sterilization
    Storage

## Slide 30: Veterans Administration Facilities
“To care for him who shall have borne the battle and for his widow , and his orphan” Abraham Lincoln, 1865 Inauguration - VA Mott
Veterans Administration (VA) Hospitals
  Located throughout the US
  Sterile Processing Department - SPD is Central Service
    Has it’s own certification program

## Slide 31
  VA requirement to maintain certification
    Chiefs – 20 CEU’s
    Supervisors – 17 CEU’s
    SPD Techs – 5 CEU’s
  Directives are the “Standards”
    Organization structure
    Employee development
    Infection control
    Inventory management
    Safety standards

## Slide 32
Directives Continued
  Decontamination
  Preparation area
  Loading / operating sterilizers
  Distribution
  Inventory
  Equipment tracking
  Quality Control

## Slide 33
Practice Differences –
  To assure using proven practices for the best care available to the Veteran
Main differences
  Expiration Dates of one year
    Must be reprocessed at that time
  No 3rd party reprocessors
    Must use VA facilities
  No single use devices are reprocessed

## Slide 34
  Single wrappers x2 used to wrap items
    To allow aseptic opening
    To maintain a sterile field
  Peel pouches must be heat sealed – not self-sealing
    Concern regarding proper sealing
  No writing on packages – must write on tape and apply that
    Concern re integrity of package material

## Slide 35
  All items are sterilized after decontamination process
    Before going to the preparation area for assembly
  BI tests are incubated and read at 48 hours
    3 hour tests can be used, but . . .
    48 hour tests must still be run and documented
  Validation of reprocessed items it not performed by VA personnel
    Only those approved on the 510K application are allowed

## Slide 36
  Use of Internal CI is at the discretion of SPD personnel
  Sterilization of liquids is not permitted

## Slide 37: Additional Related Practices
Sterile Processing services all occur in these practices:
  Clinics
  Veterinary hospitals
  Third party reprocessing facilities
  Some manufacturers

## Slide 38
Wherever instruments and equipment are needed for patient care . . .
Central Service skills are needed

## Slide 39
The End 