## Slide 1: Progress Test 3 Review

## Slide 2: When using a Mechanical Washer, what should be done to ensure proper cleaning?
1.
2.
3.
4.

## Slide 3: 1. 1. Separate Multi-level Trays 2. Lids on trays should be opened 3. Instruments should be disassembled and opened 4. Items should be washed on the appropriate cycle (check ___?)

## Slide 4: True or False? All items may be washed in the same cycle?

## Slide 5: FALSE!! Items are washed on the cycle appropriate to the device.
Hospital equipment, such as IV pumps and feeding pumps should be decontaminated __________________.

## Slide 6: After each use
____________ and _________approved for the disinfection of endoscopes.

## Slide 7: Glutaraldehyde and ortho-phthalaldehyde(OPA)
What is disinfection?

## Slide 8: Chemical that is used on inantimate objects but does NOT kill spores.
What is an antiseptic?

## Slide 9: Used on living tissues, such as skin to slow growth of microorganisms.
What is the difference between high-level disinfection and sterilization?

## Slide 10: High-level disinfection does not kill spores, sterilization kills spores but not prions.
True or False? You can decontaminate before you sterilize, but you don’t have to decontaminate before you disinfect

## Slide 11: You can clean without sterilizing or disinfecting, but you can’t sterilize or disinfect without cleaning.
.

## Slide 12: False! You must decontaminate (clean) before disinfecting and sterilizing!
True or False? Disinfectants can make something sterile.

## Slide 13: False! Disinfection does not kills spores, only sterilization does.
What is the difference between a detergent and a disinfectant ?

## Slide 14: Detergent – soap Disinfectant – chemical that kills most microorganisms except spores.
When liquid chemicals are labeled as both a high-level disinfectant and a sterilant, the time required to achieve sterilization is ______________than the time required to achieve a high-level disinfection.

## Slide 15: longer
What is the difference between a sterilant and sterilization?

## Slide 16: A sterilant or sterilization agent is a physical item or a chemical that has sufficient microbicidal activity to achieve sterility (kills spores). A sterilant may be used in sterilization.
The pH level of a detergent measures it’s ________________ or ______________.

## Slide 17: Acidity or Alkalinity
A ph of 0-6 is ___________________ and a ph of 8-14 is______________.

## Slide 18: A pH of 0-6 is acidic and a pH of 8-14 is alkaline
What is the preferred pH for detergents?

## Slide 19: Neutral or mildly alkaline
What does Lipase break down?

## Slide 20: Fatty deposits (lip =fat)
What does a Protease Enzyme break down?

## Slide 21: Blood, mucous, feces, albumin
What does the enzyme Amylase break down?

## Slide 22: Starch
What is the process called when Ultrasonic waves pass through a cleaning solution, the molecules are set in rapid motion and small gas bubbles develop. As the bubbles become larger, they implode? which type of cleaner uses it?

## Slide 23: Cavitation Ultra sonic cleaner
What should not be placed in an Ultrasonic Cleaner?

## Slide 24: Chrome plated, ebonized, made of plastic, cork, glass, wood, chrome, rubber
This cleaning process relies on a combination of water, temperature, special detergent, and a spray force action. What is it called and which type of washer uses it?

## Slide 25: Impingement Mechanical Washer
When running a mixed load of containers and instruments, the _____________ cycle should be used for maximum effectiveness

## Slide 26: instrument
What is regulated medical waste? It must be____________.

## Slide 27: Waste capable of transmitting infectious disease. It must be red bagged.
What are some examples?

## Slide 28: Sharps, materials contaminated with blood, urine, and other body secretions, human tissue and body parts, human blood and body fluids
According to the Spaulding Classification System, ___________ are Instruments or objects introduced directly into the blood stream or other normally sterile areas. Examples include cardiac catheters and implants. Sterilization is recommended over disinfection.

## Slide 29: Critical Items
Examples of these include non-invasive flexible fiber optic endoscopes, endotracheal tubes, anesthesia breathing circuits, and cystoscopes. These items come into contact with mucous membranes, they do not ordinarily penetrate body surfaces. Sterilization is desirable but not absolutely essential, so High-level disinfection is recommended.

## Slide 30: Semi-Critical items
These items come into contact with patient but mostly with unbroken skin. Examples include blood pressure cuffs, crutches, bed boards, etc.

## Slide 31: Non-critical
____________ disinfection kills all vegetative microorganisms, tuberlce bacilli, most fungi, non-lipid and small viruses, and lipid and medium viruses but not large numbers of bacterial spores.

## Slide 32: High-level
____________ kills vegetative microorganisms, Myobacterium, Tuberculosis, var. bovis, fungi, lipid and non-lipid and medium-sized and small viruses, but necessarily bacterial spores.

## Slide 33: Intermediate-level
Disinfectants in this process cannot be relied upon to kill bacterial endospores, Myobacterium, all fungi, and small or lipid viruses.

## Slide 34
Classification of Patient Care Items p 158
Body contact | Destruction Method | Item Class
Intact skin |  | 
Mucous Membranes |  | 
Sterile Body Cavity |  | 

## Slide 35: Disinfectants
Name | Disinfectant type | Uses | Notes
Quaternary Ammonium Compounds “QUATS” |  |  | 
Phenolics |  |  | 
Ethyl or Isopropyl Alcohol |  |  | 
Chlorine |  |  | 
Buffered Iodine |  |  | 
Glutaraldehyde |  |  | 
OPA |  |  | 
Formaldehyde |  |  |