## Slide 1: Progress Test 3 Review
Part 2

## Slide 2
Detergents used in a mechanical washer should be______________________

## Slide 3: Low-foaming and a neutral pH
What will decrease the likelihood of mineral scale deposits?

## Slide 4: Softened water
anything that can be disassembled must be _______________________
during cleaning.

## Slide 5: disassembled(taken apart)
How do cleaning enzymes work?

## Slide 6: products are commonly used to clean heavily soiled items they break down or "digest" large organic molecules to facilitate their removal.

## Slide 7: To achieve a reasonable level of disinfection, alcohol must used as an Intermediate-level disinfectant must remain in wet contact with the surface of the object being disinfected for a minimum for _________ minutes.

## Slide 8: 5 minutes!!
What is another name for 400 series stainless steel ?

## Slide 9: Martensitic
Can disinfectants make something sterile?

## Slide 10: NO!! Disinfection and Sterilization are two separate processes, and disinfection cannot kill spores like sterilization can
When marking instruments, Instrument marking tape should be wrapped approximately ___________ times around the device.

## Slide 11: 1 to 1 ½!
How is the decision made to sterilize or use high-level disinfection?

## Slide 12: It’s according to the Spaulding Classification system
The purpose of a suction stylet is to__________________

## Slide 13: unclog the suction during surgery
How may instruments be marked?
1.
2.
3.

## Slide 14: 1. Instrument marking tape 2. Acid etching 3. Laser etching
What is wrong with electric etching/engraving?

## Slide 15: It damages the instrument and makes them more difficult to clean
Which lasts longer? Tungsten Carbide or Stainless Steel?

## Slide 16: Tungsten Carbide
Which would last longer? Stainless Steel or Martensitic Steel?

## Slide 17: n/a – they are the same thing!
These scissors have a black handle _________________.

## Slide 18: Microgrind, or Supercut Scissors

## Slide 19
When processing powered surgical instruments:
Never _________________.
Clean _________________.
Rinse__________________.
Use _____________________.

## Slide 20
Never immerse handpieces, attachments, or batteries in any solution, including water.
Clean surgical debris from attachments and handpieces using a nylon brush and mild detegent.
Rinse under running water while assuring that the water does not enter the battery contact area.
Use a decontamination battery to protect electrical components from moisture.

## Slide 21
Can most endoscopes be sterilized by high temperature?

## Slide 22: No! High temperature can damage the scopes
Which solutions are both approved for the disinfection of endoscopes?

## Slide 23: Glutaraldehyde and ortho-phthalaldehyde(OPA)
The largest operating channel in a flexible endoscope is called :

## Slide 24: instrument "biopsy" channel
After use, loaner instrumentation must be ____________________ before it is shipped out.

## Slide 25: decontaminated
Do all flexible endoscopes have internal channels?

## Slide 26: No, some do not.
What must be done with flexible endoscopes that fail a leak test ? Can you continue to use them?

## Slide 27: It is marked for repair, and must not be used
What is the machine called that can be used to process endoscopes?

## Slide 28: AER – Automated endoscope reprocessor
Can endoscopes be sterilized? Why or Why Not?

## Slide 29: No, because they are easily damaged and the temperature is too high
Cystoscope involves the visualization of the _______________.

## Slide 30: Urethra and bladder
The Gastroscope is used to visualize the ___________________________.

## Slide 31: Upper part of the digestive tract (esophagus, stomach, duodenum)
Which scopes are used to visualize the colon? Which is which?

## Slide 32: Colonoscope – visual inspection of the entire large intestine sigmoidoscope – visual inspection of the lower part of the large intestine
What should be used to thoroughly rinse and remove all traces of disinfectant from an endoscopes channels?

## Slide 33: filtered water
What is the first step when processing flexible endoscopes?

## Slide 34: Pre cleaning
When are instruments lubricated?

## Slide 35: After cleaning
Which are all the power sources for surgical instruments?

## Slide 36: Electric, Battery & Pneumatic