## Slide 1: Progress Test 4
Review Part B

## Slide 2
Cellulose-containing packaging materials are not compatible with ________________sterilization.

## Slide 3: hydrogen peroxide gas plasma
This type of sterilization involves the use of a toxic gas

## Slide 4: Ethylene Oxide
If EtO is so toxic, why is it used?

## Slide 5: it has better penetration capabilities than ozone and hydrogen peroxide gas plasma.
What type of packaging may be used with:
Ethylene Oxide
Hydrogen Peroxide/Plasma
Ozone

## Slide 6
Eto – all standard packaging
Hydrogen per/plasma – Nonwoven polypropolene or Tyvek
Ozone – Packaging compatible with most products

## Slide 7
True or False? Ethylene oxide must be monitored with chemical, physical, and biological monitors, but hydrogen peroxide gas plasma, and ozone sterilization only need biological monitors.

## Slide 8: FALSE! Ethylene oxide, hydrogen peroxide gas plasma, and ozone sterilization process must all be monitored using chemical, physical, and biological monitors.
Which type of materials should be used with EtO?

## Slide 9: Metal carts and baskets, since they don’t absorb EtO
Low temperature sterilization works with a process called ________________.

## Slide 10: Oxidation
Which has the longest turnaround time, EtO, Hydrogen Peroxide (Plasma), or Ozone?

## Slide 11: Eto- 1-4 hours exposure, 8-12 hours aeration
What is the most effective type of dry heat sterilization ? Why?

## Slide 12: Mechanical Convection- Gravity convection prone to air layering – p 313
What is a D-Value?

## Slide 13: The amount of time that it takes to kill 90% of the microorganisms present in an object
What is Geobacillus stearothermophilus ?

## Slide 14: The spore used in the biological indicator
Do chemical indicators prove that an item is sterile?

## Slide 15: No - provide a visual indication that an item was exposed to a sterilization process
In which type of sterilizer should a Bowie Dick test be run?

## Slide 16: dynamic-air-removal steam sterilizers
How do you elevate the pressure in a steam sterilizer?

## Slide 17: increase the steam pressure
The two most common temps in a steam sterilizer are:

## Slide 18: 250 degrees and 270 - 275 degrees F
If the sterilizer has successfully killed all the bacterial spores in a biological test, is it positive or negative?

## Slide 19: Negative!
Cellulose materials cannot be processed within a ____________sterilizer.

## Slide 20: Gas plasma
When placing ring-handled instruments in an instrument tray, you should:

## Slide 21: unlock the handles and open the instruments
When arranging plastic paper pouches in the sterilizer, how should the pouches be arranged?

## Slide 22: paper-to-plastic
What would be included on a load control information tag?

## Slide 23: Sterilizer number date sterilized load number
What is PCD?

## Slide 24: Process Challenge Device (p. 318)
Creutzfeldt-Jakob Disease is caused by :

## Slide 25: prions
The most widely used temperature for dry heat sterilization is _______ degrees Fahrenheit for __________ hours.

## Slide 26: 320 Degrees F 2 hours
What is the difference between validation and verification?

## Slide 27: Validation-Manufacturer Verification- healthcare facility