## Slide 1: Progress Test 4
Review Part 1

## Slide 2
Tests which use live bacterial spores to challenge the efficacy of the sterilization process and provide a direct measure of lethality are called:

## Slide 3: Biological Indicator Test
When using Paper-plastic pouches, which side should you write on?

## Slide 4: The plastic side! Why?
Upon opening, paper-plastic pouch seals must be _______________________.

## Slide 5: incapable of resealing
You are wrapping a basin set to be sterilized, should you put a pack of scissors, which is inside a paper/plastic sterilization pouch, inside the basin and wrap them together?

## Slide 6
No, never place Paper/plastic sterilization pouches inside wrapped sets or containers
The term "superheated steam" means:

## Slide 7: Dry Steam
What provides a written record of sterilizer cycle activity?

## Slide 8: Mechanical Recording Charts Printout
You have to recall a load. What would you refer to In order to find those instruments?

## Slide 9: the sterilization log
All rigid-sterilization containers have _______________________seals.

## Slide 10: tamper-evident
To prevent contamination, packs should be kept ______ to_____inches above the floor.

## Slide 11: 8 to 10 inches
There should be at least __________ to ______________inches between the highest package and the ceiling to allow for proper circulation

## Slide 12: 8-10 inches
The relative humidity in CS should be:

## Slide 13: Less than 75%
The FDA classifies sterilization packaging as a:

## Slide 14: Class II Medical Device
WHAT is FIFO?

## Slide 15: First In, First out What does it mean? Examples?
What is wicking material? What should never be used as wicking material?

## Slide 16: Facilitates drying Gauze squares
In wrapping flat objects, this is “a package within a package,” meaning that the package has been wrapped twice, the contents have been wrapped in sequence.

## Slide 17: Sequential
This package is only wrapped once, but it requires special double-layered, synthetic non-woven material bound on 2 to 4 sides.

## Slide 18: Simultaneous
This fold is the most frequently used on for larger packs and instrument trays.

## Slide 19: Square fold
This fold is commonly used for small packs, most instruments sets, and individual items.

## Slide 20: Envelope fold
What is Flash Sterilization? When is it used?

## Slide 21: U unwrapped instruments sterilized for immediate use emergencies!!
May implantable devices be Flash Sterilized?

## Slide 22: No! Why not?
You need to flash sterilize a single instrument without a lumen. How long of a cycle must you use? What temp?

## Slide 23: 3 minutes @ 270 degrees F
How about with complex or lumined instruments, mixed materials, or multiple instruments?

## Slide 24: 1o min @ 270 Deg F
What should be placed in each tray to be flash sterilized?

## Slide 25: Chemical Indicators
Class 5 integrators are a good choice for flash sterilization because they monitor which parameters?

## Slide 26: time & temperature & moisture
This is a liquid oxidizing agent that is an affect biocide at low temperatures.

## Slide 27: Peracetic Acid (PA)
The more bioburden that is present on an object, the more ________________________.

## Slide 28: Difficult is to sterilize
Where is the chamber drain located on most steam sterilizers? How often must it be cleaned?

## Slide 29: Front or center of floor Daily
The sterilizer’s gauges and/or controls(monitors) provide a __________ and ________record of sterilization conditions.

## Slide 30: visual and written
What is the aeration time required for Hydrogen Peroxide (Plasma) and Ozone?

## Slide 31: Not required!
What is the special consideration that must be made in terms of flash sterilizing instruments with lumens?

## Slide 32: All devices and all lumens must be thoroughly cleaned