## Slide 1: Threading Tools

## Slide 2: Taps
The hand taps are delicate tools used for cutting internal threads (inside a drilled hole). The picture above shows the main parts of a tap.
Standard Taps over ¼ inch in diameter are made in three different shapes; Taper tap, Plug tap, and Bottoming tap.

## Slide 3: Taper Taps
Taper Taps are used to start a thread. The flutes and cutting teeth are tapered. Very little metal is removed when starting the taper tap in a hole. As the tap progresses into the hole, the flutes become larger and cut away more metal until the full thread size is reached. When you use this tap, make sure it goes as far into the hole as is possible. Other-wise a full thread will not be cut and bolts will bind during installation.

## Slide 4
Plug taps are also used to start threads, but they are not as tapered as the Taper tap. Plug taps cut full threads sooner than taper taps because of their design. Plug taps are harder to start than taper taps. The tap used most is the Plug tap.
Plug Taps

## Slide 5: Bottoming & Pipe Taps
Bottoming taps are used after plug taps to cut full threads to the bottom of blind holes.
The Pipe tap is used to tap holes for pipe fittings; such as standard transmission drain and refill plugs, grease fittings, differential plugs, copper tubing fittings etc.

## Slide 6: Tap Handle
Tap handles are clamped to the driving head of taps and are used to turn taps in holes. Taps handles are usually adjustable and vary in style.

## Slide 7: Dies
Dies are used to cut machine screw threads on the outside of metal rods, or round stock.
Dies are round or hex shaped. They have a three or four lobed hole in the center to form flutes. The flutes have cutting teeth.
So that the dies start easily on round stock, one or both sides of the die’s flutes are tapered.
*Always start the round stock into the tapered side of the die, or you will break the die.

## Slide 8: Die Stocks
Die stocks are used to turn dies for thread cutting, like the tap handle turns taps. The die fits in the hole and is tightened in place with the set screw.

## Slide 9: Rethreading Dies
Rethreading dies are used to repair damaged threads. They are usually hex shaped and have six flutes instead of four, as in standard dies.
*DO NOT cut new threads with a rethreading die, it will damage the tool.

## Slide 10: Thread Pitch Gauge
Thread pitch gauges are used to measure the threads per inch on bolts, nuts, and other threaded surfaces. A thread pitch gauge has many blades, with teeth of different sizes on each blade. They all fit inside a case, just like a pocket knife.
You can read threads per inch with a ruler, counting the actual threads in an inch, but the thread pitch gauge eliminates counting. This cuts down on errors.

## Slide 11
The drawing below shows how a thread pitch gauge is used. The number “10” on the blade means there are 10 threads per inch. If you count the threads, you will see it is easier and faster to use the thread pitch gauge.

## Slide 12: Metric Thread
Another type of thread that is becoming very common in the automotive industry, is the metric type thread. The drawing below shows a Metric thread pitch gauge being used. The number 1.75 on the gauge indicates the thread pitch is the fastener as 1.75 mm. Metric thread pitch may vary from 0.90 mm to 3.0 mm. The most common thread pitches are 1.0 to 2.0.

## Slide 13: For More Information visit the site below:
http://www.answers.com/topic/taps-and-dies