## Slide 1
Cardiopulmonary Procedures
Chapter 27

## Slide 2: Learning Objectives Lesson 27.1: Introduction to Electrocardiography (Slide 1 of 2)
State the purpose of electrocardiography.
Identify each of the following components of the ECG cycle:
  P wave
  QRS complex
  T wave
  PR segment
  ST segment
  PR interval
  QT interval
  Baseline following the T wave

## Slide 3: Learning Objectives Lesson 27.1: Introduction to Electrocardiography (Slide 1 of 2)
State the purpose of the standardization mark.
State the functions of the electrodes, amplifier, and galvanometer.
List the 12 leads that are included in an ECG.

## Slide 4: Introduction to Electrocardiography (Slide 1 of 7)
Electrocardiograph: Instrument used to record the electrical activity of the heart
Electrocardiogram (ECG): Graphic representation of the electrical activity of the heart
  Cardiovascular disorders can cause abnormal changes on an ECG

## Slide 5: Introduction to Electrocardiography (Slide 2 of 7)
Purposes of electrocardiography
  Evaluate the following symptoms
    Chest pain
    Shortness of breath
    Dizziness
    Heart palpitations
  Detect abnormality in heart rate or rhythm (dysrhythmia)
  Detect presence of impaired blood flow to heart muscle (cardiac ischemia)
  Help diagnose damage to heart caused by myocardial infarction
  Determine the presence of hypertrophy of the heart

## Slide 6: Introduction to Electrocardiography (Slide 3 of 7)
Purposes of electrocardiography
  Detect myocarditis or pericarditis
  Assess the effect on the heart of digitalis or other cardiac drugs
  Determine the presence of electrolyte disturbances
  Assess the progress of rheumatic fever
  Detect congenital heart defects
  Performed before surgery to assess cardiac risk during surgery
  As part of a complete physical examination

## Slide 7: Introduction to Electrocardiography (Slide 4 of 7)
ECG cannot detect all cardiovascular disorders
  Cannot always detect impending heart disease (e.g., MI)
ECG is taken with patient in a resting state
  Only records 10 seconds of the heart’s activity
    If patient has an intermittent dysrhythmia, may not occur during this brief time
  Patient with angina pectoris
    Does not usually have symptoms in a resting state; ECG may appear normal

## Slide 8: Introduction to Electrocardiography (Slide 5 of 7)
To obtain a complete assessment of cardiac functioning ECG must be used in combination with:
  Patient’s symptoms
  Health history
  Physical examination
  Other diagnostic and laboratory tests

## Slide 9: Introduction to Electrocardiography (Slide 6 of 7)
MA responsible for running ECG, which includes:
  Preparation of the patient
  Operation of electrocardiograph
  Identification and elimination of artifacts
  Care and maintenance of the electrocardiograph
Notes: The MA should explain the procedure to the patient.

## Slide 10: Introduction to Electrocardiography (Slide 7 of 7)
ECG machine formats
  Single-channel format: One lead recorded at a time
  Three-channel format: Three leads recorded at one time
    Most offices use this
Notes: The MA must read the operating manual before performing an ECG.
Refer to Figure 27.1.

## Slide 11: Cardiac Cycle (Slide 1 of 2)
Represents one complete heartbeat
Consists of:
  Contraction of atria
  Contraction of ventricles
  Relaxation of entire heart
Notes: Refer to Figure 27.2.

## Slide 12: Cardiac Cycle (Slide 2 of 2)
ECG: Records electrical activity that causes cardiac cycle to occur
ECG cycle: Graphic representation of cardiac cycle

## Slide 13: Waves (Slide 1 of 4)
P wave
  Represents electrical activity associated with contraction of the atria
  Known as atrial depolarization
Notes: The ECG cycle is recorded and read from left to right, beginning with the P wave.

## Slide 14: Waves (Slide 2 of 4)
QRS complex (consists of Q, R, S waves)
  Represents electrical activity associated with contraction of the ventricles
    Known as ventricular depolarization
  Ventricles are larger than atria
    Requires a stronger electrical stimulus to depolarize ventricles—causes R wave to be taller than P wave

## Slide 15: Waves (Slide 3 of 4)
T wave
  Represents electrical recovery of the ventricles
    Known as ventricular repolarization
  Muscle cells are recovering in preparation for another impulse
  Atrial repolarization (electrical recovery of atria)
    Occurs following P wave
    Occurs at same time as ventricular depolarization (QRS complex)—causes it to be masked by QRS complex; therefore does not appear as a separate wave on the ECG cycle

## Slide 16: Waves (Slide 4 of 4)
U wave
  Occasionally follows T wave
  Small wave
  May be associated with repolarization

## Slide 17: Baseline, Segments, and Intervals (Slide 1 of 2)
Baseline
  Flat, horizontal line that separates various waves
  Heart is at rest (polarized)
No electrical activity is occurring in heart

## Slide 18: Baseline, Segments, and Intervals (Slide 2 of 2)
Baseline
  Electrocardiograph doesn’t have anything to record
    This is why the baseline is flat
  Waves deflect either upward or downward from baseline
    Positive deflection: Wave deflects upward
    Negative deflection: Wave deflects downward
ECG: Divided into segments and intervals between P wave and T wave
  Purpose: Interpretation and analysis of ECG

## Slide 19: Segments (Slide 1 of 2)
Segment: Portion of the ECG between two waves
PR segment
  Time interval from the end of atrial depolarization to the beginning of ventricular depolarization
    Represents time needed for impulse to be delayed at AV node, then travel through bundle of His and Purkinje fibers to ventricles

## Slide 20: Segments (Slide 2 of 2)
ST segment
  From the end of ventricular depolarization to the beginning of repolarization of ventricles

## Slide 21: Intervals
Interval: Length of a wave or length of wave with a segment
PR interval
  Time interval from the beginning of atrial depolarization to the beginning of ventricular depolarization
QT interval
  Time interval from the beginning of ventricular depolarization to the end of repolarization of the ventricles

## Slide 22: Baseline
Baseline (after T wave or U wave)
  Period when entire heart returns to resting or polarized state

## Slide 23: Electrocardiograph Paper (Slide 1 of 5)
Paper divided into two sets of squares
  Small square: 1 mm high and 1 mm wide
  Large square: 5 mm high and 5 mm wide
    Each large square is made up of 25 small squares
Notes: Refer to Figure 27.3.

## Slide 24: Electrocardiograph Paper (Slide 2 of 5)
Provider uses graph to measures waves, intervals, and segments
Determines if ECG is within normal limits

## Slide 25: Electrocardiograph Paper (Slide 3 of 5)
Heart disease
  Can trigger abnormal changes on ECG cycle
    Causes results to fall outside normal limits
    Example: Cardiac ischemia (due to CAD) can cause depressed S-T segment and inverted T wave
    Example: Myocardial infarction can cause larger than normal Q wave and elevated S-T segment

## Slide 26: Electrocardiograph Paper (Slide 4 of 5)
Paper contains a thermosensitive coating
  Black or red graph printed on top of coating
Thermal print head
  Produces ECG tracing
Generates heat in a prescribed pattern

## Slide 27: Electrocardiograph Paper (Slide 5 of 5)
Thermosensitive paper
  Comes in contact with heated print head
    Coating of paper turns black where it is heated
    Produces ECG tracing
Paper is also pressure-sensitive
  Handle carefully to avoid making impressions
    May interfere with proper reading of ECG

## Slide 28: Standardization of the Electrocardiograph (Slide 1 of 3)
Electrocardiograph must be standardized for every recording
  Quality control measure
    Ensures an accurate and reliable recording
    Also means ECG run on one electrocardiograph compares in accuracy with a recording run on another machine
Notes: Compare the standardization of an electrocardiograph to balancing a scale before taking a patient’s weight.

## Slide 29: Standardization of the Electrocardiograph (Slide 2 of 3)
Normal standardization mark
  Height: 10 mm (10 small squares)
  Width: Approximately 2 mm wide (2 small squares)
Notes: Refer to Figure 27.4.

## Slide 30: Standardization of the Electrocardiograph (Slide 3 of 3)
Three-channel machine
  Automatically records standardization marks
  One mark recorded at beginning and end of each ECG strip
If standardization mark is more or less than 10 mm high
  Machine must be adjusted
  Consult operating manual for adjustment information

## Slide 31: Electrocardiograph Leads (Slide 1 of 6)
Consists of 12 leads
  Lead: A tracing of the electrical activity of the heart between two electrodes
Each lead
  Provides an electrical “photograph” of heart’s activity from a different angle
  Results in 12 “photographs” of the heart
    Facilitates thorough interpretation of heart's activity

## Slide 32: Electrocardiograph Leads (Slide 2 of 6)
Electrode
  Made of a substance that is a good conductor of electricity
  Picks up electrical impulses given off by the heart
    Conducts impulse into machine by lead wires
Notes: Electrodes are attached to the patient’s skin. Leads are attached to the electrodes.

## Slide 33: Electrocardiograph Leads (Slide 3 of 6)
Amplifier: Device located in machine that amplifies the electrical impulses
  Electrical impulses given off by the heart are very small (0.0001 to 0.003 volt)
Must be made larger (amplified)

## Slide 34: Electrocardiograph Leads (Slide 4 of 6)
Galvanometer: Changes amplified voltages into mechanical motion
Thermal print head: Records heart tracing on ECG paper
Ten lead wires: Attached to patient
Used to take 12 electrical “photographs” of heart

## Slide 35: Electrocardiograph Leads (Slide 5 of 6)
Four limb lead wires
  Right arm (RA)
  Left arm (LA)
  Right leg (RL): Ground
    Not used for recording
    Serves as an electrical reference point
  Left leg (LL)
Notes: The tips of the limb lead wires are labeled (RA, LA, RL, LL) and must be attached correctly in order to obtain an accurate ECG.

## Slide 36: Electrocardiograph Leads (Slide 6 of 6)
Chest lead wires
  Abbreviated V
  Uses six chest electrodes
Notes: The tips of the chest lead wires are labeled (V1–V6) and must be attached correctly to obtain an accurate ECG.

## Slide 37: Electrodes (Slide 1 of 5)
Used to record a resting 12-lead electrocardiogram
Contain a thin layer of a metallic substance
  Good conductor of electricity
Square in shape
  Tab extends from one end
    Allows for firm attachment of alligator clip
Notes: The patient may want to remove the electrodes himself or herself after the ECG is performed.
Refer to Figures 27.5 and 27.6.

## Slide 38: Electrodes (Slide 2 of 5)
Electrolyte gel combined with an adhesive
  Located on back of electrode
    Electrolyte: A substance that facilitates the transmission of the heart’s electrical impulse
  Skin is a poor conductor of electricity
    Electrolyte must be used when recording ECG
  Adhesive: Allows for firm adherence of electrode to skin
    No adhesive on tab—allows for attachment of alligator clip

## Slide 39: Electrodes (Slide 3 of 5)
Electrolyte gel combined with an adhesive
  Applied to the skin
    Held in place with adhesive backing
    Thrown away after use
  Available on cards containing 10 electrodes

## Slide 40: Electrodes (Slide 4 of 5)
Electrolyte gel combined with an adhesive
  Foil-lined pouch
    Holds 10 cards of electrodes (100 electrodes per pouch)
    Preserves moisture
    Prevents electrolyte from drying out
  Expiration date
    Stamped on each electrode pouch (and box containing the pouches)
    Always check expiration date before applying
    Electrolyte gel on outdated electrodes may be dried out—unable to transmit a good ECG signal

## Slide 41: Electrodes (Slide 5 of 5)
Electrolyte gel combined with an adhesive
  Store properly to prevent electrolyte drying
    Cool area (less than 75º F or 24º C)
    Away from sources of heat
  After opening electrode pouch
    Seal by folding over the end of it
    Place pouch in a zip-lock plastic bag to preserve moisture

## Slide 42: Bipolar Leads (Slide 1 of 2)
Each bipolar lead uses two limb electrodes to record electrical activity of the heart
  Lead I: Records electrical current between right arm and left arm
  Lead II: Records electrical current between right arm and left leg
  Lead III: Records electrical current between left arm and left leg
Notes: Explain to students that each lead takes a “picture” of the heart.
Refer to Figure 27.7.

## Slide 43: Bipolar Leads (Slide 2 of 2)
Lead II shows heart’s rhythm more clearly than other leads
  Rhythm strip: Longer recording (12 inches) of lead II; often requested by provider

## Slide 44: Augmented Leads (Slide 1 of 3)
aVR (augmented voltage—right arm)
  Records electrical current traveling between right arm electrode and a central point between left arm and left leg

## Slide 45: Augmented Leads (Slide 2 of 3)
aVL (augmented voltage—left arm)
  Records electrical current traveling between
    Left arm electrode and a central point between right arm and left leg

## Slide 46: Augmented Leads (Slide 3 of 3)
aVF (augmented voltage: left leg or foot)
  Records electrical current traveling between left leg electrode and a central point between right arm and left arm
Leads I, II, III, aVR, aVL, and aVF
  Provides electrical photograph of heart’s activity from side to side and from top to bottom of heart

## Slide 47: Chest Leads (Slide 1 of 4)
V1, V2, V3, V4, V5, and V6
  Record heart’s voltage from front to back of heart from a central point “inside” the heart to a point on the chest wall where each chest electrode is placed
Notes: It takes a lot of practice to properly locate the chest leads.

## Slide 48: Chest Leads (Slide 2 of 4)
Leads must be properly located to ensure an accurate and reliable recording
  Example: If V1 and V2 are placed in third (instead of fourth) intercostal space, changes can occur to P and T waves that falsely indicate heart disease
Notes: Refer to Figure 27.8.

## Slide 49: Chest Leads (Slide 3 of 4)
When first learning to locate electrode sites, helps to mark location of chest with a felt-tipped pen
Normally ECG is recorded with paper moving at a speed of 25 mm/second

## Slide 50: Chest Leads (Slide 4 of 4)
Recommended positions for ECG chest electrodes
  V1, fourth intercostal space at right margin of sternum
  V2, fourth intercostal space at left margin of sternum
  V3, midway between positions 2 and 4
  V4, fifth intercostal space at junction of left midclavicular line
  V5, at horizontal level of position 4 at left anterior axillary line
  V6, at horizontal level of position 4 at left midaxillary line

## Slide 51: Patient Preparation (Slide 1 of 2)
Minimal preparation required for an ECG
Purpose: Facilitate placement of electrodes
Ensure good adhesion of the electrodes to skin

## Slide 52: Patient Preparation (Slide 2 of 2)
Instruct patient in the following
  Do not apply body lotion, oil, or power on day of test
    May make it more difficult to apply electrodes
  Wear comfortable clothing
  Wear a shirt or blouse that can easily be removed
Women should not wear full-length hosiery (e.g., pantyhose or tights)
Notes: Click to add notes

## Slide 53: Maintenance of the Electrocardiograph (Slide 1 of 3)
Casing
  Clean frequently
    Use a soft cloth slightly dampened with a mild detergent to remove dust and dirt
    Do not use solvents or abrasives—can damage finish of casing
Notes: Instructions for cleaning the electrocardiograph are included in the operating manual.

## Slide 54: Maintenance of the Electrocardiograph (Slide 2 of 3)
Patient cable, lead wires, and power cord
  Clean periodically with a cloth moistened with a disinfectant
Never immerse cables in cleaning solution
  Could damage them
Inspect cables frequently for cracks or fraying
  Replace if needed
Notes: Check to make sure lead wires and cables are intact and not frayed.

## Slide 55: Maintenance of the Electrocardiograph (Slide 3 of 3)
Check metal tip of each lead wire for adhesive/electrolyte gel residue
  Can interfere with transmission of a good ECG signal
  Remove residue with alcohol wipe using pressure and friction
Reusable alligator clips: Clean thoroughly with alcohol wipe after patient use
Should fit snugly on metal tip of each lead wire

## Slide 56: Learning Objectives Lesson 27.2: Taking an Electrocardiogram, Holter Monitor Electrocardiography, and Cardiac Dysrhythmias (Slide 1 of 2)
Describe the function served by each of the following:
  Three-channel recording
  Interpretive electrocardiography
  Electronic health record connectivity
  Teletransmission

## Slide 57: Learning Objectives Lesson 27.2: Taking an Electrocardiogram, Holter Monitor Electrocardiography, and Cardiac Dysrhythmias (Slide 2 of 2)
Identify each of the following types of artifact, and state its causes:
  Muscle
  Wandering baseline
  60-cycle interference
  Interrupted baseline
List the reasons for applying a Holter monitor.
List the three categories of cardiac dysrhythmias.
State examples of cardiac dysrhythmias.

## Slide 58: Three-Channel Recording Capability (Slide 1 of 4)
Records electrical activity of three leads simultaneously
  Single-channel records only one lead at a time
Advantage: ECG can be run in less time
Notes: Most offices use a three-channel ECG machine.
See Procedure 27.1: Running a 12-Lead, Three-Channel Electrocardiogram.

## Slide 59: Three-Channel Recording Capability (Slide 2 of 4)
Leads recorded simultaneously
  I, II, III
  aVR, aVL, aVF
  V1, V2, V3
  V4, V5, V6

## Slide 60: Three-Channel Recording Capability (Slide 3 of 4)
Electrocardiograph automatically labels each lead with its appropriate abbreviation
Requires three-channel recording paper (8½ by 11 inch)
  Printout fits easily into a paper-based medical record

## Slide 61: Three-Channel Recording Capability (Slide 4 of 4)
Most have copy capability
  Quickly produces duplicate copy of an ECG just recorded
Some have memory storage
  Specific number of ECGs can be stored for later retrieval
  Misplaced ECG can be retrieved and printed out again
Notes: Refer to Figure 27.9.

## Slide 62: Interpretive Electrocardiograph (Slide 1 of 3)
Built-in computer program
  Analyzes recording as it is being run
Provides immediate information on heart’s activity
  Leads to earlier diagnosis and treatment
Notes: Should a computer-interpreted ECG also be reviewed by a cardiologist? Explain the reason for your answer. (Answers will vary.)

## Slide 63: Interpretive Electrocardiograph (Slide 2 of 3)
Patient data must be entered into electrocardiograph before running
  Patient age
  Sex
  Height
  Weight
  Medications
Notes: A computer keypad is used to enter the data.
Refer to Figure 27.10.

## Slide 64: Interpretive Electrocardiograph (Slide 3 of 3)
Patient data and analysis are printed at top of recording
  Along with reason for interpretation
Results reviewed and interpreted further by provider
Notes: The provider signs the ECG report after reviewing it.

## Slide 65: EHR Connectivity (Slide 1 of 2)
Allows electrocardiograph to be linked with office computer
  Either wirelessly or through a USB port
Digital image of ECG sent to computer
  Displayed on screen of computer

## Slide 66: EHR Connectivity (Slide 2 of 2)
Software also analyzes ECG
  Displays this information on screen
    Along with reason for each interpretation
Copy of ECG can be printed out (if needed)
ECG report is reviewed and interpreted further by the provider
ECG stored electronically in patient’s EMR

## Slide 67: Teletransmission
Transmits recording electronically over phone line to ECG data interpretation site
Recording interpreted by cardiologist
  Along with computer analysis
Interpretation and ECG recording
  Electronically transmitted to sending office on the same day
Notes: The MA may be responsible for transmitting the ECG to a cardiologist.

## Slide 68: Artifacts (Slide 1 of 4)
Important to produce a clear and concise ECG
  Can be easily read and interpreted by computer and provider
Occasionally artifacts appear in recording
  Artifact: Additional electrical activity picked up by electrocardiograph
    Interferes with normal appearance of ECG cycles

## Slide 69: Artifacts (Slide 2 of 4)
Affects quality of recording
  Makes it difficult to manually measure ECG cycles
May cause a false-positive on ECGs analyzed by a computer
Artifacts must be identified and corrected by the MA

## Slide 70: Artifacts (Slide 3 of 4)
Most common artifacts
  Muscle
  Wandering baseline
  60-cycle interference (AC artifact)

## Slide 71: Artifacts (Slide 4 of 4)
If unable to correct artifacts, machine may be broken
  Contact service technician with the following information
    What has already been done to locate and correct the problem
    Leads in which artifact occurs
    Sample of the artifact

## Slide 72: Muscle Artifact (Slide 1 of 3)
Characterized by fuzzy, irregular baseline
Due to:
  Involuntary muscle movement (somatic tremor)
  Voluntary muscle movement
Notes: Refer to Figure 27.11A.

## Slide 73: Muscle Artifact (Slide 2 of 3)
Caused by apprehensive patient
  To correct: Reduce apprehension
    Relaxes muscles—explain the procedure; reassure patient that ECG is painless
Caused by patient discomfort
  To correct: Make patient more comfortable
    Ensure table is wide enough to support patient’s arms and legs; place pillow under patient’s head; ensure room temperature is comfortable to patient (patient has removed clothing and may be cold; can cause shivering)

## Slide 74: Muscle Artifact (Slide 3 of 3)
Caused by patient movement
  To correct: Instruct patient to lie still and not to talk
Caused by physical condition
  Nervous system disorder that may prevent relaxation (e.g., Parkinson’s disease)—patient trembles continuously
  Difficult to obtain an ECG free of artifacts
  To reduce artifacts—have patient put hands under buttocks with palms facing downward

## Slide 75: Wandering Baseline Artifact (Slide 1 of 3)
Caused by loose electrodes
  Results in poor transmission of electrical impulse
  To correct: Ensure electrodes are attached firmly to patient’s skin
    If electrode pulls loose: Reattach with tape; replace with a new electrode
    Ensure clips are firmly attached to electrodes
    Ensure patient cable is well supported on patient's abdomen or table to prevent pulling of lead wires on electrodes—can cause electrodes to pull away from skin
    Do not allow cable to dangle
Notes: Refer to Figure 27.11B.
When should a new disposable electrode be applied if an electrode comes loose? (If the electrolyte has dried out)
If a clip is damaged, replace it with a new clip.

## Slide 76: Wandering Baseline Artifact (Slide 2 of 3)
Caused by dried-out electrolyte on electrode
  Prevents good adhesion of electrodes to skin
  To correct: Replace it with a new electrode
    Check expiration date stamped on electrode pouch (or box) to make sure within their expiration date
Caused by body creams, oils, or lotions on skin at electrode application site
  To correct: Remove by rubbing with alcohol using friction
Notes: When should a new disposable electrode be applied if an electrode comes loose? (If the electrolyte has dried out)

## Slide 77: Wandering Baseline Artifact (Slide 3 of 3)
Caused by excessive movement of the chest wall during respiration
  To correct: Encourage patient to relax and breathe more calmly

## Slide 78: 60-Cycle Interference Artifact (Slide 1 of 4)
Also known as AC artifact
Due to electrical interference
Electric current can leak out from power used by electrical appliances in room
  May be picked up by patient and carried into machine—results in a 60-cycle interference artifact
Appearance of 60-cycle interference artifact
  Small straight spiked lines that are consistent
    Causes baseline to be thick and unreadable
Notes: The ECG should be plugged into an outlet by itself.
Refer to Figure 27.11C.

## Slide 79: 60-Cycle Interference Artifact (Slide 2 of 4)
Caused by lead wires not following body contour
  Dangling lead wires pick up electric current
  To correct: Arrange lead wires to follow body contour and to lie flat

## Slide 80: 60-Cycle Interference Artifact (Slide 3 of 4)
Caused by other electrical equipment in room leaking electric current
  To correct: Unplug nearby electrical equipment (lamps, autoclave, electrically powered examining table)
Caused by wiring in walls, ceiling, floors
  To correct: Move patient table away from walls
Notes: An electrician may be needed if interference keeps occurring.
Jewelry and watches do not interfere with recording; not necessary to remove unless they interfere with placement of electrodes.

## Slide 81: 60-Cycle Interference Artifact (Slide 4 of 4)
Caused by improper grounding of the electrocardiograph
  Machine is automatically grounded when plugged in (by three-prong plug)
  Check plug to make sure prongs are not loose or damaged
  Ensure plug is securely in wall outlet
  RL electrode picks up electric current from patient and carries it into machine—electric current is then carried away by grounding system of machine
Notes: An outlet may become loose. Have the outlet replaced if this happens.

## Slide 82: Interrupted Baseline Artifact
Caused by metal tip of lead wire becoming detached from alligator clip
  To correct: Reattach lead to alligator clip
Caused by frayed or broken patient cable
  To correct: Replace patient cable
Notes: Check all equipment before use.
Refer to Figure 27.11D.

## Slide 83: Holter Monitor Electrocardiography (Slide 1 of 3)
Portable ambulatory monitoring system
Continuously records electrical activity of the heart for 24 hours or more
Also known as ambulatory electrocardiographic monitor (AEM)
Notes: Refer to Figure 27.12.

## Slide 84: Holter Monitor Electrocardiography (Slide 2 of 3)
Detects cardiac abnormalities that occur while patient is engaged in normal daily routine
Holter system designed so that patient is able to maintain daily activities
  Minimal inconveniences
Notes: A patient who has had open-heart surgery may periodically undergo Holter monitor electrocardiography.

## Slide 85: Holter Monitor Electrocardiography (Slide 3 of 3)
Similar to a resting 12-lead ECG
  Electrical impulses given off by heart are picked up by electrodes
    Transmitted through lead wires to a recording device
  Different than a resting 12-lead ECG
    Only about 10 seconds of heart’s activity are recorded with a 12-lead ECG
Holter monitor records heartbeat continuously for an extended period of time
Notes: Refer to Figure 27.13.

## Slide 86: Purpose (Slide 1 of 2)
Used to diagnose cardiac rate, rhythm, and conduction abnormalities
Most frequently used to:
  Assess the rate and rhythm of the heart during daily activities
  Evaluate patients with unexplained chest pain, dizziness, or syncope (fainting)

## Slide 87: Purpose (Slide 2 of 2)
Most frequently used to:
  Discover intermittent cardiac dysrhythmias not picked up on a routine resting 12-lead ECG
    Resting ECG: Only records between 40 and 50 heartbeats
    Holter monitor: Records approximately 100,000 heartbeats in a 24-hour period
  Detect myocardial ischemia
  Assess the effectiveness of antidysrhythmic medications
    Examples: Digitalis and antianginal medications
  Assess the effectiveness of a pacemaker

## Slide 88: Digital Holter Monitor (Slide 1 of 3)
To document heart’s activity, use either:
  External (removable) memory card
  Internal (nonremovable) memory card

## Slide 89: Digital Holter Monitor (Slide 2 of 3)
Lightweight and battery-powered
Can be:
  Clipped onto a belt around waist
  Held in a protective pouch
    Hung around patient’s neck with a lanyard
Notes: Batteries are used to run the monitor.
A new battery needs to be inserted each time a Holter monitor is applied.
Refer to Figure 27.14.

## Slide 90: Digital Holter Monitor (Slide 3 of 3)
Continuously records electrical activity of heart
  For 24 hours, 48 hours, or 72 hours
    Most providers order a 24-hour recording
  Stores it on the memory card
Automatically stops recording after monitoring period is completed

## Slide 91: Evaluating Results (Slide 1 of 3)
At end of monitoring period Holter monitor removed from patient
Memory card information uploaded to computer
Specialized ECG software
  Performs calculations on the data
  Prepares an ECG summary report
    Displayed on screen of the computer

## Slide 92: Evaluating Results (Slide 2 of 3)
Computer-generated ECG report
  Summarizes information about:
    Patient’s heart rate and rhythm
    Any abnormalities that occurred during the monitoring period
  Includes selected samples of patient’s cardiac activity
    Patient event-strips
    Any abnormal cardiac activity (e.g., dysrhythmias)
  Results reviewed and interpreted further by provider

## Slide 93: Evaluating Results (Slide 3 of 3)
Computer-generated ECG report
  Report can be:
    Printed out and stored in PPR (patient-based paper record)
    Stored electronically in patient’s EMR (electronic medical record)

## Slide 94: Cardiac Dysrhythmias (Slide 1 of 5)
Normal ECG consists of P wave, QRS complex, and T wave
  Repeats in a regular pattern
Normal sinus rhythm: ECG that is within normal limits
  Waves, intervals, segments, cardiac rate fall within normal range

## Slide 95: Cardiac Dysrhythmias (Slide 2 of 5)
Normal heart rate range: 60 to 100 beats/minute
Sinus bradycardia: Below 60 beats/minute
Sinus tachycardia: Above 100 beats/minute

## Slide 96: Cardiac Dysrhythmias (Slide 3 of 5)
Cardiac dysrhythmia: Abnormal electrical activity in the heart causing an irregular heartbeat
  Most are harmless
  Some can be serious (even life-threatening)

## Slide 97: Cardiac Dysrhythmias (Slide 4 of 5)
Categories of cardiac dysrhythmias
  Extra beats
  Abnormal rhythm (dysrhythmia)
  Abnormal heart rate

## Slide 98: Cardiac Dysrhythmias (Slide 5 of 5)
Cardiac dysrhythmias include:
  Atrial premature contraction
  Paroxysmal atrial tachycardia
  Atrial flutter
  Atrial fibrillation
  Premature ventricular contraction
  Ventricular tachycardia
  Ventricular fibrillation

## Slide 99: Learning Objectives Lesson 27.3: Pulmonary Function Testing, Peak Flow Measurement, and Home Oxygen Therapy (Slide 1 of 3)
List the different pulmonary function tests.
List indications for performing spirometry testing.
Describe patient preparation for spirometry.
Explain the purpose of postbronchodilator spirometry.
Identify the symptoms of an asthma attack.

## Slide 100: Learning Objectives Lesson 27.3: Pulmonary Function Testing, Peak Flow Measurement, and Home Oxygen Therapy (Slide 2 of 3)
List examples of asthma triggers.
Explain the difference between long-term control and quick-relief asthma medications.
Describe the purpose of a peak flow meter.
Explain why oxygen is needed by the body.
Describe what occurs when the body cannot maintain an adequate blood oxygen level.

## Slide 101: Learning Objectives Lesson 27.3: Pulmonary Function Testing, Peak Flow Measurement, and Home Oxygen Therapy (Slide 3 of 3)
Identify the conditions that may require home oxygen therapy.
List and describe the three common types of oxygen delivery systems.
List and describe the two types of devices used to administer home oxygen therapy.
Describe oxygen safety guidelines.

## Slide 102: Pulmonary Function Tests (PFTs)
Purpose of PFT: To assess lung functioning
Assists in detection of pulmonary disease
Pulmonary function tests include:
  Spirometry
  Lung volumes
  Diffusion capacity
  Arterial blood gas studies
  Pulse oximetry
  Cardiopulmonary exercise tests

## Slide 103: Spirometry (Slide 1 of 4)
Noninvasive screening test often performed in medical office
Spirometer: Computerized electronic instrument
  Measures
    Amount of air that is expelled from the lungs
    Rate at which air is expelled
  Report printed out as a table and graph
Notes: Refer to Figure 27.5.

## Slide 104: Spirometry (Slide 2 of 4)
Considered a screening test
Abnormal results require:
  Additional PFT tests
  Possibly a CT scan

## Slide 105: Spirometry (Slide 3 of 4)
Indications for performing spirometry
  Patients who exhibit symptoms of lung dysfunction (e.g., dyspnea)
  Patients at high risk for lung disease
    Smoking
    Exposure to environmental pollutants; coal dust, asbestos, exhaust fumes
Notes: The provider will order the test to be performed. The MA is responsible for instructing the patient about the test.

## Slide 106: Spirometry (Slide 4 of 4)
Indications for performing spirometry
  Patients with lung disease
    Asthma
    Chronic bronchitis
    Emphysema
  Patients who will undergo surgery
    To assess probable lung performance during an operation
  Patients who need to be evaluated for lung disability or impairment
    For a compensation program (e.g., coal miner)

## Slide 107: Patient Preparation (Slide 1 of 2)
Do not eat a heavy meal for eight hours before the test
  Full stomach interferes with performing breathing maneuver
Stop smoking at least eight hours before test
Do not take bronchodilators four hours before test

## Slide 108: Patient Preparation (Slide 2 of 2)
Do not engage in strenuous activity four hours before test
Wear loose, nonrestrictive clothing
  Keeps chest area free
  Easier to perform breathing maneuver

## Slide 109: Postbronchodilator Spirometry
Ordered when results of spirometry indicate an obstruction
Purpose: Informs provider how treatment will work in patients with obstructed airway
How performed
  Patient inhales a bronchodilator
  Spirometry test is run 10 to 15 minutes later
Notes: A breathing treatment may be administered or the patient may use his or her inhaler prescribed by the provider.

## Slide 110: Asthma (Slide 1 of 3)
Chronic lung disease
  Affects smaller bronchi and bronchioles
Failure to treat asthma can lead to serious complications
  Example: Permanent lung damage
Can occur at any age (but more common in children and young adults)
  Affects boys more frequently before puberty, girls more frequently after puberty

## Slide 111: Asthma (Slide 2 of 3)
Characteristics of asthma
  Chronic inflammation of the small airways
  Recurrent attacks of:
    Coughing
    Chest tightness
    Shortness of breath
  Wheezing
    A continuous, high-pitched, whistling, musical sound heard particularly during exhalation and sometimes during inhalation

## Slide 112: Asthma (Slide 3 of 3)
Asthma attack usually followed by a symptom-free period
Can be controlled by:
  Recognizing warning signs and symptoms of an attack
  Treating symptoms when they first occur

## Slide 113: Asthma Attack (Slide 1 of 7)
Varies in frequency and severity
May come on suddenly or gradually
May last for only 10 to 15 minutes or for hours or even days
Important to treat symptoms when they first occur
  Prevents them from getting worse—could cause a severe asthma attack (may require emergency care)

## Slide 114: Asthma Attack (Slide 2 of 7)
Normal individual: Airways to lungs are fully open
  Allows air to move easily in and out of lungs
Patient with asthma: Airways are always inflamed
  Airways are hypersensitive to certain stimuli known as asthma triggers
    Can “trigger” an asthma attack

## Slide 115: Asthma Attack (Slide 3 of 7)
Asthma triggers
  Vary from one patient to another
  Sometimes difficult to determine what specific triggers cause a patient’s asthma attack
  May vary from one season to the next
  Common allergens that may trigger an asthma attack
    House dust
    Pollens
    Molds
    Animal danders and cockroaches

## Slide 116: Asthma Attack (Slide 4 of 7)
Asthma triggers
  Environmental irritants, activities, or events
    Air pollutants
    Tobacco smoke
    Chemical fumes (e.g., perfume, paint, gasoline)
    Vigorous physical exercise
    Upper respiratory viral infections
    Exposure to cold
    Emotional stress

## Slide 117: Asthma Attack (Slide 5 of 7)
Reaction occurs when airways of patient are stimulated by a trigger
  Bronchial tubes begin to constrict and swell
    Causes patient to experience asthma symptoms
  Symptoms may be mild and go away on their own, or with minimal treatment with medication
  Symptoms may lead to a full-blown asthma attack
Notes: Refer to Figure 27.16.

## Slide 118: Asthma Attack (Slide 7 of 7)
During a severe asthma attack
  Bronchial tubes continue to constrict and swell and become clogged with mucus
    Results in less air moving in and out of lungs—leads to a decrease in oxygen available to body
    Causes patient to experience coughing; chest tightness; shortness of breath; wheezing
Important to treat symptoms when they first occur
  Prevents them from getting worse—could cause a severe asthma attack (may require emergency care)

## Slide 119: Diagnosis and Treatment (Slide 1 of 8)
Diagnosed through a careful and detailed medical history
  Of particular importance
    Patient’s symptoms
    Family history of asthma
    Home and work environment
    Living habits

## Slide 120: Diagnosis and Treatment (Slide 2 of 8)
Provider also performs a thorough physical examination
  To detect symptoms resulting from asthma (e.g., wheezing)
Laboratory and diagnostic tests usually ordered
  May include:
    Pulmonary function tests (e.g., spirometry)
    Allergy testing
Arterial blood gas studies

## Slide 121: Diagnosis and Treatment (Slide 3 of 8)
Asthma is a chronic disease with no cure
  Most patients are able to lead a normal life through proper management and treatment
General treatment of asthma
  Identifying and avoiding asthma triggers (if possible)
Preventing and alleviating symptoms through drug therapy

## Slide 122: Diagnosis and Treatment (Slide 4 of 8)
Long-term control medication
  Helps relieve bronchial inflammation
  Prevents symptoms from occurring
  Helps the patient have fewer and milder asthma attacks
  Typically taken every day

## Slide 123: Diagnosis and Treatment (Slide 5 of 8)
Long-term control medication
  Examples
    Corticosteroids (Flovent, Azmacort, Vanceril, and AeroBid)
    Singulair
    Accolate
    Serevent
    Alupent
    Advair

## Slide 124: Diagnosis and Treatment (Slide 6 of 8)
Quick-relief medication (also called rescue medication)
  Opens the airways quickly by dilating the bronchial tubes
  Taken when patient is experiencing symptoms to prevent or control an asthma attack
  Examples: Fast-acting bronchodilators (Proventil, Ventolin, and Xopenex)

## Slide 125: Diagnosis and Treatment (Slide 7 of 8)
Many asthma medications delivered through an inhaler
  Allows medication to go directly to lungs
Notes: Refer to Figure 27.17.

## Slide 126: Diagnosis and Treatment (Slide 8 of 8)
Nebulizer: Breathing machine used to treat an asthma attack at home
  May be used with quick-relief medications
Some asthma medications administered orally
  Take longer to work
    Must first travel through digestive and circulatory systems before reaching lungs

## Slide 127: Peak Flow Meter (Slide 1 of 5)
Portable, handheld manual or digital device
Used to measure a breathing maneuver
Manual peak flow meter
  Consists of a plastic tube with a sliding indicator
Indicator manually moves along a scale of numbers when patient performs the breathing maneuver
Notes: See Procedure 27.2: Measuring Peak Flow Rate.
Refer to Figure 27.18.

## Slide 128: Peak Flow Meter (Slide 2 of 5)
Digital peak flow meter
  Automatically measures breathing maneuver
  Displays measurement digitally on a screen
Notes: Refer to Figure 27.19.

## Slide 129: Peak Flow Meter (Slide 3 of 5)
Measures how quickly air flows out of the lungs
  When patient exhales forcefully
Frequently used by patients with asthma
  Recommended for patients with moderate to severe asthma
Measurements obtained from peak flow meter are not as accurate as those obtained by spirometry

## Slide 130: Peak Flow Meter (Slide 4 of 5)
Peak flow meter can be used easily by a patient at home
Peak flow measurements provide patient with important information
  When to take medication
  Severity of asthma attack
Different brands of peak flow meters are available
  Peak flow measurements between brands may vary
  If more than one meter is purchased, always buy the same brand

## Slide 131: Peak Flow Meter (Slide 5 of 5)
Available in two ranges
  Low range
    Ranges from 0 to 300
    Used by young children and some older patients
  Full range
    Ranges from 0 to 800
    Used by older children, teenagers, and adults
    Adult has much larger bronchial tubes than a child—needs the wider range
Notes: Refer to Figure 27.20.

## Slide 132: Peak Flow Rate (PFR) (Slide 1 of 4)
Maximum volume of air measured in L/min (liters per minute)
  That can be exhaled when the patient blows into a peak flow meter as forcefully and as rapidly as possible

## Slide 133: Peak Flow Rate (PFR) (Slide 2 of 4)
Patient performs a breathing maneuver
  Takes a deep breath until the lungs are completely full
  Blows all the air out of the lungs and into the mouthpiece as hard and as fast as possible
  Causes sliding indicator to move up scale of meter
  Indicator stops and remains at patient’s peak flow rate

## Slide 134: Peak Flow Rate (PFR) (Slide 3 of 4)
To obtain most accurate PFR
  Patient should perform three acceptable breathing maneuvers
  Record the highest of three measurements
  The three measurements should be about the same
    Shows an acceptable breathing maneuver was performed each time
    Especially important when evaluating a child’s peak flow measurement

## Slide 135: Peak Flow Rate (PFR) (Slide 4 of 4)
MA often responsible for:
  Instructing patient in procedure for using a peak flow meter at home
  Obtaining peak flow rate of a patient with asthma at the medical office

## Slide 136: Schedule of Use (Slide 1 of 2)
Should be used by patients with moderate to severe asthma
  To determine how well asthma is being controlled
Provider determines schedule of use based on severity and frequency of asthma symptoms

## Slide 137: Schedule of Use (Slide 2 of 2)
Most providers recommend use of peak flow meter at least once a day
  Preferably in the morning before taking asthma medication
When patient is having symptoms
Twice a day for patient with more severe form of asthma
  Morning and evening

## Slide 138: Purpose of Peak Flow Measurements
Used to monitor change in patient’s airflow
  To determine how well asthma is being controlled
High number: Air is moving easily out of the patient’s lungs
Low number: Airways are narrowed
  Air cannot move easily through them
  Results in a decrease in oxygen available to the body

## Slide 139: Care and Maintenance (Slide 1 of 2)
MA should instruct patient in proper care of (manual) peak flow meter
  Dirt collecting on meter may result in inaccurate measurements
To clean meter:
  Wash weekly with warm soapy water
  Rinse thoroughly with warm water
  Remove excess water by gently shaking meter
  Air dry completely before use

## Slide 140: Care and Maintenance (Slide 2 of 2)
Many peak flow meters can be cleaned
  By placing them in the dishwasher (on top shelf)
    Check manufacturer’s instructions for this information
Inspect peak flow meter periodically for damage
  Cracks could cause air to leak out of the meter
    Leads to inaccurate readings
With proper care, should last 2 to 3 years

## Slide 141: Home Oxygen Therapy (Slide 1 of 5)
Oxygen
  Colorless, odorless, and tasteless gas
  Vital to human body
  Transported to blood by tissues
    Oxygen taken into cells, combines with glucose to produce energy
Necessary for carrying out metabolic processes that sustain life—breathing; beating of heart

## Slide 142: Home Oxygen Therapy (Slide 2 of 5)
When lungs cannot deliver enough oxygen to body, reduction in amount of oxygen in blood
  Results in hypoxemia: A decrease in the oxygen saturation of the blood
    Leads to hypoxia: Reduction in the oxygen supply to the tissues of the body

## Slide 143: Home Oxygen Therapy (Slide 3 of 5)
Failure to maintain adequate blood oxygen level can result in progressive deterioration of patient
  Death of cells
  Organ failure
  Body system failure
  Death
Prescription for home oxygen therapy may be written for conditions that reduce amount of oxygen in body (hypoxemia)
  Example: Severe chronic obstructive pulmonary disease (COPD)

## Slide 144: Home Oxygen Therapy (Slide 4 of 5)
Increases oxygen supply to lungs
  Raises blood oxygen to normal levels
  Increases availability of oxygen to the tissues
Helps to alleviate effects of low oxygen levels
  Shortness of breath and fatigue

## Slide 145: Home Oxygen Therapy (Slide 5 of 5)
Helps patient have better quality of life and live longer
Most commonly prescribed for patients with severe COPD caused by smoking
Also prescribed for:
  Asthma
  Occupational lung disease
  Lung cancer
  Cystic fibrosis
  Congestive heart failure

## Slide 146: Oxygen Delivery Systems (Slide 1 of 2)
Flow rate: Amount of supplemental oxygen prescribed for a patient
  Measured in liters per minute (L/min)
  Example
    If patient has been prescribed 2 L/min: Each minute: 2 L of oxygen flows from oxygen delivery system into tubing and into patient’s upper airway

## Slide 147: Oxygen Delivery Systems (Slide 2 of 2)
Type prescribed based on:
  Patient’s condition
  Patient’s personal preference
  Ease of equipment use
  Cost
Can be used alone or in combination with another system to meet oxygen needs of patient

## Slide 148: Compressed Oxygen Gas (Slide 1 of 3)
Oxygen gas
  Compressed under high pressure, then stored in a container
    Referred to as a cylinder or tank
Notes: Refer to Figure 27.1A.

## Slide 149: Compressed Oxygen Gas (Slide 2 of 3)
Compressed oxygen cylinders
  Vary in size
    Large stationary cylinder: Used at home by patient
    Small portable cylinder: Placed in a carrying device (e.g., shoulder bag) when the patient goes outside the home

## Slide 150: Compressed Oxygen Gas (Slide 3 of 3)
Regulator and flow meter
  Control flow rate of oxygen
  Flow of oxygen out of the cylinder is constant
Oxygen-conserving device may be attached to system
  Conserves oxygen and avoids waste
    Releases oxygen gas only when patient inhales—cuts off release of oxygen when patient exhales
Notes: Refer to Figure 27.21B.

## Slide 151: Liquid Oxygen (Slide 1 of 2)
Oxygen gas subjected to extremely cold temperature
  Changes from gas to very cold liquid
Stored in insulated tank
  Lining similar to a thermos
Takes up less space than compressed oxygen gas
  Example: 1 L of liquid oxygen is equal to 860 L of compressed oxygen gas
  Container of liquid oxygen lasts four times longer than compressed oxygen gas of same weight

## Slide 152: Liquid Oxygen (Slide 2 of 2)
Liquid oxygen system consists of
  Large stationary tank: Primary oxygen reservoir of oxygen
  Small portable tank used outside the home
    Filled from large primary tank for use outside the home
    Hung over shoulder or pulled on roller cart
Liquid oxygen released from its tank
  Changes into a gas
  Patient breathes it in
Notes: Refer to Figure 27.22.

## Slide 153: Oxygen Concentrator (Slide 1 of 3)
Electrically powered device
  Weighs about 35 pounds
  Size of a large suitcase
Notes: Refer to Figure 27.23A.

## Slide 154: Oxygen Concentrator (Slide 2 of 3)
Works by:
  Separating oxygen out of air
  Concentrating it
  Storing it for use by patient
Equipped with a built-in flow meter
Allows the prescribed flow rate to be set

## Slide 155: Oxygen Concentrator (Slide 3 of 3)
Portable battery-powered systems have recently been developed
  Weigh about 10 pounds
  Can provide patient with oxygen for 8 hours at a flow rate of 2 L/min
  Have replaced liquid oxygen or compressed gas cylinders for mobility
Notes: Refer to Figure 27.23B.

## Slide 156: Oxygen Administration Devices
Device used to administer oxygen to upper airway from the delivery system
Device used depends on:
  Expected duration of therapy
  Personal preference and needs of patient

## Slide 157: Nasal Cannula (Slide 1 of 3)
Most frequently used
Consists of soft plastic tubing with a two-pronged device inserted into patient’s nose
Notes: Refer to Figure 27.24.

## Slide 158: Nasal Cannula (Slide 2 of 3)
Tubing loops over patient’s ears and is secured under chin
  Connects to oxygen delivery system
Advantage of nasal cannula
  Does not interfere with ability to talk, eat, or drink

## Slide 159: Nasal Cannula (Slide 3 of 3)
Wash cannula once or twice a week using liquid soap and water
  Rinsed thoroughly
  Allow to air dry
Replace cannula every 2 to 4 weeks

## Slide 160: Face Mask (Slide 1 of 3)
Consists of:
  Plastic mask that fits over patient’s nose and mouth
  Face mask strap
  Tightened around head to ensure secure fit
  Oxygen tubing used to connect face mask to oxygen delivery system
Notes: Refer to Figure 27.25.

## Slide 161: Face Mask (Slide 2 of 3)
Not used as frequently as nasal cannula
  Bulky
  Must be removed:
    For eating or drinking
    To communicate effectively
Often used for patients who need a high flow of oxygen
  Can deliver oxygen at a flow rate between 5 and 15 L/min
Face mask may also be preferred when patient has nasal congestion (e.g., cold)

## Slide 162: Face Mask (Slide 3 of 3)
Wearing nasal cannula for extended period:
  Can cause irritation of nose
  To reduce irritation—wear nasal cannula during day and face mask at night
Care
  Wash once or twice a week using liquid soap and water
  Rinse thoroughly and dry
  Replace with new one every 2 to 4 weeks
    Sooner if it becomes cracked or discolored

## Slide 163: Oxygen Safety Guidelines (Slide 1 of 4)
Home medical supply company provides specific instructions on safe use, care, and maintenance of equipment
Oxygen is a safe gas as long as used properly
  Not flammable nor will it explode
  Greatly increases combustion rate of a fire
    If something catches fire—will make flame hotter, causes it to burn faster and more vigorously
    Result: A fire involving oxygen can appear explosive-like

## Slide 164: Oxygen Safety Guidelines (Slide 2 of 4)
Store oxygen in clean, dry, well-ventilated room
  If kept in closed area (e.g., closet), a small amount of oxygen gas that is continually vented from unit can accumulate in a confined space and become a fire hazard
Oxygen cylinders and liquid oxygen tanks must remain upright at all times
Secure to a fixed object or place in a stand

## Slide 165: Oxygen Safety Guidelines (Slide 3 of 4)
Never smoke while using oxygen
  Post “No Smoking: Oxygen in Use” signs where oxygen is kept
Keep oxygen supply at least six to eight feet away from open flames
  Examples: Gas stoves, lighted fireplaces, and candles
Keep oxygen supply at least six to eight feet away from intense heat
  Examples: Radiators, furnaces, and space heaters

## Slide 166: Oxygen Safety Guidelines (Slide 4 of 4)
Keep oxygen supply away from flammable products
  Examples: Cleaning fluid, paint thinner, and aerosol sprays
Do not lubricate oxygen equipment with oil or grease
  These substances are flammable
Be sure to have functioning smoke detectors in the home
Buy a fire extinguisher
  Be familiar with how to use it

## Slide 167
Questions?