## Slide 1
Urinalysis
Chapter 30

## Slide 2: Learning Objectives Lesson 30.1: Collection of Urine (Slide 1 of 2)
List conditions that may cause polyuria and oliguria.
Define the terms used to describe symptoms of the urinary system.
Explain why a first-voided morning specimen is often preferred for urinalysis.

## Slide 3: Learning Objectives Lesson 30.1: Collection of Urine (Slide 1 of 2)
Explain the purpose of collecting a clean-catch midstream specimen and a first-catch urine specimen.
Explain the purpose of a 24-hour urine collection.

## Slide 4: Composition of Urine (Slide 1 of 5)
Physiological change in body caused by disease can create a disturbance in kidney function
  Can be detected by examination of urine

## Slide 5: Composition of Urine (Slide 2 of 5)
Urine is composed of:
  Water: 95%
  Organic and inorganic waste products: 5%
    Organic wastes: Urea, uric acid, ammonia, and creatinine
    Urea is present in greatest amounts—derived from breakdown of proteins
    Inorganic wastes: Chloride, sodium, potassium, calcium, magnesium, phosphate, sulfate

## Slide 6: Composition of Urine (Slide 3 of 5)
Normal adult excretes 750 to 2000 mL of urine per day
  Varies based on:
    Amount of fluid consumed
    Amount lost through other means (perspiration, feces)
Notes: A quart is equal to approximately 1000 mL.

## Slide 7: Composition of Urine (Slide 4 of 5)
Polyuria: Excessive increase in urine output
  Caused by:
    Excessive intake of fluids
    Intake of fluids that contain caffeine (mild diuretic)
    Drugs (diuretics)
    Pathological conditions (e.g., diabetes, renal disease)

## Slide 8: Composition of Urine (Slide 5 of 5)
Oliguria: Decreased output of urine
  Less than 400 mL in 24 hours
  Caused by:
    Decreased fluid intake
    Dehydration
    Profuse perspiration
    Vomiting
    Diarrhea
    Kidney disease
  Micturition: Normal act of voiding urine

## Slide 9: Terms Related to the Urinary System (Slide 1 of 3)
Anuria: Failure of the kidneys to produce urine
Diuresis: Secretion and passage of large amounts of urine
Dysuria: Difficult or painful urination
Frequency: The condition of having to urinate often
Hematuria: Blood present in urine

## Slide 10: Terms Related to the Urinary System (Slide 2 of 3)
Nocturia: Excessive (voluntary) urination during the night
Nocturnal enuresis: The inability of the patient to control urination at night during sleep (bedwetting)
Pyuria: Pus present in the urine

## Slide 11: Terms Related to the Urinary System (Slide 3 of 3)
Retention: The inability to empty the bladder
  The urine is being produced normally but is not being voided
Urgency: The immediate need to urinate
Urinary incontinence: The inability to retain urine

## Slide 12: Collection of Urine (Slide 1 of 2)
Advantages of urine testing
  Urine is easily available
  Does not require:
    An invasive procedure
    Use of special equipment
Notes: Urine testing is a quick method used to detect the presence of pathological conditions.

## Slide 13: Collection of Urine (Slide 2 of 2)
To obtain accurate urine test results, adhere to proper urine collection procedures
  Ensures collection of proper specimen

## Slide 14: Guidelines for Urine Collection (Slide 1 of 4)
Make sure to obtain an adequate volume (usually 30 to 50 mL)
Properly label each specimen: Avoids mix-up of specimens
  Patient’s name and DOB
  Date and time of collection
  Type of specimen (i.e., urine)
Notes: Inform the patient how much urine he or she needs to collect.

## Slide 15: Guidelines for Urine Collection (Slide 2 of 4)
Record medications patient is taking on laboratory requisition and in patient’s chart
  Some medications interfere with the accuracy of test results
Do not collect a specimen during menstruation
  May contaminate the specimen with blood
    Result in false-positive results on test for blood

## Slide 16: Guidelines for Urine Collection (Slide 3 of 4)
Difficult for some patients to void under stress and anxiety
  Be patient and relay understanding to patient

## Slide 17: Guidelines for Urine Collection (Slide 4 of 4)
May be difficult to obtain from a child
  May need to use another collection method
    Urine collection bag
    Suprapubic aspiration
    Catheterization
Notes: The parent will usually accompany a child to the restroom.

## Slide 18: Urine Specimen Collection Methods (Slide 1 of 2)
Type of test being performed often dictates the collection method
  Examples
    Pregnancy test: First-voided morning specimen
    Identification of a UTI: Clean-catch midstream collection

## Slide 19: Urine Specimen Collection Methods (Slide 2 of 2)
Most offices use disposable plastic specimen containers
  Available in different sizes
  Have lids to:
    Prevent spillage
    Reduce contamination of the specimen

## Slide 20: Random Specimen
Urine testing is often performed on a freshly voided specimen
MA instructs patient to void into clean, dry, wide-mouthed container
Urine is tested immediately

## Slide 21: First-Voided Morning Specimen (Slide 1 of 2)
Contains greatest concentration of dissolved substances
Small amount of a substance detected more easily
Instruct patient to collect first specimen of the morning
  Preserve it in refrigerator

## Slide 22: First-Voided Morning Specimen (Slide 2 of 2)
Provide patient with specimen container
  To prevent use of a container that harbors contaminants
    Could cause inaccurate test results

## Slide 23: Clean-Catch Midstream Specimen (Slide 1 of 5)
Microorganisms are NOT normally present in:
  Urinary bladder
  Most of urethra
Notes: See Procedure 30.1: Clean-Catch Midstream Specimen Collection Instructions.

## Slide 24: Clean-Catch Midstream Specimen (Slide 2 of 5)
Microorganisms are normally present in:
  Distal urethra
  Urinary meatus

## Slide 25: Clean-Catch Midstream Specimen (Slide 3 of 5)
Clean-catch: Required when urine is cultured and examined for bacteria
  To prevent contamination of the specimen with normally present microorganisms
Only microorganisms causing patient’s condition are desired in specimen
Ordered for:
  Detection of a UTI
  Evaluate effectiveness of drug therapy for a UTI

## Slide 26: Clean-Catch Midstream Specimen (Slide 4 of 5)
Clean-catch procedure
  Sterile container is used
  To prevent contamination of specimen with normal flora
    Microorganisms are removed from urinary meatus by having patient cleanse the meatus
    Microorganisms are flushed out of distal urethra by having patient void a small amount into toilet

## Slide 27: Clean-Catch Midstream Specimen (Slide 5 of 5)
Reduces possibility of having to obtain urine specimen by:
  Bladder catheterization: Passing of a sterile catheter through the urethra into the bladder
  Suprapubic aspiration of bladder: Passing of a sterile needle through the abdominal wall into the bladder

## Slide 28: Guidelines (Slide 1 of 3)
Collected by patient at office
MA provides instructions
  Provide complete instructions to prevent contamination of specimen with bacteria
    Avoid patient having to collect another specimen

## Slide 29: Guidelines (Slide 2 of 3)
When collected, MA should immediately cap and label the container
  Patient’s name and DOB
  Date and time of collection
  Type of collection (clean-catch)

## Slide 30: Guidelines (Slide 3 of 3)
Test specimen immediately (or refrigerate)
  To ensure reliable test results
If sent to outside laboratory
  Complete the laboratory request form
  Record in patient's chart information on transport of specimen to laboratory

## Slide 31: First-Catch Urine Specimen
Can be used to test for presence of chlamydia and gonorrhea using nucleic acid amplification (NAA) test
Patient should not urinate for at least one hour prior to collection of urine specimen
  Should also not cleanse the genital area before collection
Patient should collect only 15-30 mL of initial urine stream in container
Notes: The first 15 to 30 mL of urine voided by the patient contains the greatest concentration of chlamydia and/or gonorrhea bacteria (if present), resulting in a greater likelihood that the NAA test will detect these pathogens.
Following collection of the specimen, the medical assistant, using a disposable pipette, is responsible for transferring 2 mL of the urine specimen to a transport tube.
The specimen should then be placed in a biohazard specimen bag and stored in the refrigerator for pickup by a courier from an outside laboratory

## Slide 32: Twenty-Four Hour Urine Specimen (Slide 1 of 10)
Quantitative measurement of specific urinary components
Greater accuracy of measurement than with random specimen
Notes: The MA is responsible for instructing the patient and providing the supplies needed for the 24-hour urine specimen.

## Slide 33: Twenty-Four Hour Urine Specimen (Slide 2 of 10)
Examples of substances measured
  Calcium
  Creatinine
  Lead
  Potassium
  Protein
  Urea nitrogen
Notes: The volume of urine is also measured. This is important with certain diseases.

## Slide 34: Twenty-Four Hour Urine Specimen (Slide 3 of 10)
Often used to:
  Diagnose the cause of kidney stone formation
  Assist in the control and prevention of new stone formation

## Slide 35: Twenty-Four Hour Urine Specimen (Slide 4 of 10)
Large container used (3000 mL)
  Used to store urine collected over 24 hours
To prevent changes in the quality of the specimen
  Specimen must be kept refrigerated
  Or placed in an ice chest

## Slide 36: Twenty-Four Hour Urine Specimen (Slide 5 of 10)
Some containers also contain a preservative
  Maintains quality of specimen
  Hazardous chemical warning label should be attached to container
  Instruct patient not to discard or touch the preservative

## Slide 37: Twenty-Four Hour Urine Specimen (Slide 6 of 10)
Patient is also provided with container to collect specimen
  Female: Urine “hat”
    Placed over commode under toilet seat
  Male: Collection cup
After collection: Urine is placed into the large specimen container

## Slide 38: Twenty-Four Hour Urine Specimen (Slide 7 of 10)
Patient is also provided with container to collect specimen
  Makes collection easier and safer
  If patient voids directly into container with preservative—could splash onto patient’s skin resulting in a chemical burn

## Slide 39: Twenty-Four Hour Urine Specimen (Slide 8 of 10)
MA should provide both written and verbal instructions
  Drink normal amount of fluid during collection period
  Avoid alcohol for 24 hours before and during collection
Notes: An example of a drug that may interfere with the test is aspirin.
Some foods may also interfere with the test.

## Slide 40: Twenty-Four Hour Urine Specimen (Slide 9 of 10)
MA should provide both written and verbal instructions
  Choose 24-hour period when you will be at home
    So urine won’t have to be transported
  Do not perform during menstruation

## Slide 41: Twenty-Four Hour Urine Specimen (Slide 10 of 10)
Physician may want patient to discontinue certain medications for one week before the test
Notes: Why would discontinuing medication help with the test results? Ask student for their thoughts. (Answers will vary.)

## Slide 42: Learning Objectives Lesson 30.2: Testing and Analysis of Urine (Slide 1 of 2)
List changes that may occur if urine is allowed to remain standing for longer than 1 hour.
List factors that may cause urine to have an unusual color or become cloudy.
Identify the various tests that are included in the physical and chemical examination of urine.
List the structures that may be found in a microscopic examination of urine.

## Slide 43: Learning Objectives Lesson 30.2: Testing and Analysis of Urine (Slide 2 of 2)
Explain the basis for urine pregnancy tests.
List the guidelines that must be followed in a urine pregnancy test to ensure accurate test results.

## Slide 44: Urine Changes (Slide 1 of 2)
Changes that take place if specimen stands out for more than one hour
  Bacteria in environment that get into specimen—work on urea (acidic)
    Converting it to ammonia (alkaline)
    Changes pH of urine: Acid urine becomes alkaline; may result in false-positive result on protein test
  Bacteria multiply resulting in cloudy specimen; increase in nitrite

## Slide 45: Urine Changes (Slide 2 of 2)
Changes that take place if specimen stands out for more than one hour
  If glucose is present in specimen: Amount decreases
    Microorganisms use glucose for food
  If any red or white blood cells are present: They may break down
  Casts decompose after several hours

## Slide 46: Analysis of Urine (Slide 1 of 5)
Urinalysis: Analysis of urine
Consists of:
  Physical examination
  Chemical examination
  Microscopic examination

## Slide 47: Analysis of Urine (Slide 2 of 5)
Deviation from normal on urinalysis
  Assists in diagnosis and treatment of pathological conditions of:
    Urinary system
    Other body systems

## Slide 48: Analysis of Urine (Slide 3 of 5)
May be performed:
  As screening measure
    Part of physical examination
  Assist in the diagnosis of a patient’s condition
  Evaluate effectiveness of therapy
    After treatment has been initiated

## Slide 49: Analysis of Urine (Slide 4 of 5)
Perform urinalysis on a fresh or preserved specimen
  If specimen cannot be examined with 1 hour of voiding
    Preserve immediately in refrigerator
    Before testing: Return to room temperature; thoroughly mix specimen (rotate urine container)

## Slide 50: Analysis of Urine (Slide 5 of 5)
Perform urinalysis on a fresh or preserved specimen
  If urine is allowed to stand at room temperature for longer than 1 hour, changes may occur

## Slide 51: Physical Examination of Urine
For accurate evaluation of color and appearance
  Specimen must be in a clear plastic or glass container
Notes: Good lighting is also needed to inspect the urine.

## Slide 52: Color (Slide 1 of 4)
Ranges from almost colorless to dark yellow
  Dilute urine: Lighter yellow
    Occurs as day progresses and more fluids are consumed
  Concentrated urine: Darker yellow (e.g., first-voided specimen)
    Occurs because fluid consumption is decreased at night

## Slide 53: Color (Slide 2 of 4)
Color due to yellow pigment: Urochrome
  From breakdown of hemoglobin
  Color varies among different shades of yellow throughout the day

## Slide 54: Color (Slide 3 of 4)
Classifications used to describe color
  Light yellow
  Yellow
  Dark yellow
  Light amber
  Amber
  Dark amber
Color of urine specimen assists in determining additional tests that may be necessary
Notes: Refer to Figure 30.1.

## Slide 55: Color (Slide 4 of 4)
Abnormal color may be due to:
  Presence of hemoglobin or blood (reddish color)
  Bile pigments (yellow-brown or greenish)
  Fat droplets or pus (milky color)
  Some foods and medications
Abnormal color helps to determine additional tests needed
Notes: Beets and asparagus may cause urine to exhibit an abnormal color.

## Slide 56: Appearance (Slide 1 of 2)
Fresh urine: Usually clear or transparent
  Becomes cloudy on standing out too long
Cloudiness in freshly voided specimen
  Presence of bacteria, pus, blood, fat, yeast, sperm, mucous threads, or fecal contaminants
  Microscopic examination: Performed on cloudy specimens to determine cause
    Cloudiness resulting from bacteria may be caused by a UTI

## Slide 57: Appearance (Slide 2 of 2)
Classifications used to describe appearance
  Clear
  Slightly cloudy
  Cloudy
  Very cloudy
Notes: Refer to Figure 30.2.

## Slide 58: Odor
Freshly voided urine: Slightly aromatic odor
Urine standing for long periods: Ammonia odor
  As a result of breakdown of urea by bacteria
Urine of diabetic patients may have fruity odor: Presence of ketones
Urine of patient with UTI: Foul-smelling odor
Certain foods (e.g., asparagus causes a musty smell)
Odor not generally used in diagnosis of the patient’s condition

## Slide 59: Specific Gravity (Slide 1 of 5)
Measures weight of urine as compared with the weight of an equal volume of distilled water
Indicates amount of dissolved substances present in urine
Provides information on ability of the kidney to dilute or concentrate the urine
Decreased specific gravity (SG)
  Chronic renal insufficiency
  Diabetes insipidus
  Malignant hypertension

## Slide 60: Specific Gravity (Slide 2 of 5)
Increased SG
  Adrenal insufficiency
  Congestive heart failure
  Hepatic disease
  Diabetes mellitus with glycosuria
  Conditions causing dehydration (e.g., fever, vomiting, and diarrhea)

## Slide 61: Specific Gravity (Slide 3 of 5)
Normal range for SG of urine: 1.003 to 1.030
  Usually between 1.010 and 1.025
  SG of distilled water: 1.000

## Slide 62: Specific Gravity (Slide 4 of 5)
Dilute urine: Lower SG (fewer dissolved substances)
  Urine is more dilute after fluid consumption
Concentrated urine: Higher SG (more dissolved substances)
  Urine is more concentrated in morning
    Increased amount of dissolved substances

## Slide 63: Specific Gravity (Slide 5 of 5)
Measurement of SG
  Reagent strip method: Most common method used to measure SG
    Color comparison determination
    Strip dipped in urine
    Results compared with color chart

## Slide 64: Chemical Examination of Urine (Slide 1 of 7)
Used to assist in diagnosis of:
  Kidney function
  Urinary tract infections
  Carbohydrate metabolism (diabetes mellitus)
  Liver function

## Slide 65: Chemical Examination of Urine (Slide 2 of 7)
Substances present in excess (abnormal) amounts in the blood are usually removed by urine
  Example: Glucose is normally present in blood—if it exceeds a certain level, the excess is excreted in urine
Indirect means of detecting abnormal amounts of chemicals in the body
Detection of substances that do not normally appear in the absence of disease
  Examples: Blood and nitrite

## Slide 66: Chemical Examination of Urine (Slide 3 of 7)
Chemical tests that are routinely performed
  pH
  Glucose
  Protein
  Ketone

## Slide 67: Chemical Examination of Urine (Slide 4 of 7)
Other tests that may be performed
  Blood
  Bilirubin
  Urobilinogen
  Nitrite
  Leukocytes

## Slide 68: Chemical Examination of Urine (Slide 5 of 7)
Qualitative test results
  Purpose
    Indicate whether or not a substance is present in urine
    Provide approximate indication of amount of substance present
  Interpretation of results
    Usually involves use of color comparison chart

## Slide 69: Chemical Examination of Urine (Slide 6 of 7)
Qualitative test results
  Results recorded in terms of:
    Trace, 1+, 2+, 3+
    Trace, small, moderate, large
    Negative or positive
  Useful as a screening test
  Easy to perform

## Slide 70: Chemical Examination of Urine (Slide 7 of 7)
Quantitative test results
  Indicate exact amount of chemical substance present in the body
  Results reported in measurable units
    Example: 14 mg/dL
  Obtaining quantitative result on urine specimen
    Usually involves use of complex equipment and testing procedures
  Not usually performed in the medical office

## Slide 71: Urine Testing Kits (Slide 1 of 6)
Most frequently used in the medical office for chemical testing of urine
  Advantages
    Contain premeasured reagent
    Easy to perform
    Provide immediate results
Most are qualitative test results: Positive result indicates need for further testing

## Slide 72: Urine Testing Kits (Slide 2 of 6)
Rely on color change for interpretation of results
  Color chart used to make a visual comparison

## Slide 73: Urine Testing Kits (Slide 3 of 6)
To ensure accurate and reliable test results
  Carefully read and follow manufacturer’s instruction sheet
Test strips that contain more than one reagent
  May require different time intervals for reading results

## Slide 74: Urine Testing Kits (Slide 4 of 6)
Certain medications may affect results
  Listed in instructions
Expiration date must be checked before using
  Do not use if past the expiration date
    Test results may be inaccurate

## Slide 75: Urine Testing Kits (Slide 5 of 6)
Should not be used if:
  Color change has occurred on strip
  Tested strip is a color that does not match chart
Light, heat, and moisture can affect strips
  Store in cool, dry area
  Tests are packaged in a light-resistant container

## Slide 76: Urine Testing Kits (Slide 6 of 6)
Never transfer from original container to another
  Another container may contain moisture, dirt, chemicals
    Could affect test results
Recording test results
  Indicate brand name of test that was used (e.g., Multistix 10SG)

## Slide 77: pH (Slide 1 of 3)
Unit that indicates acidity or alkalinity of a solution
Range of pH scale: 0.0 to 14.0
  Lower the number: Greater the acidity
  Higher the number: Greater the alkalinity
Notes: Another word for alkalinity is basic.

## Slide 78: pH (Slide 2 of 3)
pH readings
  Neutral: 7.0
  Acid: Below 7
  Alkaline: Above 7

## Slide 79: pH (Slide 3 of 3)
Perform test on freshly voided urine
  If urine is allowed to stand out, it becomes more alkaline
    Urea is converted to ammonia by bacteria
pH of urine: Ranges from 4.6 to 8.0 (usually around 6.0, which is acidic)
High reading on a fresh specimen may indicate bacterial infection of urinary tract
Notes: If a urine test is abnormal, do not discard the urine until the physician approves of discarding it. The physician may want to run further tests on the urine.

## Slide 80: Glucose (Slide 1 of 3)
Should not normally be present in urine
Glucose in the blood is filtered through nephrons and reabsorbed into the body
If glucose concentration in blood becomes too high: Renal threshold is exceeded
  Kidneys unable to reabsorb all of the glucose back into the blood
    Results in glycosuria: Glucose in the urine

## Slide 81: Glucose (Slide 2 of 3)
If glucose concentration in blood becomes too high: Renal threshold is exceeded
  Renal threshold: Concentration at which a substance in the blood not normally excreted by the kidney begins to appear in the urine
  Renal threshold for glucose: Generally between 160 and 180 mg/dL

## Slide 82: Glucose (Slide 3 of 3)
Diabetes: Most common cause of glycosuria
Alimentary glucosuria: Patient has a low renal threshold
  Glucose may appear after consumption of large quantities of sugar
Notes: Alimentary glucosuria may appear during pregnancy.

## Slide 83: Protein (Slide 1 of 2)
Proteinuria: Presence of protein in the urine
  Temporary increase may be caused by stress or strenuous exercise
Conditions causing proteinuria
  Glomerular filtration problems
  Renal diseases
  Bacterial infections of the urinary tract
Notes: Urine that contains large amounts of protein may be foamy.

## Slide 84: Protein (Slide 2 of 2)
If proteinuria occurs: Physician usually orders examination of sediment
  To see what is causing the protein to be in the patient’s urine (e.g., bacteria)

## Slide 85: Ketone (Slide 1 of 3)
Three types of ketone bodies
  Beta-hydroxybutyric acid
  Acetoacetic acid
  Acetone

## Slide 86: Ketone (Slide 2 of 3)
Normal products of fat metabolism
Can be used by muscle tissue as a source of energy
When more than normal amounts of fat are metabolized
  Muscles cannot handle all of the ketones that result
Ketosis: Accumulation of large amounts of ketone bodies in tissues and body fluids
Notes: In healthy individuals, ketones are formed in the liver.

## Slide 87: Ketone (Slide 3 of 3)
Ketonuria: Presence of ketone bodies in the urine
  Body rids itself of excess ketones by excreting them in urine
Conditions causing ketonuria
  Uncontrolled diabetes
  Starvation
  Diet composed almost entirely of fat

## Slide 88: Bilirubin (Slide 1 of 4)
Lifespan of RBC: 120 days
RBC contains hemoglobin
  Function of hemoglobin: Transports oxygen in the body

## Slide 89: Bilirubin (Slide 2 of 4)
When a RBC breaks down: Hemoglobin breaks down
  Releases bilirubin (vivid yellow pigment)
Bilirubin: Normally transported to liver and excreted with bile
  Eventually leaves body through intestines (feces)
Notes: Bilirubin gives the color to the feces.

## Slide 90: Bilirubin (Slide 3 of 4)
With certain liver conditions
  Liver cannot accept bilirubin
  Bilirubin is transported to kidneys
    Excreted into urine: Bilirubinuria—causes urine to be yellow-brown or greenish

## Slide 91: Bilirubin (Slide 4 of 4)
Conditions causing bilirubinuria
  Gallstones
  Hepatitis
  Cirrhosis of the liver

## Slide 92: Urobilinogen
Conditions causing increase in urobilinogen in urine
  Excessive hemolysis of red blood cells
  Infectious hepatitis
  Cirrhosis
  Congestive heart failure (CHF)
  Mononucleosis

## Slide 93: Blood
Considered abnormal (unless due to menstruation)
  Hematuria: Presence of blood in the urine
Conditions causing hematuria
  Injury
  Cystitis
  Tumors of bladder
  Urethritis
  Kidney stones
  Certain kidney disorders

## Slide 94: Nitrite (Slide 1 of 3)
Indicates presence of a pathogen in urinary tract (UTI)
Pathogens present in the urine in the bladder causes nitrate to convert to nitrite
  Nitrate: Normally present in the urine
  Nitrite: Normally absent in the urine
Notes: What is the name of the most common pathogen that infects the bladder? (Escherichia coli)

## Slide 95: Nitrite (Slide 2 of 3)
Perform on urine that has been in bladder 4 to 6 hours (first-voided specimen)
  To ensure the pathogens have converted nitrate to nitrite

## Slide 96: Nitrite (Slide 3 of 3)
Should not be performed on specimen that has been standing out
  Results in a false-positive result
    Caused by environmental bacterial contamination of the specimen
Screening test usually followed with culture
  To identify the pathogen

## Slide 97: Leukocytes (Slide 1 of 2)
Leukocyturia: Presence of leukocytes in the urine
  Accompanies inflammation of kidneys and lower urinary tract
Conditions causing leukocyturia
  Acute and chronic pyelonephritis
  Cystitis
  Urethritis

## Slide 98: Leukocytes (Slide 2 of 2)
Recommended specimen for women
  Clean-catch midstream collection
    Prevents contamination of specimen with leukocytes from vaginal secretions
    Can cause false-positive test results

## Slide 99: Reagent Strips (Slide 1 of 4)
Most common test used in medical office to test urine
Disposable plastic strips: Contain reagent areas for testing chemicals in urine

## Slide 100: Reagent Strips (Slide 2 of 4)
Results provide physician with information to assist in the diagnosis of:
  Kidney function conditions (e.g., kidney stones)
  UTI
  Carbohydrate metabolism conditions (e.g., diabetes mellitus)
  Liver function conditions (e.g., hepatitis)

## Slide 101: Reagent Strips (Slide 3 of 4)
Test results also provide physician with information related to:
  Acid-base balance of the body
  Urine concentration

## Slide 102: Reagent Strips (Slide 4 of 4)
Provide qualitative test results
  Positive result requires further testing
Number and type of reagent areas depend on the particular brand
Always read manufacturer’s instructions before performing the test

## Slide 103: Guidelines for Reagent Strip Urine Testing (Slide 1 of 7)
Preferred type of specimen: Freshly voided and thoroughly mixed
  If not possible: Refrigerate specimen
    Before testing: Allow to return to room temperature; thoroughly mix specimen
Notes: See Procedure 30.2: Chemical Testing of Urine with the Multistix 10 SG Reagent Strip.

## Slide 104: Guidelines for Reagent Strip Urine Testing (Slide 2 of 7)
Type of collection
  Most designed to be used with a random specimen
  Certain tests require a special collection procedure
    Nitrite test: First-voided morning specimen
    Leukocyte test: Clean-catch midstream specimen

## Slide 105: Guidelines for Reagent Strip Urine Testing (Slide 3 of 7)
Specimen container
  Must be clean
    To prevent inaccurate test results
  Must be large enough
    To allow for complete immersion of strip
Notes: The MA should make sure all of the chemicals have been exposed to urine.

## Slide 106: Guidelines for Reagent Strip Urine Testing (Slide 4 of 7)
Time intervals
  Read results at exact time intervals
    Specified on color chart
  Do not read any test results after 2 minutes

## Slide 107: Guidelines for Reagent Strip Urine Testing (Slide 5 of 7)
Interpretation of results
  Compare with color chart in good lighting
    To obtain a good visual match

## Slide 108: Guidelines for Reagent Strip Urine Testing (Slide 6 of 7)
Storage of reagent strips: Cool, dry area with the cap tightly closed
  Reagents on strips are sensitive to light, heat, and moisture
    Container includes a desiccant to absorb moisture: Do not remove

## Slide 109: Guidelines for Reagent Strip Urine Testing (Slide 7 of 7)
Storage of reagent strips: Cool, dry area with the cap tightly closed
  Store at a temperature between 59º F (15º C) and 86º F (30º C)
    Do not store in refrigerator or freezer
  Tan-to-brown discoloration or darkening on reagent areas
    Indicates deterioration of strips
    Do not use strips: Test results would be inaccurate

## Slide 110: Quality Control Testing (Slide 1 of 4)
Ensures reliability of test results
  Determines if strips are reacting properly
  Confirms that the test is being properly performed and accurately interpreted

## Slide 111: Quality Control Testing (Slide 2 of 4)
Example: Chek-Stix control checks reliability of Multistix
  Consists of a plastic strip with seven synthetic ingredients
  Reconstituted in distilled water for 30 minutes
    Ingredients dissolve in the water
Notes: Refer to Figure 30.3.

## Slide 112: Quality Control Testing (Slide 3 of 4)
Example: Chek-Stix control checks reliability of Multistix
  Resulting solution is tested with a Multistix reagent strip
    Using the same procedure as a urine specimen
  Expected values outlined on a sheet accompanying the control strips
    Record control test results in a quality control log
    If expected values are not obtained: Determine cause of problem and correct it—outdated strips or control; improper storage of strips or control; error in technique.

## Slide 113: Quality Control Testing (Slide 4 of 4)
Perform quality control
  When you open a new bottle of strips
  Question of reliability with testing strips

## Slide 114: Urine Analyzer (Slide 1 of 2)
Performs chemical examination of urine automatically
  Uses reagent strips
Advantages
  Quick and easy
  Results are interpreted automatically
Notes: The results are printed out and filed in the patient’s chart.

## Slide 115: Urine Analyzer (Slide 2 of 2)
Clinitek Analyzer
  Automatically reads Multistix
  Results printed out
    Abnormal results are flagged
Notes: Refer to Figure 30.4.

## Slide 116: Microscopic Examination of Urine (Slide 1 of 3)
Urine sediment: Solid materials contained in urine
  Sediment sample is placed on a slide by MA
  Viewed under a microscope by physician
  Helps clarify results of physical and chemical examination
Notes: The MA must be knowledgeable in using the microscope.
See Procedure 30.3: Prepare a Urine Specimen for Microscopic Examination: Kova Method.

## Slide 117: Microscopic Examination of Urine (Slide 2 of 3)
First-voided morning specimen preferred: More concentrated
  Contains more dissolved substances
    Small amounts of abnormal substances are more likely to be detected

## Slide 118: Microscopic Examination of Urine (Slide 3 of 3)
Important to use a fresh specimen
  Changes occur if specimen is left standing out
    Affects reliability of test results
MA responsible for preparing urine specimen
  For microscopic examination by the physician

## Slide 119: Red Blood Cells (Slide 1 of 2)
Round, colorless, biconcave discs
Normal: 0 to 5 per high-power field
Notes: See Table 30.1: Structures in Urine Sediment.

## Slide 120: Red Blood Cells (Slide 2 of 2)
More than 5 per high-power field may indicate bleeding along the urinary tract
Concentrated urine causes RBCs to become shrunken or crenated
Dilute urine causes RBCs to swell and hemolyze
  Will not be seen under a microscope
  Will still show a positive on reagent strip test (for blood)

## Slide 121: White Blood Cells
Round, granular, with a nucleus
Approximately 1.5 times larger than RBC
Normal: 0 to 8 per high-power field
More than 8 per high-power field may indicate inflammation of genitourinary tract

## Slide 122: Epithelial Cells (Slide 1 of 3)
Most structures making up urinary system are composed of several layers of epithelial cells
Outer layer
  Constantly being sloughed off
  Replaced by cells underneath

## Slide 123: Epithelial Cells (Slide 2 of 3)
Squamous epithelial cells: Large, clear, flat cells with irregular shape
  Contain small nucleus
  Come from urethra, bladder, vagina
  Normally present in small amounts in urine
Notes: Urine sediment usually contains squamous epithelial cells.

## Slide 124: Epithelial Cells (Slide 3 of 3)
Renal epithelial cells: Round with large nucleus
  Come from deeper layers of urinary tract
  Presence in urine is abnormal
Notes: The presence of renal epithelial cells can indicate inflammation and serious damage to the kidneys.

## Slide 125: Casts (Slide 1 of 3)
Cylindrical structures: Formed in lumen of nephron tubules
Materials in tubules harden and are flushed out: Appear in urine as casts
Generally indicate diseased condition
Notes: Casts indicate renal disease.

## Slide 126: Casts (Slide 2 of 3)
Named according to what they contain
  Hyaline casts: Pale, colorless cylinders with rounded edges
    Vary in size
  Granular casts: Hyaline casts that contain granules
  Fatty casts: Hyaline casts that contain fat droplets
  Waxy casts: Light yellowish with serrated edges
    Appear to be made of wax

## Slide 127: Casts (Slide 3 of 3)
Cellular casts: Hyaline casts that contain organized structures
  Named for what they contain
    RBC casts
    WBC casts
    Epithelial casts

## Slide 128: Crystals (Slide 1 of 4)
Variety may be found in urine
Type and number vary with urine pH

## Slide 129: Crystals (Slide 2 of 4)
Abnormal crystals
  Leucine
  Tyrosine
  Cystine
  Cholesterol

## Slide 130: Crystals (Slide 3 of 4)
Crystals that commonly appear in acidic urine
  Amorphous urates
  Uric acid
  Calcium oxalate

## Slide 131: Crystals (Slide 4 of 4)
Commonly appear in alkaline urine
  Amorphous phosphate
  Triple phosphate
  Calcium phosphate
  Ammonium urate

## Slide 132: Miscellaneous Structures (Slide 1 of 5)
Mucous threads: Normally present in small amounts in urine
Long, wavy, threadlike structures with pointed ends

## Slide 133: Miscellaneous Structures (Slide 2 of 5)
Bacteria: Rod shaped or round
  Should not normally be present
  Presence of more than a few may indicate:
    Contamination of specimen during collection
    UTI
Notes: The urine may appear cloudy due to the presence of bacteria.

## Slide 134: Miscellaneous Structures (Slide 3 of 5)
Yeast cells
  Smooth, refractile bodies with oval shape
  Small buds project from cells
  In females
    Usually vaginal contaminant caused by Candida albicans (yeast infection)
  May also be present in patients with diabetes

## Slide 135: Miscellaneous Structures (Slide 4 of 5)
Parasites
  May be present as a contaminate from fecal or vaginal material
  Trichomonas vaginalis: Parasite that causes trichomoniasis vaginitis

## Slide 136: Miscellaneous Structures (Slide 5 of 5)
Spermatozoa
  May be present in men or women after intercourse
  Have round heads, long, slender, hairlike tails

## Slide 137: Urine Pregnancy Testing (Slide 1 of 2)
Purpose
  To determine if a woman is pregnant
  Before certain medications are given or procedures performed that may cause injury to a fetus

## Slide 138: Urine Pregnancy Testing (Slide 2 of 2)
Immunological tests often used in the office
  Test results rely on the presence of human chorionic gonadotropin (HCG)
Concentrated urine specimen required (first-voided morning)
HCG: Produces positive result

## Slide 139: Human Chorionic Gonadotropin (Slide 1 of 2)
Produced by developing fertilized egg
  Small amounts secreted into urine and blood
Immediately after conception and implantation: Level of HCG rises rapidly
  Can detect pregnancy with a serum pregnancy test as early as 6 days before the first missed period

## Slide 140: Human Chorionic Gonadotropin (Slide 2 of 2)
Highest level: Occurs 8 weeks after conception
  After this time, HCG declines
72 hours after delivery: HCG disappears entirely
Pregnancy tests are more sensitive in the first trimester
  May even show a negative reaction during the second and third trimester

## Slide 141: Immunoassay Tests (Slide 1 of 5)
Used in medical office to detect pregnancy
Convenient to perform
Provide immediate test results
Positive and negative reactions
  Results in a specific visible reaction
  That can be observed and interpreted

## Slide 142: Immunoassay Tests (Slide 2 of 5)
Commercially available in testing kits
Contain required reagents and supplies
Each kit performs a specific number of tests
Product insert included
  Must follow exactly to prevent inaccurate test results
Most are 99% accurate
  With low occurrence of false-positive test results

## Slide 143: Immunoassay Tests (Slide 3 of 5)
Brand names
  QuickVue One Step
  OSOM
  ICON

## Slide 144: Immunoassay Tests (Slide 4 of 5)
Early prediction pregnancy tests
  May be able to detect pregnancy as early as 2-3 days before first missed period
    May sometimes show a false-negative when performed early (repeat later to confirm results)
  Accurate results more probable if urine testing one week after a missed period

## Slide 145: Immunoassay Tests (Slide 5 of 5)
Results observed as a color change
Instructions for interpreting results
  Included in product insert

## Slide 146: Guidelines for Urine Pregnancy Testing (Slide 1 of 12)
Use clean, disposable urine containers
Preferred specimen: First-voided morning specimen
  Contains highest concentration of HCG
  However, a random specimen can be used
Notes: See Procedure 30.4: Performing a Urine Pregnancy Test.

## Slide 147: Guidelines for Urine Pregnancy Testing (Slide 2 of 12)
Specific gravity should be determined before the test
  Less than 1.007: Too dilute for testing
    Could cause a false-negative result

## Slide 148: Guidelines for Urine Pregnancy Testing (Slide 3 of 12)
Urine specimen should be at room temperature
Kit should be stored according to manufacturer's instructions
  Most testing kits are stored at room temperature (between 59º F [15º C] and 86º F [30º C])
    Away from direct sunlight
Kit past the expiration date should not be used

## Slide 149: Guidelines for Urine Pregnancy Testing (Slide 4 of 12)
If more than one patient is being tested
  Label each testing device with patient’s name
    Prevents mix-up of specimens

## Slide 150: Guidelines for Urine Pregnancy Testing (Slide 5 of 12)
Most testing kits include an internal control
  Performed at same time as testing procedure
  Determines:
    Whether sufficient amount of specimen was added to cassette
    If correct technique was followed

## Slide 151: Guidelines for Urine Pregnancy Testing (Slide 6 of 12)
Internal control
  Performed at the same time as the test procedure
  Determines whether the specimen is sufficient for testing purposes

## Slide 152: Guidelines for Urine Pregnancy Testing (Slide 7 of 12)
If it does not perform as expected
  Test result is invalid
    Must retest the specimen
Document internal control in quality control log
  For first test run each day

## Slide 153: Guidelines for Urine Pregnancy Testing (Slide 8 of 12)
Perform a positive and negative external control
  With each new lot of urine pregnancy testing kits
  Monthly thereafter
External controls are used to:
  Determine if testing reagents are performing properly
  Detect any errors in technique

## Slide 154: Guidelines for Urine Pregnancy Testing (Slide 9 of 12)
External controls
  Consist of commercially available solutions
  May be included with test system or may need to be purchased separately

## Slide 155: Guidelines for Urine Pregnancy Testing (Slide 10 of 12)
Control procedure
  Performed in a similar manner
    To procedure for performing the test on a specimen collected from a patient
  Instead of adding the patient specimen to testing device
    Control is added
  Positive control should produce a positive result
  Negative control should produce a negative result
  Document result in a quality control log

## Slide 156: Guidelines for Urine Pregnancy Testing (Slide 11 of 12)
Failure of external control to produce expected results may be due to:
  Deterioration of testing components due to improper storage
  Improper environmental testing conditions
  Errors in technique used to perform the procedure

## Slide 157: Guidelines for Urine Pregnancy Testing (Slide 12 of 12)
Conditions that can result in a positive result (other than normal pregnancy)
  Ectopic pregnancy
  Molar pregnancy

## Slide 158: Serum Pregnancy Test (Slide 1 of 2)
Radioimmunoassay (RIA) for HCG: Used to detect HCG in serum of blood
More sensitive than urine testing
  Can detect pregnancy earlier with more accuracy
Can detect pregnancy at approximately eighth day after fertilization (6 days before first missed period)
Uses radioisotope technique
  Capable of detecting minute amounts of HCG in the blood

## Slide 159: Serum Pregnancy Test (Slide 2 of 2)
Use
  Diagnose abnormalities (ectopic pregnancy)
  Follow course of early pregnancy
    When abnormalities of embryonic development are suspected
  Provide early diagnosis of pregnancy in high-risk patients
    Example: Patient with diabetes mellitus

## Slide 160
Questions?