## Slide 1
Phlebotomy
Chapter 31

## Slide 2: Learning Objectives Lesson 31.1: Introduction to Venipuncture (Slide 1 of 2)
List and describe the general guidelines that should be followed when performing a venipuncture.
Explain how each of the following blood specimens is obtained:
  Clotted blood
  Serum
  Whole blood
  Plasma

## Slide 3: Learning Objectives Lesson 31.1: Introduction to Venipuncture (Slide 2 of 2)
List the layers into which the blood separates into when an anticoagulant is added to the specimen.
List the layers into which the blood separates into when an anticoagulant is not added to the specimen.
List the OSHA safety precautions that must be followed during venipuncture and when separating serum or plasma from whole blood.

## Slide 4: Introduction to Phlebotomy (Slide 1 of 4)
Purpose of phlebotomy: Collect blood for laboratory analysis
  Phlebotomy: Incision of a vein for the removal of blood
  Phlebotomist: Individual collecting the blood sample

## Slide 5: Introduction to Phlebotomy (Slide 2 of 4)
Specimen may be:
  Tested at the office
  Taken to an outside laboratory for testing
    Must be placed in a biohazard specimen bag

## Slide 6: Introduction to Phlebotomy (Slide 3 of 4)
Specimen may be:
  Taken to an outside laboratory for testing
    Needs to be accompanied by a laboratory request
    Informs laboratory what tests to run—MA completes laboratory request: on computer; manually (by hand)

## Slide 7: Introduction to Phlebotomy (Slide 4 of 4)
Types of blood collections
  Arterial puncture: Performed in a hospital setting—to assess blood for:
    Oxygen level
    Carbon dioxide level
    Acid-base balance
  Venipuncture
  Skin puncture

## Slide 8: Venipuncture (Slide 1 of 3)
Venipuncture (VP): Puncturing of a vein for the removal of a venous blood sample
  Performed when a large blood specimen is needed for testing

## Slide 9: Venipuncture (Slide 2 of 3)
Methods
  Vacuum tube: Use of an evacuated tube (glass or plastic tube containing a vacuum)
    Fastest
    Most convenient
    Most often used

## Slide 10: Venipuncture (Slide 3 of 3)
Methods
  Butterfly and syringe: For difficult draws
    Small veins
    Sclerosed (hardened veins)
Notes: The supplies for the butterfly method are more expensive than those for the vacuum tube method.

## Slide 11: General Guidelines for Venipuncture
Verify any advance preparation
Review specimen collection and handling requirements
Identify the patient
Reassure the patient
Assemble equipment and supplies
Position the patient
Apply tourniquet
Select a site for venipuncture
Obtain type of blood specimen required
Follow Occupational Safety and Health Administration (OSHA) Bloodborne Pathogens Standard

## Slide 12: Patient Preparation for Venipuncture (Slide 1 of 5)
Provide patient with advance preparation (if required)
  Most tests require no preparation

## Slide 13: Patient Preparation for Venipuncture (Slide 2 of 5)
Most common preparation
  Fasting: Abstaining from food or fluid (except water) for a specified amount of time
    Usually 12 to 14 hours
  Avoidance of medication

## Slide 14: Patient Preparation for Venipuncture (Slide 3 of 5)
Patient preparation is listed in reference sources
  Outside laboratory
    Laboratory directory
    Technical support

## Slide 15: Patient Preparation for Venipuncture (Slide 4 of 5)
Patient preparation is listed in reference sources
  POL
    Instructions included with blood analyzers and testing kits

## Slide 16: Patient Preparation for Venipuncture (Slide 5 of 5)
Ask patient if he or she has prepared properly before performing VP
  If patient has not prepared, do not collect specimen
    Unless directed by physician
    If VP is rescheduled, review preparation requirements with patient

## Slide 17: Review Collection and Handling Requirements (Slide 1 of 2)
Includes:
  Collection supplies
  Type of specimen (e.g., serum, whole blood)
  Amount necessary for laboratory analysis
  Techniques for collecting specimen
  Proper handling and storage of specimen

## Slide 18: Review Collection and Handling Requirements (Slide 2 of 2)
Refer to appropriate reference source
  Outside laboratory: Laboratory directory
  POL: Manufacturers’ instructions accompanying the test system
Notes: Refer to Figure 31.2.

## Slide 19: Identification of the Patient (Slide 1 of 2)
Use two forms of identification
  Name
  Date of birth
Avoids collecting specimen on wrong patient
  Could lead to inaccurate diagnosis and wrong treatment

## Slide 20: Identification of the Patient (Slide 2 of 2)
Ask patient to state full name and date of birth
  Compare with information in patient’s chart
If patient is not properly identified
  Could lead to incorrect labeling of specimen
    May result in inaccurate patient diagnosis and wrong treatment

## Slide 21: Assemble the Equipment and Supplies (Slide 1 of 7)
Use appropriate blood tubes
  If tubes are substituted, may not yield proper type of specimen—may affect test results
1106 W Tortolita Mountain Circle 165

## Slide 22: Assemble the Equipment and Supplies (Slide 2 of 7)
Check each tube before use to ensure it is not:
  Broken
  Cracked
  Otherwise damaged

## Slide 23: Assemble the Equipment and Supplies (Slide 3 of 7)
Check expiration date
  Do not use if outdated
Notes: Refer to Figure 31.3.

## Slide 24: Assemble the Equipment and Supplies (Slide 4 of 7)
Label each blood tube
  Unlabeled specimen
    Cause for rejection of specimen by the laboratory
  Use two unique identifiers to label specimen
    Unique identifier: Information that clearly identifies a specific patient
      Example: Patient’s name and DOB

## Slide 25: Assemble the Equipment and Supplies (Slide 5 of 7)
Label each blood tube
  Method for labeling specimen: Computerized bar code label

## Slide 26: Assemble the Equipment and Supplies (Slide 6 of 7)
Label each blood tube
  Method for labeling specimen: Handwritten information on label
    Patient’s name and DOB
    Date and time of collection
    MA’s initials
    Other information required by laboratory
Notes: Refer to Figure 31.4.

## Slide 27: Assemble the Equipment and Supplies (Slide 7 of 7)
Label each blood tube
  Complete laboratory request for specimens transported to an outside laboratory
  Follow medical office policy as to when to label tubes
    Some offices prefer tubes to be labeled before specimen is drawn
    Other offices want tubes labeled right after specimen is obtained

## Slide 28: Reassuring the Patient (Slide 1 of 3)
Explain VP procedure in an unhurried and confident manner
  Helps reduce patient fears—relaxes veins
    Makes procedure easier to perform
    Less pain for patient

## Slide 29: Reassuring the Patient (Slide 2 of 3)
Instruct patient to remain still
Tell patient that a small amount of pain is associated with the procedure
  Never tell the patient that the VP will not hurt

## Slide 30: Reassuring the Patient (Slide 3 of 3)
Just before inserting the needle, tell patient he or she will “feel a small stick”
  Avoids startling the patient: Could cause patient to move
    Movement causes pain
    Could damage VP site

## Slide 31: Patient Position for Venipuncture (Slide 1 of 5)
Important to a successful collection
Proper positioning
  Allows easy access to vein
  More comfortable for patient
Position depends on vein being used

## Slide 32: Patient Position for Venipuncture (Slide 2 of 5)
Most common VP site: Antecubital space
  Patient should be seated in a chair
  Arm extended in downward position—to form straight line from shoulder to wrist
    With palm facing up
    Arm should not bend at elbow
Notes: Refer to Figure 31.5.

## Slide 33: Patient Position for Venipuncture (Slide 3 of 5)
Most common VP site: Antecubital space
  Arm should be well supported on the armrest
    By rolled towel
    By patient placing fist of the other hand under the elbow

## Slide 34: Patient Position for Venipuncture (Slide 4 of 5)
Never have patient on stool or standing
  Fainting could occur: Patient may be injured
If patient has fainted in the past from VP or is nervous
  Place in a semireclining position on the examining table

## Slide 35: Patient Position for Venipuncture (Slide 5 of 5)
Venous reflux: Blood flows from evacuated tube back into patient’s vein during the procedure
  Could cause patient to have adverse reaction to a tube additive
    Particularly EDTA
  To prevent: Keep patient’s arm in a downward position
    Evacuated tube remains below the VP site—fills from the bottom up

## Slide 36: Application of the Tourniquet (Slide 1 of 3)
Purpose: Makes patient’s veins stand out so that they are easier to palpate
Causes venous blood to slow down and pool in veins in front of tourniquet
  Makes veins more prominent
    More visible
    Can be palpated
Notes: Tourniquets can be made of latex. Make sure the patient is not allergic to latex. If he or she is allergic, use a latex-free tourniquet.

## Slide 37: Application of the Tourniquet (Slide 2 of 3)
When applying: Important to obtain correct tension
  Should slow venous flow without affecting arterial flow
  Too tight: Obstructs arterial and venous flow
    May produce inaccurate test results

## Slide 38: Application of the Tourniquet (Slide 3 of 3)
When applying: Important to obtain correct tension
  Too loose: Veins do not stand out enough to be palpated
  Correct tension
    Should fit snugly
    Not pinch skin

## Slide 39: Guidelines for Applying the Tourniquet (Slide 1 of 6)
Do not apply over sores or burned skin
Place 3 to 4 inches above bend in elbow
  Allows adequate room for:
    Cleansing site
    Performing VP

## Slide 40: Guidelines for Applying the Tourniquet (Slide 2 of 6)
Apply treatment so that it is snug
  Should not pinch patient’s skin
  Should not be painful to patient
Ask patient to clench fist: Pushes blood from lower arm into veins for easier palpation
  Ask patient to clench and unclench fist a few times
    Avoid vigorous pumping: Could lead to hemoconcentration

## Slide 41: Guidelines for Applying the Tourniquet (Slide 3 of 6)
Never leave on for more than one minute
  Uncomfortable for patient
  Causes venous blood to stagnate: Venous stasis
    Plasma filters into tissues: Causes hemoconcentration

## Slide 42: Guidelines for Applying the Tourniquet (Slide 4 of 6)
Never leave on for more than one minute
  Hemoconcentration: An increase in the concentration of blood components
    Caused by a decrease in the fluid content of the blood
    Can alter test results

## Slide 43: Guidelines for Applying the Tourniquet (Slide 5 of 6)
Remove tourniquet when good blood flow is established
  When first learning venipuncture: Best to remove tourniquet just before removing needle—may move needle
    No more blood flow
    Must redraw

## Slide 44: Guidelines for Applying the Tourniquet (Slide 6 of 6)
Always remove tourniquet before removing needle
  If needle is removed first, blood is forced out of the puncture site causing a hematoma
  Hematoma: A swelling or mass of coagulated blood caused by a break in a blood vessel
Wipe tourniquet with a disinfectant (alcohol) if reusable
  Throw away if disposable
Notes: Have the patient unclench his or her fist before removing the needle.

## Slide 45: Rubber Tourniquet (Slide 1 of 2)
Flat, soft band of rubber
  One inch wide
  15 to 18 inches long
  Advantage: Easily removed with one hand
Notes: The MA should make sure the tourniquet end is accessible for easy removal.

## Slide 46: Rubber Tourniquet (Slide 2 of 2)
Position
  3 to 4 inches above bend in elbow
  Should lie flat against patient’s skin
  Flaps must be directed upward so that they do not dangle in working area
Notes: Make sure the tourniquet lies flat against the patient’s skin.
Refer to Figure 31.6.

## Slide 47: Velcro-Closure Tourniquet (Slide 1 of 2)
Band of rubber or elastic with Velcro attached at the ends
Advantages
  Easier to apply than a rubber tourniquet
  More comfortable for patient
Notes: Refer to Figure 31.7.

## Slide 48: Velcro-Closure Tourniquet (Slide 2 of 2)
Disadvantages
  More difficult to remove
  May not fit around arm of obese patients

## Slide 49: Site Selection for Venipuncture (Slide 1 of 7)
Best site for most patients: Veins in antecubital space
  Easy to draw blood
    Patient with large visible veins
  Difficult to draw blood
    Small veins
    Veins that cannot be palpated
Notes: Refer to Figure 31.8.

## Slide 50: Site Selection for Venipuncture (Slide 2 of 7)
Antecubital veins
  Usually have wide lumen
  Close to surface of skin
    Makes them easily accessible

## Slide 51: Site Selection for Venipuncture (Slide 3 of 7)
Antecubital veins
  Usually have thick walls
    Less likely to collapse
  Skin is less sensitive
    Less pain for patient

## Slide 52: Site Selection for Venipuncture (Slide 4 of 7)
Do not use small spidery veins on the surface of skin
  Not suitable for VP
  Antecubital veins lie beneath these veins
Notes: Patients typically know which of their veins is the best one to use for VP.

## Slide 53: Site Selection for Venipuncture (Slide 5 of 7)
Veins to use in antecubital space
  Median cubital: Best vein
  Large vein: Does not roll
  Located in middle of antecubital space—cannot be used
    When it lies deep in the tissues: Cannot be palpated
    Is scarred from repeated VPs

## Slide 54: Site Selection for Venipuncture (Slide 6 of 7)
Veins to use in antecubital space
  Basilic and cephalic: Located on opposite sides of antecubital space
    Use: When median cubital cannot be used
    Cephalic: Located on thumb-side of hand
    Basilic: Located on little-finger side of hand
    Disadvantage: May roll and escape puncture—to prevent, apply firm pressure below vein to stabilize it

## Slide 55: Site Selection for Venipuncture (Slide 7 of 7)
Brachial artery: Also located in antecubital space (used to measure BP)
  Lies deeper in the tissues
  Artery pulsates, is more elastic, and has a thicker wall than a vein
  If punctured: Patient feels more pain and blood is bright red and comes out pulsing—if this occurs:
    Remove tourniquet and then needle
    Apply pressure with gauze pad for 4 to 5 minutes
Notes: Palpate your brachial artery. You can locate it by feeling for the brachial pulse.

## Slide 56: Guidelines for Site Selection (Slide 1 of 12)
Ensure adequate lighting
  Facilitates selection of vein

## Slide 57: Guidelines for Site Selection (Slide 2 of 12)
Ensure that veins “stand out” as much as possible
  Apply tourniquet
  Ask patient to clench fist

## Slide 58: Guidelines for Site Selection (Slide 3 of 12)
Examine antecubital veins of both arms
  Patient may have larger veins in one arm than in other
  Ask patient which vein was previously used for VP

## Slide 59: Guidelines for Site Selection (Slide 4 of 12)
Use inspection and particularly palpation to select a vein
  Vein does not have to be seen to be a good selection
  Palpation alone can be used to locate a vein
  Vein feels like an elastic tube
    Gives under the pressure of the fingertips
Notes: Follow the vein direction with your fingertip.

## Slide 60: Guidelines for Site Selection (Slide 5 of 12)
Palpate for the median cubital vein first
  Advantages over other antecubital veins
    Usually bigger
    Anchored better
    Bruises less
    Poses smallest risk of injuring underlying structures (nerves)
Notes: Define median. (Middle)

## Slide 61: Guidelines for Site Selection (Slide 6 of 12)
Palpate for the median cubital vein first
  If median cubital cannot be seen, but can still be palpated
    Use as a first choice
  If median cubital vein is good in both arms
    Select the one that is the fullest
Notes: If a vein cannot be seen, but can be palpated, look for skin marks to help remember the location of the vein.

## Slide 62: Guidelines for Site Selection (Slide 7 of 12)
Palpate for the median cubital vein first
  Cephalic: Second choice
    Does not roll and bruise as easily as basilic
  Basilic: Last choice—may cause injury to underlying structures
    In some individuals, branches of median nerve lie close to basilic
    Lie in close proximity to the brachial artery

## Slide 63: Guidelines for Site Selection (Slide 8 of 12)
Thoroughly assess vein
  Place one or two fingertips over vein
    Index and middle finger
  Press lightly, then release pressure
  Do not use thumb to palpate (not as sensitive)
  Suitable vein feels round, firm, elastic, and engorged
    When an engorged vein is depressed and released, it springs back in a rounded, filled state

## Slide 64: Guidelines for Site Selection (Slide 9 of 12)
Determine size, depth, and direction of vein
  Thoroughly palpate vein

## Slide 65: Guidelines for Site Selection (Slide 10 of 12)
Determine size, depth, and direction of vein
  Trace the path of the vein
    By rolling the index finger back and forth over vein
  Inspect and palpate vein for problems
    Small
    Hard
    Bumpy
    Flat

## Slide 66: Guidelines for Site Selection (Slide 11 of 12)
Mentally “map” puncture site on patient’s arm with skin marks
  Site may be near freckle, wrinkle, or pigmented area
  Helpful in making stick when vein cannot be seen and can only be palpated
Do not leave tourniquet on for more than one minute
  Causes:
    Patient discomfort
    Hemoconcentration

## Slide 67: Guidelines for Site Selection (Slide 12 of 12)
Techniques to make veins more prominent
  Remove tourniquet and have patient dangle arm over side of chair for 1 to 2 minutes
  Tap vein site sharply with index finger and second finger
  Gently massage arm from wrist to elbow
  Apply warm, moist washcloth for five minutes

## Slide 68: Alternative Venipuncture Sites (Slide 1 of 5)
Alternative sites
  Inner forearm
  Wrist area above thumb
  Back of hand
Notes: Refer to Figure 31.9.

## Slide 69: Alternative Venipuncture Sites (Slide 2 of 5)
Alternative veins
  Smaller than antecubital veins
  Have thinner walls
Use alternative veins when all possibilities at the antecubital site have been considered
  Example: May be able to use butterfly on a small antecubital vein

## Slide 70: Alternative Venipuncture Sites (Slide 3 of 5)
Use veins in hands as a last resort
  Have a tendency to roll because:
    Not supported by much tissue
    Close to the surface of the skin—makes them more difficult to stick

## Slide 71: Alternative Venipuncture Sites (Slide 4 of 5)
Use veins in hands as a last resort
  Abundant supply of nerves in hand
    Makes procedure uncomfortable for patient
  Thin walls—make them susceptible to:
    Collapsing
    Bruising
    Phlebitis

## Slide 72: Alternative Venipuncture Sites (Slide 5 of 5)
In some patients, hand veins may be only accessible site
  Examples
    Obese patients
    Elderly patients
Notes: Do not stick at the junction of a vein.

## Slide 73: Types of Blood Specimens (Slide 1 of 4)
Type of blood specimen required depends on type of test to be performed
  Examples
    Serum: Required for most blood chemistry studies
    Whole blood: Required for a complete blood count (CBC)
Notes: What is the difference between serum and whole blood? (See the next slides for answers.)

## Slide 74: Types of Blood Specimens (Slide 2 of 4)
Clotted blood: Obtained from tube with no anticoagulant
  Causes blood cells to clot
Serum: Obtained from clotted blood
  Allow specimen to stand and then centrifuge it
  Because tube does not contain an anticoagulant, separates into:
    Top layer: Serum
    Bottom layer: Clotted blood cells

## Slide 75: Types of Blood Specimens (Slide 3 of 4)
Whole blood: Obtained from tube containing an anticoagulant to prevent clotting of blood cells
  Tube must be gently rotated 8 to 10 times after collection
    To mix anticoagulant with blood
Notes: Do not shake the tube.

## Slide 76: Types of Blood Specimens (Slide 4 of 4)
Plasma: Obtained from whole blood that has been centrifuged
  Because tube contains an anticoagulant, separates into:
    Top layer: Plasma
    Middle layer: Buffy coat (white blood cells and platelets)
    Bottom layer: Red blood cells (RBCs)

## Slide 77: Layers of Blood (Slide 1 of 2)
When an anticoagulant is added to the specimen
  Plasma
  Buffy coat
  Cells
Notes: Refer to Figure 31.10B.

## Slide 78: Layers of Blood (Slide 2 of 2)
When an anticoagulant is not added to the specimen
  Serum
  Cells (clot)
Notes: Refer to Figure 31.10A.

## Slide 79: OSHA Safety Precautions (Slide 1 of 5)
To avoid exposure to blood-borne pathogens during VP
  Wear gloves
  Avoid hand-to-mouth contact while working with blood specimens
    Eating
    Drinking
    Applying makeup
  Wear a face shield (or mask and eye protection):
    Whenever splashes, spray, splatter, or droplets of blood may be generated

## Slide 80: OSHA Safety Precautions (Slide 2 of 5)
To avoid exposure to blood-borne pathogens during VP
  Perform all procedures involving blood in a manner to minimize splashing, spraying, splattering, and generating droplets of blood
  Bandage cuts before gloving
  Sanitize hands after removing gloves
  If hands or other skin surface comes in contact with blood: Wash with soap and water immediately

## Slide 81: OSHA Safety Precautions (Slide 3 of 5)
To avoid exposure to blood-borne pathogens during VP
  If mucous membranes come in contact with blood: Flush with water immediately
  Do not break, bend, or shear contaminated venipuncture needles
  Do not recap contaminated venipuncture needle

## Slide 82: OSHA Safety Precautions (Slide 4 of 5)
To avoid exposure to blood-borne pathogens during VP
  Locate the sharps container as close as possible to the area of use
    Immediately after use: Discard VP setup in biohazard sharps container
  Place blood specimens in containers that prevent leakage during collection, handling, processing, storage, transport, and shipping

## Slide 83: OSHA Safety Precautions (Slide 5 of 5)
To avoid exposure to blood-borne pathogens during VP
  Handle laboratory equipment and supplies properly and with care
    As indicated by the manufacturer
      Example: Wait for centrifuge to come to a complete stop before opening
  Do not store food in refrigerator where testing supplies or specimens are stored
  If exposed to blood, report incident immediately to your physician-employer
Notes: An incident report needs to be filled out if you are exposed to blood.

## Slide 84: Learning Objectives Lesson 31.2: Performing a Venipuncture (Slide 1 of 2)
State the additive content of each of the following vacuum tubes, and list the types of blood specimens that can be obtained from each: red, lavender, gray, light blue, green, and royal blue.
Identify and explain the order of draw for the vacuum tube and butterfly methods of venipuncture.

## Slide 85: Learning Objectives Lesson 31.2: Performing a Venipuncture (Slide 2 of 2)
List and describe the guidelines for use of evacuated tubes.
Identify possible problems during a venipuncture.
List four ways to prevent a blood specimen from becoming hemolyzed.

## Slide 86: Vacuum Tube Method of Venipuncture (Slide 1 of 2)
Frequently used to collect venous blood specimens
Ideal for collecting blood from antecubital veins that are of adequate size
  To withstand the pressure of the vacuum in the evacuated tube
Notes: See Procedure 31.1: Venipuncture – Vacuum Tube Method.

## Slide 87: Vacuum Tube Method of Venipuncture (Slide 2 of 2)
Vacuum tube system
  Collection needle
  Plastic needle holder
  Evacuated tube
Notes: Refer to Figure 31.11.

## Slide 88: Needle (Slide 1 of 6)
Double-pointed needle with threaded hub
  Screws into plastic holder
Packaged in a sealed twist-apart container
  Do not use if seal is broken
  Printed on paper seal
    Needle gauge
    Needle length
Notes: Refer to Figure 31.12.

## Slide 89: Needle (Slide 2 of 6)
Needle consists of:
  Anterior needle: Is longer and has a beveled point
    Bevel: Facilitate entry into skin and vein
Notes: Locate the bevel on a needle.

## Slide 90: Needle (Slide 3 of 6)
Needle consists of:
  Posterior needle: Pierces rubber stopper of evacuated tube—needle has a rubber sleeve that functions as a valve
    When needle is pushed into rubber stopper, sleeve compresses—exposes needle opening; allows blood to enter tube

## Slide 91: Needle (Slide 4 of 6)
Needle consists of:
  Posterior needle: Pierces rubber stopper of evacuated tube—needle has a rubber sleeve that functions as a valve
    When tube is removed, sleeve slides back over needle opening—closes off opening; stops flow of blood

## Slide 92: Needle (Slide 5 of 6)
Gauge sizes for VP: 20 to 22
  21 gauge: Most commonly used
  22 gauge: Recommended for children and adults with smaller veins
  20 gauge: When a large volume tube is used
    Manufacturer often color-codes needle guard by gauge for easier identification

## Slide 93: Needle (Slide 6 of 6)
Length of needle: 1 inch and 1½ inches
  Length used based on individual preference
    1 inch: Less intimidating to patient; offers more control during stick
    1½ inch: Allows more room for stabilizing the vein

## Slide 94: Safety-Engineered Venipuncture Devices (Slide 1 of 2)
OSHA stipulates requirements
  To reduce needlestick and other sharps injuries among health care workers
Employers must evaluate and implement safer medical devices
  Includes safety-engineered VP devices
Notes: Refer to Figure 31.13.

## Slide 95: Safety-Engineered Venipuncture Devices (Slide 2 of 2)
Employers must evaluate and implement safer medical devices
  Have built-in safety features to reduce risk of needlestick injuries
Notes: The MA should hear a click when this safety feature is activated.

## Slide 96: Plastic Holder (Slide 1 of 3)
Consists of plastic cylinder with two openings
  Small opening: Used to secure needle
  Large opening: Holds evacuated tube

## Slide 97: Plastic Holder (Slide 2 of 3)
Flange: Extension on large opening
  Assists in insertion and removal of tubes
  Prevents holder from rolling when placed on a flat surface

## Slide 98: Plastic Holder (Slide 3 of 3)
Indention on holder
  Marks point at which the posterior needle starts to enter rubber stopper of tube
    Do not insert tube stopper past this point before entering the vein—causes tube to fill with air; blood is not able to enter the tube
Notes: The tube should lie in the plastic holder until the needle enters the vein.

## Slide 99: Evacuated Tubes
Glass tube with:
  Rubber stopper
  Hemogard closure stopper
Contains vacuum that creates suction
  Pulls blood specimen into tube
Tube additive must not:
  Alter blood components
  Affect laboratory test
Notes: If you are in the vein, blood will automatically flow into the vacuum tube when you push it onto the posterior needle.
Refer to Figure 31.14 and 31.15.

## Slide 100: Additive Content of Evacuated Tubes (Slide 1 of 11)
Color coded for easy identification of additive
Red: Does not contain an anticoagulant
  Used to obtain clotted blood or serum
  Serum required for:
    Immunologic tests
    Most blood chemistries

## Slide 101: Additive Content of Evacuated Tubes (Slide 2 of 11)
Red/gray speckled tube (“tiger-top”)
  Gold stopper: If using Hemogard tubes
  Used to obtain serum
  Does not contain an anticoagulant

## Slide 102: Additive Content of Evacuated Tubes (Slide 3 of 11)
Red/gray speckled tube (“tiger-top”)
  Gold stopper: If using Hemogard tubes
    Contains a clot activator—makes RBCs clot more quickly to yield serum: Invert tube 5 times after drawing to mix clot activator with specimen
    Also contains a gel—separates cells from serum when tube is centrifuged

## Slide 103: Additive Content of Evacuated Tubes (Slide 4 of 11)
Lavender: EDTA (anticoagulant)
  Used to obtain whole blood or plasma
  Most common use: Collect a blood specimen for a CBC

## Slide 104: Additive Content of Evacuated Tubes (Slide 5 of 11)
Light blue: Sodium citrate (anticoagulant)
  Used to obtain whole blood or plasma
  Most common use: Coagulation tests (e.g., prothrombin time)

## Slide 105: Additive Content of Evacuated Tubes (Slide 6 of 11)
Green: Heparin (anticoagulant)
  Used for blood gas determinations and pH assays
Gray: Sodium fluoride/potassium oxalate (anticoagulant)
  Used to obtain whole blood or plasma
  Most common use: OGTT

## Slide 106: Additive Content of Evacuated Tubes (Slide 7 of 11)
Royal blue: EDTA or no additive
  Made of refined glass and a special stopper
  Used to detect trace elements (e.g., lead, arsenic)

## Slide 107: Additive Content of Evacuated Tubes (Slide 8 of 11)
Additive tube used depends on type of test performed
  MA must determine correct stopper color
  Example: CBC requires lavender-stoppered tube
  Do not substitute one additive tube for another
    Leads to inaccurate results

## Slide 108: Additive Content of Evacuated Tubes (Slide 9 of 11)
Tubes are available in different sizes: Range between 2 mL and 10 mL
  Size selected depends on the amount of specimen required for the test
Information on amount of specimen and stopper color required
  Outside laboratory: Indicated in laboratory directory
  POL: Indicated in instructions accompanying blood analyzer or testing kit

## Slide 109: Additive Content of Evacuated Tubes (Slide 10 of 11)
Label of tube indicates:
  Additive content
  Expiration date
  Tube capacity
  Fill indicator
    To indicate when vacuum has been exhausted—tube is full

## Slide 110: Additive Content of Evacuated Tubes (Slide 11 of 11)
Hemogard closure stopper
  Consists of rubber stopper with a plastic closure that overhangs outside of tube
    Acts as a single unit to reduce the likelihood of coming in contact with contents of tube
  If need to gain access to blood in tube (e.g., testing, further processing)
    Prevents splattering of blood
  Conventional rubber stopper-evacuated tube; pops as top is removed
  Color coding is similar to rubber-stoppered tubes

## Slide 111: Order of Draw for Multiple Tubes (Slide 1 of 5)
Blood culture tube
  Yellow-stoppered glass tube
    Contains SPS (anticoagulant)
  Drawn first to prevent contamination by other tubes
  Used for blood cultures and other tests that require a sterile specimen
Notes: See Table 31.1: Order of Draw for Collection of Multiple Evacuated Tubes.

## Slide 112: Order of Draw for Multiple Tubes (Slide 2 of 5)
Coagulation tubes (light blue)
  Prevents additives from other tubes from getting into the tube
  If butterfly used to collect specimen, modification in technique is required
    Butterfly tubing: Contains air (0.3 to 0.5 mL)
    If light blue tube is first or only tube drawn; must draw 5-mL red tube first and discard

## Slide 113: Order of Draw for Multiple Tubes (Slide 3 of 5)
Coagulation tubes (light blue)
  Some of tube’s vacuum exhausted by air in tubing—results in underfilling tube (underfilled tube results in incorrect anticoagulant to blood ratio)
  Causes inaccurate result when performing coagulation test
  To prevent erroneous test results, make sure to completely fill coagulation tube to exhaustion of vacuum

## Slide 114: Order of Draw for Multiple Tubes (Slide 4 of 5)
Serum tubes (Red, red/gray, gold)
  Includes:
    Tubes with or without a clot activator
    Tubes with or without a gel barrier
  Prevents contamination of serum tubes by tubes with an anticoagulant

## Slide 115: Order of Draw for Multiple Tubes (Slide 5 of 5)
Anticoagulant tubes in this order:
  Green
  Lavender
  Royal blue (tube that contains EDTA)
  Gray
    Prevents cross-contamination between different types of anticoagulants—cross-contamination may lead to inaccurate test results
Notes: Tubes should be lined up in the correct order of draw when the MA is performing venipuncture.

## Slide 116: Evacuated Tube Guidelines (Slide 1 of 13)
Select proper tubes
  According to tests being performed
  Amount of specimen required

## Slide 117: Evacuated Tube Guidelines (Slide 2 of 13)
Check tubes for cracks: Will no longer have a vacuum
Check expiration date: Outdated tube may not have a vacuum

## Slide 118: Evacuated Tube Guidelines (Slide 3 of 13)
Make sure each tube is properly labeled
  Avoids mixing up specimens
  Bar codes are often used to identify specimens
    Laboratory instruments that do the testing read the bar codes—automatically record results onto laboratory report
    Printed information is included on bar code label
    Attach correct bar code label to blood tube
Notes: Refer to Figure 31.17.

## Slide 119: Evacuated Tube Guidelines (Slide 4 of 13)
Powdered additive tubes (gray-stoppered tube)
  Gently tap tube just below stopper
    Dislodges additive from stopper
    If additive is trapped in stopper—could cause erroneous test results

## Slide 120: Evacuated Tube Guidelines (Slide 5 of 13)
Take precautions to avoid premature loss of vacuum
  Can be caused by:
    Dropping tube
    Pushing posterior needle through stopper before puncturing vein
    Partially pulling needle out of patient's arm during VP

## Slide 121: Evacuated Tube Guidelines (Slide 6 of 13)
To make a puncture:
  Use a continuous steady motion at a 15-degree angle to patient's skin
Notes: The bevel must be facing up.

## Slide 122: Evacuated Tube Guidelines (Slide 7 of 13)
To make a puncture:
  Do not use:
    Slow timid motion—painful to patient
    Rapid, jabbing motion—painful to patient; could cause needle to go through vein resulting in failure to obtain blood; hematoma
Notes: Practice inserting a VP needle into a practice arm until you attain the correct motion.
Once you puncture the patient’s vein, the patient will not experience pain as long as you do not move the needle.

## Slide 123: Evacuated Tube Guidelines (Slide 8 of 13)
Follow proper order of draw to prevent:
  Contamination of nonadditive tubes with additive tubes
  Cross-contamination between different types of additive tubes
    Leads to inaccurate test results

## Slide 124: Evacuated Tube Guidelines (Slide 9 of 13)
Fill tubes until vacuum is exhausted
  Blood ceases to flow into tube
  Tube will be almost, but not quite, full
  If tube is removed before vacuum is exhausted
    Rush of air enters tube—damages RBCs
  Tube with anticoagulant ensures proper ratio of additive to blood

## Slide 125: Evacuated Tube Guidelines (Slide 10 of 13)
Remove last tube from plastic holder before removing needle from vein
  Prevents blood from dripping out of needle after withdrawing it

## Slide 126: Evacuated Tube Guidelines (Slide 11 of 13)
Mix tubes containing anticoagulant immediately after drawing
  Rotate tube gently 8 to 10 times
    Provides adequate mixing without causing hemolysis
    Hemolysis: The breakdown of blood cells—shaking tube can result in hemolysis

## Slide 127: Evacuated Tube Guidelines (Slide 12 of 13)
Mix tubes containing anticoagulant immediately after drawing
  Clotting of blood can be caused by:
    Not mixing tubes immediately
    Inadequate mixing—may cause inaccurate test results

## Slide 128: Evacuated Tube Guidelines (Slide 13 of 13)
After VP: Top of stopper may contain residual blood
  Follow OSHA standards when handling tubes

## Slide 129: Butterfly Method of Venipuncture (Slide 1 of 10)
Also called winged infusion method
  Winged infusion set used to perform the procedure
Term butterfly derived from plastic wings located between needle and tubing
Notes: Refer to Figure 31.18.

## Slide 130: Butterfly Method of Venipuncture (Slide 2 of 10)
Advantages
  Provides better control when making puncture
  Less pressure exerted on vein from evacuated tube
    Pressure must travel through a length of tubing
    Minimizes pressure on vein
Notes: See Procedure 31.2: Venipuncture – Butterfly Method.

## Slide 131: Butterfly Method of Venipuncture (Slide 3 of 10)
Recommended for:
  Adult patients with small antecubital veins
  Children: Typically have small antecubital veins
  When antecubital veins are unavailable
    Alternative site is used (e.g., hand)—may occur with elderly or obese patients

## Slide 132: Butterfly Method of Venipuncture (Slide 4 of 10)
Alternative sites
  Veins are smaller
  Have a thin wall
  More likely to collapse

## Slide 133: Butterfly Method of Venipuncture (Slide 5 of 10)
Gauge of needle: 21 to 23
Length of needle: ½ to ¾ inch
  Short and sharp needle makes it easier to stick difficult veins

## Slide 134: Butterfly Method of Venipuncture (Slide 6 of 10)
For an extremely small vein:
  Use a 23-gauge needle to prevent rupture of vein
  Use smaller volume tube (2 mL)
    Large tube: Too much vacuum pressure on vein—vein may collapse

## Slide 135: Butterfly Method of Venipuncture (Slide 7 of 10)
Wings may be color coded by gauge
  For easier identification
    Green: 21 gauge
    Light blue: 23 gauge

## Slide 136: Butterfly Method of Venipuncture (Slide 8 of 10)
Needle attached to tubing
  Tubing lengths
    7 inch
    12 inch
Notes: Tubing must be extended to prevent kinks.

## Slide 137: Butterfly Method of Venipuncture (Slide 9 of 10)
Adapters for winged infusion sets
  Luer adapter: Attached to posterior needle
    Plastic holder screwed onto Luer adapter
  Hub adapter: Used to attach a syringe

## Slide 138: Butterfly Method of Venipuncture (Slide 10 of 10)
Safety needles available
  Shield that covers contaminated needle
Notes: The shield clicks and locks into place over the needle.

## Slide 139: Guidelines for the Butterfly Method (Slide 1 of 6)
Patient position
  Antecubital, wrist, and forearm veins
    Arm in straight line from shoulder to wrist

## Slide 140: Guidelines for the Butterfly Method (Slide 2 of 6)
Patient position
  Hand veins
    Hand on armrest—have patient make a loose fist or grasp a rolled towel; causes hand veins to stand out
    Locate vein between knuckles and wrist bones

## Slide 141: Guidelines for the Butterfly Method (Slide 3 of 6)
Position of tourniquet
  Forearm or wrist: 3 inches above site
  Hand: Just above wrist bone

## Slide 142: Guidelines for the Butterfly Method (Slide 4 of 6)
Compress plastic wings together
  Insert with bevel up at 15-degree angle to skin
  After entering vein; decrease angle to 5 degrees

## Slide 143: Guidelines for the Butterfly Method (Slide 5 of 6)
Slowly thread needle inside vein an additional ¼ inch
  Anchors (seats) needle in center of vein
    Can use both hands to change tubes

## Slide 144: Guidelines for the Butterfly Method (Slide 6 of 6)
To prevent venous reflux
  Keep tube and holder in a downward position
    Ensures that tube fills from bottom up
Follow proper order of draw (same as for vacuum tube method)

## Slide 145: Failure to Obtain Blood (Slide 1 of 7)
May occur with:
  Obese patients
    May have small superficial veins
    Suitable vein buried deep in adipose tissue

## Slide 146: Failure to Obtain Blood (Slide 2 of 7)
May occur with:
  Elderly patients with arteriosclerosis
    May have thick and hard veins—difficult to puncture
  Small or thin-walled veins may collapse

## Slide 147: Failure to Obtain Blood (Slide 3 of 7)
After two unsuccessful attempts:
  Ask for assistance in obtaining blood specimen

## Slide 148: Failure to Obtain Blood (Slide 4 of 7)
Failure to obtain blood once needle has been inserted
  Not inserting needle far enough
    Prevents needle from entering the vein
Notes: Refer to Figure 31.21.

## Slide 149: Failure to Obtain Blood (Slide 5 of 7)
Failure to obtain blood once needle has been inserted
  Inserting needle too far causes needle to go through the vein
  Bevel opening becoming lodged against wall of vein
Notes: Bruising may occur if the needle goes through the vein.

## Slide 150: Failure to Obtain Blood (Slide 6 of 7)
Remove needle if blood is not obtained
  Do not probe vein
    Uncomfortable for patient
    May affect integrity of blood specimen—leads to inaccurate test results
Notes: Probing may also result in phlebitis.

## Slide 151: Failure to Obtain Blood (Slide 7 of 7)
Occasionally, evacuated tube may lose its vacuum
  Causes
    Manufacturing defect
    Improper handling of tube
  Remove tube and insert another one
Notes: Have extra tubes available.

## Slide 152: Inappropriate Puncture Sites (Slide 1 of 2)
Patient complains of pain or soreness at a potential site
  Avoid site
Do not use areas that are:
  Scarred
  Bruised
  Burned
  Adjacent to areas of infection

## Slide 153: Inappropriate Puncture Sites (Slide 2 of 2)
Avoid an arm with edema
  Makes it difficult to locate a vein
  Takes longer for puncture to heal
Avoid arm to which a cast is applied
Avoid arm on the same side of a radical mastectomy

## Slide 154: Scarred and Sclerosed Veins (Slide 1 of 3)
Caused by:
  Many venipunctures over period of years
    Scar tissue develops in wall of vein
  Elderly patients with arteriosclerosis
    Veins become thickened
Notes: What conditions require frequent venipunctures? (Patient on Coumadin therapy)

## Slide 155: Scarred and Sclerosed Veins (Slide 2 of 3)
Veins feel stiff and hard
Difficult to stick
Blood return may be poor
  Caused by narrowed lumen

## Slide 156: Scarred and Sclerosed Veins (Slide 3 of 3)
Recommended: Use another vein
  If not possible, insert needle with careful pressure to avoid going through vein

## Slide 157: Rolling Veins
Side veins have a tendency to roll
  Cephalic
  Basilic
To prevent rolling, apply firm pressure with thumb
  Apply the pressure to the side of the vein and below the vein
    Stabilizes the vein; keeps thumb out of the way when making the puncture

## Slide 158: Collapsing Veins (Slide 1 of 3)
Most likely to collapse
  Small veins
  Veins with thin walls

## Slide 159: Collapsing Veins (Slide 2 of 3)
Most likely to occur with vacuum tube method
  Sucking action of vacuum causes vein to collapse
    Blocks flow of blood into tube
    Result: Small amount of blood enters the tube and then stops

## Slide 160: Collapsing Veins (Slide 3 of 3)
Use butterfly or syringe method on patients with small veins
  Better control
  Less pressure on vein

## Slide 161: Premature Needle Withdrawal (Slide 1 of 2)
Needle comes out of vein prematurely
Caused by:
  Patient movement
  Improper VP technique

## Slide 162: Premature Needle Withdrawal (Slide 2 of 2)
Blood is forced out of puncture site from pressure of the tourniquet
Immediate action is required to prevent a hematoma
  Remove tourniquet immediately
  Place a gauze pad on site
  Apply pressure with gauze until bleeding stops

## Slide 163: Hematoma (Slide 1 of 3)
Blood leaks from puncture site of the vein into surrounding tissue
  Results in a bruise

## Slide 164: Hematoma (Slide 2 of 3)
Causes
  Needle inserted too far and goes through vein
  Bevel opening is partially in vein and partially out of vein
  Applying insufficient pressure after needle removal

## Slide 165: Hematoma (Slide 3 of 3)
First sign: Sudden swelling in area around the puncture site
  Remove tourniquet and needle immediately (if needle is still in vein)
  Apply pressure until bleeding stops

## Slide 166: Hemolysis (Slide 1 of 3)
Hemolysis: Breakdown of blood cells
Blood cells are fragile
  Rough handling may cause hemolysis
  Produces inaccurate test results

## Slide 167: Hemolysis (Slide 2 of 3)
To prevent hemolysis:
  Store tubes at room temperature
    Chilled tubes can result in hemolysis
  Allow alcohol to air dry completely
    Alcohol entering specimen can cause hemolysis

## Slide 168: Hemolysis (Slide 3 of 3)
To prevent hemolysis:
  Do not use a small-gauge needle to collect the specimen
    Causes RBCs to rupture as they pass through the needle lumen
  Practice good technique in collecting the specimen
  Always handle the blood specimen tube carefully
    Do not shake or handle roughly

## Slide 169: Fainting (Slide 1 of 2)
VP may cause dizziness or fainting
  May occur during or after VP
Notes: If a patient has fainted from a venipuncture in the past, what should the MA do before performing the procedure? (Perform the VP with the patient in a reclining position.)

## Slide 170: Fainting (Slide 2 of 2)
What to do
  Protect patient from injury
    Example: Prevent patient from falling
  Place patient in position that promotes blood flow to brain
  Notify physician for further treatment
Notes: Refer to Highlight on Vasovagal Syncope (Fainting) in textbook.

## Slide 171: Learning Objectives Lesson 31.3: Serum Specimen and Skin Puncture
Explain how the serum separator tube functions in the collection of a serum specimen.
Explain when a skin puncture would be preferred over a venipuncture.
Describe each of the following skin puncture devices: disposable semiautomatic lancet and reusable semiautomatic lancet.
List and describe the guidelines for performing a finger puncture.

## Slide 172: Serum (Slide 1 of 3)
Serum: Plasma from which the clotting factor fibrinogen has been removed
Normally clear and yellow
Serum contains dissolved substances
  Glucose
  Cholesterol
  Lipids
  Sodium

## Slide 173: Serum (Slide 2 of 3)
Serum contains dissolved substances
  Potassium
  Chloride
  Antibodies
  Hormones
  Enzymes

## Slide 174: Serum (Slide 3 of 3)
Many laboratory tests require a serum specimen
  To determine if substances are within normal range
  To detect any substances that are not normally present

## Slide 175: Tube Selection (Slide 1 of 2)
To collect serum
  Tube with no anticoagulants (red-stoppered or SST)

## Slide 176: Tube Selection (Slide 2 of 2)
Serum recovered is only part of total blood specimen
  Must use a tube that is 2½ times amount required for test
    Example: To obtain 2 mL of serum—must use a 5-mL red-stoppered or SST tube (2 × 2½ = 5)

## Slide 177: Preparation of the Specimen (Slide 1 of 2)
Allow tube to stand upright at room temperature for 30 to 45 minutes
  Allows clot formation; yields more serum
If centrifuged immediately:
  Clotting factors do not have time to settle into cell layer
  Result in formation of a fibrin clot in the serum layer
    Spongy substance that occupies space
    Interferes with adequate serum collection
Notes: A fibrin clot will also form in an SST if it is not allowed to stand.
Refer to Figure 31.22.

## Slide 178: Preparation of the Specimen (Slide 2 of 2)
Do not let blood stand for more than one hour
  Leaching of substances from cell layer into serum
    Leads to inaccurate test results

## Slide 179: Removal of Serum (Slide 1 of 5)
After allowing specimen to stand, centrifuge specimen for 10 minutes

## Slide 180: Removal of Serum (Slide 2 of 5)
Red stopper tube: Remove serum with a pipette and place it in transfer tube
  Do not disturb cell layer of the clot
    Draws RBCs into serum layer
  If cells enter serum, recentrifuge the specimen

## Slide 181: Removal of Serum (Slide 3 of 5)
Hold serum up to light to inspect for the presence of:
  Intact RBCs
  Hemolyzed blood
  If present, specimen has a reddish appearance
    Must recentrifuge

## Slide 182: Removal of Serum (Slide 4 of 5)
After centrifuging intact RBCs
  Cells settle to bottom of tube
  Serum can be removed

## Slide 183: Removal of Serum (Slide 5 of 5)
After centrifuging hemolyzed blood
  Serum will still have a reddish appearance
    RBCs have ruptured
    Releases hemoglobin into serum
  Not suitable for laboratory tests; inaccurate test results
  Must collect another specimen

## Slide 184: Serum Separator Tubes (Slide 1 of 5)
Serum separator evacuated tube (SST) facilitates collection of serum specimen
Identified by red and slate-gray stopper
  If using Hemogard tube: Gold stopper

## Slide 185: Serum Separator Tubes (Slide 2 of 5)
Used for collection and separation of blood
Thixotropic gel in bottom of tube
Notes: Refer to Figure 31.23A.

## Slide 186: Serum Separator Tubes (Slide 3 of 5)
Blood collected and placed upright for 30 to 45 minutes
  To allow for clot formation of blood cells
Centrifuge for proper length of time (10 minutes)
  Less than 10 minutes can result in an incomplete gel barrier

## Slide 187: Serum Separator Tubes (Slide 4 of 5)
During centrifugatio:
  Gel temporarily becomes fluid
  Moves to dividing point between serum and clotted cells
  Reforms into a solid gel
Serves as a barrier between serum and clot
Notes: Refer to Figure 31.23B.

## Slide 188: Serum Separator Tubes (Slide 5 of 5)
Serum can be transported in an SST
  Inspect tube carefully
    To make sure gel barrier is firmly attached to glass wall
  If a complete barrier has not formed:
    Remove serum; place it in transfer tube—prevents leaching of substances from cell layer into serum (leads to inaccurate test results)

## Slide 189: Skin Puncture (Slide 1 of 4)
Used to obtain capillary blood specimen
Also called capillary puncture
Testing done at medical office
Notes: A capillary is a minute blood vessel that is finer than hair.

## Slide 190: Skin Puncture (Slide 2 of 4)
Examples of tests
  Hemoglobin
  Hematocrit
  Blood glucose
  Mononucleosis
  Prothrombin time

## Slide 191: Skin Puncture (Slide 3 of 4)
Skin puncture performed when test requires small amount of blood
  Preferred for infants and young children
    Venipuncture is difficult to perform on children in these age groups
  Adult has no acceptable veins (as a last resort)

## Slide 192: Skin Puncture (Slide 4 of 4)
Before collecting specimen
  Select puncture site
  Select skin puncture device
  Obtain proper microcollection device

## Slide 193: Puncture Sites (Slide 1 of 2)
Fingertip preferred for adults
  Third or fourth finger
  Earlobe is no longer recommended
    Blood in earlobe contains a higher concentration of hemoglobin than fingertip
    Slower flow of blood makes it harder to collect specimen

## Slide 194: Puncture Sites (Slide 2 of 2)
Plantar surface of heel: Infant (birth to 1 year)
  Never perform finger puncture on an infant
    Amount of tissue between skin and bone is small—injury to bone is likely
  After child is walking—can perform on fingertip

## Slide 195: Skin Puncture Devices (Slide 1 of 5)
Types
  Disposable semiautomatic retractable lancet device
  Reusable semiautomatic retractable lancet device
Depth of puncture
  Adults: Must not be deeper than 3.1 mm
  Infants (heel) and children: Must not be deeper than 2.0 mm

## Slide 196: Skin Puncture Devices (Slide 2 of 5)
If puncture is too deep, may penetrate bone
  Could result in:
    Osteochondritis: Inflammation of bone and cartilage
    Osteomyelitis: Inflammation of bone due to bacterial infection
  To prevent, use spring-loaded blade available in different lengths to control the depth of the puncture
Notes: The blade length is listed on the box of lancets.

## Slide 197: Skin Puncture Devices (Slide 3 of 5)
Blade length selected
  Based on:
    Size of patient’s fingers
    Amount of blood specimen required

## Slide 198: Skin Puncture Devices (Slide 4 of 5)
Blade length selected
  Shorter blade
    Adults with thin fingers
    Children
    When only a drop of blood required
  Longer blade
    To obtain enough blood to fill a microcollection device

## Slide 199: Skin Puncture Devices (Slide 5 of 5)
OSHA recommends retractable lancets
  To reduce sharps injuries

## Slide 200: Disposable Semiautomatic Lancet (Slide 1 of 4)
Spring-loaded plastic holder
  Metal blade is inside holder
Different length blades available to control depth of the puncture
Plastic holder may be color coded for ease in identifying blade length
Notes: See Procedure 31.3: Skin Puncture – Disposable Semiautomatic Lancet Device.
Refer to Figure 31.24 A and B.

## Slide 201: Disposable Semiautomatic Lancet (Slide 2 of 4)
Plastic holder conceals blade
  Protects MA from accidental needlestick
  Patient cannot see blade during puncture
    Results in less apprehension

## Slide 202: Disposable Semiautomatic Lancet (Slide 3 of 4)
To perform puncture
  Lancet device placed on patient's skin
  Device is activated—methods:
    Depressing activator button on top of lancet
    Pushing lancet firmly onto puncture site
Notes: Place lancet firmly against the skin for proper puncture.

## Slide 203: Disposable Semiautomatic Lancet (Slide 4 of 4)
To perform puncture
  Blade is forced into skin by spring
  Blade retracts into the holder
  Lancet device is discarded into biohazard sharps container

## Slide 204: Reusable Semiautomatic Lancet (Slide 1 of 3)
Wide variety available
  Not all are appropriate for use in the medical office
Safest type
  The part that may become contaminated is retractable and disposed of easily
  Reduces risk of sharps injuries

## Slide 205: Reusable Semiautomatic Lancet (Slide 2 of 3)
Glucolet II: Plastic, spring-loaded holder and a lancet/endcap
  Plastic holder is reusable
  Lancet/endcap is disposable
Notes: Refer to Figure 31.24.C.

## Slide 206: Reusable Semiautomatic Lancet (Slide 3 of 3)
To perform puncture
  Lancet/endcap is placed on skin
  Release button is depressed
  Blade is forced into skin by spring
  Blade retracts into the endcap
  Lancet/endcap is removed; discarded into biohazard sharps container

## Slide 207: Microcollection Devices
Specimen may be placed directly onto a reagent strip
  Example: Blood glucose monitors
May be collected with a microcollection device
  Device used depends on laboratory equipment being used
  Examples: Capillary tubes, microcollection tubes

## Slide 208: Capillary Tubes
Consists of disposable glass or plastic tube
Depending on size, can hold 5 to 75 µL of blood
Used for hematocrit determination
Notes: Refer to Figure 31.25A.

## Slide 209: Microcollection Tubes (Slide 1 of 2)
Small plastic tube with removable blood collector tip
  Tip designed to collect capillary blood from skin puncture
  After collecting specimen, collector tip is removed, discarded, and replaced by a plastic plug

## Slide 210: Microcollection Tubes (Slide 2 of 2)
Small plastic tube with removable blood collector tip
  Available with or without additives
  Plugs are color coded to correspond to evacuated tube VP system
Notes: Refer to Figure 31.25B.

## Slide 211: Guidelines for Performing a Finger Puncture (Slide 1 of 14)
If laboratory test requires advance preparation:
  Verify that patient is prepared properly
Patient should be seated comfortably in a chair
  Arm firmly supported
  Palm facing up

## Slide 212: Guidelines for Performing a Finger Puncture (Slide 2 of 14)
Instruct patient to remain still
  Just before making puncture, tell patient a small stick will be felt
    Avoids startling patient
Notes: The MA should secure the finger in case the patient flinches.

## Slide 213: Guidelines for Performing a Finger Puncture (Slide 3 of 14)
Use lateral part of tip of third or fourth finger of nondominant hand
  Capillary bed is large
  Skin is easy to penetrate
  Puncture site should be free of:
    Lesions
    Scars
    Bruises
    Edema

## Slide 214: Guidelines for Performing a Finger Puncture (Slide 4 of 14)
Use lateral part of tip of third or fourth finger of nondominant hand
  Do not use index finger
    Skin is more callused, harder to penetrate
    Patient uses index finger more, will notice pain longer
  Do not use little finger
    Amount of tissue between skin surface and bone is small—could result in injury to bone

## Slide 215: Guidelines for Performing a Finger Puncture (Slide 5 of 14)
Site may be warmed; increases blood flow
  Gently massage finger from base to tip
  Place hand in warm water
Notes: Chemical packs are also available to warm puncture sites.

## Slide 216: Guidelines for Performing a Finger Puncture (Slide 6 of 14)
Cleanse site with antiseptic wipe and allow it to dry thoroughly
  If alcohol is not dry:
    Round drop of blood does not form on the finger—blood leaches out on patient's skin: difficult to collect
    Alcohol can enter blood specimen—leads to inaccurate test results
    Patient experiences a stinging sensation during puncture

## Slide 217: Guidelines for Performing a Finger Puncture (Slide 7 of 14)
Firmly grasp finger in front of the most distal knuckle joint
  Apply enough pressure to cause fingertip to become hard and red
    Ensures adequate penetration and depth of puncture
Select the site
  Make puncture in fleshy portion of fingertip
    Slightly to the side of center

## Slide 218: Guidelines for Performing a Finger Puncture (Slide 8 of 14)
Select the site
  Do not puncture side or very tip of finger
    To prevent injury to the bone
  Position blade perpendicular to lines of the fingerprint (not parallel)
    Facilitates formation of well-formed drop of blood that is easy to collect—if not perpendicular, blood flow follows lines of fingerprint and runs down finger

## Slide 219: Guidelines for Performing a Finger Puncture (Slide 9 of 14)
Firmly press lancet device against puncture site
  Activate spring-loaded device
  If not enough pressure is applied, puncture is not deep enough
    Poor blood flow results; may need to puncture patient again
Notes: Refer to Figure 31.26.

## Slide 220: Guidelines for Performing a Finger Puncture (Slide 10 of 14)
Firmly press lancet device against puncture site
  With a good puncture, blood flows freely
  Deep puncture hurts no more than a superficial one

## Slide 221: Guidelines for Performing a Finger Puncture (Slide 11 of 14)
Wipe away the first drop of blood with a gauze pad
  Diluted with alcohol and tissue fluid
    Not a suitable specimen: Could cause inaccurate test results

## Slide 222: Guidelines for Performing a Finger Puncture (Slide 12 of 14)
Allow large drop to form by applying gentle pressure near the puncture
  Can massage the tissue surrounding the puncture site to promote blood flow
  Do not squeeze excessively: Causes dilution of specimen with tissue fluid
    May lead to inaccurate test results

## Slide 223: Guidelines for Performing a Finger Puncture (Slide 13 of 14)
Allow large drop to form by applying gentle pressure near the puncture
  Collect specimen using appropriate microcollection device

## Slide 224: Guidelines for Performing a Finger Puncture (Slide 14 of 14)
Check site to make sure bleeding has stopped
  Apply adhesive bandage if needed

## Slide 225
Questions?