## Slide 1: Hematology Chapter 32

## Slide 2: Learning Objectives Lesson 32.1: Hematology (Slide 1 of 2)
List the tests included in a complete blood count.
State the reference range for each of the following hematologic tests:
  Hemoglobin
  Hematocrit
  Red and white blood cell counts
  Differential cell count
  Platelet count
  PT/INR

## Slide 3: Learning Objectives Lesson 32.1: Hematology (Slide 2 of 2)
State the purpose of the hematocrit and list the layers into which the blood separates after it has been centrifuged.
Explain how the RBC indices can help diagnose the various types of anemia.
Explain the purpose of the differential cell count.
State the purpose of the PT/INR test.
List the advantages of PT/INR home testing.

## Slide 4: Introduction to Hematology (Slide 1 of 7)
The study of blood
  Includes:
    Morphological appearance of blood cells
    Function of blood cells
    Diseases of the blood and blood-forming tissues

## Slide 5: Introduction to Hematology (Slide 2 of 7)
Laboratory analysis in hematology
  Purpose: Examining blood to detect pathologic conditions
  Includes:
    Performing blood cell counts
    Evaluating the clotting ability of blood
    Identifying cell types
  Determines if each blood component falls within its reference range
    Hemoglobin (Hgb or Hb)
    Hematocrit (Hct)
    White blood cell (WBC) count
Notes: The complete blood count (CBC) test is a screening test.

## Slide 6: Introduction to Hematology (Slide 3 of 7)
Specific hematology tests
  Red blood cell (RBC) count
  Differential white blood cell count (diff)
  Erythrocyte sedimentation rate (ESR)
  Platelet count (Plt)

## Slide 7: Introduction to Hematology (Slide 4 of 7)
Hematology tests
  May be performed in the medical office
  CLIA-waived automated blood analyzers designed for the medical office
    Perform laboratory tests with accurate test results and in a short time

## Slide 8: Introduction to Hematology (Slide 5 of 7)
Hematology tests
  CLIA-waived automated blood analyzers designed for the medical office
    Operating manual accompanies each analyzer—information included: Operation; test parameters; care and maintenance

## Slide 9: Introduction to Hematology (Slide 6 of 7)
Complete blood count (CBC)
  Most frequently performed hematological test
  Performed on:
    New patients
    Patients with a pathologic condition

## Slide 10: Introduction to Hematology (Slide 7 of 7)
Complete blood count (CBC)
  Tests included in a CBC
    White blood cell (WBC) count
    Red blood cell (RBC) count
    Platelet count
    Hemoglobin (Hgb or Hb)
    Hematocrit (Hct)
    Differential white blood cell count (diff)
    Red blood cell indices
Notes: An example of a laboratory report indicating results of a CBC is presented in Figure 32.1.

## Slide 11: Reference Ranges (Slide 1 of 2)
Hemoglobin
  Adult female: 12-16 g/dL
  Adult male: 14-18 g/dL
Hematocrit
  Woman: 37%-47%
  Man: 40%-54%
Red and white blood cell counts
  WBC: 4,500-11,000 WBCs per cubic millimeter of blood
  RBC (woman): 4-5.5 million RBCs per cubic millimeter of blood
  RBC (man): 4.5-6.2 million RBCs per cubic millimeter of blood

## Slide 12: Reference Ranges (Slide 2 of 2)
Differential cell count
  Neutrophils: 40% to 75%
  Eosinophils: 1% to 6%
  Basophils: 0% to 2%
  Lymphocytes: 20% to 40%
  Monocytes: 3% to 10%
Platelet count
PT/INR
  10-20 seconds

## Slide 13: Hemoglobin Determination (Slide 1 of 9)
Hemoglobin (Hgb): Major component of RBCs
Hemoglobin transports oxygen to tissue cells
Responsible for red color of RBCs

## Slide 14: Hemoglobin Determination (Slide 2 of 9)
Reference range
  Adult female: 12 to 16 g/dL
  Adult male: 14 to 18 g/dL
Hemoglobin performed as individual test or as part of CBC

## Slide 15: Hemoglobin Determination (Slide 3 of 9)
Decreased hemoglobin level occurs with:
  Anemia (especially iron-deficiency anemia)
  Hyperthyroidism
  Cirrhosis of the liver
  Severe hemorrhaging

## Slide 16: Hemoglobin Determination (Slide 4 of 9)
Decreased hemoglobin level occurs with:
  Hemolytic reactions
  Certain systemic diseases
    Leukemia
    Hodgkin’s disease

## Slide 17: Hemoglobin Determination (Slide 5 of 9)
Increased hemoglobin level occurs with:
  Polycythemia
  COPD
  CHF

## Slide 18: Hemoglobin Determination (Slide 6 of 9)
CLIA-waived hemoglobin analyzer
  Used to measure hemoglobin in the medical office
  Permits processing of the specimen in a short time
    With accurate and reliable test results
  Allows physician to evaluate the condition while patient is still at office
  Requires only a finger puncture to perform test rather than venipuncture
Notes: Refer to Figure 32.2.

## Slide 19: Hemoglobin Determination (Slide 7 of 9)
CLIA-waived hemoglobin analyzer
  Manufacturer provides an operating manual that includes:
    Information to perform quality control procedures—important to ensure analyzer is functioning properly
    Precautions to take when running test
    Storage and stability of testing devices and control reagents
    Collection of specimen
    Procedure for testing the specimen

## Slide 20: Hemoglobin Determination (Slide 8 of 9)
CLIA-waived hemoglobin analyzer
  Follow hemoglobin procedure exactly as presented in the operating manual
    Testing device placed in analyzer
    Skin puncture is performed
    Drop of blood placed on testing device
    Analyzer determines hemoglobin results
    Results displayed on screen of analyzer

## Slide 21: Hemoglobin Determination (Slide 9 of 9)
CLIA-waived hemoglobin analyzer
  Follow hemoglobin procedure exactly as presented in the operating manual
    Results are recorded in patient’s chart: Date and time; name of test (hemoglobin); results measured in g/dL

## Slide 22: Hematocrit (Slide 1 of 6)
Abbreviated Hct
Hematocrit means “to separate blood”
  Solid cellular elements separated from plasma
    By centrifuging an anticoagulated blood specimen
  Heavier RBCs become packed and settle to bottom of the tube
Notes: The hematocrit capillary tube is lined with an anticoagulant.

## Slide 23: Hematocrit (Slide 2 of 6)
Hematocrit means “to separate blood”
  Top layer: Contains clear, straw-colored plasma
  Between layers is small, thin, yellowish-gray layer
    Buffy coat contains platelets and WBCs
Notes: Refer to Figure 32.3.

## Slide 24: Hematocrit (Slide 3 of 6)
Purpose of hematocrit: Measures percentage of packed RBCs in whole blood
Reference range
  Women: 37% to 47%
  Men: 40% to 54%

## Slide 25: Hematocrit (Slide 4 of 6)
Low reading: May indicate anemia
High reading: May indicate polycythemia
Used with other tests to diagnose patient’s condition

## Slide 26: Hematocrit (Slide 5 of 6)
Microhematocrit method
  Most often used in the medical office
  Blood obtained by skin puncture
    Using a disposable capillary tube lined with anticoagulant
  Blood drawn into the capillary tube
    Sealed with a sealing compound

## Slide 27: Hematocrit (Slide 6 of 6)
Microhematocrit method
  Centrifuged for 3 to 5 minutes
    Packs the RBCs
  Results read at top of the packed cell column
Notes: See Procedure 32.1: Hematocrit.

## Slide 28: White Blood Cell Count (Slide 1 of 6)
Approximate measurement of number of WBCs in circulating blood
Adult reference range: 4,500 to 11,000 WBC/mm3 of blood
  Expressed as 4.5 to 11.0 (×103/mm3) on laboratory reports

## Slide 29: White Blood Cell Count (Slide 2 of 6)
Leukocytosis: Increase in the number of WBCs (greater than 11,000)
  Most commonly seen in acute infections
    Appendicitis
    Chicken pox
    Diphtheria
    Infectious mononucleosis
    Meningitis
    Rheumatic fever

## Slide 30: White Blood Cell Count (Slide 3 of 6)
Leukocytosis: Increase in the number of WBCs (greater than 11,000)
  Normal elevation can occur in:
    Pregnancy
    Strenuous exercise
    Stress
    Treatment with corticosteroids

## Slide 31: White Blood Cell Count (Slide 4 of 6)
Leukopenia: Decreased WBC
  Viral infections
  Chemotherapy
  Radiation therapy

## Slide 32: White Blood Cell Count (Slide 5 of 6)
If WBC is performed in the medical office
  CLIA-nonwaived automated blood cell counter must be used
    Moderately complex test

## Slide 33: White Blood Cell Count (Slide 6 of 6)
Blood cell counter
  Can also perform:
    RBC
    Platelet count
    Hemoglobin
    Hematocrit
    Differential WBC count
    Calculation of RBC indices
Notes: Refer to Figure 32.4.

## Slide 34: Red Blood Cell Count (Slide 1 of 3)
Measurement of number of RBCs in whole blood
Reference range
  Women: 4 to 5.5 million/mm3 of blood
    On laboratory report expressed as 4 to 5.5 (×106 mm3)
  Men: 4.5 to 6.2 million/mm3 of blood
    On laboratory report expressed as 4.5 to 6.2 (×106 mm3)

## Slide 35: Red Blood Cell Count (Slide 2 of 3)
Performed using blood cell counter
Decrease in red blood count
  Anemia
  Hodgkin's disease
  Leukemia

## Slide 36: Red Blood Cell Count (Slide 3 of 3)
Increase in red blood count
  Polycythemia
  Dehydration
  Pulmonary fibrosis

## Slide 37: Red Blood Cell Indices (Slide 1 of 4)
Measurements that are reported as part of the CBC
Provide information about the size and hemoglobin content of red blood cells
Notes: Name the five WBCs.

## Slide 38: Red Blood Cell Indices (Slide 2 of 4)
RBC indices include:
  MCV: Mean corpuscular volume
  MCH Mean corpuscular hemoglobin
  MCHC: Mean cell hemoglobin concentration
  RDW: Red cell distribution width

## Slide 39: Red Blood Cell Indices (Slide 3 of 4)
Obtained from calculations performed on certain test results included in a CBC
  RBC count, hemoglobin, and hematocrit
  Calculation automatically performed by blood cell analyzer that performs CBC

## Slide 40: Red Blood Cell Indices (Slide 4 of 4)
Anemia: Decrease in the number of red blood cells or the amount of hemoglobin
  Are over 400 types of anemia
    Many are rare conditions
  Each of the various forms of anemia (e.g., iron-deficiency anemia, pernicious anemia) may alter one or more of the RBC indices
    This information is used to assist in the diagnosis of the type of anemia present

## Slide 41: White Blood Cell Differential Count (Slide 1 of 3)
Five types of WBCs each having a certain:
  Appearance
  Size
  Shape
  Function
Notes: Refer to Figure 32.5.

## Slide 42: White Blood Cell Differential Count (Slide 2 of 3)
Purpose of differential
  To identify and count the five types of WBCs in a representative blood sample
    Increase or decrease in one or more types—assists physician in making a diagnosis

## Slide 43: White Blood Cell Differential Count (Slide 3 of 3)
Can be performed automatically or manually
  Manual method
    Allows for closer inspection of abnormal white blood cells
Automatic analyzer flags abnormalities
  Laboratory then performs a manual differential count

## Slide 44: Automatic Method
Blood cell counter used (e.g., Coulter counter)
Specimen requirement
  EDTA-anticoagulated blood specimen
    Lavender-stoppered tube
Blood cell counter automatically performs differential count
  Prints results on a laboratory report

## Slide 45: Manual Method (Slide 1 of 6)
Blood specimen can be made from:
  Fresh whole blood (preferred)
  EDTA-anticoagulated blood
    Smear must be made within 24 hours after collection
Other anticoagulants alter:
  Morphology of WBCs
  Staining reaction of WBCs
Notes: See Procedure 32.2: Preparation of a Blood Smear for a Differential Cell Count.

## Slide 46: Manual Method (Slide 2 of 6)
Slides placed in a protective container for transport to outside laboratory
Laboratory personnel stain smear (Wright’s stain)
  Because WBCs are clear and colorless
  After staining
    Nucleus, cytoplasm, and granules take characteristic color of their cell type—aids in identification of the five different types of white blood cells

## Slide 47: Manual Method (Slide 3 of 6)
Minimum of 100 WBCs identified
  Each assigned to an appropriate category
    Neutrophils
    Eosinophils
    Basophils
    Lymphocytes
    Monocytes

## Slide 48: Manual Method (Slide 4 of 6)
Number of each type is recorded as a percentage
  Reflects overall distribution of WBCs in patient’s blood

## Slide 49: Manual Method (Slide 5 of 6)
Slide also examined for abnormalities in RBC morphology
  Size
  Shape
  Structure

## Slide 50: Manual Method (Slide 6 of 6)
Reference range for differential count
  Neutrophils: 40% to 75%
  Eosinophils: 1% to 6%
  Basophils: 0% to 2%
  Lymphocytes: 20% to 40%
  Monocytes: 3% to 10%

## Slide 51: PT/INR (Slide 1 of 6)
Combination of:
  PT (prothrombin time) test
  Mathematical calculation
Calculation performed on PT test to arrive at a standardized value
  Known as an INR (international normalized ratio)

## Slide 52: PT/INR (Slide 2 of 6)
PT test
  Measures how long it takes blood to clot
  Results measured in seconds
  Reference range: 10 to 20 seconds
    Means blood should clot within 10 to 20 seconds

## Slide 53: PT/INR (Slide 3 of 6)
Variety of testing reagents can be used to measure PT
  Each works in a different way to assess the clotting ability of blood
  PT result obtained when using one reagent
    Cannot be compared to PT result tested using a different reagent

## Slide 54: PT/INR (Slide 4 of 6)
Variety of testing reagents can be used to measure PT
  To account for differences
    Coagulation analyzer performs a mathematical calculation on PT to convert to a standardized ratio: Known as an INR
  INR allows patient’s PT test results to be compared
    Regardless of testing reagent used to run the test

## Slide 55: PT/INR (Slide 5 of 6)
PT/INR result
  Expressed as a number because value is a ratio
  Does not have a unit of measurement attached to it
  Healthy individual with a normal clotting ability
    Should have a PT/INR result that falls between 0.8 and 1.2

## Slide 56: PT/INR (Slide 6 of 6)
PT/INR result
  Higher the number, the longer it takes for blood to clot
    Example: PT/INR of 3.0—blood would take longer to clot than an individual with a PT/INR of 1.0
  Risk of spontaneous bleeding begins to rise dramatically as INR reaches 4.0 or higher

## Slide 57: Purpose (Slide 1 of 9)
Most commonly performed on patients undergoing long-term warfarin therapy
Warfarin
  Brand names
    Coumadin
    Jantoven
  Anticoagulant that inhibits the formation of blood clots in the body
  Interferes with the blood clotting mechanism in the body
    Takes blood longer to clot

## Slide 58: Purpose (Slide 2 of 9)
PT/INR test measures effect that warfarin has on the clotting ability of the blood
Warfarin prescribed for patients who are likely to form clots
  Heart attack
  Stroke
  Thrombophlebitis
    Also known as deep vein thrombosis (DVT)

## Slide 59: Purpose (Slide 3 of 9)
Warfarin prescribed for patients who are likely to form clots
  Atrial fibrillation: Irregular heartbeat that can cause blood to pool in the heart
    May cause a blood clot to form—can travel to the brain resulting in a stroke
  Heart valve replaced with a mechanical valve
    Increased risk of clot forming on a mechanical valve—may cause a heart blockage

## Slide 60: Purpose (Slide 4 of 9)
PT/INR test also ordered on patients exhibiting signs and symptoms of a coagulation disorder
  Unexplained nosebleeds
  Excessive bleeding from gums
  Easy bruising
  Heavy menstrual periods
  Unexplained blood in the stool or urine

## Slide 61: Purpose (Slide 5 of 9)
Physician determines PT/INR range for patient on long-term warfarin therapy
  Depends on condition being treated
Desired PT/INR range for a patient on warfarin therapy
  Following a stroke or heart attack or for a patient with recurring atrial fibrillation
    Between 2.0 and 3.0
  For a patient with a mechanical valve replacement
    Between 2.5 and 3.5

## Slide 62: Purpose (Slide 6 of 9)
Goal of warfarin therapy
  Increase clotting time to a level that prevents formation of blood clots
    Without causing excessive bleeding or bruising
Patient must undergo periodic PT/INR testing
  To ensure patient remains in his or her ideal PT/INR range
    Minimizes complications of warfarin therapy

## Slide 63: Purpose (Slide 7 of 9)
Frequency of testing depends on:
  Stability of patient’s previous test results
  Occurrence of conditions that may cause test results to fall outside of the patient’s desired range

## Slide 64: Purpose (Slide 8 of 9)
When patient is first placed on warfarin therapy
  PT/INR test is performed once or twice a week
    To assess patient’s response to warfarin
  Based on PT/INR results
    Dosage adjusted so that results become stable and consistently fall within patient’s ideal PT/INR range

## Slide 65: Purpose (Slide 9 of 9)
Once test results become stabilized
  Patient should have a PT/INR test performed every 2 to 4 weeks
If the PT/INR result is outside of the patient’s predetermined ideal range
  Physician adjusts warfarin dosage
  Goal is to bring patient back into optimal range

## Slide 66: Collection of the Specimen (Slide 1 of 3)
Requires a small (4 to 5 mL) tube of blood
Must collect in a sodium citrate tube (light blue)
  Sodium citrate prevents specimen from clotting without affecting test results
Notes: Refer to Figure 32.6.

## Slide 67: Collection of the Specimen (Slide 2 of 3)
Butterfly method
  Draw a 5-mL red-stoppered discard tube first (before light blue tube)
    To prevent air in tubing from entering the light blue tube
  If light blue-stoppered tube is filled first
    Results in an incorrect anticoagulant-to-blood ratio—leads to inaccurate test results

## Slide 68: Collection of the Specimen (Slide 3 of 3)
Important to fill tube to the exhaustion of the vacuum
  Underfilled tube leads to inaccurate test results
Most light blue tubes have a fill indicator
  To determine if tube has been completely filled
Once tube has been drawn
  Immediately and gently invert it three to four times
    To mix anticoagulant with blood
Place in a biohazard specimen bag along with a laboratory request
  For pickup by laboratory courier

## Slide 69: Performing a PT/INR Test (Slide 1 of 4)
CLIA-waived handheld coagulation analyzers are commercially available
  For performing a PT/INR test in the medical office
Advantage of coagulation analyzers
  Require only a finger puncture (rather than a venipuncture)
Notes: Refer to Figure 32.7.

## Slide 70: Performing a PT/INR Test (Slide 2 of 4)
Coagulation analyzer operating manual includes information on:
  Quality control procedures
  Precautions to take when running the test
  Storage and stability of testing strips
  Collection of the specimen
  Procedure for testing the specimen

## Slide 71: Performing a PT/INR Test (Slide 3 of 4)
Follow PT/INR procedure exactly as presented in the operating manual
Basic procedure
  Place a testing strip in the analyzer
  Perform a skin puncture
  Place a drop of blood on the strip

## Slide 72: Performing a PT/INR Test (Slide 4 of 4)
Basic procedure
  Countdown period
    Analyzer determines PT results
    Calculates INR
  Results are displayed on screen of the analyzer
  Record results in patient’s chart
    Date and time
    Name of test (PT/INR)
    Ratio value

## Slide 73: PT/INR Home Testing (Slide 1 of 4)
Health insurance company of a patient on long-term warfarin therapy
  May provide the patient with a coagulation analyzer to test blood at home
Notes: The medical assistant may need to instruct the patient in the procedure for performing the test at home.
Refer to Figure 32.8.

## Slide 74: PT/INR Home Testing (Slide 2 of 4)
Patient does not have to make periodic visits to a laboratory or medical office
  To have a PT/INR test performed
Patient is able to test blood without a laboratory order
  Can check PT/INR immediately when conditions occur that might indicate a problem
    Examples: Nosebleeds, bleeding gums, or unexplained bruising
    Treatment can be instituted immediately to prevent the problem from getting worse

## Slide 75: PT/INR Home Testing (Slide 3 of 4)
Other factors that can affect the PT/INR results
  Change in diet
  Prescription and OTC medications that interact with warfarin
  Vitamins
  Herbal preparations

## Slide 76: PT/INR Home Testing (Slide 4 of 4)
Other factors that can affect the PT/INR results
  Change in level of exercise
  Illness
  Smoking
  Alcohol consumption
Important for patients to keep physician informed
  Certain factors that may alter their body’s response to warfarin

## Slide 77
Questions?